## Slide 1: CS 203 A: Advanced Computer Architecture Winter 2018
Instructor
Laxmi N. Bhuyan
Office: WCH 442
E-mail: bhuyan@cs.ucr.edu
Tel: (951) 827-2281
Office Hours: M, Th – 3.30-4.30 pm

## Slide 2: CS 203A Course Syllabus, Winter 2018
Text: Computer Architecture: A Quantitative Approach by Hennessy and Patterson, MK Publisher, 5th Edition
Introduction to computer Architecture, Performance (Chapter 1)
Memory Hierarchy Design (Appendix B and Chapter 2)
Review of Pipelining, Hazards, Branch Prediction (Appendix C)
Instruction level parallelism, Dynamic scheduling, and Speculation (Appendix C and Chapter 3)
Introduction to Multiprocessors and Thread Level Parallelism (Chapter 5)
Prerequisite: CS 161 or consent of the instructor

## Slide 3: Grading
Grading: Based on Curve
Test1: 30 points
Test 2: 40 points
Project (3 Phases): 30 points
Home assignments may be given to practice for the test, but won’t be graded.
One project is based on group of 2 students. Use Architecture simulator.

## Slide 4: What is “Computer Architecture”?
I/O system
Processor
Compiler
Operating System
(Unix; Windows 9x)
Application (Netscape)
Digital Design
Circuit Design
Instruction Set
Architecture
Key Idea: levels of abstraction
  hide unnecessary implementation details
  helps us cope with enormous complexity of real systems
Datapath & Control
transistors, IC layout
Memory
Hardware
Software
Assembler
CS 203

## Slide 5: Instruction Set: The Critical Interface
instruction set
software
hardware

## Slide 6
Chapter 1
Fundamentals of Quantitative Design and Analysis
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 7: The von Neumann Computer
Von Neumann Computer: A program is written as a sequence of instructions, represented by binary numbers. The instructions are stored in the memory just as data. They are read one by one, decoded and then executed by the CPU.
Stored-Program Concept – Storing programs as numbers – by John von Neumann – Eckert and Mauchly worked in engineering the concept.
Moore’s Law– The number of transistors in a CPU double every 1.5 years => CPU power

## Slide 8: Defining Computer Architecture
“Old” view of computer architecture:
  Instruction Set Architecture (ISA) design
  i.e. decisions regarding:
    registers, memory addressing, addressing modes, instruction operands, available operations, control flow instructions, instruction encoding
More “System” architecture:
  Specific requirements of the target machine
  Design to maximize performance within constraints: cost, power, and availability
  Includes ISA, microarchitecture, Compiler, O/S
Defining Computer Architecture

## Slide 9: Computer Technology
Performance improvements:
  Improvements in semiconductor technology
    Feature size, clock speed
  Improvements in computer architectures
    Enabled by compilers, UNIX
    ILP and multithreading
  Together have enabled:
    Lightweight computers
    Productivity-based managed/interpreted programming languages
Introduction

## Slide 10: Current Trends in Architecture
Cannot continue to leverage Instruction-Level parallelism (ILP)
  Single processor performance improvement ended in 2003 due to the power wall
New models for performance:
  Data-level parallelism (DLP)
  Thread-level parallelism (TLP)
  Request-level parallelism (RLP)
These require explicit restructuring of the application
Introduction

## Slide 11: Classes of Computers
Personal Mobile Device (PMD)
  e.g. start phones, tablet computers
  Emphasis on energy efficiency and real-time
Desktop Computing
  Emphasis on price-performance
Servers
  Emphasis on availability, scalability, throughput
Clusters / Warehouse Scale Computers
  Used for “Software as a Service (SaaS)”
  Emphasis on availability and price-performance
  Sub-class: Supercomputers, emphasis: floating-point performance and fast internal networks
Embedded Computers
  Emphasis: price
Classes of Computers

## Slide 12: RISC Vs CISC
CISC (complex instruction set computer)
  VAX, Intel X86, IBM 360/370, etc.
RISC (reduced instruction set computer)
  MIPS, DEC Alpha, SUN Sparc, IBM 801

## Slide 13: RISC vs. CISC
Characteristics of ISAs
Motivation for RISC: powerful and complex instructions are rarely used but slow down the clock => RISC design. Use silicon space for cache, TLB, etc
Only Load/Store instructions do memory access

## Slide 14: MIPS Instruction Layout
Load/Store Architecture

## Slide 15
IBM 360/370 Instruction Formats

## Slide 16
An x86-64 instruction may be at most 15 bytes in length. It consists of the following components in the given order, where the prefixes are at the least-significant (lowest) address in memory:
Legacy prefixes (1-4 bytes, optional)
Opcode with prefixes (1-4 bytes, required)
ModR/M (1 byte, if required)
SIB (1 byte, if required)
Displacement (1, 2, 4 or 8 bytes, if required)
Immediate (1, 2, 4 or 8 bytes, if required)
Intel IA Instruction Formats

## Slide 17: Uniprocessor Performance
Constrained by power, instruction-level parallelism, memory latency
RISC
Instruction Level Parallelism (ILP)
Multicore
processor
The Power Wall

## Slide 18: Measuring Performance
Typical performance metrics:
  Response time
  Throughput
Speedup of X relative to Y
  Execution timeY / Execution timeX
Execution time
  Wall clock time: includes all system overheads
  CPU time: only computation time
Benchmarks
  Kernels (e.g. matrix multiply)
  Toy programs (e.g. sorting)
  Synthetic benchmarks (e.g. Dhrystone)
  Benchmark suites (e.g. SPEC06fp, TPC-C)
Measuring Performance

## Slide 19: Principles of Computer Design
The Processor Performance Equation
Principles

## Slide 20: Principles of Computer Design
Principles
Different instruction types having different CPIs

## Slide 21
EXAMPLE
Frequency of FP operations = 25% and average CPI of FP operations = 4.0
Average CPI of other instructions = 1.33
Frequency of FPSQR instructions = 2% and CPI for FPSQR = 20
Two design alternatives are to either decrease the CPI of FPSQR to 2 or to decrease the average CPI of all FP operations to 2.5. Compare the performance of the two alternatives

## Slide 22: Example
Instruction mix of a RISC architecture.
Currently, it is a load-store architecture. Add a register-memory ALU instruction.
=> One op. in register, one op. in memory
=> The new instruction will take 2 cc but will also increase the Branches to 3 cc.
HW: What fraction of loads must be eliminated with the new instruction for this to pay off?

## Slide 23: Parallelism
Classes of parallelism in applications:
  Data-Level Parallelism (DLP)
  Task-Level Parallelism (TLP)
Classes of architectural parallelism:
  Instruction-Level Parallelism (ILP)
  Vector architectures/Graphic Processor Units (GPUs)
  Thread-Level Parallelism (Multiprocessor)
  Request-Level Parallelism
Classes of Computers

## Slide 24: Flynn’s Taxonomy
Single instruction stream, single data stream (SISD)
Single instruction stream, multiple data streams (SIMD)
  Vector architectures
  Multimedia extensions
  Graphics processor units (GPU)
Multiple instruction streams, single data stream (MISD)
  No commercial implementation
Multiple instruction streams, multiple data streams (MIMD)
  Tightly-coupled MIMD
  Loosely-coupled MIMD
Classes of Computers

## Slide 25: Popular Flynn Categories
SISD (Single Instruction Single Data stream)
  A sequential computer which exploits no parallelism in either the instruction or data streams. Single control unit (CU) fetches single Instruction Stream (IS) from memory. The CU then generates appropriate control signals to direct single processing element (PE) to operate on single Data Stream (DS) i.e. one operation at a time.
MISD (Multiple Instruction Single Data stream)
  ???; multiple processors on a single data stream
  Multiple instructions operate on a single data stream. Uncommon architecture

## Slide 26
SIMD (Single Instruction Multiple Data)
A computer which exploits multiple data streams against a single instruction stream to perform operations which may be naturally parallelized.
  Examples: Illiac-IV (1st machine), Array processor, GPU, Simple programming model, Low overhead, Flexibility, suitable for most scientific applications, not suitable for general-purpose applications
MIMD (Multiple Instruction Multiple Data stream)
  Multiple autonomous processors simultaneously executing different instructions on different data.
  Examples: C.mmp (1st machine), All modern Multicore machines, Clusters, Top 500 supercomputers, Data centers
    Flexible
    Use off-the-shelf micros

## Slide 27: Compute Speedup – Amdahl’s Law
Speedup is due to enhancement(E):
TimeBefore
TimeAfter
= ExTimebefore x [(1-F) +
F
S
]
Speedup(E)
=
ExTimebefore
ExTimeafter
=
1
F
S
]
[(1-F) +
Let F be the fraction where enhancement is applied => Also, called parallel fraction and (1-F) as the serial fraction. S is the number of processors
Execution timeafter
Serial
Serial
Parallel F
When S -> infinity, E = 1/(1-F), If F is 10%, the maximum speed up is 1.1 for large S

## Slide 28: Amdahl’s Law – An Example
Q: Floating point instructions improved to run 2X;
but only 10% of execution time are FP ops. What is the execution time and speedup after improvement?
F = 0.1, S = 2
ExTimeafter = ExTimebefore x [ (1-0.1) + 0.1/2 ] = 0.95 ExTimebefore
Speedup =
ExTimebefore
ExTimeafter
=
1
0.95
= 1.053