## Slide 1: Lecture 10: Dynamic Branch Prediction

## Slide 2: Branch Prediction
Static prediction
  Always taken, always not taken
  Delayed Branch
  Compiler directed (branch likely, branch not likely)
Dynamic Branch Prediction
  1 bit predictor – remember last taken/not taken per branch
    Use a branch-prediction buffer or branch-history table with 1 bit entry
    Use part of the PC (low-order bits) to index buffer/table – Why?
      Multiple branches may share the same bit
    Invert the bit if the prediction is wrong
    Backward branches for loops will be mispredicted twice
    EX: If a loop branches 9 times in a row and not taken once, what is the prediction accuracy? Ans: Misprediction at the first loop and last loop => 80% prediction accuracy although branch is taken 90% time.

## Slide 3: Dynamic Branch Prediction
Basic 2-bit predictor:
  For each branch:
    Predict taken or not taken
    If the prediction is wrong two consecutive times, change prediction
Correlating predictor:
  Branch outcomes affect each other!!
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes of preceding m co-related branches
Local predictor:
  Consider a branch’s past along with other banks!!
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes for the last n occurrences of this branch
Tournament predictor:
  Combine correlating predictor with local predictor
Branch Prediction

## Slide 4: 2-bit Branch Prediction
Has 4 states instead of 2, allowing for more information about tendencies
A prediction must miss twice before it is changed
Good for backward branches of loops – occurs largely in a program

## Slide 5: Branch History Table (BHT) Or Branch Prediction Buffer
01
BHT
branch PC
BHT has limited size
2 bits by low N PC bits (e.g. 4K entries for 10 PC bits)
Uses low-order bits of branch PC to choose entry
Measure misprediction instead of prediction
Prediction Buffer = 4K

## Slide 6: Observations
Prediction Accuracy ranges from 99% to 82% or a misprediction rate of 1% to 18%
Mis-prediction for integer programs (gcc, espresso, eqntott, li) is substantially higher than FP programs (nasa7, matrix300, tomcatv, doduc, spice, fppp)
Branch penalty involves both mis-prediction rate and branch frequency, and is higher for integer benchmarks
Prediction accuracy improves with buffer size, but doesn’t improve beyond 4K entries (Fig. C.20 next slide)

## Slide 7
Figure C.17 Prediction accuracy of a 4096-entry 2-bit prediction buffer versus an infinite buffer for the SPEC89 benchmarks. Although these data are for an older version of a subset of the SPEC benchmarks, the results would be comparable for newer versions with perhaps as many as 8K entries needed to match an infinite 2-bit predictor.

## Slide 8: Advanced Branch Prediction Technique Correlating or Two-level Predictors
Correlating branch predictors also look at other branches for clues. Consider the following example.
  if (aa==2) -- branch b1
  aa = 0;
  if (bb==2) --- branch b2
  bb = 0;
  if(aa==bb) --- branch b3 – {Clearly depends on the results of b1 and b2}
  If b1 is not taken and b2 is not taken, b3 will be taken. If prediction of b3 is based only on its own history (instead of also those of b1 and b2), it is not an accurate prediction.
(1,2) predictor – uses history of 1 branch and uses a 2-bit predictor
(m,n) predictor – uses the behavior of last m branches to choose from 2**m branch predictors, each of which is an n-bit predictor for a single branch.

## Slide 9: Correlating or Two-level Branch Predictor
The global history of the most recent m branches is recorded in an m-bit shift register, where each bit represents whether the branch is taken (1) or not (0). The branch prediction buffer is indexed by using a concatenation of the low-order bits of the branch address with m-bit global history.
If we use m = 2 branches as histories, then there are 4 possibilities (T-T, T-NT, NT-NT, NT-T). For each possibility, we need to use a predictor (1-bit, 2-bit).
EXAMPLE:
Assume a (2,2) branch prediction buffer with 64 entries. A 2-bit shift register (global bits) is used to keep the history of the last two branches with 1 as taken (T) and 0 as not taken (NT). Then the 4 low-order bits of the branch + 2 global bits form a 6-bit address, shown below.
2 bits
4 bits
1
64
Address
Buffer

## Slide 10: Performance of Correlating Branch Prediction
With 1024 entries, (2,2) performs better than a 4096 entry non-correlating 2-bit predictor.
Outperforms a 2-bit predictor with infinite number of entries

## Slide 11: Tournament Predictor
Tournament Predictors use multiple predictors, one based on global information (many recent branches) and another based on local information (current branch), and combining them with a selector. Existing tournament predictors use a 2-bit saturating counter per branch (similar to a simple 2-bit counter) to choose from two predictors (local, global or mix) based on which was most effective in recent branch prediction.
DEC Alpha and the AMD Opteron processors use tournament predictors.
Intel Core Duo and i7 processors use sophisticated 2-level predictors.

## Slide 12
Figure 3.5 A tournament predictor using the branch address to index a set of 2-bit selection counters, which choose between a local and a global predictor. In this case, the index to the selector table is the current branch address. The two tables are also 2-bit predictors that are indexed by the global history and branch address, respectively. The selector acts like a 2-bit predictor, changing the preferred predictor for a branch address when two mispredicts occur in a row. The number of bits of the branch address used to index the selector table and the local predictor table is equal to the length of the global branch history used to index the global prediction table. Note that misprediction is a bit tricky because we need to change both the selector table and either the global or local predictor.

## Slide 13
Figure 3.4 The misprediction rate for three different predictors on SPEC89 as the total number of bits is increased. The predictors are a local 2-bit predictor, a correlating predictor that is optimally structured in its use of global and local information at each point in the graph, and a tournament predictor. Although these data are for an older version of SPEC, data for more recent SPEC benchmarks would show similar behaviour, perhaps converging to the asymptotic limit at slightly larger predictor sizes.
Tournament Predictor

## Slide 14
Figure 3.9 The misprediction rate for the integer SPECCPU2006 benchmarks on the Intel Core i7 920 and 6700. The misprediction rate is computed as the ratio of completed branches that are mispredicted versus all completed branches. This could understate the misprediction rate somewhat because if a branch is mispredicted and led to another mispredicted branch (which should not have been executed), it will be counted as only one misprediction. On average, the i7 920 mispredicts branches 1.3 times as often as the i7 6700.

## Slide 15: Branch Target Buffer (BTB)
BTB is a cache that contains the predicted PC value instead of whether the branch will take place or not (Ex. Loop address)
Is the current instruction a branch ?
• BTB provides the answer before the current instruction is decoded and therefore enables fetching to begin AT the IF-stage .
What is the branch target ?
• BTB provides the branch target if the prediction is a taken direct branch (for not taken branches the target is simply PC+4 ) .

## Slide 16: BTB Fig. 2.22

## Slide 17: BTB operations
BTB hit, prediction taken → 0 cycle delay
BTB hit, misprediction ≥ 2 cycle penalty – Correct BTB
BTB miss, branch ≥ 1 cycle penalty (Detected at the ID stage and entered in BTB)

## Slide 18: BTB Performance
Two things can go wrong
  BTB miss (misfetch)
  Mispredicted a branch (mispredict)
Suppose for branches, BTB hit rate of 85% and predict accuracy of 90%, misfetch penalty of 2 cycles and mispredict penalty of 5 cycles. What is the average branch penalty?
  2*(15%) + 5*(85%*10%)
BTB and BPT can be used together to perform better prediction

## Slide 19: Decoupled Fetch
Separate out IF from the pipeline and integrate with the following components. So, the pipeline consists of Issue, Read, EX, and WB
Integrated Branch Prediction – Branch predictor is part of the Instruction Fetch Unit (IFU).
Instruction Prefetch – Fetch instn from IM ahead of PC with the help of branch predictor and store in a prefetch buffer.
Instruction Memory Access and Buffering - Keep on filling the Instruction Queue independent of the execution => Decoupled Execution?
Instruction Fetch Unit (IFU).

## Slide 21: Branch Prediction Summary
The better we predict, the higher penalty we might incur for misprediction
2-bit predictors capture tendencies well
Correlating predictors improve accuracy, particularly when combined with 2-bit predictors
Accurate branch prediction does no good if we don’t know there was a branch to predict
BTB identifies branches in IF stage
BTB combined with branch prediction table identifies branches to predict, and predicts them well