## Slide 1: Lecture 12: Compiler Optimization Chapter 3

## Slide 2: Superscalar Processor: MIPS R4000 pipeline

## Slide 3: Consider RAW hazards only FP Loop: Where are the Hazards?
Consider the following example;
For (i=1000; i>0; i=i-1)
x[i] = x[i] + s;
MIPS code:
Loop: LD F0,0(R1) ;F0=vector element
ADDD F4,F0,F2 ;add scalar from F2
SD 0(R1),F4 ;store result
SUBI R1,R1,8 ;decrement pointer 8B (DW)
BNEZ R1,Loop ;branch R1!=zero
Where are the stalls?
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1

## Slide 4: FP Loop Showing Stalls
9 clocks: Rewrite code to minimize stalls?
1 Loop: LD F0,0(R1) ;F0=vector element
2 stall – LD delay
3 ADDD F4,F0,F2 ;add scalar in F2
4 stall
5 stall - 2 cycles delay between floating point store
6 SD 0(R1),F4 ;store result
7 SUBI R1,R1,8 ;decrement pointer 8B (DW)
8 BNEZ R1,Loop ;branch R1!=zero
9 stall ;delayed branch slot

## Slide 5: Minimizing Stalls Technique 1: Compiler Optimization
6 clocks, but actual work is only 3 cycles for LD, ADD and SD!!
Swap BNEZ and SD by changing address of SD
1 Loop: LD F0,0(R1)
2 SUBI R1,R1,8
3 ADDD F4,F0,F2
4 Stall – Needs 2 cycles delay between floating point operation and store. So, one stall is needed.
5 BNEZ R1,Loop ;delayed branch
6 SD 8(R1),F4 ;Address altered from 0(R1) to 8(R1) when moved past SUBI
Notes: 3 clocks doing work, 3 overhead (stall, branch, sub)

## Slide 6: Another Way
6 clocks
There isn’t much scope for further optimization because the basic block is too small
Basic Block: A sequence of instructions without entry or exit
1 Loop: LD F0,0(R1)
2 stall
3 ADDD F4,F0,F2
4 SUBI R1,R1,8 ;Move SD instruction to delay slot
5 BNEZ R1,Loop ;delayed branch
6 SD 8(R1),F4 ;Offset altered when moved past SUBI
Swap BNEZ and SD by changing address of SD
Notes: 3 clocks doing work, 3 overhead (stall, branch, sub)

## Slide 7: Compiler Technique 2: Loop Unrolling
1 Loop: LD F0,0(R1)
2 ADDD F4,F0,F2 ;1 cycle delay *
3 SD 0(R1),F4 ;drop SUBI & BNEZ – 2cycles delay *
4 LD F6,-8(R1)
5 ADDD F8,F6,F2 ; 1 cycle delay
6 SD -8(R1),F8 ;drop SUBI & BNEZ – 2 cycles delay
7 LD F10,-16(R1)
8 ADDD F12,F10,F2 ; 1 cycle delay
9 SD -16(R1),F12 ;drop SUBI & BNEZ – 2 cycles delay
10 LD F14,-24(R1)
11 ADDD F16,F14,F2 ; 1 cycle delay
12 SD -24(R1),F16 ; 2 cycles daly
13 SUBI R1,R1,#32 ;alter to 4*8;
14 BNEZ R1,LOOP ; Delayed branch
15 NOP
*As per earlier specifications, 1 cycle delay for FP operation after load. 2 cycles delay for store after FP.
15 + 4 x (1+2) = 27 clock cycles, or 6.75 cycles per iteration < 9 cycles without unrolling.
Disadvantage: Increase in Code memory and no. of registers.

## Slide 8: Minimize Stall + Loop Unrolling
1 Loop: LD F0,0(R1)
2 LD F6,-8(R1)
3 LD F10,-16(R1)
4 LD F14,-24(R1)
5 ADDD F4,F0,F2
6 ADDD F8,F6,F2
7 ADDD F12,F10,F2
8 ADDD F16,F14,F2
9 SD 0(R1),F4
10 SD -8(R1),F8
11 SD -16(R1),F12
12 SUBI R1,R1,#32
13 BNEZ R1,LOOP ; Delayed branch
14 SD 8(R1),F16 ; 8-32 = -24
14 clock cycles, or 3.5 per iteration

## Slide 9: How to obtain CPI<1?
Issue more than one instruction per cycle
Compiler needs to do a good job in scheduling code (rearranging code sequence) – statically scheduled
Fetch up to n instructions as an issue packet if issue width is n
Check hazards during issue stage (including decode)
  Issue checks are too complex to perform in one clock cycle
  Needs to check hazards within among current and all the earlier instructions in execution.
In effect an n-fold pipeline with complex issue logic and large set of bypass paths. EX: Dual Issue Pipeline below.
Type Pipe Stages Int. instruction IF ID EX MEM WB FP instruction IF ID EX MEM WB Int. instruction IF ID EX MEM WB FP instruction IF ID EX MEM WB Int. instruction IF ID EX MEM WB FP instruction IF ID EX MEM WB

## Slide 10: Execution with 2-Issue ILP
What if executed on a 2-issue superscalar machine with one integer (EX or Ld/St) unit and one FPU? Also assume that the FPU takes one cycle for a FP operation.
EX Unit FPU Unit
1 Loop: LD F0,0(R1)
2 SUBI R1,R1,8 Stall – Delay between LD and FP operation
3 Stall- ADDD F4,F0,F2
4 Stall - Delay between ADD and SD - 2 cycles
5 BNEZ R1,Loop
6 SD 8(R1),F4 - Branch Delay
No improvement - Basic Block Size is too small!
Consider the same MIPS code:
Loop: LD F0,0(R1); F0=vector element
ADDD F4,F0,F2; add scalar from F2
SD 0(R1),F4 ;store result
SUBI R1,R1,8 ; decrement pointer 8B (DW)
BNEZ R1,Loop; branch R1!=zero
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1

## Slide 11: Compiler Optimization – Technique 2: Loop Unrolling
EX: One LD/ST unit and one FP ALU
1 Loop: LD F0,0(R1)
2 LD F6,-8(R1)
3 LD F10,-16(R1) ADDD F4,F0,F2
LD F14,-24(R1) ADDD F8,F6,F2
SUBI R1,R1,#32 ADDD F12,F10,F2
6 SD 32(R1),F4 ADDD F16,F14,F2
7 SD 24(R1),F8
8 SD 16(R1),F12
9 BNEZ R1,LOOP ; Delayed branch
SD 8(R1),F16 ; R1 was reduced by 32.
So, 8-32 = -24
10 clock cycles, or 2.5 per iteration

## Slide 12: Steps Compiler Performed to Unroll
Check OK to move the S.D after DSUBUI and BNEZ, and find amount to adjust S.D offset
Determine unrolling the loop would be useful by finding that the loop iterations were independent
Rename registers to avoid name dependencies
Eliminate extra test and branch instructions and adjust the loop termination and iteration code
Determine loads and stores in unrolled loop can be interchanged by observing that the loads and stores from different iterations are independent
  requires analyzing memory addresses and finding that they do not refer to the same address.
Schedule the code, preserving any dependences needed to yield same result as the original code

## Slide 13: Static Multiple Issue: Very Long Instruction Word (VLIW) Architectures. Chapter 3.7 EX:Intel/HP Itanium
Wide-issue processor that relies on compiler to
  Packet together independent instructions to be issued in parallel
  Schedule code to minimize hazards and stalls
Very long instruction words (3 to 8 operations)
  Can be issued in parallel without checks
  If compiler cannot find independent operations, it inserts nops
Advantage: simpler HW for wide issue
  Faster clock cycle
  Lower design & verification cost
Disadvantages:
  Code size
  Requires aggressive compilation technology

## Slide 14: Traditional VLIW Hardware
Multiple functional units, many registers (e.g. 128)
  Large multiported register file (for N FUs need ~3N ports)
Simple instruction fetch unit
  No checks, direct correspondence between slots & FUs
Instruction format
  16 to 24 bits per op => 5*16=80 bits to 5*24=120 bits wide
  Can share immediate fields (1 per long instruction)

## Slide 15
Itanium Microarchitecture

## Slide 16: Consider the Previous Example
EX: One LD/ST unit and one FP ALU
1 Loop: LD F0,0(R1)
2 LD F6,-8(R1)
3 LD F10,-16(R1) ADDD F4,F0,F2
4 LD F14,-24(R1) ADDD F8,F6,F2
5 SD 0(R1),F4 ADDD F12,F10,F2
6 SD -8(R1),F8 ADDD F16,F14,F2
7 SD -16(R1),F12
8 SUBI R1,R1,#32
9 BNEZ R1,LOOP ; Delayed branch
SD 8(R1),F16 ; R1 was reduced by 32. So, 8-32 = -24 10 clock cycles, or 2.5 per iteration
MIPS code:
Loop: LD F0,0(R1) ;F0=vector element
ADDD F4,F0,F2 ;add scalar from F2
SD 0(R1),F4 ;store result
SUBI R1,R1,8 ;decrement pointer 8B (DW)
BNEZ R1,Loop ;branch R1!=zero
How does this change with a VLIW processor?

## Slide 17: Loop Unrolling in VLIW Hardware in Previous Slide: 2 LD/ST, 2 FPU, 1 INT
Memory Memory FP FP Int. op/ Clock reference 1 reference 2 operation 1 op. 2 branch
L.D F0,0(R1) L.D F6,-8(R1) 1
L.D F10,-16(R1) L.D F14,-24(R1) 2
L.D F18,-32(R1) L.D F22,-40(R1) ADD.D F4,F0,F2 ADD.D F8,F6,F2 3
L.D F26,-48(R1) L.D F30,-56(R1) ADD.D F12,F10,F2 ADD.D F16,F14,F2 4
ADD.D F20,F18,F2 ADD.D F24,F22,F2 5
S.D 0(R1),F4 S.D -8(R1),F8 ADD.D F28,F26,F2 ADD.D F32,F30,F2 6
S.D -16(R1),F12 S.D -24(R1),F16 7
S.D -32(R1),F20 S.D -40(R1),F24 DSUBUI R1,R1,#56 8
S.D -48(R1),F28 S.D -56(R1),F32 (assuming no branch delay) BNEZ R1,LOOP 9
Unrolled 8 times to avoid delays. 8 results (loops) in 9 clocks, or 1.125 clocks per iteration
=> 2X compared to 2-way superscalar (SS)
Average: 24 operations in 9 cycles or approx. 2.7 ops per clock
and 53% efficiency because of 5 ALUs
Actually, unrolling 10 times is even better because we can fill in the stall in LD/ST unit and increase the time only by 1 cycle
Note: Need many more registers in VLIW compared to superscalar

## Slide 18: How Can the HW Help the Compiler with Discovering ILP?
Compiler’s performance is critical for VLIW processors
  Find many independent instructions & schedule them in best
  possible way
What limits the compiler’s ability to discover ILP
  Name dependencies (WAW & WAR)
    Can eliminate with large number of registers
  Branches
    Limit compiler’s ability to schedule
    Modern VLIW processors use branch prediction too
  Dependencies through memory
    Force the compiler to use conservative schedule
Can the HW help the compiler?
  Ideally, with techniques simpler than those for superscalar processors