## Slide 1: Lecture 13: ILP Hardware Schemes Chapter 3 and Appendix C

## Slide 2: HW Schemes: Instruction Parallelism
Compiler or Static instruction scheduling can avoid some pipeline hazards.
  e.g. filling branch delay slot.
  Difficult compiler optimization process for complex architectures
  It can’t know the WAR and WAW dependencies at compile time
Why in HW at run time?
  Works when can’t know dependence at compile time
    WAW can only be detected at run time
  Compiler simpler
  Code for one machine runs well on another
Key idea: Allow instructions behind stall to proceed even if there is dependency. Check it at the time of execution. Then independent instructions, which are behind, can be executed.
DIVD F0,F2,F4
ADDD F10,F0,F8
SUBD F8,F8,F14
  But, both structural and data hazards are checked in MIPS. ADDD is stalled at ID, SUBD can not even proceed to ID.
  Enables out-of-order execution => out-of-order completion

## Slide 3: HW Schemes: Scoreboard CDC 6600 Appendix C
Scoreboard replaces ID with 2 stages (Issue and RO)
  1. Issue—decode instructions, check for structural hazards, Issue in order if the functional unit is free and no WAW.
  Read operands (RO)—wait until no (RAW) data hazards, then read operands
  In the previous example - ADDD would stall at RO, and SUBD could proceed with no stalls.
Scoreboards allow instruction to execute whenever 1 & 2 hold, not waiting for prior instructions.
IF ISSUE
RO EX1 … EXm
RO EX1 … ……..EXn
RO EX1 … ……….. EXp
WB?
WB?
WB – if no WAR
…

## Slide 4: Scoreboard Implications
Out-of-order completion => WAR, WAW hazards may happen
Solutions for WAR
  Stall Write to allow Reads to take place; Read registers only during Read Operands (RO) stage.
For WAW, must detect hazard: stall in the Issue stage until other completes
Need to have multiple instructions in execution phase => multiple execution units or pipelined execution units
Scoreboard keeps track of dependencies, state or operations
  Monitors every change in the hardware.
  Determines when to read operands, when can execute, when can write back.
  Hazard detection and resolution is centralized.

## Slide 5
Figure C.54 The basic structure of a MIPS processor with a scoreboard. The scoreboard’s function is to control instruction execution (vertical control lines). All of the data flow between the register file and the functional units over the buses (the horizontal lines, called trunks in the CDC 6600). There are two FP multipliers, an FP divider, an FP adder, and an integer unit. One set of buses (two inputs and one output) serves a group of functional units. The details of the scoreboard are shown in Figures C.55 to C.58.

## Slide 6: Four Stages of Scoreboard Control
1. Issue—decode instructions & check for structural hazards (ID1)
  If a functional unit for the instruction is free and no other active instruction has the same destination register (WAW), the scoreboard issues the instruction to the functional unit and updates its internal data structure. If a structural or WAW hazard exists, then the instruction issue stalls, and no further instructions will issue until these hazards are cleared.
2. Read operands—wait until no data hazards, then read operands (ID2)
  A source operand is available if no earlier issued active instruction is going to write it, or if the register containing the operand is being written by a currently active functional unit (RAW hazard). When the source operands are available, the scoreboard tells the functional unit to proceed to read the operands from the registers and begin execution. The scoreboard resolves RAW hazards dynamically in this step, and instructions may be sent into execution out of order.

## Slide 7: Four Stages of Scoreboard Control
3.Execution—operate on operands (EX)
  The functional unit begins execution upon receiving operands. When the result is ready, it notifies the scoreboard that it has completed execution.
4.Write result—finish execution (WB)
  Once the scoreboard is aware that the functional unit has completed execution, the scoreboard checks for WAR hazards. If none, it writes results. If WAR, then it stalls the instruction.
  Example:
  DIVD F0,F2,F4
  ADDD F10,F0,F8
  SUBD F8,F8,F14
  CDC 6600 scoreboard would stall SUBD until ADDD reads operands

## Slide 8
Example Scoreboard Status in CDC 6600 (Fig. c.54) consisting of 2 FP Mult, 1 FP Div, 1 FP Add, 1 Int unit

## Slide 9: Review: Scoreboard
Limitations of 6600 scoreboard
  Complex Centralized Control
  Limited to instructions in basic block (small window)
  Large number of functional units (structural hazards)
  Stall on WAR hazards
  Stall on WAW hazards
        DIV.D F0, F2, F4
        ADD.D F6, F0, F8
        S.D F6, 0(R1)
        SUB.D F8, F10, F14
        MUL.D F6, F10, F8
WAR
WAW

## Slide 10: Dynamic Scheduling: Tomasulo Algorithm
For IBM 360/91 about 3 years after CDC 6600 that proposed scoreboarding (Centralized scheme)
Differences between Tomasulo Algorithm & Scoreboard
  Control & buffers distributed with Function Units vs. centralized in scoreboard; called “reservation stations (rs)”
  Registers in instructions replaced by pointers to reservation station buffer
  Instruction results are passed directly to the FU from rs rather than from registers through common data bus (CDB) Common Data Bus broadcasts results to all FUs
  HW renaming of registers to avoid WAW hazards
  Buffer operand values to avoid WAR hazards
  Load and Stores treated as FUs as well
Why study? Lead to Alpha 21264, HP 8000, MIPS 10000, Pentium II, Power PC 604 …

## Slide 11
Figure 3.6 The basic structure of a MIPS floating-point unit using Tomasulo’s algorithm. Instructions are sent from the instruction unit into the instruction queue from which they are issued in first-in, first-out (FIFO) order. The reservation stations include the operation and the actual operands, as well as information used for detecting and resolving hazards. Load buffers have three functions: (1) hold the components of the effective address until it is computed, (2) track outstanding loads that are waiting on the memory, and (3) hold the results of completed loads that are waiting for the CDB. Similarly, store buffers have three functions: (1) hold the components of the effective address until it is computed, (2) hold the destination memory addresses of out-standing stores that are waiting for the data value to store, and (3) hold the address and value to store until the memory unit is available. All results from either the FP units or the load unit are put on the CDB, which goes to the FP register file as well as to the reservation stations and store buffers. The FP adders implement addition and subtraction, and the FP multipliers do multiplication and division.

## Slide 12: Avoiding WAR and WAW Hazards
        1. DIV.D F0, F2, F4
        2. ADD.D F6, F0, F8
        3. S.D F6, 0(R1)
        4. SUB.D F8, F10, F14
        5. MUL.D F6, F10, F8
Implemented through reservation stations (rs) per functional unit
  Buffers an operand as soon as it is available – avoids WAR hazards. The basic idea is that a reservation station (rs) fetches and buffers an operand as soon as it is available without waiting until the instruction execution. Equivalent to Register renaming. Since the instructions are issued to rs in order, the operands are read in order without being effected by out-of-order executions.
  Registers know the pending instruction. Or the rs that will provide their inputs – avoids WAW hazards. The last write in a sequence of same-register-writing actually updates the register
Where are the hazards?
RAW between 1 and 2, 2 and 3 (SD), 4 and 5
WAR between 2 and 4, 3 and 5
WAW between 2 and 5

## Slide 13: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  Stall if structural hazard, ie. no space in the rs. If reservation station (rs) is free, the issue logic issues instr to rs & read operands into rs if ready (may be waiting for an operation) (Register renaming => Solves WAR). Make status of destination register waiting for this latest instn even if the previous instn writing to this register hasn’t completed => Solves WAW hazards.
2. Execution—operate on operands (EX)
  When both operands are ready then execute; if not ready, watch CDB for result – Solves RAW
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available. Write result into dest. reg. if its status is r. => Solves WAW.
Normal data bus: data + destination (“go to” bus)
CDB: data + source (“come from” bus because the register is waiting)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does broadcast

## Slide 14: Reservation Station Components
Op—Operation to perform in the unit (e.g., + or –)
Vj, Vk— Value of the source operand.
Qj, Qk— Name of the RS that would provide the source operands. Value zero means the source operands already available in Vj or Vk, or is not waiting.
Busy—Indicates reservation station or FU is busy
A – Holds information for memory address calculation
for load/store. Initially, the immediate value is stored here.
After address calculation, effective address is stored here.
Register File Status Qi:
Qi —Indicates which functional unit will write each register, if one exists. Blank (0) when no pending instructions that will write that register meaning that the value is already available.

## Slide 15
Fig.3.7 Reservation stations and register tags shown when all instructions have issued, but only the first load has completed and written its result on the CDB.The 2nd load has completed effective address calculation but is waiting on the memory unit. Notice that ADDD has a WAR hazard with DIVD and could complete before.
Reservation Stations – 1 Load, 1 Store, 1 ADD and 1 MUL units
Functional Unit (Qi) Mult1 Load2 Add2 Add1 Mult2
For SUB- Load 1 result has gone into Vk register, but waiting for Load 2 to provide Vj
ADDD is waiting for Add1 and Load 2 to provide operands for Vj and Vk

## Slide 16: Tomasulo Example Cycle 0

## Slide 17: Tomasulo Example Cycle 1

## Slide 18: Tomasulo Example Cycle 2

## Slide 19: Tomasulo Example Cycle 3

## Slide 20: Tomasulo Example Cycle 4

## Slide 21: Tomasulo Example Cycle 5

## Slide 22: Tomasulo overlap iterations of loops
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling if branch is taken)
Reservation stations
  Permit instruction issue to advance past integer control flow operations
  Also buffer old values of registers - totally avoiding the WAR stall
If we predict that branches are taken, using reservation stations will dynamically unroll the loop
Other perspective: Tomasulo building data flow dependency graph on the fly

## Slide 23: Tomasulo Example (Loop Unrolling)
Dynamic Scheduling, Multiple Issue, and Speculation
Assume 2-issue superscalar with one integer and one ld/store unit

## Slide 24: Tomasulo’s scheme offers 2 major advantages
Distribution of the hazard detection logic
  distributed reservation stations and the CDB
  If multiple instructions waiting on single result, & each instruction has other operand, then instructions can be released simultaneously by broadcast on CDB
  If a centralized register file were used, the units would have to read their results from the registers when register buses are available
Elimination of stalls for WAW and WAR hazards

## Slide 25: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264, IBM PPC 620 in CA:AQA 2/e, but not in silicon!
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc stores
Non-precise interrupts!
  We will address this later