## Slide 1: Lecture 14: Tomasulo Contd. Chapter 3

## Slide 2: Three Stages of Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  Stall if structural hazard, ie. no space in the rs. If reservation station (rs) is free, the issue logic issues instr to rs & read operands into rs if ready (may be waiting for an operation) (Register renaming => Solves WAR). Make status of destination register waiting for this latest instn even if the previous instn writing to this register hasn’t completed => Solves WAW hazards.
2. Execution—operate on operands (EX)
  When both operands are ready then execute; if not ready, watch CDB for result – Solves RAW
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available. Write result into dest. reg. if its status is r. => Solves WAW.
Normal data bus: data + destination (“go to” bus)
CDB: data + source (“come from” bus because the register is waiting)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does broadcast

## Slide 3: Reservation Station Components
Op—Operation to perform in the unit (e.g., + or –)
Vj, Vk— Value of the source operand.
Qj, Qk— Name of the RS that would provide the source operands. Value zero means the source operands already available in Vj or Vk, or is not waiting.
Busy—Indicates reservation station or FU is busy
A – Holds information for memory address calculation
for load/store. Initially, the immediate value is stored here.
After address calculation, effective address is stored here.
Register File Status Qi:
Qi —Indicates which functional unit will write each register, if one exists. Blank (0) when no pending instructions that will write that register meaning that the value is already available.

## Slide 4
Fig.3.7 Reservation stations and register tags shown when all instructions have issued, but only the first load has completed and written its result on the CDB.The 2nd load has completed effective address calculation but is waiting on the memory unit. Notice that ADDD has a WAR hazard with DIVD and could complete before.
Reservation Stations – 1 Load, 1 Store, 1 ADD and 1 MUL units
Functional Unit (Qi) Mult1 Load2 Add2 Add1 Mult2
For SUB- Load 1 result has gone into Vk register, but waiting for Load 2 to provide Vj
ADDD is waiting for Add1 and Load 2 to provide operands for Vj and Vk

## Slide 5: Tomasulo Example Cycle 0

## Slide 6: Tomasulo Example Cycle 1

## Slide 7: Tomasulo Example Cycle 2

## Slide 8: Tomasulo Example Cycle 3

## Slide 9: Tomasulo Example Cycle 4

## Slide 10: Tomasulo Example Cycle 5

## Slide 11: Tomasulo Example
Loop: LD R2,0(R1) ;R2=array element
DADDIU R2,R2,#1 ;increment R2
SD R2,0(R1) ;store result
DADDIU R1,R1,#8 ;increment pointer
BNE R2,R3,LOOP ;branch if not last element
Assume load and store take 2 cycles, one for address computation and another for memory access.
Assume 2-issue superscalar processor – One EX and a LD/ST
Show the timing of Tomasulo execution
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 12: 2-Issue Tomasulo (One Integer and One LD/ST Unit) Loop Unrolling
Dynamic Scheduling, Multiple Issue, and Speculation
1 EX and 1 LD/ST units
Wait for BNE
Wait for BNE

## Slide 13: Tomasulo’s scheme offers 2 major advantages
Distribution of the hazard detection logic
  distributed reservation stations and the CDB
  If multiple instructions waiting on single result, & each instruction has other operand, then instructions can be released simultaneously by broadcast on CDB
  If a centralized register file were used, the units would have to read their results from the registers when register buses are available
Elimination of stalls for WAW and WAR hazards

## Slide 14: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264,
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc stores
Non-precise interrupts!
  We will address this later

## Slide 15: Tomasulo overlap iterations of loops
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling if branch is taken)
Reservation stations
  Permit instruction issue to advance past integer control flow operations
  Also buffer old values of registers - totally avoiding the WAR stall
If we predict that branches are taken, using reservation stations will dynamically unroll the loop
Other perspective: Tomasulo building data flow dependency graph on the fly

## Slide 16: Superscalar with Speculation
Speculative execution – execute control dependent instructions even when we are not sure if they should be executed
With branch prediction, we speculate on the outcome of the branches and execute the program as if our guesses were correct.
Misprediction? Hardware undo – Rollback and Recovery, called boosting
  In Tomasulo, instructions after the branch can be fetched and issued in-order, but can not execute before the branch is resolved – See LD instructions after BNE in the last slide.
  Speculation allows them to execute with care.
Multi-issue + branch prediction + Tomasulo => Speculation
Implemented in a number of processors:
PowerPC 603/604/G3/G4, Pentium II/III/4, Alpha 21264, AMD K5/K6/Athlon, MIPS R10k/R12k

## Slide 17: Hardware Modifications
Speculated instructions execute and generate results. Should they be written into register file? Should they be passed onto dependent instructions (in reservation stations)?
Separate the bypassing paths from actual completion of an instruction. Do not allow speculated instructions to perform any updates that cannot be undone.
When instructions are no longer speculative, allow them to update register or memory – instruction commit.
  Out-of-order execution, in-order commit
Then where are the instructions and their results between execution completion and instruction commit? Instructions may finish considerably before their commit.
Reorder buffer (ROB) holds the results of instructions that have finished execution but have not committed.
  ROB is a source of operands for instructions, much like the store buffer

## Slide 18: HW support for More ILP
Need HW buffer for results of uncommitted instructions: reorder buffer (ROB)
  4 fields: instr, destination, value, ready
  Reorder buffer can be operand source => more registers like RS
  Supplies operands between execution complete & commit
  No more store buffers before Memory operations because no dependency on stores. Performed as instr. Commit.
  Use reorder buffer number instead of reservation station when execution completes
  Once operand commits, result is put into register and removed from ROB
  Instructions commit in order
  As a result, its easy to undo speculated instructions on mispredicted branches or on exceptions
Reorder
Buffer
FP Regs
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations

## Slide 19: Four Steps of Speculative Tomasulo Algorithm
1. Issue— get instruction from FP Op Queue
  If reservation station and reorder buffer slot free, issue instr & send operands & reorder buffer no. for destination (this stage sometimes called “dispatch”)
2. Execution— operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result; when both in reservation station, execute; checks RAW
3. Write result— finish execution (WB)
  Write on Common Data Bus to all awaiting FUs & reorder buffer; mark reservation station available.
4. Commit— update register with reorder result
  When instr. at head of reorder buffer & result present, update register with result (or store to memory) and remove instr from reorder buffer (also called “graduation”). Mispredicted branch flushes reorder buffer (also called boosting)

## Slide 20: Original Tomasulo’s algorithm

## Slide 21: Overview of Design
Figure 3.17 The basic organization of a multiple issue processor with speculation. In this case, the organization could allow a FP multiply, FP add, integer, and load/store to all issues simultaneously (assuming one issue per clock per functional unit). Note that several datapaths must be widened to support multiple issues: the CDB, the operand buses, and, critically, the instruction issue logic, which is not shown in this figure. The ROB subsumes store buffers. Stores still execute in two steps, but the second step is performed by instruction commit.
Revised Tomasulo for Speculation