## Slide 1: Lecture 15: Speculation and Commercial Examples Sections 3.8, 3.10, and 3.13

## Slide 2: ILP with Dynamic Scheduling, Multiple Issue and Speculation
Extend Tomasulo’s algorithm to issue multiple instructions per clock to the reservation stations
Issuing multiple instructions in a dynamically scheduled processor is very complex because these instructions may depend on each other.
Extending to speculation is still more complex, but all modern superscalar processors implement dynamic scheduling, multiple issue and speculation
Reservation station and pipeline control tables must be updated. Two different approaches to issue multiple instructions: (1) Divide a cycle to two half-cycles, one to do the checking and update the tables, and the second to issue the instructions; (2) Build logic to handle two or more instructions in the same cycle. Every possible combination of the instructions must be considered!

## Slide 3: Overview of Design
Figure 3.17 The basic organization of a multiple issue processor with speculation. In this case, the organization could allow a FP multiply, FP add, integer, and load/store to all issues simultaneously (assuming one issue per clock per functional unit). Note that several datapaths must be widened to support multiple issues: the CDB, the operand buses, and, critically, the instruction issue logic, which is not shown in this figure. The ROB subsumes store buffers. Stores still execute in two steps, but the second step is performed by instruction commit.
Revised Tomasulo for Speculation

## Slide 6: Space-Time Diagram Example 2
Loop: LD R2,0(R1) ;R2=array element
DADDIU R2,R2,#1 ;increment R2
SD R2,0(R1) ;store result
DADDIU R1,R1,#8 ;increment pointer
BNE R2,R3,LOOP ;branch if not last element
Consider the same 2-issue Tomasulo with one integer and another floating point unit
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 7: 2-Issue Tomasulo (No speculation)
Dynamic Scheduling, Multiple Issue, and Speculation
1 EX and 1 LD/ST units
Wait for BNE
Wait for BNE

## Slide 8: With Speculation
Dynamic Scheduling, Multiple Issue, and Speculation
Note: 1. Perfect branch prediction and speculation is assumed.
2. . No need to wait until BNE finishes (cycle 7). LD can start at cycle 5. Note the execution times of the LD instructions after BNE and compare with no speculation case

## Slide 9: Avoiding Memory Hazards
WAW and WAR hazards through memory are eliminated with speculation because actual updating of memory occurs in order, when a store is at head of the ROB, and hence, no earlier loads or stores can still be pending
RAW hazards through memory are maintained by two restrictions:
  not allowing a load to initiate the second step of its execution if any active ROB entry occupied by a store has a Destination field that matches the value of the A field of the load, and
  maintaining the program order for the computation of an effective address of a load with respect to all earlier stores.
these restrictions ensure that any load that accesses a memory location written to by an earlier store cannot perform the memory access until the store has written the data

## Slide 10: Register renaming, virtual registers versus Reorder Buffers
Alternative to Reorder Buffer is a larger virtual set of registers and register renaming
Virtual registers hold both architecturally visible registers + temporary values
  replace functions of reorder buffer and reservation station
Renaming process maps names of architectural registers to registers in virtual register set
  Changing subset of virtual registers contains architecturally visible registers
Simplifies instruction commit: mark register as no longer speculative, free register with old value
Adds 40-80 extra registers: Alpha, Pentium,… Most Out-of-Order processors today use extended registers with renaming

## Slide 11: How much to speculate?
Speculation Pro: uncover events that would otherwise stall the pipeline (cache misses)
Speculation Con: costly if exceptional event occurs when speculation was incorrect
Typical solution: speculation allows only low-cost exceptional events (1st-level cache miss)
When expensive exceptional event occurs, (2nd-level cache miss or TLB miss) processor waits until the instruction causing event is no longer speculative before handling the event
Assuming single branch per cycle: future may speculate across multiple branches!

## Slide 12
Figure 3.25 The fraction of instructions that are executed as a result of misspeculation is typically much higher for integer
Programs (the first five) versus FP programs (the last five).
Speculation Efficiency

## Slide 13: Multiple Issue
Multiple Issue and Static Scheduling

## Slide 14
Figure 3.36 The basic structure of the A8 pipeline is 13 stages. Three cycles are used for instruction fetch and four for instruction decode, in addition to a five-cycle integer pipeline. This yields a 13-cycle branch misprediction penalty. The instruction fetch unit tries to keep the 12-entry instruction queue filled.
A8 is a dual-issue statically scheduled superscalar with dynamic issue detection, which allows the processor to issue one or two instructions per clock. A simple score board structure is used to track when an instruction can issue. A8 uses a dynamic branch predictor with 512-entry 2-way set associative BTB and a 4K-entry global history buffer (GHB), indexed by the branch history and current PC. GHB is accessed only if there is a miss in the BTB.
Example: ARM A8 Datapath

## Slide 15: IBM Power 4 Datapath

## Slide 16
Figure 3.41 The Intel Core i7 pipeline structure shown with the memory system components. The total pipeline depth is 14 stages, with branch mispredictions costing 17 cycles. There are 48 load and 32 store buffers. The six independent functional units can each begin execution of a ready micro-op in the same cycle.
Intel Core i7 uses an aggressive out-of-order four-issue dynamically scheduled speculative pipeline structure.
Fetch: Instruction fetch unit fetches 16 bytes from Icache and places them in predecode instruction buffer. This stage breaks them into individual x86 instructions – nontrivial because x86 instructions can be 1 to 17 bytes. A process called micro-op fusion takes place, where some instructions (like compare and branch) are fused to single operation.
ID - Decode: Three simple decoders to convert x86 instructions to MIPS-like instns called micro-ops and one micro-code (micro-program) to convert from complex x86 instns. Loop stream detector detects small loops (28 instns or 256 bytes) and directly issues those micro-operations without going through IF and ID stages.
IF
ID
EX,
WB,
Com
Common Reservation Station for all FUs

## Slide 17: AMD Opteron Datapath

## Slide 18
Processor | Micro architecture | Fetch / Issue / Execute | FU | Clock Rate (GHz) | Transis-tors Die size | Power
Intel Pentium 4 Extreme | Speculative dynamically scheduled; deeply pipelined; SMT | 3/3/4 | 7 int. 1 FP | 3.8 | 125 M 122 mm2 | 115 W
AMD Athlon 64 FX-57 | Speculative dynamically scheduled | 3/3/4 | 6 int. 3 FP | 2.8 | 114 M 115 mm2 | 104 W
IBM Power5 (1 CPU only) | Speculative dynamically scheduled; SMT; 2 CPU cores/chip | 8/4/8 | 6 int. 2 FP | 1.9 | 200 M 300 mm2 (est.) | 80W (est.)
Intel Itanium 2 | Statically scheduled VLIW-style | 6/5/11 | 9 int. 2 FP | 1.6 | 592 M 423 mm2 | 130 W
Head to Head ILP competition

## Slide 19: Performance on SPECint2000

## Slide 20: Performance on SPECfp2000

## Slide 21: Normalized Performance: Efficiency
Rank | I tanium2 | Pen t I um4 | A t h l on | Powe r 5
Int/Trans | 4 | 2 | 1 | 3
FP/Trans | 4 | 2 | 1 | 3
Int/area | 4 | 2 | 1 | 3
FP/area | 4 | 2 | 1 | 3
Int/Watt | 4 | 3 | 1 | 2
FP/Watt | 2 | 4 | 3 | 1

## Slide 22: No Silver Bullet for ILP
No obvious overall leader in performance
The AMD Athlon leads on SPECInt performance followed by the Pentium 4, Itanium 2, and Power5
Itanium 2 and Power5, which perform similarly on SPECFP, clearly dominate the Athlon and Pentium 4 on SPECFP
Itanium 2 is the most inefficient processor both for Floating point and integer code for all but one efficiency measure (SPECFP/Watt)
Athlon and Pentium 4 both make good use of transistors and area in terms of efficiency,
IBM Power5 is the most effective user of energy on SPECFP and essentially tied on SPECINT

## Slide 23: Limits to ILP
Doubling issue rates above today’s 3-6 instructions per clock, say to 6 to 12 instructions, probably requires a processor to
  issue 3 or 4 data memory accesses per cycle,
  resolve 2 or 3 branches per cycle,
  rename and access more than 20 registers per cycle, and
  fetch 12 to 24 instructions per cycle.
The complexities of implementing these capabilities is likely to mean sacrifices in the maximum clock rate
  e.g, widest issue processor is the Itanium 2, but it also has the slowest clock rate, despite the fact that it consumes the most power!

## Slide 24
Figure 3.26 ILP available in a perfect processor (like perfect branch prediction, infinite register renaming, infinite window size, perfect cache, etc) for six of the SPEC92 benchmarks. The first three programs are integer programs, and the last three are floating-point programs. The floating-point programs are loop intensive and have large amounts of loop-level parallelism.
ILP Available in a perfect processor

## Slide 25
Figure 3.27 The amount of parallelism available versus the window size for a variety of integer and floating-point programs with up to 64 arbitrary instruction issues per clock. Although there are fewer renaming registers than the window size, the fact that all operations have one-cycle latency and the number of renaming registers equals the issue width allows the processor to exploit parallelism within the entire window. In a real implementation, the window size and the number of renaming registers must be balanced to prevent one of these factors from overly constraining the issue rate.

## Slide 26: EXAMPLE: A speculative superscalar with a 64-entry window achieves one-half of the ideal issue rate measured for this window size (Fig. 3.27). The cache has 0.01 misses per instruction, but it hides 25% of the miss penalty (50 ns) on every miss due to dynamic scheduling. With processor operating at 2.5 GHz clock, what is the MIPS rate for the SPEC gcc benchmark?
ANSWER:
The actual issue rate of the processor = 0.5 x ideal issue rate from Fig. 3.27 for 64-entry buffer = 0.5 x 9 = 4.5.
The ideal pipeline CPI of the processor = 1/issue rate = 1/issue rate = 1/4.5 = 0.22
Actual CPI including cache miss = Ideal CPI + Misses per instruction x miss penalty
Miss penalty = 0.75 x Memory access time/clock cycle = 0.75 x 50 ns/400 ps = 94 cycles
Actual CPI = 0.22 + 0.01 x 94 = 1.16
Instruction Execution Rate = 2500 MHz/1.16 = 2155 MIPS

## Slide 27: Limits to ILP
Most techniques for increasing performance increase power consumption
The key question is whether a technique is energy efficient: does it increase power consumption faster than it increases performance?
Multiple issue processors techniques all are energy inefficient:
  Issuing multiple instructions incurs some overhead in logic that grows faster than the issue rate grows
  Growing gap between peak issue rates and sustained performance
Number of transistors switching = f(peak issue rate), and performance = f( sustained rate), growing gap between peak and sustained performance  increasing energy per unit of performance

## Slide 28: Commentary
Itanium architecture does not represent a significant breakthrough in scaling ILP or in avoiding the problems of complexity and power consumption
Instead of pursuing more ILP, architects are increasingly focusing on thread level parallelism (TLP) implemented with single-chip multiprocessors
In 2000, IBM announced the 1st commercial single-chip, general-purpose multiprocessor, the Power4, which contains 2 Power3 processors and an integrated L2 cache
  Since then, Sun Microsystems, AMD, and Intel have switch to a focus on single-chip multiprocessors rather than more aggressive uniprocessors.
Right balance of ILP and TLP is unclear today
  Perhaps right choice for server market, which can exploit more TLP, may differ from desktop, where single-thread performance may continue to be a primary requirement

## Slide 29: And in conclusion …
Limits to ILP (power efficiency, compilers, dependencies …) seem to limit to 3 to 6 issue for practical options
Explicitly parallel (Data level parallelism or Thread level parallelism) is next step to performance
Coarse grain vs. Fine grained multihreading
  Only on big stall vs. every clock cycle
Simultaneous Multithreading if fine grained multithreading based on OOO superscalar microarchitecture
  Instead of replicating registers, reuse rename registers
Itanium/EPIC/VLIW is not a breakthrough in ILP
Balance of ILP and TLP decided in marketplace