## Slide 1: Lecture 16 Multithreading

## Slide 2: Performance beyond single thread ILP
ILP is limited in a program particularly due to limited window size, data dependency and branches
There can be much higher natural parallelism in some applications in the form of loops (e.g., Database or Scientific codes)
Explicit Thread Level Parallelism or Data Level Parallelism
Thread: process with own instructions and data
  thread may be a process part of a parallel program of multiple processes, or it may be an independent program
  Each thread has all the state (instructions, data, PC, register state, and so on) necessary to allow it to execute
SPMD Model: Execute same program identical instructions on different data (Each also a thread)

## Slide 3: Thread Level Parallelism (TLP)
ILP exploits implicit parallel operations within a loop or straight-line code segment (basic block)
TLP explicitly represented by multiple threads of execution that are inherently parallel at the program level
To software, a dual-threaded processor looks like two distinct CPUs, and the operating system takes advantage of this by scheduling two threads of execution on it.
Goal: Use multiple instruction streams to improve
  Throughput of computers that run many programs
  Execution time of multi-threaded programs
TLP more cost-effective to exploit than ILP
Very suitable for multicore processors

## Slide 4: Dealing with Pipeline Hazards
Each instruction depends on the previous instruction. Assume no bypassing.
  LW r1, 0(r2)
  LW r5, 12(r1)
  ADDI r5, r5, #12
  SW r5, 12(r1)
How can we avoid the stalls due to dependencies between instructions in a pipeline?
One way is to interleave execution of instructions from different program threads on the same pipeline

## Slide 5: Hardware Multithreading
Interleave 4 threads, T1-T4, on non-bypassed 5-stage pipe
T1: LW r1, 0(r2)
T2: ADD r7, r1, r4
T3: XORI r5, r4, #12
T4: SW 0(r7), r5
T1: LW r5, 12(r1)

## Slide 6: Multithreading to Avoid Memory Latency
General processors switch to another context on I/O operation => Software Multithreading, Multiprogramming, etc. An O/S function. Large overhead! Why? Context switch
Why not context switch on a cache miss? => Hardware multithreading.
Can we afford that overhead with context switching? => Need changes in architecture to avoid stack operations. How to achieve it?
Have many contexts CPU resident (not memory resident) by having separate PCs and registers for each thread. No need to store them in stack on context switching.

## Slide 7: New Approach: Mulithreaded Execution
Multithreading: multiple threads to share the functional units of 1 processor via overlapping
  processor must duplicate independent state of each thread e.g., a separate copy of register file, a separate PC, and for running independent programs, a separate page table
  memory shared through the virtual memory mechanisms, which already support multiple processes
  HW for fast thread switch; much faster than full process switch  100s to 1000s of clocks
When to switch?
  Alternate instruction per thread (fine grain)
  When a thread is stalled, perhaps for a cache miss, another thread can be executed (coarse grain)

## Slide 8: Simple Multithreaded Pipeline
Have to carry thread select down pipeline to ensure correct state bits read/written at each pipe stage. This is similar to carrying the control bits in a pipelined design across the stages

## Slide 9: Fine-Grained Multithreading
Switches between threads on each instruction, causing the execution of multiple threads to be interleaved
Usually done in a round-robin fashion, skipping any stalled threads
CPU must be able to switch threads every clock
Advantage is that it can hide both short and long stalls, since instructions from other threads executed when one thread stalls
Disadvantage is that it slows down execution of individual threads, since a thread ready to execute without stalls will be delayed by instructions from other threads
Used on Sun’s Niagara (will see later)

## Slide 10: Course-Grained Multithreading
Switches threads only on costly stalls, such as L2 cache misses
Advantages
  Relieves the need to have very fast thread-switching
  Doesn’t slow down thread, since instructions from other threads issued only when the thread encounters a costly stall
Disadvantage is hard to overcome throughput losses from shorter stalls, due to pipeline start-up costs
  Since CPU issues instructions from 1 thread, when a stall occurs, the pipeline must be emptied or frozen
  New thread must fill pipeline before instructions can complete
Because of this start-up overhead, coarse-grained multithreading is better for reducing penalty of high cost stalls, where pipeline refill << stall time
Used in IBM AS/400, GPU (next class)

## Slide 11: Sun Niagara 2 (Multithreaded Sparc processor)
Sun T5120 Niagara 2 – Fine-grained multithreading
  8 cores on chip each with 2 pipelines/core
  4 HW threads/pipeline => 64 threads
Thread Scheduling: First schedule on different cores in a round-robin manner to avoid resource contention then on different pipeline and finally within the same pipeline
Notes: 11
(b) The bars show the average utilization (%) at each level in the core; the lines represent the range of peak high and peak low values (%).

## Slide 13: Do both ILP and TLP?
TLP and ILP exploit two different kinds of parallel structure in a program
Could a processor oriented at ILP also exploit TLP?
  functional units are often idle in data path designed for ILP because of either stalls or dependences in the code
Could the TLP be used as a source of independent instructions that might keep the processor busy during stalls?
Could TLP be used to employ the functional units that would otherwise lie idle when insufficient ILP exists?

## Slide 14: Simultaneous Multithreading (SMT)
Simultaneous multithreading (SMT): insight that dynamically scheduled processor already has many HW mechanisms to support multithreading
  Large set of virtual registers that can be used to hold the register sets of independent threads
  Register renaming provides unique register identifiers, so instructions from multiple threads can be mixed in datapath without confusing sources and destinations across threads
  Out-of-order completion allows the threads to execute out of order, and get better utilization of the HW
Just add a per thread renaming table and keep separate PCs in a superscalar processor
  Independent commitment can be supported by logically keeping a separate reorder buffer for each thread

## Slide 15: Multithreaded Categories
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 16: Design Challenges in SMT
Since SMT makes sense only with fine-grained implementation, what is its impact on single thread performance?
  A preferred thread approach sacrifices neither throughput nor single-thread performance?
  Unfortunately, with a preferred thread, the processor is likely to sacrifice some throughput, when preferred thread stalls
Larger register file needed to hold multiple contexts
Not affecting clock cycle time, especially in
  Instruction issue - more candidate instructions need to be considered
  Instruction completion - choosing which instructions to commit may be challenging
Ensuring that cache and TLB conflicts generated by SMT do not degrade performance

## Slide 17: Simultaneous Multithreaded Processor

## Slide 18: Intel Pentium-4 Xeon Processor
Hyperthreading == SMT
Dual physical processors, each 2-way SMT
Logical processors share nearly all resources of the physical processor
  Caches, execution units, branch predictors
Die area overhead of hyperthreading ~5 %
When one logical processor is stalled, the other can make progress (Coarse-grained multithreading)
  No logical processor can use all entries in instruction queues when two threads are active
A processor running only one active software thread to run at the same speed with or without hyperthreading

## Slide 19
Intel Pentium-4 Xeon Processor
The allocator logic takes uops from the uop queue and allocates many of the key machine buffers needed to execute each uop. Each logical processor can use up to a maximum of 63 re-order buffer entries, 24 load buffers, and 12 store buffer entries.
2. The two sets of queues are called the memory instruction queue and the general instruction queue, respectively.
3. Five uop schedulers are used to schedule different types of uops for the various execution units. Collectively, they can dispatch up to six uops each clock cycle.

## Slide 20: Intel Xeon Performance

## Slide 21
Power 4
Power 5
2 fetch (PC), 2 initial decodes
2 commits (architected register sets)

## Slide 22: Changes in Power 5 to support SMT
Increased associativity of L1 instruction cache and the instruction address translation buffers
Added per thread load and store queues
Increased size of the L2 (1.92 vs. 1.44 MB) and L3 caches
Added separate instruction prefetch and buffering per thread
Increased the number of virtual registers from 152 to 240
Increased the size of several issue queues
The Power5 core is about 24% larger than the Power4 core because of the addition of SMT support

## Slide 23: Power 5 thread performance ...
Relative priority of each thread controllable in hardware.
For balanced operation, both threads run slower than if they “owned” the machine.