## Slide 1: GPGPU Overview
-- Devashree Tripathy
Slide credit: Slides adapted from
© David Kirk/NVIDIA and Wen-mei W. Hwu, 2007-2016
Tor M. Aamodt, UBC

## Slide 2: CPU and GPU are designed very differently
CPU
Latency Oriented Cores
Chip
Core
Local Cache
Registers
SIMD Unit
Control
GPU
Throughput Oriented Cores
Chip
Compute Unit
Cache/Local Mem
Registers
SIMD Unit
Threading

## Slide 3: CPUs: Latency Oriented Design
Powerful ALU
  Reduced operation latency
Large caches
  Convert long latency memory accesses to short latency cache accesses
Sophisticated control
  Branch prediction for reduced branch latency
  Data forwarding for reduced data latency
Cache
ALU
Control
ALU
ALU
ALU
DRAM
CPU

## Slide 4: GPUs: Throughput Oriented Design
Small caches
  To boost memory throughput
Simple control
  No branch prediction
  No data forwarding
Energy efficient ALUs
  Many, long latency but heavily pipelined for high throughput
Require massive number of threads to tolerate latencies
  Threading logic
  Thread state
DRAM
GPU

## Slide 5: Applications Use Both CPU and GPU
CPUs for sequential parts where latency matters
  CPUs can be 10X+ faster than GPUs for sequential code
GPUs for parallel parts where throughput wins
  GPUs can be 10X+ faster than CPUs for parallel code

## Slide 12
Fine-grain Multithreading

## Slide 13: Extra resources
GPGPU-Sim 3.x Manualhttp://gpgpu-sim.org/manual/index.php/GPGPU-Sim_3.x_Manual

## Slide 14: GPU Microarchitecture Overview
Single-Instruction, Multiple-Threads
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 15: GPU Microarchitecture
Companies tight lipped about details of GPU microarchitecture.
Several reasons:
  Competitive advantage
  Fear of being sued by “non-practicing entities”
  The people that know the details too busy building the next chip
Model described next, embodied in GPGPU-Sim, developed from: white papers, programming manuals, IEEE Micro articles, patents.

## Slide 18
FERMI SM ARCHITECTURE
Two shader processors (SPs) with 16 cores each. Two warp schedulers with dispatch units. Each dispatches half warp (16 threads) to one SP with 16 cores or to LDST or SFU.
Each SM features 32 single-precision CUDA cores, 16 load/store units, four Special Function Units (SFUs), a 64KB block of high speed on-chip memory (see L1+Shared Memory subsection) and an interface to the L2 cache (see L2 Cache subsection).
Load/Store Units: Allow source and destination addresses to be calculated for 16 threads per clock. Load and store the data from/to cache or DRAM.
Special Functions Units (SFUs): Execute transcendental instructions such as sin, cosine, reciprocal, and square root. Each SFU executes one instruction per thread, per clock; a warp executes over eight clocks. The SFU pipeline is decoupled from the dispatch unit, allowing the dispatch unit to issue to other execution units while the SFU is occupied.

## Slide 19: GPU Microarchitecture Overview
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 20: Inside a SIMT Core
Fine-grained multithreading
  Interleave warp execution to hide latency
  Register values of all threads stays in core
SIMT
Front End
SIMD Datapath
Fetch
Decode
Schedule
Branch
Done (Warp ID)
Memory Subsystem
Icnt.
Network
SMem
L1 D$
Tex $
Const$
Reg
File

## Slide 21: Inside a SIMT Core (2.0)
Started from a 5-stage In-Order Pipeline
  Add fine-grained multithreading
  Add SIMT stacks
Schedule
+ Fetch
Decode
Register
Read
Execute
Memory
Writeback
Notes: As we learn more about the GPU design, we tried to add more detail to this model. At some point, we feel that we need to redesign from scratch.

## Slide 22: Inside a SIMT Core (3.0)
SIMT Front End
SIMD Datapath
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
Redesign Model
  Three decoupled warp schedulers
  Scoreboard
  Operand collector
  Multiple SIMD functional unit
Scheduler 1
Scheduler 2
Scheduler 3

## Slide 23: Fetch + Decode
Arbitrate the I-cache among warps
  Cache miss handled by fetching again later
Fetched instruction is decoded and then stored in the I-Buffer
  1 or more entries / warp
  Only warp with vacant entries are considered in fetch
Inst. W1
r
Inst. W2
Inst. W3
v
r
v
r
v
To
Fetch
Issue
Decode
Score-
Board
Issue
ARB
PC
1
PC
2
PC
3
A
R
B
Selection
T
o
I
-
C
a
c
h
e
Valid[1:N]
I-Cache
Decode
I-Buffer
Fetch
Valid[1:N]

## Slide 24: Instruction Issue
Select a warp and issue an instruction from its I-Buffer for execution
  Round-Robin Priority
  GT200 (e.g. Quadro FX 5800): Allow dual issue
  Fermi: Odd/Even scheduler
For each issued instruction:
  Functional execution
  Obtain info from functional simulator
  Generate coalesced memory accesses
  Reserve output register in scoreboard
  Update SIMT stack

## Slide 25: Scoreboard
Checks for RAW and WAW dependency hazard
  Flag instructions with hazards as not ready in I-Buffer (masking them out from the scheduler)
Instructions reserves registers at issue
Release them at writeback

## Slide 26: SIMT Stack
A: v = foo[tid.x];
B: if (v < 10)
C: v = 0;
else
D: v = 10;
E: w = bar[tid.x]+v;
Time
Handles Branch Divergence
D
E
0011
C
E
1100
B
-
1111
PC
RPC
Active Mask
E
-
1111
A
T1
T2
T3
T4
B
T1
T2
T3
T4
C
T1
T2
D
T3
T4
E
T1
T2
T3
T4
SIMT Stack
foo[] = {4,8,12,16};
One stack per warp

## Slide 27: Operand Collector
Term “Operand Collector” appears in figure in NVIDIA Fermi Whitepaper
Operand Collector Architecture (US Patent: 7834881)
  Interleave operand fetch from different threads to achieve full utilization
Bank 0
Bank 1
Bank 2
Bank 3
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
…
…
…
…
add.s32 R3, R1, R2;
No Conflict
mul.s32 R3, R0, R4;
Conflict at bank 0

## Slide 28: Operand Collector (1)
Issue instruction to collector unit.
Collector unit similar to reservation station in tomasulo’s algorithm.
Stores source register identifiers.
Arbiter selects operand accesses that do not conflict on a given cycle.
Arbiter needs to also consider writeback (or need read+write port)

## Slide 29: ALU Pipelines
SIMD Execution Unit
Fully Pipelined
Each pipe may execute a subset of instructions
Configurable bandwidth and latency (depending on the instruction)
Default: SP + SFU pipes

## Slide 30: Writeback
Each pipeline has a result bus for writeback
Exception:
  SP and SFU pipe shares a result bus
  Time slots on the shared bus is pre-allocated

## Slide 31: Memory Unit
Model timing for memory instructions
Support half-warp (16 threads)
  Double clock the unit
  Each cycle service half the warp
Has a private writeback path

## Slide 32: Detailed SIMT Core

## Slide 33: Review: In-order Scoreboard
Scoreboard: a bit-array, 1-bit for each register
  If the bit is not set: the register has valid data
  If the bit is set: the register has stale data
    i.e., some outstanding instruction is going to change it
Issue in-order: RD  Fn (RS, RT)
  If SB[RS] or SB[RT] is set  RAW, stall
  If SB[RD] is set  WAW, stall
  Else, dispatch to FU (Fn) and set SB[RD]
Complete out-of-order
  Update GPR[RD], clear SB[RD]
Regs[R1]
Regs[R2]
Regs[R3]
Regs[R31]
1
0
0
0
Register File
Scoreboard
[Gabriel Loh]
+
Notes: H&P-style notation

## Slide 34: Example
- | - | - | -
- | - | - | -
Warp 0
Warp 1
ld r7, [r0]
mul r6, r2, r5
add r8, r6, r7
Index 0
Index 1
Scoreboard
Index 2
Warp 0
Warp 1
Instruction Buffer
i0 i1 i2 i3
Index 3
r7 | - | - | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
r7 | r6 | - | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 1 | 0 | 0
ld r7, [r0] | 0 | 0 | 0 | 0
mul r6, r2, r5 | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 1 | 0 | 0
r7 | r6 | r8 | -
- | - | - | -
r7 | r6 | r8 | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 0 | 0 | 0
r7 | - | r8 | -
- | - | - | -
ld r7, [r0] | 0 | 0 | 0 | 0
add r8, r6, r7 | 1 | 0 | 0 | 0
r7 | - | r8 | -
- | - | - | -
add r8, r6, r7 | 0 | 0 | 0 | 0
- | - | r8 | -
- | - | - | -
Code
+

## Slide 35: Warp Scheduling Basics

## Slide 36: Loose Round Robin (LRR)
Goes around to every warp and issue if ready (R)
If warp is not ready (W), skip and issue next ready warp
Issue: Warps all run at the same speed, potentially all reaching memory access phase together and stalling.
R
R
W
R
R
R
R
Select
All Warps
Execution Units
W
. . .

## Slide 37: Two-level (TL)
Warps are grouped into two groups:
  Pending warps (potentially waiting on long latency instr.)
  Active warps (Ready to execute)
  Warps move between Pending and Active groups
Within the Active group, issue LRR
Goal: Overlap warps performing computation with warps performing memory access
P
P
P
P
P
P
P
A
A
A
A
Select
Pending Warps
Active Warps
Execution Units
P
. . .
. . .

## Slide 38: Greedy-then-oldest (GTO)
Schedule from a single warp until it stalls
Then pick the oldest warp (time warp assigned to core)
Goal: Improve cache locality for greedy warp
R
R
W
R
R
R
R
Select
All Warps
Execution Units
W
. . .

## Slide 39
Thank you!
Questions?
Conclusion | 39