## Slide 1
Chapter 5
Multiprocessors and
Thread-Level Parallelism
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Why Multiprocessors?
Microprocessors as the fastest CPUs
  Collecting several much easier than redesigning 1
Complexity of current microprocessors
  Do we have enough ideas to sustain 2X/1.5yr?
  Can we deliver such complexity on schedule?
Slow (but steady) improvement in parallel software (scientific apps, databases, OS)
Emergence of embedded and server markets driving microprocessors in addition to desktops
  Embedded functional parallelism
  Network processors exploiting packet-level parallelism
  SMP Servers and cluster of workstations for multiple users – Less demand for parallel computing

## Slide 3: Introduction
Thread-Level parallelism
  Have multiple program counters
  Uses MIMD model
  Targeted for tightly-coupled shared-memory multiprocessors
For n processors, need n threads
Amount of computation assigned to each thread = grain size
  Threads can be used for data-level parallelism, but the overheads may outweigh the benefit
  SPMD: Single Program Multiple Data – Most of the scientific applications use this paradigm
Introduction

## Slide 4: Classification of Parallel Processors
MIMD - Multiple Instruction Multiple Data stream - True Multiprocessors – Multicores and Clusters
1. Shared Memory Multiprocessor – All processors share the same address space. Interprocessor communication through load/store operations to a shared memory.
EX: SMP Servers, NUMA servers
2. Message Passing Multiprocessor - Each processor has its own memory, and interprocessor communication through explicit message passing through “send” and “receive operations.
EX: IBM SP2, Cray XD1, and Clusters
Their advantages and disadvantages?

## Slide 5: Shared Address/Memory Multiprocessor Model
Communicate via Load and Store
  Oldest and most popular model
Based on timesharing: processes on multiple processors vs. sharing single processor
process: a virtual address space and ~ 1 thread of control
  Multiple processes can overlap (share), but ALL threads share a process address space
Writes to shared address space by one thread are visible to reads of other threads
  Usual model: share code, private stack, some shared heap, some private heap
  Concepts of Synchronization and Lock

## Slide 6: Programming Model: Shared Memory
Program is a collection of threads of control.
  Can be created dynamically, mid-execution, in some languages
Each thread has a set of private variables, e.g., local stack variables
Also a set of shared variables, e.g., static variables, shared common blocks, or global heap.
  Threads communicate implicitly by writing and reading shared variables.
  Threads coordinate by synchronizing on shared variables
Pn
P1
P0
s
s = ...
y = ..s ...
Shared memory
i: 2
i: 5
Private memory
i: 8
Notes: Example: think of a thread as a subroutine that gets called on on processor, executed on another
Like concurrent programming on a uniprocessor (as studied in CS162).

## Slide 7: Message Passing Model
Whole computers (CPU, memory, I/O devices) communicate as explicit I/O operations
Message passing "multicomputer" with separate address space per processor
Send specifies local buffer + receiving process on remote computer
Receive specifies sending process on remote computer + local buffer to place data
Send+receive => memory-memory copy, where each supplies local address, AND does pair-wise synchronization!

## Slide 8: Advantages shared-memory communication model
Compatibility with SMP hardware
Ease of programming when communication patterns are complex or vary dynamically during execution
Ability to develop apps using familiar SMP model, attention only on performance critical accesses
Lower communication overhead, better use of BW for small items, due to implicit communication and memory mapping to implement protection in hardware, rather than through I/O system
HW-controlled caching to reduce remote comm. by caching of all data, both shared and private.

## Slide 9: Advantages message-passing communication model
The architecture is scalable – Easy to build, communication penalty may be high for large systems
Communication explicit => simpler to understand; in shared memory it can be hard to know when communicating and when not, and how costly it is
Explicit communication focuses attention on costly aspect of parallel computation, sometimes leading to improved structure in multiprocessor program
Synchronization is naturally associated with sending messages, reducing the possibility for errors introduced by incorrect synchronization
Easier to use sender-initiated communication, which may have some advantages in performance

## Slide 10: Shared Memory Types
Symmetric multiprocessors (SMP)
  Small number of cores
  Share single memory with uniform memory latency
  Not scalable due to main memory and bus conflicts
Distributed shared memory (DSM)
  Memory distributed among processors, but single address space
  Non-uniform memory access/latency (NUMA) – Cache coherent NUMA (CC-NUMA)
  Processors connected via direct (switched) and non-direct (multi-hop) interconnection networks
  Provides shared memory programming with message passing scalability
Introduction

## Slide 11: SMP Interconnect
Processors to Memory AND to I/O
Bus based: all memory locations equal access time so SMP = “Symmetric MP”
Can have interleaved memories
Performance limited by bus bandwidth
Crossbar based: All memory access times are equal = SMP
Provides higher bandwidth with interleaved memories
Difficult to scale due to centralized control

## Slide 12
FIGURE 7.17 Four recent multiprocessors, each using two sockets for the processors. Starting from the upper left hand corner, the computers are: (a) Intel Xeon e5345 (Clovertown), (b) AMD Opteron X4 2356 (Barcelona), (c) Sun UltraSPARC T2 5140 (Niagara 2), and (d) IBM Cell QS20. Note that the Intel Xeon e5345 (Clovertown) has a separate north bridge chip not found in the other microprocessors. Copyright © 2009 Elsevier, Inc. All rights reserved.
Commercial SMPs

## Slide 14
Bulldozer
2 nodes 8 cores each on same die
CC-NUMA Machines

## Slide 15
Heterogeneous Architecture: Big.LITTLE Odroid Board
GPU
Heterogeneity: 4 big A-15 cores, 4 small A-7 cores and a GPU

## Slide 16
The big.LITTLE ARM Architecture used in Android Phones
Use A7 for Light Loads and A15 for Heavy Loads. Significant difference in energy between Cortex-A15 and Cortex-A7 comes from the different pipeline lengths and out-of-order issue.

## Slide 17
The big.LITTLE ARM Architecture used in Android Phones
While Cortex-A7 (Figure 1) is an in-order, non-symmetric dual-issue processor with a pipeline length of between 8-stages and 10-stages, Cortex-A15 (Figure 2) is an out-of-order sustained triple-issue processor with a pipeline length of between 15-stages and 24-stages.

## Slide 18
18
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 4.74 Specification of the ARM Cortex-A8
and the Intel Core i7 920.
From CS 161 5th Edition Book

## Slide 19: Heterogeneous Multiprocessors: SGI® Altix® 4700 Servers
Using FPGA to accelerate computation
Shared-memory NUMAflex™ (CC-NUMA?) architecture
512 sockets or 1024 cores under one instance of Linux and as much as 128TB of globally addressable memory
Dual-core Intel® Itanium® 2 Series 9000 cpus
High Bandwidth Fat-Tree Interconnection Network, called NUMALink
SGI® RASC™ Blade: Two high performance Xilinx Virtex 4 LX200 FPGA chips with 160K logic cells

## Slide 20: Cache Coherence Problem
Processors may see different values through their caches:
Centralized Shared-Memory Architectures

## Slide 21: Cache Coherence
Coherence
  All reads by any processor must return the most recently written value
  Writes to the same location by any two processors are seen in the same order by all processors
Consistency
  When a written value will be returned by a read
  If a processor writes location A followed by location B, any processor that sees the new value of B must also see the new value of A
Centralized Shared-Memory Architectures

## Slide 22: Potential HW Coherency Solutions
Snooping Solution (Snoopy Bus):
  Send all requests for data to all processors
  Processors snoop to see if they have a copy and respond accordingly
  Requires broadcast, since caching information is at processors
  Works well with bus (natural broadcast medium)
  Dominates for small scale machines (most of the market)
Directory-Based Schemes:
  Keep track of what is being shared in 1 centralized place (logically)
  Distributed memory => distributed directory for scalability (avoids bottlenecks)
  Send point-to-point requests to processors via network
  Scales better than Snooping
  Actually existed BEFORE Snooping-based schemes

## Slide 23: Cache-Coherent Non-Uniform Memory Access Machine (CC-NUMA)
Memory distributed to each processor, but the address space is shared => Offers scalability of message passing but shared memory programming with low latency
Non-uniform Memory Access (NUMA) time depending on the memory location
Each processor has a local cache, the cache coherence is maintained by hardware (through Directory) => CC-NUMA

## Slide 24: Distributed Directory MPs

## Slide 25: Scalable, High Perf. Interconnection Network
At Core of Parallel Computer Arch.
Requirements and trade-offs at many levels
  Elegant mathematical structure
  Deep relationships to algorithm structure
  Managing many traffic flows
  Electrical / Optical link properties
Little consensus
  interactions across levels
  Performance metrics?
  Cost metrics?
  Workload?
=> Need holistic understanding

## Slide 26: Performance Metrics: Latency and Bandwidth
Bandwidth
  Need high bandwidth in communication
  Match limits in network, memory, and processor
  Challenge is link speed of network interface vs. bisection bandwidth of network
Latency
  Affects performance, since processor may have to wait
  Affects ease of programming, since requires more thought to overlap communication and computation
  Overhead to communicate is a problem in many machines
Latency Hiding
  How can a mechanism help hide latency?
  Increases programming system burden
  Examples: overlap message send with computation, prefetch data, switch to other tasks