## Slide 1: CS 203: Advanced Computer Architecture Winter 2017
Laxmi N. Bhuyan
Lecture 2: Chapter 1
Technology and Power

## Slide 2: Compute Speedup – Amdahl’s Law
Speedup is due to enhancement(E):
TimeBefore
TimeAfter
= ExTimebefore x [(1-F) +
F
S
]
Speedup(E)
=
ExTimebefore
ExTimeafter
=
1
F
S
]
[(1-F) +
Let F be the fraction where enhancement is applied => Also, called parallel fraction and (1-F) as the serial fraction. S is the number of processors
Execution timeafter
Serial
Serial
Parallel F
When S -> infinity, E = 1/(1-F), If F is 10%, the maximum speed up is 1.1 for large S

## Slide 3: Acceleration/Improvement Amdahl’s Law – An Example
Q: Floating point instructions improved to run 2X;
but only 10% of execution time are FP ops. What is the execution time and speedup after improvement?
F = 0.1, S = 2
ExTimeafter = ExTimebefore x [ (1-0.1) + 0.1/2 ] = 0.95 ExTimebefore
Speedup =
ExTimebefore
ExTimeafter
=
1
0.95
= 1.053

## Slide 4: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns (micro meter) in 1971 to . 032 microns (32 nm) in 2011. Now 22 nm
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically
  Moore’s Law: Number of transistors doubles every one and half years => If CPU power is proportional to the number of transistors, it also doubles every 1.5 years.
Trends in Technology

## Slide 5: Manufacturing ICs
Yield: proportion of working dies per wafer

## Slide 6: Trends in Technology
Integrated circuit technology
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
DRAM capacity: 25-40%/year (slowing)
Flash capacity: 50-60%/year
  15-20X cheaper/bit than DRAM
Magnetic disk technology: 40%/year
  15-25X cheaper/bit then Flash
  300-500X cheaper/bit than DRAM
Trends in Technology

## Slide 7
Energy and Power
Energy = Mass x Velocity**2
= kg x (meter/secs)**2

## Slide 11: CPU Power Consumption
Look back at i7 power benchmark
  At 100% load: 258W
  At 50% load: 170W (66%)
  At 10% load: 121W (47%)
Google data center
  Mostly operates at 10% – 50% load
  At 100% load less than 1% of the time
Consider designing processors to make power proportional to load => Our research focuses on reducing power/energy consumption in CPUs and data centers. Energy proportionality

## Slide 12
C is the capacitive load, Vdd is the supply voltage, fc is the frequency, and Ilkg is the leakage current

## Slide 14
LEAKAGE POWER AND DYNAMIC
POWER OVER PROCESS NODES
Leakage power increases
exponentially every technology generation.
Dynamic power per gate @ same frequency decreases every technology generation.
Overall device dynamic power increases.
Leakage power becoming a more dominant factor
in total power dissipation

## Slide 15
LEAKAGE POWER VERSUS TEMPERATURE
Leakage power depends exponentially on temperature.
It may account for 40%–50% of total power dissipation.
Temperature is a very important factor to consider
in the context of power

## Slide 16: Power Trends
In CMOS IC technology
§1.5 The Power Wall
×1000
×30
5V → 1V
During last 30 years

## Slide 17: Power
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is the limit of what can be cooled by air
Trends in Power and Energy

## Slide 18: Reducing Power
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?
Multicore Architectures
Power Gating and DVFS

## Slide 19: Dynamic Energy and Power
Dynamic energy
  Transistor switch from 0 -> 1 or 1 -> 0
  ½ x Capacitive load x Voltage2
Dynamic power
  ½ x Capacitive load x Voltage2 x Frequency. Reduction through DVFS and Power (Clock) gating.
  Either Per-core or Chip-wide DVFS.
  Reducing clock rate reduces power, not energy consumption of an application/program. Reducing clock frequency increases time of execution.
Trends in Power and Energy
F(GHz) | 3.4 | 3.3 | 3.2 | 3 | 2.9 | 2.8 | 2.6 | 2.4 | 2.2 | 2.1 | 2 | 1.7 | 1.6
V | 1.071 | 1.046 | 1.026 | 0.991 | 0.976 | 0.956 | 0.956 | 0.956 | 0.951 | 0.951 | 0.951 | 0.946 | 0.946
Chip-wide DVFS for Intel Quad core Ivy Bridge. Not much change in voltage due to transistor threshold.

## Slide 20: Static Power
Static power consumption
  Currentstatic x Voltage
  Scales with number of transistors
  To reduce: DVS (limited by threshold voltage for transistors) and power gating
Trends in Power and Energy
Figure 2: Power gating overview

## Slide 21: CPU C-States for an Intel Quadcore Processor
Cutting down the power consumption during the through per-core sleep states (C-states).
  C1: partly clock gating
  C3: full clock gating
  C6: power gating
EBT: Energy Break-even Time - minimum inactivity time required to compensate the cost of state switching

## Slide 22
Mode | Name | What it does | CPUs
C0 | Operating State | CPU fully turned on | All CPUs
C1 | Halt | Stops CPU main internal clocks via software; bus interface unit and APIC are kept running at full speed. | 486DX4 and above
C1E | Enhanced Halt | Stops CPU main internal clocks via software and reduces CPU voltage; bus interface unit and APIC are kept running at full speed. | All socket LGA775 CPUs
C1E | — | Stops all CPU internal clocks. | Turion 64, 65-nm Athlon X2 and Phenom CPUs
C2 | Stop Grant | Stops CPU main internal clocks via hardware; bus interface unit and APIC are kept running at full speed. | 486DX4 and above
C2 | Stop Clock | Stops CPU internal and external clocks via hardware | Only 486DX4, Pentium, Pentium MMX, K5, K6, K6-2, K6-III
C2E | Extended Stop Grant | Stops CPU main internal clocks via hardware and reduces CPU voltage; bus interface unit and APIC are kept running at full speed. | Core 2 Duo and above (Intel only)
CPU-C States
C3 | Sleep | Stops all CPU internal clocks | Pentium II, Athlon and above, but not on Core 2 Duo E4000 and E6000
C3 | Deep Sleep | Stops all CPU internal and external clocks | Pentium II and above, but not on Core 2 Duo E4000 and E6000; Turion 64
C3 | AltVID | Stops all CPU internal clocks and reduces CPU voltage | AMD Turion 64
C4 | Deeper Sleep | Reduces CPU voltage | Pentium M and above, but not on Core 2 Duo E4000 and E6000 series; AMD Turion 64
C4E/C5 | Enhanced Deeper Sleep | Reduces CPU voltage even more and turns off the memory cache | Core Solo, Core Duo and 45-nm mobile Core 2 Duo only
C6 | Deep Power Down | Reduces the CPU internal voltage to any value, including 0 V | 45-nm mobile Core 2 Duo only

## Slide 23
EXAMPLE
You are designing a system for a real-time application in which a deadline of 500 micro secs must be met. You find that your system can execute the necessary code in 300 micro secs.
How much energy do you save through CPU C-states C1, C2 and C3?
1. How much CPU frequency can you reduce theoritically to save power but not miss the deadline? How much is the energy saving, if any?
2. Answer considering the DVFS table, given by earlier, by the manufacturer.
Instead of DVFS, you can put the CPU to sleep. Taking into account the transition overhead, how much time it can sleep and how much is the energy saving?

## Slide 24
ARM big.LITTLE ARCHITECTURE
Used in Samsung Phones

## Slide 25
Figure 4 Cortex-A15-Cortex-A7 DVFS Curves
Figure 5: Tracking the load of a task