## Slide 1: Lecture 3: Appendix B (Read CS 161 material) Memory Hierarchy—Ways to Reduce Misses

## Slide 2: Introduction
Programmers want unlimited amounts of memory with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Temporal and spatial locality insures that nearly all references can be found in smaller memories (Q. What are temporal and spatial localities?)
  Gives the illusion of a large, fast memory being presented to the processor
Introduction

## Slide 3: Why More on Memory Hierarchy?
Processor-Memory
Performance Gap
Growing
Notes: Y-axis is performance
X-axis is time
Latency
Cliché:
Not e that x86 didn’t have cache on chip until 1989

## Slide 4: The Goal: Illusion of large, fast, cheap memory
Fact: Large memories are slow, fast memories are small
How do we create a memory that is large, cheap and fast (most of the time)?
Hierarchy of Levels
  Uses smaller and faster memory technologies close to the processor
  Fast access time in highest level of hierarchy
  Cheap, slow memory furthest from processor
The aim of memory hierarchy design is to have access time close to the highest level and size equal to the lowest level

## Slide 5: Memory Hierarchy
Introduction

## Slide 6: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors:
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references
      = 409.6 GB/s!
    DRAM bandwidth is only 6% of this (25 GB/s)
    Requires:
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
Introduction

## Slide 7: Multilevel On-Chip Caches
§5.10 Real Stuff: The AMD Opteron X4 and Intel Nehalem
Per core: 32KB L1 I-cache, 32KB L1 D-cache, 512KB L2 cache,
8 MB L3 cache, 4-way interleaved, shared by all cores.
Intel Nehalem 4-core processor

## Slide 8: 3-Level Cache Organization
 | Intel Nehalem | AMD Opteron X4
L1 caches (per core) | L1 I-cache: 32KB, 64-byte blocks, 4-way, approx LRU replacement, hit time n/a L1 D-cache: 32KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | L1 I-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, hit time 3 cycles L1 D-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, write-back/allocate, hit time 9 cycles
L2 unified cache (per core) | 256KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | 512KB, 64-byte blocks, 16-way, approx LRU replacement, write-back/allocate, hit time n/a
L3 unified cache (shared) | 8MB, 64-byte blocks, 16-way, replacement n/a, write-back/allocate, hit time n/a | 2MB, 64-byte blocks, 32-way, replace block shared by fewest cores, write-back/allocate, hit time 32 cycles
n/a: data not available |  | 
Unified cache: Instructions and Data are put together in the same cache. Q: Why is L1 cache usually split?

## Slide 9: Memory Hierarchy Technology
Random Access:
  “Random” is good: access time is the same for all locations
  DRAM: Dynamic Random Access Memory
    High density, low power, cheap, slow
    Dynamic: need to be “refreshed” regularly
  SRAM: Static Random Access Memory
    Low density, high power, expensive, fast
    Static: content will last “forever”(until lose power)
“Not-so-random” Access Technology:
  Access time varies from location to location and from time to time
  Examples: Disk, CDROM
Sequential Access Technology: access time linear in location (e.g.,Tape)
We will concentrate on random access technology
  The Main Memory: DRAMs + Caches: SRAMs
Notes: The technology we used to build our memory hierarchy can be divided into two categories: Random Access and Non-so-Random Access.
Unlike all other aspects of life where the word random usually associates with bad things, random, when associates with memory access, for the lack of a better word, is good!
Because random access means you can access any random location at any time and the access time will be the same as any other random locations.
Which is NOT the case for disks or tape where the access time for a given location at any time can be quite different from some other random locations at some other random time.
As far as Random Access technology is concerned, we will concentrate on two specific technologies: Dynamic RAM and Static RAM.
The advantages of Dynamic RAMs are high density, low cost, and low power so we can have a lot of them without burning a hole in our budget or our desktop.
The disadvantages of DRAM are they are slow. Also they will forget what you tell them if you don’t remind them constantly (Refresh). We will talk more about refresh later today.
SRAM only has one redeeming feature: it is fast. Other than that, they have low density, expensive, and burn a lot of power. Oh, SRAM actually has another redeeming feature. They will not forget what you tell them. They will keep whatever you write to them forever.
Well “forever” is a long time. So lets just say it will keep your data as long as you don’t pull the plug on your computer.
In the next two lectures, we will be focusing on DRAMs and SRAMs.
We will not get into disk until the Virtual Memory lecture a week from now.
+3 = 19 min. (X:59)

## Slide 10: Review: Four Questions for Memory Hierarchy Designers
Q1: Where can a block be placed in the upper level? (Block placement)
  Fully Associative, Set Associative, Direct Mapped
Q2: How is a block found if it is in the upper level? (Block identification)
  Tag/Block
Q3: Which block should be replaced on a miss? (Block replacement)
  Random, LRU, FIFO
Q4: What happens on a write? (Write strategy)
  Write Back or Write Through (with Write Buffer)

## Slide 11: CS 161: Cache Organization
  Direct mapped cache: n blocks per cache.
  Map block i from memory to mod i/n of cache, where n is the number of blocks in cache => Congruent mapping
  Set-associative mapping: s sets, n/s blocks per set.
  Map block i from memory to set mod i/n of cache, where n is the number of sets in cache. Put the block into any block inside the set.
  Fully associative mapping: one set per cache (s = n).
Map block i from memory to any block of the cache
tag
offset
index
Direct mapping
log n
log b
tag
offset
index
Set-associative mapping
log s
log b
tag
offset
Fully associative mapping
log b

## Slide 12: Example: 2-way Set Associative Cache
Cache Data
Block 0
Cache Tag
Valid
:
:
:
Cache Data
Block 0
Cache Tag
Valid
:
:
:
Cache
Block
Hit
mux
tag
index
offset
address
=
=
Notes: This is called a 2-way set associative cache because there are two cache entries for each cache index. Essentially, you have two direct mapped cache works in parallel.
This is how it works: the cache index selects a set from the cache. The two tags in the set are compared in parallel with the upper bits of the memory address.
If neither tag matches the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data on the side where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 13: Write Policy: Write-Through vs Write-Back
Write-through: all writes update cache and underlying memory/cache
  Can always discard cached data - most up-to-date data is in memory
  Cache control bit: only a valid bit
Write-back: all writes simply update cache
  Write it back to memory when the block is replaced
  Flagged write-back
  Cache control bits: both valid and dirty bits
Other Advantages:
  Write-through:
    memory (or other processors) always have latest data
    Simpler management of cache
  Write-back:
    Needs much lower bus bandwidth due to infrequent access
    Better tolerance to long-latency memory?

## Slide 14: Review: Cache performance
Miss-oriented Approach to Memory Access:
  CPIExecution includes ALU and Memory instructions
Separating out Memory component entirely
  AMAT = Average Memory Access Time
  CPIALUOps does not include memory instructions

## Slide 15: EXAMPLE: Impact on Performance
Suppose a processor executes at
  Clock Rate = 200 MHz (5 ns per cycle), Ideal (no misses) CPI = 1.1
  50% arith/logic, 30% ld/st, 20% control
Suppose that 10% of load/store operations get 50 cycle miss penalty
Suppose that 1% of instructions get same miss penalty (Why is the miss rate for instructions lower than data?)
CPI = ideal CPI + average stalls per instruction
= 1.1(cycles/ins) + [ 0.30 (DataMops/ins) x 0.10 (miss/DataMop)
x 50 (cycle/miss)] + [ 1 (InstMop/ins) x 0.01 (miss/InstMop)
x 50 cycle/miss)] = (1.1 + 1.5 + .5) cycle/ins = 3.1
Total no. of memory accesses = one per instrn + 0.3 for data = 1.3 Thus, AMAT=[(1+0.01x50)+0.3(1+0.1x50)]/1.3 = 2.54 cycles => instead of one cycle.
58% (1.5/2.54) of the time the proc is stalled waiting for data memory!

## Slide 16: Unified vs Split Caches
Unified vs. Separate I&D (Harvard Architecture)
Example:
  16KB I&D: Inst miss rate=0.64%, Data miss rate=6.47%
  32KB unified: Aggregate miss rate=1.99% For unified cache, the miss rate is lower (why?)
Which is better (ignore L2 cache)?
  Assume 33% data ops  1/1.33 = 75% memory accesses from instructions and 25% accesses are for data
  hit time=1, miss time=50
  Note that data hit has 1 stall for unified cache (only one port)
AMATHarvard=75%x(1+0.64%x50)+25%x(1+6.47%x50) = 2.05
AMATUnified=75%x(1+1.99%x50)+25%x(1+1+1.99%x50)= 2.24
Proc
I-Cache-1
Proc
Unified
Cache-1
Unified
Cache-2
D-Cache-1
Proc
Unified
Cache-2
For unified cache, bandwidth is lower and AMAT is higher

## Slide 17: Where do misses come from?
Classifying Misses: 3 Cs
  Compulsory—The first access to a block is not in the cache, so the block must be brought into the cache. Also called cold start misses or first reference misses. (Misses in even an Infinite Cache)
  Capacity—If the cache cannot contain all the blocks needed during execution of a program, capacity misses will occur due to blocks being replaced and later retrieved. (Misses in Fully Associative, Size X Cache)
  Conflict—If block-placement strategy is set associative or direct mapped, conflict misses (in addition to compulsory & capacity misses) will occur because a block can be discarded and later retrieved if too many blocks map to its set. Also called collision misses or interference misses. (Misses in N-way Associative, Size X Cache)
4th “C”:
  Coherence - Misses caused by cache coherence.
Notes: Intuitive Model by Mark Hill

## Slide 18: 3Cs Absolute Miss Rate (SPEC92)
Conflict
Note the big difference between direct and 2-way cache.
Directly mapped

## Slide 19
Figure 2.9 Energy consumption per read increases as cache size and associativity are increased
Figure 2.8 Relative access times generally increase as cache size and associativity are increased.

## Slide 20: How to Improve Cache Performance?
1. Reduce the miss rate,
2. Reduce the miss penalty, or
3. Reduce the time to hit in the cache.

## Slide 21: Memory Hierarchy Basics
Basic cache optimizations:
  Larger block size
    Reduces compulsory misses
    Increases capacity and conflict misses, increases miss penalty
  Larger total cache capacity to reduce miss rate
    Increases hit time, increases power consumption
  Higher associativity
    Reduces conflict misses
    Increases hit time, increases power consumption
Introduction

## Slide 22: Larger Block Size (fixed size&assoc)
Reduced
compulsory
misses
Increased
Conflict
Misses

## Slide 23: Fast Hit Time + Low Conflict => Victim Cache
How to combine fast hit time of direct mapped, yet still avoid conflict misses?
Add buffer to place data discarded from cache
Check both the cache and victim buffer simultaneously on data request from the CPU
Jouppi [1990]: 4-entry victim cache removed 20% to 95% of conflicts for a 4 KB direct mapped data cache
Used in Alpha, HP machines
Opteron L3 cache
To Next Lower Level In
Hierarchy
DATA
TAGS
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator

## Slide 24: Reducing Misses by Hardware Prefetching of Instructions & Data
E.g., Instruction Prefetching
  Sequential prefetch or block prefetching
  Most processors fetch 2 blocks of instructions on a miss
  Cache Pollution if fetched block is unused!
  Extra block placed in “stream buffer”
  On miss check stream buffer
Works with data blocks too:
  Jouppi [1990] 1 data stream buffer satisfied 25% misses from 4KB cache; 4 streams got 43%
  Palacharla & Kessler [1994] for scientific programs for 8 streams satisfied 50% to 70% of misses from 2 64KB, 4-way set associative caches
  Data Prediction is difficult
Prefetching relies on having extra memory bandwidth that can be used without penalty
Question: What to prefetch and when to prefetch? Instruction prefetch is fine, but data?

## Slide 25: Hardware Prefetching
Fetch two blocks on miss (next sequential block)
Advanced Optimizations
Pentium 4 Pre-fetching
Intel Core i7 supports hardware prefetching to both L1 and L2 caches

## Slide 26: Leave it to the Programmer? Software Prefetching Data
Data Prefetch – Explicit prefetch instructions
  Load data into register (HP PA-RISC loads)
  Cache Prefetch: load into cache (MIPS IV, PowerPC, SPARC v. 9)
  Special prefetching instructions cannot cause faults; a form of speculative execution
Prefetching comes in two flavors:
  Binding prefetch: Requests load directly into register.
    Must be correct address and register!
  Non-Binding prefetch: Load into cache.
    Can be incorrect. Faults?
Issuing Prefetch Instructions takes time
  Is cost of prefetch issues < savings in reduced misses?
  Higher superscalar reduces difficulty of issue bandwidth

## Slide 27: Summary: Miss Rate Reduction
3 Cs: Compulsory, Capacity, Conflict
  0. Larger cache
  1. Reduce Misses via Larger Block Size
  2. Reduce Misses via Higher Associativity
  3. Reducing Misses via Victim Cache
  4. Reducing Misses via Pseudo-Associativity
  5. Reducing Misses by HW Prefetching Instr, Data
  6. Reducing Misses by SW Prefetching Data
  7. Reducing Misses by Compiler Optimizations
Prefetching comes in two flavors:
  Binding prefetch: Requests load directly into register.
    Must be correct address and register!
  Non-Binding prefetch: Load into cache.
    Can be incorrect. Frees HW/SW to guess!