## Slide 1: Lecture 4 Pipeline Contd. (Appendix C)
Instructor: L.N. Bhuyan
CS 203A Advanced Computer Architecture

## Slide 2: Exercise C1
Use the following code segment:
Loop: LD R1, 0 (R2) ; load R1from address 0+R2
DADDI R1, R1, #1 ; R1 = R1 + 1
SD R1, 0 (R2) ; store R1 at address 0+R2
DADDI R2, R2, #4 ; R2 = R2 + 4
DSUB R4, R3, R2 ; R4 = R3 – R2
BNEZ R4, Loop ; branch to Loop if R4! = 0

## Slide 3
BNEZ F D X M W

## Slide 4
There is a stall in BNEZ because there is a data dependence with DSUB. Moving the comparator and adder to decode stage doesn’t help. The condition is resolved only after EX stage even with forwarding.

## Slide 5: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
Assume the memory address of B is stored in register $t0. E, F, and A memory locations are one word apart consecutively.
Assume Internal forwarding
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 6: Arithmetic Pipeline: Ex. MIPS R4000
MIPS R4000 pipeline
Arithmetic Pipeline: The multiplier and adder are pipelined, but divider is not => Must wait 21 cycles to initiate another divide execution
Instructions are issued in order, but they complete out-of-order because of different latencies for different instructions

## Slide 7
Out of Order Completion

## Slide 8: R4000 Performance
Base ideal CPI of 1:
  Load stalls (1 or 2 clock cycles)
  Branch stalls (2 cycles + unfilled slots)
  FP result stalls: RAW data hazard (wait for FP results)
  FP structural stalls: Not enough FP hardware (parallelism)
Notes: Integer programs, major delay is branch stalls
FP its structural stalls

## Slide 9: Data Hazards in Out-Of-Order Machines
Instructions executed out of order can give rise to further data hazards. They are unavoidable when instruction level parallelism is used – like in MIPS 4000 with multiple pipelined arithmetic units.
Two different instructions using the same storage location may finish at different times because they may use different pipelines as in MIPS 4000
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
read-after-write
(RAW)
write-after-read
(WAR)
write-after-write
(WAW)
True dependence
(real)
anti dependence
(artificial)
output dependence
(artificial)

## Slide 10: WAR: Why do they exist? (Antidependence)
Recall WAR
  add R1, R2, R3
  sub R2, R4, R1
  or R1, R6, R3
Problem: swap means introducing false RAW hazards if sub finishes earlier than add
Can’t happen in in-order pipeline since reads happen in ID but writes happen in WB
Can happen in out-of-order reads, e.g. out-of-order execution
Artificial: can be removed if sub used a different destination register => Register Renaming

## Slide 11: WAW (Output Depndence)
    add R1, R2, R3
    sub R2, R4, R1
    or R1, R6, R3
Problem: Would leave wrong value in R1 for the sub if it finishes earlier than add
Can’t happen in in-order pipeline in which every instruction takes same cycles since writes are in-order
Can happen in the presence of multi-pipeline operations, i.e., out-of-order writes
Artificial: using different destination register would solve => Register Renaming

## Slide 12
I1. Load R1, A /R1 Memory(A)/
I2. Add R2, R1 /R2  (R2)+(R1)/
I3. Add R3, R4 /R3  (R3)+(R4)/
I4. Mul R4, R5 /R4  (R4)*(R5)/
I5. Comp R6 /R6  Not(R6)/
I6. Mul R6, R7 /R6  (R6)*(R7)/
Due to Superscalar (multi-pipeline) Processing, it is possible that I4
completes before I3 starts. Similarly the value of R6 depends on the
beginning and end of I5 and I6. Unpredictable result!
I1
I3
I5
I6
I4
I2
RAW
WAR
WAW and
RAW
Flow
dependence
Anti-
dependence
Flow, Anti
and Output
dependence,
Program order
Dependence Graph Example

## Slide 13: Register Renaming
Rewrite the previous program as:
I1. R1b  Memory (A)
I2. R2b  (R2a) + (R1b)
I3. R3b  (R3a) + (R4a)
I4. R4b  (R4a) * (R5a)
I5. R6b  -(R6a)
I6. R6c  (R6b) * (R7a)
Allocate more registers and rename the registers that really do not have flow dependency. The WAR hazard between I3 and I4, and WAW hazard between I5 and I6 have been removed.
These two hazards also called Name dependencies

## Slide 14: Control Hazards
Branch problem:
  branches are resolved in EX stage (Needs adder)
   2 cycles penalty on taken branches
  Ideal CPI =1. Assuming 2 cycles for all branches and 32% branch instructions  new CPI = 1 + 0.32*2 = 1.64
Solutions:
  Reduce branch penalty: change the datapath – new adder needed in ID stage. Branch delay reduced to one cycle.
  Fill branch delay slot(s) with a useful instruction.
  Fixed branch prediction.
  Static branch prediction.
  Dynamic branch prediction.

## Slide 15: MIPS Pipelined Datapath
A
d
d
r
e
s
s
4
3
2
0
A
d
d
A
d
d
r
e
s
u
l
t
S
h
i
f
t
l
e
f
t
2
I
n
s
t
r
u
c
t
i
o
n
M
u
x
0
1
A
d
d
P
C
0
A
d
d
r
e
s
s
W
r
i
t
e
d
a
t
a
M
u
x
1
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
1
6
S
i
g
n
e
x
t
e
n
d
W
r
i
t
e
r
e
g
i
s
t
e
r
W
r
i
t
e
d
a
t
a
R
e
a
d
d
a
t
a
1
A
L
U
r
e
s
u
l
t
M
u
x
A
L
U
Z
e
r
o
Imem
Dmem
Regs
IF/ID
ID/EX
EX/MEM
MEM/WB
5
Fetch Decode Execute Memory Write Back
MOVE

## Slide 16: Reducing Branch Delay
Move hardware to determine outcome to ID stage – Only one cycle penalty. Additional hardware:
  Target address adder
  Register comparator
Example: Assume branch taken
  36: sub $10, $4, $8 40: beq $1, $3, 7 -> Offset 7–Jump to 44+7x4 = 72 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)

## Slide 17
Appendix C – Question C.1
Solution C.1 a.
R1: LD -> DADDI - RAW
R1: DADDI -> SD - RAW
R1: LD -> DADDI - WAW
R2: LD -> DADDI - WAR
R2: SD -> DADDI - WAR
R2: DADDI -> DSUB - RAW
R4: DSUB -> BNEZ - RAW
What if it is a simple 5-stage linear pipeline?

## Slide 19
There is a stall in BNEZ because there is a data dependence with DSUB. Moving the comparator and adder to decode stage doesn’t help. The condition is resolved only after EX stage even with forwarding.

## Slide 22: Control Hazards – branch delay slots
Branch delay slot filling:
  move an instruction into the slot right after the branch, hoping that its execution is necessary.
  Limitations: restrictions on which instructions can be rescheduled, compile time prediction of taken or untaken branches.

## Slide 23: Example Nondelayed vs. Delayed Branch
add M1 ,M2,M3
sub M4, M5,M6
beq M1, M4, Exit
or M8, M9 ,M10
xor M10, M1,M11
Nondelayed Branch
Exit:
add M1 ,M2,M3
sub M4, M5,M6
beq M1, M4, Exit
or M8, M9 ,M10
xor M10, M1,M11
Delayed Branch
Exit:

## Slide 24
Figure C.14 Scheduling the branch delay slot. The top box in each pair shows the code before scheduling; the bottom box shows the scheduled code. In (a), the delay slot is scheduled with an independent instruction from before the branch. This is the best choice. Strategies (b) and (c) are used when (a) is not possible. In the code sequences for (b) and (c), the use of R1 in the branch condition prevents the DADD instruction (whose destination is R1) from being moved after the branch. In (b), the branch delay slot is scheduled from the target of the branch; usually the target instruction will need to be copied because it can be reached by another path. Strategy (b) is preferred when the branch is taken with high probability, such as a loop branch. Finally, the branch may be scheduled from the not-taken fall-through as in (c). To make this optimization legal for (b) or (c), it must be OK to execute the moved instruction when the branch goes in the unexpected direction. By OK we mean that the work is wasted, but the program will still execute correctly. This is the case, for example, in (c) if R7 were an unused temporary register when the branch goes in the unexpected direction.

## Slide 25: Control Hazards: Branch Prediction
Idea: doing something is better than waiting around doing nothing
  Guess branch target, start executing at guessed position
  Execute branch, verify (check) your guess
  + minimize penalty if guess is right (to zero)
  May increase penalty for wrong guesses
  Heavily researched area in the last 15 years
Fixed branch prediction.
  Each of these strategies must be applied to all branch instructions indiscriminately.
  Predict not-taken (47% actually not taken):
    continue to fetch instruction without stalling;
    do not change any state (no register write);
    if branch is taken turn the fetched instruction into no-op, restart fetch at target address: 1 cycle penalty. Assumes branch detection at the ID stage.
  Predict taken (53%):
  more difficult, must know target before branch is decoded. no advantage in our simple 5-stage pipeline even if we move the branch to ID stage. There is 1 cycle penalty any way.

## Slide 26: MIPS with Predict Not Taken
Prediction correct
Prediction incorrect - Assuming one cycle penalty

## Slide 28: MIPS R4000 pipeline

## Slide 29: R4000 Performance
Base ideal CPI of 1:
  Load stalls (1 or 2 clock cycles)
  Branch stalls (2 cycles + unfilled slots)
  FP result stalls: RAW data hazard (wait for FP results)
  FP structural stalls: Not enough FP hardware (parallelism)
Notes: Integer programs, major delay is branch stalls
FP its structural stalls

## Slide 30: FP Loop: Where are the Hazards?
Loop: LD F0,0(R1) ;F0=vector element
ADDD F4,F0,F2 ;add scalar from F2
SD 0(R1),F4 ;store result
SUBI R1,R1,8 ;decrement pointer 8B (DW)
BNEZ R1,Loop ;branch R1!=zero
NOP ;delayed branch slot
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
Load double Store double 0
Integer op Integer op 0
Where are the stalls?

## Slide 31: FP Loop Showing Stalls
9 clocks: Rewrite code to minimize stalls?
Instruction Instruction Latency in producing result using result clock cycles
FP ALU op Another FP ALU op 3
FP ALU op Store double 2
Load double FP ALU op 1
1 Loop: LD F0,0(R1) ;F0=vector element
2 stall
3 ADDD F4,F0,F2 ;add scalar in F2
4 stall
5 stall
6 SD 0(R1),F4 ;store result
7 SUBI R1,R1,8 ;decrement pointer 8B (DW)
8 BNEZ R1,Loop ;branch R1!=zero
9 stall ;delayed branch slot

## Slide 32: Minimizing Stalls Technique 1: Compiler Optimization
6 clocks
1 Loop: LD F0,0(R1)
2 stall
3 ADDD F4,F0,F2
4 SUBI R1,R1,8 ;Move SD instruction to delay slot
5 BNEZ R1,Loop ;delayed branch
6 SD 8(R1),F4 ;Offset altered when move past SUBI
Swap BNEZ and SD by changing address of SD
Notes: 3 clocks doing work, 3 overhead (stall, branch, sub)

## Slide 33: Control Hazards: Branch Prediction
Dynamic branch prediction
  Next class