## Slide 1: Lecture 4: Cache Optimization Appendix B and Ch 2

## Slide 2: How to Improve Cache Performance?
1. Reduce the miss rate,
2. Reduce the miss penalty, or
3. Reduce the time to hit in the cache.
4. Increase bandwidth

## Slide 3: Memory Hierarchy Basics
Basic cache optimizations:
  Larger block size
    Reduces compulsory misses
    Increases capacity and conflict misses, increases miss penalty
  Larger total cache capacity to reduce miss rate
    Increases hit time, increases power consumption
  Higher associativity
    Reduces conflict misses
    Increases hit time, increases power consumption
Introduction

## Slide 4: Larger Block Size (fixed size&assoc)
Reduced
compulsory
misses
Increased
Conflict
Misses

## Slide 5: Pseudo-set associative Cache
Pseudo-set associative cache
  access the cache
  if miss, invert the high-order index bit & access the cache again
  + miss rate of 2-way set associative cache
  + close to access time of direct-mapped cache
  increase in hit time (relative to 2-way associative) if always try slow hit first
    predict which is the fast-hit block
    put the fast hit block in the same location; swap blocks if wrong
  how does pseudo-set associativity improve memory system performance?

## Slide 6: Fast Hit Time + Low Conflict => Victim Cache
How to combine fast hit time of direct mapped, yet still avoid conflict misses?
Add buffer to place data discarded from cache
Check both the cache and victim buffer simultaneously on data request from the CPU
Jouppi [1990]: 4-entry victim cache removed 20% to 95% of conflicts for a 4 KB direct mapped data cache
Used in Alpha, HP machines
Opteron L3 cache is a victim cache
To Next Lower Level In
Hierarchy
DATA
TAGS
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator
One Cache line of Data
Tag and Comparator

## Slide 7: Reducing Misses by Hardware Prefetching of Instructions & Data
E.g., Instruction Prefetching
  Sequential prefetch or block prefetching
  Most processors fetch 2 blocks of instructions on a miss
  Cache Pollution if fetched block is unused!
  Extra block placed in “stream buffer”
  On miss check stream buffer
Works with data blocks too:
  Jouppi [1990] 1 data stream buffer satisfied 25% misses from 4KB cache; 4 streams got 43%
  Palacharla & Kessler [1994] for scientific programs for 8 streams satisfied 50% to 70% of misses from 2 64KB, 4-way set associative caches
  Data Prediction is difficult, but works well with scientific applications
Prefetching relies on having extra memory bandwidth that can be used without penalty
Question: What to prefetch and when to prefetch? Instruction prefetch is fine, but data?

## Slide 8: Hardware Prefetching
Fetch two blocks on miss (next sequential block)
Advanced Optimizations
Pentium 4 Pre-fetching
Intel Core i7 supports hardware prefetching to both L1 and L2 caches

## Slide 9: Leave it to the Programmer? Software Prefetching Data
Data Prefetch – Explicit prefetch instructions
  Load data into register (HP PA-RISC loads)
  Cache Prefetch: load into cache (MIPS, PowerPC, SPARC)
Prefetching comes in two flavors:
  Binding prefetch: Requests load directly into register.
    Must be correct address and register!
  Non-Binding prefetch: Load into cache.
    Very suitable for prefetching from main memory
Issuing Prefetch Instructions takes time
  Is cost of prefetch issues < savings in reduced misses?
  Higher superscalar reduces difficulty of issue bandwidth

## Slide 10: 5. Compiler Optimization to Reduce Miss Rate
Nested loops may access data in memory non-sequentially (cache misses).
Exchange the nesting of loops can make the code access the data in order, reduce cache misses.
EX: If X is a two-dimensional array of size [5000, 100], allocated as row major, i.e. X(I,j) next X(I,j+1), then modify the program as below.
/*Before*/ for(j=0;j<100;j++) for(i=0;i<5000;i++) x[i][j]=2*x[i][j]
/*After*/ for(i=0;i<5000;i++)
for(j=0;j<100;j++) x[i][j]=2*x[i][j]

## Slide 11: EX. Block Matrix Algorithm
Operate on submatrices (blocks) instead of entire row or columns.
The submatrices can fit into cache.
/*Before*/ for(i=0;i<N;i++) for(j=0;j<N;j++){
r=0;
for(k=0;k<N;k++) r=r+y[i][k]*z[k][j];
x[i][j] = r;}
/*After*/ for(jj=0;jj<N;jj=jj+B) // among blocks
for(kk=0;kk<N;kk=kk+B) // among blocks
for(i=0;i<N;i++)
for(j=jj;j<jj+B;j++){ // within a block r=0;
for(k=kk;k<kk+B;k++) // within a block
r=r+y[i][k]*z[k][j];
x[i][j] = x[i][j] +r;
}

## Slide 12
Figure 2.8 A snapshot of the three arrays x, y, and z when N = 6 and i = 1. The age of accesses to the array elements is indicated by shade: white means not yet touched, light means older accesses, and dark means newer accesses. Compared to Figure 2.9, elements of y and z are read repeatedly to calculate new elements of x. The variables i, j, and k are shown along the rows or columns used to access the arrays.

## Slide 13
Figure 2.9 The age of accesses to the arrays x, y, and z when B = 3. Note that, in contrast to Figure 2.8, a smaller number
of elements is accessed.

## Slide 14: Summary: Miss Rate Reduction
3 Cs: Compulsory, Capacity, Conflict
  0. Larger cache
  1. Reduce Misses via Larger Block Size
  2. Reduce Misses via Higher Associativity
  3. Reducing Misses via Victim Cache
  4. Reducing Misses via Pseudo-Associativity
  5. Reducing Misses by HW Prefetching Instr, Data
  6. Reducing Misses by SW Prefetching Data
  7. Reducing Misses by Compiler Optimizations
Prefetching comes in two flavors:
  Binding prefetch: Requests load directly into register.
    Must be correct address and register!
  Non-Binding prefetch: Load into cache.
    Can be incorrect. Frees HW/SW to guess!

## Slide 15: Review: Improving Cache Performance
1. Reduce the miss rate,
2. Reduce the miss penalty, or
3. Reduce the time to hit in the cache.
4. Increase bandwidth

## Slide 16: 1. Reduce Miss Penalty: Early Restart and Critical Word First
Don’t wait for full block to be loaded before restarting CPU
  Early restart—As soon as the requested word of the block arrives, send it to the CPU and let the CPU continue execution
  Critical Word First—Request the missed word first from memory and send it to the CPU as soon as it arrives; let the CPU continue execution while filling the rest of the words in the block. Also called wrapped fetch and requested word first
Generally useful only in large blocks,
Spatial locality => tend to want next sequential word, so not clear if benefit by early restart
block

## Slide 17: 2. Reducing Miss Penalty: Read Priority over Write on Miss
Give priority to reads over writes on a miss by putting the writes in a write buffer
Write-through w/ write buffers => RAW conflicts with main memory reads on cache misses
  If simply wait for write buffer to empty, might increase read miss penalty (old MIPS 1000 by 50% )
  Check write buffer contents before read; if no conflicts, let the memory access continue
Write-back want buffer to hold displaced blocks
  Consider when a Read miss is replacing a dirty block
  Normally: Write dirty block to memory, and then do the read
  Instead copy the dirty block to a write buffer, then do the read, and then do the write
  CPU stall less since restarts as soon as do read

## Slide 18: Write Buffers
Write Buffers puts words to be written in L2 cache/memory along with their addresses.
  2 to 4 entries deep
  all read misses are checked against pending writes for dependencies (associatively)
  allows reads to proceed ahead of writes
  can coalesce writes to same block address to reduce time (next slide)
L1
L2
Write buffer
to CPU

## Slide 19: Merging Write Buffers to Reduce Miss Penalty
Write buffer to allow processor to continue while waiting to write to memory
If buffer contains modified blocks, the addresses can be checked to see if address of new data matches the address of a valid write buffer entry
If so, new data are combined with that entry
Increases block size of write for write-through cache of writes to sequential words, bytes since multiword writes more efficient to memory
The Sun T1 (Niagara) processor, among many others, uses write merging

## Slide 20: Write Merge in Write Buffers

## Slide 21: 4: Add a second-level cache
L2 Equations
AMAT = Hit TimeL1 + Miss RateL1 x Miss PenaltyL1 Miss PenaltyL1 = Hit TimeL2 + Miss RateL2 x Miss PenaltyL2
AMAT = Hit TimeL1 +
Miss RateL1 x (Hit TimeL2 + Miss RateL2 x Miss PenaltyL2)
Definitions:
  Local miss rate— misses in this cache divided by the total number of memory accesses to this cache (Miss rateL2)
  Global miss rate—misses in this cache divided by the total number of memory accesses generated by the CPU Global Miss Rate is what matters

## Slide 22: Comparing Local and Global Miss Rates
32 KB 1st level cache; Increasing 2nd level cache
Local miss rate is for L2 – Very high for small L2 size
Single cache miss rate is the rate if we have one cache of size in x-axis
Global miss rate close to single level cache rate provided L2 >> L1
The idea is to reduce miss penalty without increasing the miss rate
L1 speed affects the CPU clock cycle, but not L2 speed
Log
Cache Size

## Slide 23: AMAT Example
For every 1000 memory references, assume 40 misses in L1 and 20 misses in L2;
Hit cycle in L1 is 1, L2 is 10; Miss penalty from L2 to memory is 100 cycles; there are 1.5 memory references per instruction. What is AMAT and average stall cycles per instruction?
  AMAT = [1 + 40/1000 * (10 + 20/40 * 100) ] *cc = 3.4 cycles
  AMAT without L2 = 1 + 40/1000 * 100 = 5 cycles => An improvement of 1.6 cycles due to L2
  Average stall cycles per instruction = 1.5 * 40/1000 * 10 + 1.5 * 20/1000 * 100 = 3.6 cycles
Note: We have not distinguished reads and writes. Access L2 only on L1 miss, No separate I-cache and D-cache

## Slide 24: Reducing Miss Penalty Summary
Four techniques
  Read priority over write on miss
  Early Restart and Critical Word First on miss
  Write Buffer
  Second Level Cache
Can be applied recursively to Multilevel Caches
  Danger is that time to DRAM will grow with multiple levels of cache memories
  First attempts (compulsory misses) at L2 caches can make things worse, since increased worst case is worse