## Slide 1: Lecture 5: Cache Optimization Contd.

## Slide 2
TA: Devashree Tripathy
E-mail: dtrip003@ucr.edu
Office Hours: T, W 11-12.30 pm
WCH 463

## Slide 3: How to Improve Cache Performance?
1. Reduce the miss rate,
2. Reduce the miss penalty, or
3. Reduce the time to hit in the cache.
4. Increase bandwidth

## Slide 4: 1. Small and simple caches
L1 access time affects the CPU clock cycle
Small on-chip L1 caches – less access time
Direct mapped cache faster because no hardware comparison between blocks, but higher miss ratio
Compromise – Direct L1 cache and Set-associative L2 cache
How to predict cache access time at the design stage? – Use CACTI program

## Slide 5: Static RAM (SRAM) Cell
Six transistors in cross connected fashion
  Provides regular AND inverted outputs
  Implemented in CMOS process
Single Port 6-T SRAM Cell
Bigger the cache, more is the access time.

## Slide 6: Impact of Change in cc
Suppose a processor has the following parameters:
  CPI = 2 (w/o memory stalls)
  mem access per instruction = 1.5
Compare AMAT and CPU time for a direct mapped cache and a 2-way set associative cache assuming:
  AMATd = hit time + miss rate * miss penalty = 1*1 + 0.014*75 = 2.05 ns
  AMAT2 = 1*1.25 + 0.01*75 = 2 ns < 2.05 ns
  Execution Times:
  CPUd = (CPI*cc + mem. stall time)*IC = (2*1 + 1.5*0.014*75)IC = 3.575*IC
  CPU2 = (2*1.25 + 1.5*0.01*75)IC = 3.625*IC > CPUd !
Reason: Change in cc affects all instructions while reduction in miss rate benefit only memory instructions.
 | cc | Hit cycle | Miss penalty | Miss rate
Direct map | 1ns | 1 | 75 ns | 1.4%
2-way associative | 1.25ns(why?) | 1 | 75 ns | 1.0%

## Slide 7: Fast Hit times via Small and Simple Caches
Index tag memory and then compare takes time
 Small cache can help hit time since smaller memory takes less time to index
  E.g., L1 caches same size for 3 generations of AMD microprocessors: K6, Athlon, and Opteron
  Also L2 cache small enough to fit on chip with the processor avoids time penalty of going off chip
Simple  direct mapping
  Can overlap tag check with data transmission since no choice
Access time estimate for 90 nm using CACTI model 4.0
  Median ratios of access time relative to the direct-mapped caches are 1.32, 1.39, and 1.43 for 2-way, 4-way, and 8-way caches

## Slide 8
Figure 2.8 Relative access times generally increase as cache size and associativity are increased. These data come from the CACTI model 6.5 by Tarjan et al. (2005). The data assume typical embedded SRAM technology, a single bank, and 64-byte blocks. The assumptions about cache layout and the complex trade-offs between interconnect delays (that depend on the size of a cache block being accessed) and the cost of tag checks and multiplexing lead to results that are occasionally surprising, such as the lower access time for a 64 KiB with two-way set associativity versus direct mapping. Similarly, the results with eight-way set associativity generate unusual behavior as cache size is increased. Because such observations are highly dependent on technology and detailed design assumptions, tools such as CACTI serve to reduce the search space. These results are relative; nonetheless, they are likely to shift as we move to more recent and denser semiconductor technologies.

## Slide 9: 2. Way Prediction
Way prediction prediction: keep extra bits in cache to predict predict the “way ”, or block within the set, of next cache access. Saves access time and energy.
– Multiplexor is set early to select desired block, only 1 tag comparison performed that clock cycle in parallel with reading the cache data
-- Miss => check other blocks for matches in next clock cycle – longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s. Also, used on ARM Cortex-A8
Advanced Optimizations

## Slide 10: How to Improve Cache Performance?
1. Reduce the miss rate,
2. Reduce the miss penalty, or
3. Reduce the time to hit in the cache.
4. Increase bandwidth

## Slide 11: Handling a Cache Miss the Old Way
(1) Send the address to the next level of the hierarchy
(2) Signal a read operation
(3) Wait for the data to arrive
(4) Update the cache entry with data*, rewrite the tag, turn the valid bit on, clear the dirty bit (unless an instruction cache)
(5) Resend the memory address; this time there will be a hit.
* There are variations:
  fill the cache block, then send the requested word to the CPU
  send the requested word to the CPU as soon as it arrives at the cache (early restart)
  requested word is sent from memory first; then the rest of the block follows (requested word first)
Early restart and requested word first have a lower miss penalty, because they return execution control to the CPU earlier.

## Slide 12: 1. Non-blocking Caches
Non-blocking cache or lockup-free cache allow data cache to continue to supply cache hits during a miss
  Complicated cache controller architecture
“hit under miss” reduces the effective miss penalty by working during miss vs. ignoring CPU requests
“hit under multiple miss” or “miss under miss” may further lower the effective miss penalty by overlapping multiple misses
  Significantly increases the complexity of the cache controller as there can be multiple outstanding memory accesses
  Requires multiple memory banks (otherwise cannot support)
  Pentium Pro allows 4 outstanding memory misses

## Slide 13: Miss Status Holding Register (MSHR)
  miss status holding registers (MSHR)
    hardware structure for tracking outstanding misses
      physical address of the block
      which word in the block
      destination register number (if data)
      mechanism to merge requests to the same block
      mechanism to insure accesses to the same location execute in program order

## Slide 14: Miss Penalty for Out-of-Order (OOO) Exe. Processor.
In OOO processors, memory stall cycles are overlapped with execution of other instructions. Miss penalty should not include this overlapped part.
  mem stall cycle per instruction = mem miss per instruction x (total miss penalty – overlapped miss penalty)
For the previous example. Suppose 30% of the 75ns miss penalty can be overlapped, what is the AMAT and CPU time?
  Assume using direct map cache, cc=1.25ns to handle out of order execution.
  AMATd = 1*1.25 + 0.014*(75*0.7) = 1.985 ns
  With 1.5 memory accesses per instruction,
  CPU time =( 2*1.25 + 1.5 * 0.014 * (75*0.7))*IC = 3.6025 IC

## Slide 15
Big Improvement due to small cache

## Slide 16
Figure 2.11 The effectiveness of a nonblocking cache is evaluated by allowing 1, 2, or 64 hits under a cache miss with 9 SPECINT (on the left) and 9 SPECFP (on the right) benchmarks. The data memory system modeled after the Intel i7 consists of a 32 KiB L1 cache with a four-cycle access latency. The L2 cache (shared with instructions) is 256 KiB with a 10-clock cycle access latency. The L3 is 2 MB and a 36-cycle access latency. All the caches are eight-way set associative and have a 64-byte block size. Allowing one hit under miss reduces the miss penalty by 9% for the integer benchmarks and 12.5% for the floating point. Allowing a second hit improves these results to 10% and 16%, and allowing 64 results in little additional improvement.

## Slide 17: 2. Pipelining Cache
Pipeline cache access to improve bandwidth
  Examples of L1 access:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity
Advanced Optimizations

## Slide 18: 3. Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
  T2 (“Niagara”) L2 has 8 or 16 banks
Interleave banks according to block address. (1) Memory accesses from different processors can go to different banks.
(2) Interleaved Memory – Sequential Access from the same processor can jump from one bank to the other in the next cycle without for row and column accesses – like pipelining
Advanced Optimizations

## Slide 19: Increasing Cache/Main Memory Bandwidth via Multiple Banks
Rather than treat the cache as a single monolithic block, divide into independent banks that can support simultaneous accesses.
Banking is a standard practice in DRAMs to increase BW, and to connect many smaller chips. Ex. Bank 0 has addresses (blocks) from 0 to X-1, bank 1 from X to 2X-1, bank 2 from 2X to 3X-1.. Called High-order interleaving
Banking works best when accesses naturally spread themselves across banks  mapping of addresses to banks affects behavior of memory system
Simple mapping that works well is “sequential interleaving” or “low-ordered interleaving” or just “interleaving”
  Spread block addresses sequentially across banks
  E,g, if there 4 banks, Bank 0 has all blocks whose address modulo 4 is 0; bank 1 has all blocks whose address modulo 4 is 1; …
Notes: Answer is 3 stages between branch and new instruction fetch and 2 stages between load and use (even though if looked at red insertions that it would be 3 for load and 2 for branch)
Reasons:
1) Load: TC just does tag check, data available after DS; thus supply the data & forward it, restarting the pipeline on a data cache miss
2) EX phase does the address calculation even though just added one phase; presumed reason is that since want fast clockc cycle don’t want to sitck RF phase with reading regisers AND testing for zero, so just moved it back on phase

## Slide 22: Summary
Advanced Optimizations

## Slide 23: Cache Optimization Summary
Technique MR MP HT Complexity
Larger Block Size + – 0 Higher Associativity + – 1 Victim Caches + 2 Way prediction Caches + 2 HW Prefetching of Instr/Data + 2 Compiler Controlled Prefetching + 3 Compiler Reduce Misses + 0
Priority to Read Misses + 1 Early Restart & Critical Word 1st + 2 Non-Blocking Caches + 3 Second Level Caches + 2
miss rate
miss penalty