## Slide 1: CS203A Graduate Computer Architecture Lecture 6 Main Memory Note: Some Slides taken from Prof. Onur Mutlu’s class at CMU

## Slide 3: Memory Technology
Random Access Memory (vs. Serial Access Memory)
Cache uses SRAM: Static Random Access Memory
  No refresh (6 transistors/bit vs. 1 transistor Size: DRAM/SRAM ­ 4-8, Cost/Cycle time: SRAM/DRAM ­ 8-16
Access Time - Time between when a read is requested and when the requested data arrives
Cycle Time - The minimum time between two unrelated requests to the memory. Must include refreshing time if any
Main Memory is DRAM: Dynamic Random Access Memory
  Dynamic since needs to be refreshed periodically
  Addresses divided into 2 halves (Memory as a 2D matrix):
    RAS or Row Access Strobe
    CAS or Column Access Strobe

## Slide 4: Dynamic RAM
SRAM cells exhibit high speed/poor density (6 cells per transistor)
DRAM: simple transistor/capacitor pairs in high density form implemented in CMOS
Word Line
Bit Line
C
Sense Amp
. . .
Every read must have memory refreshing to restore the charge on the capacitor
    RAS or Row
    Access Strobe
    CAS or Column Access Strobe

## Slide 8: High Memory Demand for Multicore Processors
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references
      = 409.6 GB/s!
    DRAM bandwidth is only 6% of this (25 GB/s)
    Requires:
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
Introduction

## Slide 9
Figure 2.12 Internal organization of a DRAM. Modern DRAMs are organized in banks, typically four for DDR3. Each bank consists of a series of rows. Sending a PRE (precharge) command opens or closes a bank. A row address is sent with an Act (activate), which causes the row to transfer to a buffer. When the row is in the buffer, it can be transferred by successive column addresses at whatever the width of the DRAM is (typically 4, 8, or 16 bits in DDR3) or by specifying a block transfer and the starting address. Each command, as well as block transfers, are synchronized with a clock.
DRAM Banks

## Slide 12
block

## Slide 13: Memory Interleaving Also helps to reduce memory latency in single cores
Interleaved memory is more flexible than wide-access memory in that it can handle multiple independent accesses at once.

## Slide 14: Memory and Bus Organizations
C
P
U
C
a
c
h
e
B
u
s
M
e
m
o
r
y
C
P
U
B
u
s
M
e
m
o
r
y
M
u
l
t
i
p
l
e
x
o
r
C
a
c
h
e
C
P
U
C
a
c
h
e
B
u
s
M
e
m
o
r
y
b
a
n
k
1
M
e
m
o
r
y
b
a
n
k
2
M
e
m
o
r
y
b
a
n
k
3
M
e
m
o
r
y
b
a
n
k
0
one-word wide memory organization
wide memory organization
– a row consists of many words
Interleaved memory organization (high or low-ordered)
Expensive due to wide bus and control circuits.

## Slide 15: Memory Access Time Example
Assume that it takes 1 cycle to send the address, 15 cycles for each DRAM access and 1 cycle to send a word of data.
Assuming a cache block of 4 words and one-word wide DRAM, miss penalty = 1 + 4x15 + 4x1 = 65 cycles
With main memory and bus width of 2 words, miss penalty = 1 + 2x15 + 2x1 = 33 cycles. For 4-word wide memory, miss penalty is 17 cycles.
With interleaved memory (word-interleaved) of 4 memory banks and same bus width, the miss penalty = 1 + 1x15 + 4x1 = 20 cycles. The memory controller must supply consecutive addresses to different memory banks. Interleaving is universally adapted in high-performance computers.

## Slide 16
PC100 is a standard for internal removable computer random access memory, defined by the JEDEC. PC100 refers to Synchronous DRAMoperating at a clock frequency of 100 MHz, on a 64-bit-wide bus
Q: What are PC2100 and Rambus? Refer to Wikipedia

## Slide 17
Row Buffer
One page/row

## Slide 19
Q: Can we schedule memory accesses to maximize row buffer hit?
Memory Access Scheduling – Good research topic

## Slide 23: Memory Technology
Amdahl:
  Memory capacity should grow linearly with processor speed
  Unfortunately, memory capacity and speed has not kept pace with processors
Some optimizations:
  Multiple accesses to same row
  Synchronous DRAM
    Added clock to DRAM interface
    Burst mode with critical word first
  Wider interfaces
  Double data rate (DDR)
  Multiple banks on each DRAM device
Memory Technology

## Slide 24: DRAM Technology
Constant improvement in packaging and data transfer rate at the cost of capacity increase
DRAM followed Moore’s law for 20 years bringing out a new chip with 4 times the capacity every three years.
Due to packaging constraint, new chips double in capacity every two years
Since 2006, the capacity doubles only in four years
Improving DRAM Performance
Add timing signals for repeated access to the row buffer without another row access time. 1024-4096 bits in each row access buffer, to be read with consequent column access
Instead of asynchronous access and synchronization overhead, add clock to allow repeated access without overhead => Synchronous DRAM (SDRAM). With every clock, send data in burst mode (8-16bit transfers) –no need to send the address again
Increase bandwidth by transferring data both on rising and falling edge of the clock – double data rate (DDR) technology
Make memory buses wider. Initially, they offered 4-bit transfer mode. DDR2 and DDR3 have 16-bit buses
Add banks to allow interleaving and help power management – ex DDR3

## Slide 25: Memory Optimizations
DDR:
  DDR2
    Lower power (2.5 V -> 1.8 V)
    Higher clock rates (266 MHz, 333 MHz, 400 MHz)
  DDR3
    1.5 V
    800 MHz
  DDR4
    1-1.2 V
    1600 MHz
GDDR5 is graphics memory based on DDR3
Memory Technology

## Slide 26: Memory Optimizations
Memory Technology

## Slide 27: Memory Optimizations
Memory Technology
DIMM: Dual inline memory modules containing 4-16 DRAMs on a board

## Slide 28: Other Types of DRAM
Synchronous DRAM (SDRAM): Ability to transfer a burst of data given a starting address and a burst length – suitable for transferring a block of data from main memory to cache.
Page Mode DRAM: All bits on the same ROW (Spatial Locality)
  Don’t need to wait for wordline to recharge
  Toggle CAS with new column address
Extended Data Out (EDO)
  Overlap Data output w/ CAS toggle
  Later brother: Burst EDO (CAS toggle used to get next addr)
Rambus DRAM (RDRAM)
- Pipelined control

## Slide 29: Memory Optimizations
Graphics memory:
  Achieve 2-5 X bandwidth per DRAM vs. DDR3
    Wider interfaces (32 vs. 16 bit)
    Higher clock rate
      Possible because they are attached via soldering instead of socketted DIMM modules
Reducing power in SDRAMs:
  Lower voltage
  Low power mode (ignores clock, continues to refresh)
Memory Technology

## Slide 30: Memory Power Consumption
Memory Technology
Power consumption for a DDR3 SDRAM operating under three conditions: low power (shutdown) mode, typical system mode (DRAM active 30% for reads and 15% for writes), and fully active mode, where DRAM is continuously reading or writing. All recent SDRAMs support power down mode.

## Slide 31: Flash Memory
Type of EEPROM
Must be erased (in blocks) before being overwritten
Non volatile
Limited number of write cycles
Cheaper than SDRAM, more expensive than disk
Slower than SRAM, faster than disk
Memory Technology