## Slide 1: CS203A Computer Architecture Lecture 7 Virtual Memory (Some Slides taken from Onur Mutlu’s class at CMU)

## Slide 2: Virtual Memory
Idea 1: Many Programs sharing DRAM Memory so that context switches can occur between active users
Idea 2: Allow program to be written without memory constraints – program can exceed the size of the main memory – virtual address
Idea 3: Relocation: Parts of the program can be placed at different locations in the memory instead of a big chunk.
Idea 4: DRAM as a cache: use DRAM Memory as a kind of “cache” for disk

## Slide 3: Memory Hierarchy: The Big Picture
Data movement in a memory hierarchy.

## Slide 4: Comparing the 2 levels of hierarchy
Cache Virtual Memory
Block or Line Page
Miss Page Fault
Block Size: 32-64B Page Size: 4K-16KB
Placement: Fully Associative Direct Mapped, N-way Set Associative
Replacement: Least Recently Used LRU or Random (LRU) approximation
Write Thru or Back Write Back
How Managed: Hardware + Software Hardware (Operating System)

## Slide 5: Handling Page Faults
A page fault is like a cache miss
  Must find page in lower level of hierarchy
If valid bit is zero, the Physical Page Number points to a page on disk
When OS starts new process, it creates space on disk for all the pages of the process, sets all valid bits in page table to zero, and all Physical Page Numbers to point to disk
  called Demand Paging - pages of the process are loaded from disk only as needed
  Create “swap” space for all virtual pages on disk

## Slide 7: Virtual Memory has own terminology
Each process has its own private “virtual address space” (e.g., 232 Bytes); CPU actually generates “virtual addresses”
Each computer has a “physical address space” (e.g., 128 MegaBytes DRAM); also called “real memory”
Address translation: mapping virtual addresses to physical addresses
  Allows multiple programs to use (different chunks of physical) memory at same time
  Also allows some chunks of virtual memory to be represented on disk, not in main memory (to exploit memory hierarchy)

## Slide 8: Mapping Virtual Memory to Physical Memory
0
Physical Memory
¥
Virtual Memory
Heap
64 MB
Divide Memory into equal sized “chunks” or pages (say, 4KB each)
0
Any chunk of Virtual Memory assigned to any chunk of Physical Memory (“page”)
Stack
Heap
Static
Code
Single
Process

## Slide 9: How to Perform Address Translation?
VM divides memory into equal sized pages
Address translation relocates entire pages
  offsets within the pages do not change
  if make page size a power of two, the virtual address separates into two fields: like cache index, offset fields
Virtual Page Number
Page Offset
virtual address

## Slide 10: Mapping Virtual to Physical Address
Virtual Page Number
Page Offset
Page Offset
Physical Page Number
Translation
31 30 29 28 27 .………………….12 11 10
29 28 27 .………………….12 11 10
9 8 ……..……. 3 2 1 0
Virtual Address
Physical address = 2**30 Bytes < Virtual address
9 8 ……..……. 3 2 1 0
1KB page size

## Slide 11: Address Translation
Want fully associative page placement
How to locate the physical page?
Search impractical (too many pages)
A page table is a data structure which contains the mapping of virtual pages to physical pages
  There are several different ways, all up to the operating system, to keep this data around
Each process running in the system has its own page table (PT)
Page Table Register (PTR) indicates where the PT is located in the main memory

## Slide 12: Address Translation: Page Table
Virtual Address (VA):
virtual page nbr
offset
Page Table
Register
Page Table located in physical memory
index
into
page
table
+
Physical
Memory
Address (PA)
V: Valid bit: 1 => in memory, 0 => in disk
AR: Access Rights: None, Read Only, Read/Write, Executable
Page Table
1
Access
Rights
Physical
Page
Number
V
A.R.
P. P. N.
0
A.R.
V
A.R.
P. P. N.
...
...
disk

## Slide 13: Page Tables and Address Translation
The page table register indicates where the page for a particular process is located.

## Slide 14: Protection and Sharing in Virtual Memory
Virtual memory as a facilitator of sharing and memory protection.

## Slide 15: Optimizing for Space
Page Table too big!
  4GB Virtual Address Space ÷ 4 KB page  220 (~ 1 million) Page Table Entries Assuming 4 Bytes per entry  4 MB just for Page Table of single process!
  With 100 processes, memory required is 400 MB
Variety of solutions to tradeoff Page Table size for slower performance when PT is accessed
Virtual Memory too slow!
- Virtual Memory requires two memory accesses! One to access page table to get the memory address and another to get the real data

## Slide 16: Hierarchical Page Tables
To reduce the size of the page table
  1-level page table is too expensive for large virtual address Space
Solution
Use a limit register to restrict page table size and let it grow with more pages.
Ex: Multilevel page table,
Paging page tables, etc.
  To create small page tables for the top (heap) and bottom (stack) part of virtual memory
  The virtual address is now split into multiple chunks to index a page table “tree”
Example
  X86 paging
  AMD Opteron: Text book Append. B

## Slide 17: x86 hierarchical paging
Control Registers CR0 to CR 4 in X86 architecture. CR3 points to the page table location for a process

## Slide 18
Figure B.27 The mapping of an Opteron virtual address of 48 bits. The Opteron virtual memory implementation with four page table levels supports an effective physical address size of 40 bits. Each page table has 512 entries, so each level field is 9 bits wide. The AMD64 architecture document allows the virtual address size to grow from the current 48 bits to 64 bits, and the physical address size to grow from the current 40 bits to 52 bits.
AMD Opteron Paging

## Slide 19: How Translate Fast?
Problem: Virtual Memory requires two memory accesses!
  one to translate Virtual Address into Physical Address (page table lookup)
  one to transfer the actual data (cache hit)
  But Page Table is in physical memory! => 2 main memory accesses!
Observation: since there is locality in pages of data, must be locality in virtual addresses of those pages!
Why not create a cache of virtual to physical address translations to make translation fast? (smaller is faster)
For historical reasons, such a “page table cache” is called a Translation Lookaside Buffer, or TLB

## Slide 20: Typical TLB Format
Virtual Physical Valid Ref Dirty Access
Page Nbr Page Nbr Rights
TLB just a cache of the page table mappings
Dirty: since use write back, need to know whether or not to write page to disk when replaced
Ref: Used to calculate LRU on replacement TLB access time comparable to cache (much less than main memory access time)
“tag”
“data”

## Slide 21: Translation Lookaside Buffer
Virtual-to-physical address translation by a TLB and how the resulting physical address is used to access the cache memory.
Page
-------
One-word block in MIPS 2000

## Slide 22
V
a
l
i
d
T
a
g
D
a
t
a
P
a
g
e
o
f
f
s
e
t
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
V
a
l
i
d
1
2
2
0
2
0
1
6
1
4
C
a
c
h
e
i
n
d
e
x
3
2
D
a
t
a
C
a
c
h
e
h
i
t
2
B
y
t
e
o
f
f
s
e
t
D
i
r
t
y
T
a
g
T
L
B
h
i
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
t
a
g
3
1
3
0
2
9
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
DECStation 3100/ MIPS R2000
Virtual Address
TLB
Cache
64 entries, fully associative
Physical Address
16K entries, direct mapped

## Slide 23
PTE – Page Table Entry

## Slide 24: Translation Look-Aside Buffers
TLB is usually small, typically 32-4,096 entries
Like any other cache, the TLB can be fully associative, set associative, or direct mapped
Processor
TLB
Cache
Main
Memory
miss
hit
data
hit
miss
Disk
Memory
OS Fault Handler
page fault/ protection violation
Page Table
data
virtual addr.
physical addr.
Note: If TLB is a hit, there can be a miss in cache, but no page fault in main memory

## Slide 27: Virtual Cache
Avoid virtual to physical translation by using virtual address directly in the cache
Problems with virtual caches:
Page Level Protection
Needs flushing (purging) or process-identifier tag (PID) to distinguish
OS may use two virtual addresses for the same physical address. Results in two copies of the same data in virtual cache => Aliasing problem
I/O problem – DMA controller uses physical address to transfer data – cache coherence with cache needs mapping

## Slide 28: Virtually Indexed Physically Mapped Cache
Use part of the page offset (same in both virtual and physical addresses) to index the cache
Simultaneously read the cache and the TLB
Match tag using the physical address
Drawback: Direct mapped cache no bigger than the page size. For bigger cache, set associative cache can be used with number of sets determined by the index bits.

## Slide 29
Figure 2.16 The virtual address, physical address, indexes, tags, and data blocks for the ARM Cortex-A8 data caches and data TLB. Since the instruction and data hierarchies are symmetric, we show only one. The TLB (instruction or data) is fully associative with 32 entries. The L1 cache is four-way set associative with 64-byte blocks and 32 KB capacity. The L2 cache is eight-way set associative with 64-byte blocks and 1 MB capacity. This figure doesn’t show the valid bits and protection bits for the caches and TLB, nor the use of the way prediction bits that would dictate the predicted bank of the L1 cache.
L1 cache is virtually indexed and physically tagged. Read TLB and L1 cache simultaneously and then compare
L2 cache is physically indexed and tagged
64-byte block => 6 bits block offset
Index bits = 32KB/4x64 = 7

## Slide 30
Figure 2.21 The Intel i7 memory hierarchy and the steps in both instruction and data access. We show only reads for data. Writes are similar, in that they begin with a read (since caches are write back). Misses are handled by simply placing the data in a write buffer, since the L1 cache is not write allocated.
The intel i7 uses 48-bit virtual address and 36-bit physical address.
First level caches are virtually indexed and physically tagged. L2 and L3 are physically indexed.

## Slide 31: Typical x86 PC I/O System
Disk access through slow south bridge – considered as I/O access under OS supervision – why?

## Slide 32: I/O Data Transfer
Polling and interrupt-driven I/O
  CPU transfers data between memory and I/O data registers
  Time consuming for high-speed devices
All I/O requests need protection and separation from other processes – handled by OS virtual memory
Also disk and NIC transfers are based on physical memory addresses – Only OS can provide that through virtual memory
Direct memory access (DMA)
  OS provides starting address in memory
  I/O controller transfers to/from memory autonomously
  Controller interrupts on completion or error

## Slide 33: DMA/Cache Interaction
If DMA writes to a memory block that is cached
  Cached copy becomes stale
If write-back cache has dirty block, and DMA reads memory block
  Reads stale data
Need to ensure cache coherence
  Flush blocks from cache if they will be used for DMA
  Or use non-cacheable memory locations for I/O