## Slide 1: Lecture 8: Appendix C Pipeline Design and Hazards
Instructor: L.N. Bhuyan
CS 203A Advanced Computer Architecture

## Slide 2: MIPS Instruction Layout
Load/Store Architecture

## Slide 3
FIGURE 4.1 An abstract view of the implementation of the MIPS subset showing the major functional units and the major connections between them. All instructions start by using the pro gram counter to supply the instruction address to the instruction memory. After the instruction is fetched, the register operands used by an instruction are specified by fields of that instruction. Once the register operands have been fetched, they can be operated on to compute a memory address (for a load or store), to compute an arithmetic result (for an integer arithmetic-logical instruction), or a compare (for a branch). If the instruction is an arithmetic-logical instruction, the result from the ALU must be written to a register. If the operation is a load or store, the ALU result is used as an address to either store a value from the registers or load a value from memory into the registers. The result from the ALU or memory is written back into the register fi le. Branches require the use of the ALU output to determine the next instruction address, which comes either from the ALU (where the PC and branch offset are summed) or from an adder that increments the current PC by 4. The thick lines interconnecting the functional units represent buses, which consist of multiple signals. The arrows are used to guide the reader in knowing how information flows. Since signal lines may cross, we explicitly show when crossing lines are connected by the presence of a dot where the lines cross. Copyright © 2009 Elsevier, Inc. All rights reserved.

## Slide 4: Classic 5-stage Execution of a RISC Procesor
5 canonical stage “RISC” load-store architecture
    Instruction fetch (IF):
      get instruction from memory/cache
    Instruction decode, Register read (ID):
      translate opcode into control signals and read regs
    Execute (EX):
      perform ALU operation, load/store address, branch outcomes
    Memory (MEM):
      access memory if load/store, everyone else idle
    Writeback/retire (WB):
      write results to register file
IF
ID
EX
MEM
WB
Inst
Next Instn

## Slide 5: Pipeline Execution
Overlap execution of instructions
  Start instruction on every cycle, e.g. the new instruction can be fetched while the previous one is decoded – pipeline. Each cycle performing a specific task; number of stages is called pipeline depth (5 here)
Pipelined
Non-pipelined
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
time

## Slide 6: Multi-Cycle Pipeline Diagram
A Sequence of MIPS instructions

## Slide 7: Introduce Buffers to separate stages
Shading: Rt half read, Lt half write

## Slide 8: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 9: MIPS Pipelined Control Review
  Group control lines by pipeline stage needed
  Extend pipeline registers with control bits
  Pipeline Progress – Instruction moves with all control signals, addresses, data items => different register lengths at different stages
C
o
n
t
r
o
l
E
X
Mem
W
B
W
B
W
B
I
F
/
I
D
I
D
/
E
X
E
X
/
M
E
M
M
E
M
/
W
B
I
n
s
t
r
u
c
t
i
o
n
Mem
RegDst ALUop ALUSrc
Branch
MemRead MemWrite
MemToReg RegWrite

## Slide 10: A pipeline with multi-cycle FP operations: Arithmetic Pipeline: Ex. MIPS R4000

## Slide 11: Pipeline Hazards
Hazards are caused by conflicts between instructions. Will lead to incorrect behavior if not fixed.
  Three types:
    Structural: two instructions use same h/w in the same cycle – resource conflicts (e.g. one memory port, unpipelined divider etc).
    Data: two instructions use same data storage (register/memory) – dependent instructions.
    Control: one instruction affects which instruction is next – PC modifying instruction, changes control flow of program.

## Slide 12: Single Memory is a Structural Hazard
M
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
M
Reg
M
Reg
ALU
M
Reg
M
Reg
ALU
M
Reg
M
Reg
ALU
Reg
M
Reg
ALU
M
Reg
M
Reg
Can’t read same memory twice in same clock cycle
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 13: Harvard Architecture: Dual Memory
IM
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
How about two separate memories IM for instruction and DM for data? Almost all commercial architectures provide L1 I-cache and D-cache (Ex. MIPS Datapath)
Called Harvard Architecture
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 14: Dealing with Structural Hazards
Stall
  + simple, low cost in h/w
  Decrease IPC
Replicate the resource
  + good for performance
  Increase h/w and area
  Used for cheap resources
Pipeline the resource
  + good for performance
  Complexity, e.g. RAM
  Useful for multi-cycle resources

## Slide 15: Speed Up Equation for Pipelining
CPIpipelined = Ideal CPI + Pipeline stall clock cycles per instn
Ideal CPI x Pipeline depth Clock Cycleunpipelined
Speedup = -------------------------- X --------
Ideal CPI + Pipeline stall CPI Clock Cyclepipelined
Pipeline depth Clock Cycleunpipelined
Speedup = ------------------------ X ---------------
1 + Pipeline stall CPI/Ideal CPI Clock Cyclepipelined

## Slide 16: Example: Dual-port vs. Single-port
Machine A: Dual ported memory
Machine B: Single ported memory, but has a 1.05 times faster clock rate
Ideal CPI = 1 for both
Loads are 40% of instructions executed
SpeedUpA = Pipeline Depth/(1 + 0) x (clockunpipe/clockpipe)
= Pipeline Depth
SpeedUpB = Pipeline Depth/(1 + 0.4) x (clockunpipe/(clockunpipe / 1.05)
= (Pipeline Depth/1.4) x 1.05 = 0.75 x Pipeline Depth
SpeedUpA / SpeedUpB = Pipeline Depth/(0.75 x Pipeline Depth) = 1.33
Machine A is 1.33 times faster
Dual port Memory is equivalent to Harvard Architecture

## Slide 17: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3
Register write in 5th cycle
Register read in 5th cycle. Usually done simultaneously.
Notation: Read register in 2nd half and write on first half of the cycle

## Slide 18: Reducing Data Hazards: Bypassing or Internal Forwarding
Data available at the end of EX stage, why wait until WB stage?
  Bypass (forward) data directly to input of EX
  + Reduces/avoids stalls in a big way
    Large fraction of input operands are bypassed
  Complex
  Important: does not relieve you from having to perform WB
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add R1, R2, R3 | f | d | x | m | w |  |  |  | 
sub R2, R4, R1 |  | f | d | x | m | w |  |  | 

## Slide 19: Forwarding Paths

## Slide 20: But what if dependent on a load?
Even with bypassing, not all data dependency stalls can be avoided
  Load to an ALU immediately after
  Can be eliminated with compiler scheduling
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw R1, 16(R3) | f | d | x | m | w |  |  |  | 
sub R2, R4, R1 |  | f | d | - | x | m | w |  | 
Stall inserted here

## Slide 21: Stall/Bubble in the Pipeline
Stall inserted here
Lw: Forwarding won’t help

## Slide 22: Minimizing Data Hazard Stalls by Forwarding

## Slide 23: Exercise C1
Use the following code segment:
Loop: LD R1, 0 (R2) ; load R1from address 0+R2
DADDI R1, R1, #1 ; R1 = R1 + 1
SD R1, 0 (R2) ; store R1 at address 0+R2
DADDI R2, R2, #4 ; R2 = R2 + 4
DSUB R4, R3, R2 ; R4 = R3 – R2
BNEZ R4, Loop ; branch to Loop if R4! = 0

## Slide 25
One stall because the branch output and target is known after decode

## Slide 26: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
Assume the memory address of B is stored in register $t0. E, F, and A memory locations are one word apart consecutively.
Assume Internal forwarding
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles