## Slide 1: Lecture 9 Pipeline Contd. (Appendix C)
Instructor: L.N. Bhuyan
CS 203A Advanced Computer Architecture

## Slide 2: Arithmetic Pipeline: Ex. MIPS R4000
MIPS R4000 pipeline
Arithmetic Pipeline: The multiplier and adder are pipelined, but divider is not => Must wait 21 cycles to initiate another divide execution
Instructions are issued in order, but they complete out-of-order because of different latencies for different instructions

## Slide 3
Out of Order Completion
Stall
EX

## Slide 4
Figure C.41 The eight-stage pipeline structure of the R4000 uses pipelined instruction and data caches. The pipe stages are labeled and their detailed function is described in the text. The vertical dashed lines represent the stage boundaries as well as the location of pipeline latches. The instruction is actually available at the end of IS, but the tag check is done in RF, while the registers are fetched. Thus, we show the instruction memory as operating through RF. The TC stage is needed for data memory access, since we cannot write the data into the register until we know whether the cache access was a hit or not.
Real R4000 Pipeline
IF: First half of instruction fetch – PC selection and initiation of Icache
IS: Second half of inst fetch, complete cache access
RF: Instruction decode and register fetch
EX: Execution - Effective address calculation, ALU operation, branch target computation and condition evaluation
DF: Data fetch, first half of data cache (Dcache) access
DS: Second half of data fetch, completion of data cache access
TC: Tag check to determine whether data access hit or miss
WB: Writebacks for loads and register operations
2 cycle Load delay

## Slide 5
Figure C.38 A load instruction followed by an immediate use results in a x1 stall. Normal forwarding paths can be used after two cycles, so the add and sub get the value by forwarding after the stall. The or instruction gets the value from the register file. Because the two instructions after the load could be independent and hence not stall, the bypass can be to instructions that are three or four cycles after the load.

## Slide 6: R4000 Performance
Base ideal CPI of 1:
  Load stalls (1 or 2 clock cycles)
  Branch stalls (2 cycles + unfilled slots)
  FP result stalls: RAW data hazard (wait for FP results)
  FP structural stalls: Not enough FP hardware (parallelism)
Notes: Integer programs, major delay is branch stalls
FP its structural stalls

## Slide 7: Data Hazards in Out-Of-Order Machines
Instructions executed out of order can give rise to further data hazards. They are unavoidable when instruction level parallelism is used – like in MIPS 4000 with multiple pipelined arithmetic units.
Two different instructions using the same storage location may finish at different times because they may use different pipelines as in MIPS 4000
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
add R1, R2, R3
sub R2, R4, R1
or R1, R6, R3
read-after-write
(RAW)
write-after-read
(WAR)
write-after-write
(WAW)
True dependence
(real)
anti dependence
(artificial)
output dependence
(artificial)

## Slide 8: WAR: Why do they exist? (Antidependence)
Recall WAR
  add R1, R2, R3
  sub R2, R4, R1
  or R1, R6, R3
Problem: swap means introducing false RAW hazards if sub finishes earlier than add
Can’t happen in in-order pipeline since reads happen in ID but writes happen in WB
Can happen in out-of-order reads, e.g. out-of-order execution
Artificial: can be removed if sub used a different destination register => Register Renaming

## Slide 9: WAW (Output Depndence)
    add R1, R2, R3
    sub R2, R4, R1
    or R1, R6, R3
Problem: Would leave wrong value in R1 for the sub if it finishes earlier than add
Can’t happen in in-order pipeline in which every instruction takes same cycles since writes are in-order
Can happen in the presence of multi-pipeline operations, i.e., out-of-order writes
Artificial: using different destination register would solve => Register Renaming

## Slide 10
I1. Load R1, A /R1 Memory(A)/
I2. Add R2, R1 /R2  (R2)+(R1)/
I3. Add R3, R4 /R3  (R3)+(R4)/
I4. Mul R4, R5 /R4  (R4)*(R5)/
I5. Comp R6 /R6  Not(R6)/
I6. Mul R6, R7 /R6  (R6)*(R7)/
Due to Superscalar (multi-pipeline) Processing, it is possible that I4
completes before I3 starts. Similarly the value of R6 depends on the
beginning and end of I5 and I6. Unpredictable result!
I1
I3
I5
I6
I4
I2
RAW
WAR
WAW and
RAW
Flow
dependence
Anti-
dependence
Flow, Anti
and Output
dependence,
Program order
Dependence Graph Example

## Slide 11: Register Renaming
Rewrite the previous program as:
I1. R1b  Memory (A)
I2. R2b  (R2a) + (R1b)
I3. R3b  (R3a) + (R4a)
I4. R4b  (R4a) * (R5a)
I5. R6b  -(R6a)
I6. R6c  (R6b) * (R7a)
Allocate more registers and rename the registers that really do not have flow dependency. The WAR hazard between I3 and I4, and WAW hazard between I5 and I6 have been removed.
These two hazards also called Name dependencies

## Slide 12
Appendix C – Question C.1
Solution C.1 a.
R1: LD -> DADDI - RAW
R1: DADDI -> SD - RAW
R1: LD -> DADDI - WAW
R2: LD -> DADDI - WAR
R1: LD -> SD - WAW
R2: SD -> DADDI - WAR
R2: DADDI -> DSUB - RAW
R4: DSUB -> BNEZ - RAW
What if it is a simple 5-stage linear pipeline?

## Slide 13: Control Hazards
Branch problem:
  branches are resolved in EX stage (Needs adder)
   2 cycles penalty on taken branches
  Ideal CPI =1. Assuming 2 cycles for all branches and 32% branch instructions  new CPI = 1 + 0.32*2 = 1.64
Solutions:
  Reduce branch penalty: change the datapath – new adder needed in ID stage. Branch delay reduced to one cycle.
  Fill branch delay slot(s) with a useful instruction.
  Fixed branch prediction.
  Static branch prediction.
  Dynamic branch prediction.

## Slide 14
Figure C.25 To minimize the impact of deciding whether a conditional branch is taken, we compute the branch target address in ID while doing the conditional test and final selection of next PC in EX. As mentioned in Figure C.19, the PC can be thought of as a pipeline register (e.g., as part of ID/IF), which is written with the address of the next instruction at the end of each IF cycle.

## Slide 15: Reducing Branch Delay
Move hardware to determine outcome to ID stage – Only one cycle penalty. Additional hardware:
  Target address adder
  Register comparator
Example: Assume branch taken
  36: sub $10, $4, $8 40: beq $1, $3, 7 -> Offset 7–Jump to 44+7x4 = 72 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)

## Slide 16
Assume the initial value of R3 is R2+396

## Slide 17
There is a stall in BNEZ because there is a data dependence with DSUB. Moving the comparator and adder to decode stage doesn’t help. The condition is resolved only after EX stage even with forwarding.

## Slide 18: Control Hazards – branch delay slots
Branch delay slot filling:
  move an instruction into the slot right after the branch, hoping that its execution is necessary.
  Limitations: restrictions on which instructions can be rescheduled, compile time prediction of taken or untaken branches.

## Slide 19: Example Nondelayed vs. Delayed Branch
add M1 ,M2,M3
sub M4, M5,M6
beq M1, M4, Exit
or M8, M9 ,M10
xor M10, M1,M11
Nondelayed Branch
Exit:
add M1 ,M2,M3
sub M4, M5,M6
beq M1, M4, Exit
or M8, M9 ,M10
xor M10, M1,M11
Delayed Branch
Exit:

## Slide 20
Figure C.14 Scheduling the branch delay slot. The top box in each pair shows the code before scheduling; the bottom box shows the scheduled code. In (a), the delay slot is scheduled with an independent instruction from before the branch. This is the best choice. Strategies (b) and (c) are used when (a) is not possible. In the code sequences for (b) and (c), the use of R1 in the branch condition prevents the DADD instruction (whose destination is R1) from being moved after the branch. In (b), the branch delay slot is scheduled from the target of the branch; usually the target instruction will need to be copied because it can be reached by another path. Strategy (b) is preferred when the branch is taken with high probability, such as a loop branch. Finally, the branch may be scheduled from the not-taken fall-through as in (c). To make this optimization legal for (b) or (c), it must be OK to execute the moved instruction when the branch goes in the unexpected direction. By OK we mean that the work is wasted, but the program will still execute correctly. This is the case, for example, in (c) if R7 were an unused temporary register when the branch goes in the unexpected direction.

## Slide 21: Control Hazards: Branch Prediction
Idea: doing something is better than waiting around doing nothing
  Guess branch target, start executing at guessed position
  Execute branch, verify (check) your guess
  + minimize penalty if guess is right (to zero)
  May increase penalty for wrong guesses
  Heavily researched area in the last 15 years
Fixed branch prediction.
  Each of these strategies must be applied to all branch instructions indiscriminately.
  Predict not-taken (47% actually not taken):
    continue to fetch instruction without stalling;
    do not change any state (no register write);
    if branch is taken turn the fetched instruction into no-op, restart fetch at target address: 1 cycle penalty. Assumes branch detection at the ID stage.
  Predict taken (53%):
  more difficult, must know target before branch is decoded. no advantage in our simple 5-stage pipeline even if we move the branch to ID stage. There is 1 cycle penalty any way.

## Slide 22: MIPS with Predict Not Taken
Prediction correct
Prediction incorrect - Assuming one cycle penalty

## Slide 24
Figure C.14 Misprediction rate on SPEC92 for a profile-based predictor varies widely but is generally better for the floating-point programs, which have an average misprediction rate of 9% with a standard deviation of 4%, than for the integer programs, which have an average misprediction rate of 15% with a standard deviation of 5%. The actual performance depends on both the prediction accuracy and the branch frequency, which vary from 3% to 24%.
Static Branch Prediction