## Slide 1: FlowSense: Monitoring Network Utilization with Zero Measurement Cost
Curtis Yu1, Cristian Lumezanu2, Yueping Zhang2, Vishal Singh2, Guofei Jiang2, Harsha V. Madhyastha1
1UC Riverside, 2NEC Labs America

## Slide 2: SDN enables centralized control
A centralized controller can set its own routes on an SDN

## Slide 3: SDN enables reactive control of network
A
B
Path: A  B
We can reroute around heavily congested links
Need to know when link is congested
C
Path: A  C  B

## Slide 4: State-of-the-art measurement
Active measurements
  Injection of probes
Passive measurements
  Expensive instrumentation and infrastructure setup
SDN measurements
  Additional control traffic
Accurate measurements requires high overhead

## Slide 5: FlowSense: measuring with zero cost
Leverage existing control traffic to measure network
  No additional traffic introduced
  Network informs system of changes
As accurate as switch polling

## Slide 6: OpenFlow overview
Flow Arrival:
Packet of new flow arrives
PacketIn message sent
FlowMod message sent
New rule installed
Flow Completion:
Rule expires
Remove rule
FlowRemoved message sent
Rule | Match | Output
1 | Green | sw2
Rule | Match | Output
sw1
sw2

## Slide 7: Messages have utilization info
PacketIn
  Signals new flow on port (t1)
FlowRemoved
  Duration of entry in flow table (10s)
  Amount of traffic matched (400 MB)
Can infer utilization contributed by flow on link
t1
t1 + 10s
40 MB/s
Flow:
PacketIn
FlowRemoved

## Slide 8: Estimating utilization in FlowSense
t1
40 MB/s
10 MB/s
20 MB/s
t2
t3
t4
t5
t6
Time
f1
f2
f3
Checkpoint | Flows Left | Total Utilization
Checkpoint | Flows Left | Total Utilization
t4 | 2 | 40 MB/s
Checkpoint | Flows Left | Total Utilization
t4 | 1 | 50 MB/s
t5 | 1 | 10 MB/s
Checkpoint | Flows Left | Total Utilization
t4 | 0 | 70 MB/s
t5 | 0 | 30 MB/s
t6 | 0 | 20 MB/s

## Slide 9: FlowSense system design
Parser
  Captures and analyzes control traffic
Utilization Monitor
  Runs FlowSense algorithm
Utilization Table
  Database of checkpoints

## Slide 10: Evaluating FlowSense
Goals
  Accuracy
  Timeliness
Dataset
  Testbed of NEC OpenFlow switches
  Real-world traffic trace from a campus network switch

## Slide 11: Accuracy testbed
10 MB/s
20 MB/s
30 MB/s
45 MB/s
  1 continuous flow
  3 separate short flows

## Slide 12: FlowSense is as accurate as polling
Utilization values are very similar
FlowSense cannot replicate instantaneous utilization values

## Slide 13: Revisiting utilization estimation
t1
f1
40 MB/s
10 MB/s
f2
20 MB/s
f3
t2
t3
t4
t5
t6
Time
Checkpoint | Flows Left | Total Utilization
t4 | 2 | 40 MB/s
Checkpoint | Flows Left | Total Utilization
t4 | 0 | 70 MB/s
t5 | 0 | 30 MB/s
t6 | 0 | 20 MB/s
Delay from t4 to t6 in getting total utilization

## Slide 14: Perfect utilization information is typically delayed
In median case, total utilization known after ~100 seconds

## Slide 15: Coarse-grained estimation can be obtained soon
Only 30% of checkpoints get 90% utilization
Over 60% of checkpoints get 90% utilization

## Slide 16: Data refreshes in the order of seconds
Data refreshes around every 3 seconds

## Slide 17: Conclusion
FlowSense
  Leverage control traffic to estimate utilization
  Incurs no measurement cost
Estimates are accurate
  Comparable to switch polling
Data is timely
  Do not have to wait too long for new utilization information

## Slide 18: Future work
Measuring long flows
  Overhead of stopping the rule for measurement
Wildcard and proactive rules
  Reasonable way to merge active measurements to keep overhead low
Link Latency
  Similar method to enable zero cost measurement of latency

## Slide 19: Questions?