## Slide 1: Boosting XML filtering through a scalable FPGA-based architecture
A. Mitra, M. Vieira, P. Bakalov, V. Tsotras, W. Najjar

## Slide 2: XML Pub-Sub
XML Document is published on a server
e.g. News, Archived papers, etc.
Thousands of Content subscribers access the published document
Each subscriber query constitutes an XPATH expression
We implement XPATH expressions as regular expressions on FPGA

## Slide 3: XML Pub Sub
XML Publisher’s Document Stream
Sub 1
Sub 2
Sub 3
Sub n
Query 1
Query 2
Query 3
Query n
XML
Data
To Individual Subscribers through
Internet

## Slide 4: Two important XPATH expressions // and /
<g>
<a>
<b>
<c>
<d>
<f>
<e>
The '//' operator selects all descendants matching a Tag.
The '/' operator selects all children matching a Tag.
<b> is a child of <a> thus a//b and a/b both will return true
<g> is a descendant of <a>, thus a/g will return FALSE,
while a//g will return true

## Slide 5: Pub-Sub Implementation on FPGA
XPATH
Queries
XPATH to
PCRE
Regex
Common Prefix Optimization
TAG
Replace-ment
REGEX
To VHDL
Compiler
Synthesis,
Place and Route
Area Analysis
Congregation
With SGI-RASC Core Services
FPGA Bitstream 1
FPGA Bitstream 2
FPGA Bitstream n
FPGA Tool Flow Section

## Slide 6: Pub Sub on FPGA
XPATH expressions are converted to Regular expression hardware using our PCRE based compiler
The tag names are replaced with 32-bit hardware alias tags in the XPATH and also in published XML document
  for e.g. <index> is replaced with <a0>, <book_chapter> with <a1>, etc.
Expression with // (Ancestor Descendant) operator can be directly implemented as a regex
Expressions with / (Parent Child) operator are subsequently modified to use a hardware tag-Stack to verify parent-child relationship.
All the XPATH expressions are common prefix optimized

## Slide 7: Internal block diagram of XPATH a0//b0
XPATH Expression: a0//b0
The above block diagram implements a regular expression in hardware
The regex <a0> [\w\s]+ [<\c\d>|</\c\d>]* <b0> would match the XPATH
a0//b0.
\w is a short form for any character or number, \s is for blank space, \d is for number, \c is for any lowercase character
The last block </a0> is added as an additional check to verify <b0> was matched before <a0> closed.
<a0>
Streaming XML Character Input
<b0>
&
!</a0>
match
en
<b0>
match
en
</a0>
match
en

## Slide 8: Internal block diagram of XPATH a0/b0
XPATH Expression: a0/b0
Streaming XML Character Input
<b0>
&
!</a0>
&
TOS=<a0>
Tag filter
TOS
<TAG>
pop
push
TAG STACK on (BRAM)
Tag Input
TOS
<a0>
match
en
<a0>
match
en
<b0>
match
en
</a0>
match
en

## Slide 9: Prüfer Sequence Generator and Matching Hardware
Tag filter
<TAG>
TOS
TOS - 1
push
pop
Node0 Node1
push
A
B
<
>
/
0
1
…
…
…
a
b
…
push
A
B
<
>
/
0
1
…
…
…
a
b
…
b
0
a
0
c
0
a
Character Decoder
Character Decoder
b
0
c
a
en
en
match
Streaming XML Character Input
Twig Pattern: a0[b0]/c0
Leaf
(push then pop)
en
match
match
match
a
0
en
Q
Subsequence Match
Output

## Slide 10: Overall organization
8
BRAM
Stack
XPATHs without STACK
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XPATH
XML Document Stream
XML Query Data / Output
XPATHs with STACK
Output Priority Encoder 1
Output Priority Encoder 0
Character Pre - Decoder
2
4
Notes: B

## Slide 11: Prüfer Sequence Generator and Matching Hardware
Tag filter
<TAG>
TOS
TOS - 1
push
pop
TOS 0 TOS 1
TOS-1 0 TOS-1 1
push
A
B
<
>
/
0
1
…
…
…
a
b
…
push
A
B
<
>
/
0
1
…
…
…
a
b
…
b
0
a
0
c
0
a
0
push
A
B
<
>
/
0
1
…
…
…
a
b
…
push
A
B
<
>
/
0
1
…
…
…
a
b
…
Character Decoder
Character Decoder
Character Decoder
Character Decoder
b
0
c
a
0
en
en
match
match
Streaming XML Character Input
Twig Pattern: a0[b0]/c0
Leaf
(push then pop)

## Slide 12: 1-bit x 4 Character Pre-Decoder Match Block
8-bit ASCII Stream
A
B
<
>
/
0
1
…
…
…
a
b
…
<
a
0
>
One of the 256 1-bit output is active each clock cycle.
Hardware for tag <a0>
1
1
1
1
8
Character Decoder

## Slide 13: 8bit x 4 Character Match Block
8
<
a
0
>
8-bit ASCII Stream

## Slide 14: XPATH a0/b0
The block diagram implements a regular expression with added stack control in hardware
The modified regex
  <a0> [\w\s]+ [<\c\d>|</\c\d>]*[Stack1] <b0> would match the XPATH a0/b0.
The added modifier Stack1 would direct the compiler to introduce a match block that would match the Top of stack (TOS) to <a0> when, tag <b0> is encountered in the document.
The tag filter runs in parallel to the regexes and pushes a open tag onto the TOS, and if it encountered a close tag it would pop out the TOS

## Slide 15: XPATH Expressions on FPGA
We compile multiple XPATH expressions to Regular expressions and the [Stack] label is added to the XPATHs with / operator
We utilize common prefix optimization on the regexes
Thereafter the regexes are converted to VHDL
We have two sets of priority encoder, one for the XPATH expressions which require stack and the other for the rest of XPATH expressions.

## Slide 16: HW Performance (XPATHs with 2 Tags)
Chart: 
| 16 | 32 | 64 | 128 | 256 | 512
SLICES (common prefix) | 315 | 742 | 1353 | 2764 | 6388 | 13170
SLICES Unoptimized | 560 | 1120 | 2193 | 4338 | 8626 | 17220
Chart: 
| 16 | 32 | 64 | 128 | 256 | 512
MHz (Common Prefix) | 235.8491 | 220.7018 | 147.6669 | 137.4759 | 147.5361 | 138.7925
MHz (Unoptimized) | 227.2727 | 217.3913 | 210.9705 | 190.5488 | 183.9926 | 173.0104

## Slide 17: HW Performance (XPATHs with 4 Tags)
Chart: 
| 16 | 32 | 64 | 128 | 256 | 512
MHz (Common Prefix) | 240.3846 | 168.5488 | 152.9052 | 126.5823 | 131.5789 | 101.0101
MHz (Unoptimized) | 200 | 171.8213 | 174.8252 | 158.4786 | 148.8095 | 121.9512
Chart: 
| 16 | 32 | 64 | 128 | 256 | 512
SLICES (common prefix) | 679 | 1230 | 2406 | 5700 | 11642 | 22180
SLICES Unoptimized | 920 | 1934 | 4023 | 8083 | 19092 | 33713

## Slide 18: HW Performance (XPATHs with 6 Tags)
Chart: 
| 16 | 32 | 64 | 128 | 256 | 512
SLICES (common prefix) | 1029 | 1941 | 4354 | 8700 | 18688 | 31563
SLICES Unoptimized | 1653 | 3286 | 6388 | 10415 | 26160 | 51605
Chart: 
| 16 | 32 | 64 | 128 | 256 | 512
MHz (Common Prefix) | 222.2222 | 123.7624 | 164.4737 | 120.4819 | 108.6957 | 68.4932
MHz (Unoptimized) | 208.3333 | 208.3333 | 158.7302 | 108.6957 | 148.1481 | 126.5823

## Slide 19: SW Performance
Using Yfilter Common Prefix Optimized NFA approach
  The XPATH expressions consists of queries generated with Toxgene
  Queries are a equal mix of 2, 4, and 6 Tags
  Throughput for Parsing XML data using Yfilter from 512 XPATH expressions on a Pentium-4 Machine is = 2.4MBytes / sec
  Tested SW Throughput is nearly constant for input data size ranging from 1 MB up until 1 GB.

## Slide 20: Comparison of Performance
Common Prefix Optimized HW
  2 Tags 512 XPATH Expressions = 139 MBytes/s
  4 Tags 512 XPATH Expressions = 101 MBytes/s
  6 Tags 512 XPATH Expressions = 68 MBytes/s
Common Prefix Optimized SW Yfilter
  Yfilter 512 XPATH Expressions = 2.4 MBytes/s

## Slide 21: Performance
Performance Gain using a single FPGA (critical path)
  (68MBytes/s) / (2.4 MBytes/s) = 28.3X
Performance Gain using SGI RASC Blade (66MHz)
  (66MBytes/s) / (2.4MBytes/s) = 27.5X

## Slide 22: Linear Prüfer Sequence Generator