## Slide 1: A Network Model for the Utility Domain
Petko Bakalov, Erik Hoel, Sangho Kim

## Slide 2: The context
Utility companies (water, gas, electric ,fiber, telco) have dramatically increased the autonomous capabilities of their networks
  Switching operations (reconfiguration of the network topology) are performed by autonomous devices (e.g., SCADA) in order to optimize performance and efficiency
Distributed generation (e.g., solar power) and storage (batteries, electric cars) introduce additional complexities impacting the flow of and modeling of resources in the network
Optimization of these complex dynamic systems requires a much higher fidelity of modeling than in the past; e.g.,
  Transformer banks, substations, underground
  Order of magnitude larger than previously – e.g., 100M+ features

## Slide 3: Example: transformer bank
Transformer units
Arrestors
Fuses
Three phases
  A, B, C
Transformer unit
Arrestor
Fuse
Phase A
Phase B
Phase C

## Slide 4: Transformers wye-wye configuration
4
F
F
F
ABCN
ABCN
abcn
abcn
A
B
C
a
b
c
T
X1
X3
X2
T
X1
X3
X2
T
X1
X3
X2
n
N
H1
H2
H1
H2
H1
H2
A
B
C
a
b
c
n
A
A
A
A
B
C
F
Fuse
A
Arrestor
T
Transformer

## Slide 5: The problem
The problem: current network models have limitations and constraints that limit their ability to effectively and accurately model the rapidly increasing complexity and sophistication of the utility networks
The goal: Introduces a new utility-centric graph information model that can support the complex modeling of utility infrastructures

## Slide 6: The problem
Junction valence
Transportation networks
Low junction valence
High depth first search analysis
~10M features
Social networks
High junction valence
Shallow depth, wide breadth first search analysis
~1B features
Utility networks
Medium junction valence
Mixture of BFS and DFS analysis
~100M features
Continually edited and autonomously reconfigured

## Slide 7: Outline
Overview of the utility network model
Network index
  Logical structure
  Physical storage
Network index maintenance
  Establishing connectivity
  Maintaining connectivity
Experimental results

## Slide 8: Network model definition
A mechanism for defining and managing connectivity information between features in a geodatabase
A feature is graphic representation of a real-world object
  Lines (e.g., pipes, power lines, telephone cables)
  Points (e.g., valves, transforms, switchgear)

## Slide 9
Network Index (Graph)
Feature Sources
Metadata
Connectivity
Model
Attribute
Model
Point Features
Line Features
Table Sources
Associations
Containment
Attributes
Edge
Junction
Containment
Attributes
Edge
Junction

## Slide 10: Network index elements
The connectivity information is explicitly represented with network elements that are found in an associated network index (graph)
Three types of network
elements in the index:
  Junctions
  Edges
  Containment
Edge
Junctions
Containment

## Slide 11: Network index attributes
Network attributes are properties of the network elements that control traversability
  Cost. Certain attributes are used to measure and model impedances, such as voltage drop
  Descriptors. Those are attributes that describe characteristics of the network or its elements – such as open/closed switch

## Slide 12: Network model maintaining the index
Build – the process of discovering geographic coincidence between features that are persisted as junction and edges in the network index
As edits are made to the features, the network index becomes stale
We keep track of the modified features
  Employ the dirty area concept (an envelope encompassing the edited feature)
  When a feature is modified, a dirty area is created
The build process incrementally maintains the network index based upon the present dirty areas

## Slide 13: Outline
Overview of the utility network model
Network index
  Logical structure
  Physical storage
Network index maintenance
  Establishing connectivity
  Maintaining connectivity
Experimental results

## Slide 14: Network index logical structure
Connectivity between the features in the model using foreign keys
Those are referred as EIDs
  Junction EIDs
  Edge EIDs
  Containment EDs
Very compact representation
Network Index

## Slide 15: Network index logical structure
Typically stored in RDBMS
The information in the network topology is stored in a set of binary and relational tables
Feature Source
Feature Source
Network
Attribute
Tables
Metadata
Tables
Network index
Feature Source
Element Mapping Table
Reverse Mapping Tables
Containment& Structural attachment
Tables
Connectivity
Tables

## Slide 16: Logical network model element mapping
The Element mapping tables contains the mapping information between feature space and network elements.
Foreword element mapping – done using regular database table.
Reverse element mapping – done using binary table

## Slide 17: Logical network model connectivity table
The schema structure is designed to answer the most common adjacency query during analysis
“find the edges and junctions connected to a given junction”
For each junction, we store adjacent edge IDs, and also the IDs of the junctions at the other end of the edges
  This includes the from and to edges

## Slide 18: Physical storage model fixed length binary records
A BLOB table is essentially a contiguous binary stream of records, in which the physical storage is divided into multiple BLOB pages
Each record in the fixed size BLOB has a fixed size so the page number and the offset of the record in respect to the beginning of the page can be directly calculated

## Slide 19: Physical storage model variable length binary records
The connectivity and relationship information have variable length by nature
We fix the number of records per page - 4K
We need a fixed length index structure (or header) at the beginning of each BLOB page to store the record offsets

## Slide 20: Outline
Overview of the utility network model
Network index
  Logical structure
  Physical storage
Network index maintenance
  Establishing connectivity
  Maintaining connectivity
Experimental results

## Slide 21: Build algorithm
Initial build of the network index
  Simply a special case of a rebuild over a dirty region that encompasses the entire network
  Network index is empty prior to the initial build
Incremental (re)builds
  Rebuilt region corresponds to the dirty regions
  When we rebuild the dirty regions, the resulting network index is completely correct

## Slide 22: Build algorithm step 1: data extraction
Extract the geometry of all features in the network model.
Decompose line geometry into its constituent vertices
Store the points and vertices in a single table with X,Y attributes.

## Slide 23: Build algorithm step 2: connectivity analysis
Sort the vertex information in the table by coordinate values so that the coincident vertexes are grouped together
Analyze each group of coincident vertexes according to the connectivity model

## Slide 24: Build algorithm Step 3: junction creation
Create junction elements and populate vertex information table from the extracted connectivity nodes
For each connectivity node
Create a junction element
If there is a point feature in node
Associate the junction with the point
For each line vertex
Tag the record with the junction element

## Slide 25: Build algorithm step 4: edge creation
Create edge elements from vertex information table
Sort the vertex information table using FID
For each adjacent pair of records
If the pair involves the same line feature
Create an edge between them

## Slide 26: Outline
Overview of the utility network model
Network index
  Logical structure
  Physical storage
Network index maintenance
  Establishing connectivity
  Maintaining connectivity
Experimental results

## Slide 27: Experimental results build algorithm profiling
Expensive steps are reading and writing to the RDBMS
Sorting takes only 3% of the total time
Chart: 
| Data Extraction | Connectivity analysis | Edge creation | Junction Creation | Edge Sort | Junction Sort
Time (sec) | 279.264 | 364.193 | 306.62 | 959.543 | 15 | 35

## Slide 28: Experimental results page size sensitivity
The increase of the page size improves the performance of the analytical operation
However BLOBs take more time to be transmitted over the network
Optimal size page - 64 KB
Chart: 
Chart: 
| 512 rec | 1024 rec | 2048 rec | 4096 rec | 8192 rec | 8 KB | 16 KB | 32 KB | 64 KB | 128 KB
64 MB | 64.38 | 61.45 | 57.6 | 58.81 | 61.21
128 MB | 64.38 | 61.45 | 59.09 | 57.83 | 63.33
256 MB | 61.22 | 60.89 | 58.91 | 57.27 | 65
512 MB | 62.32 | 60.51 | 59.99 | 57.39 | 65.67

## Slide 29: Experimental results cache size sensitivity
Because we performed spatial clustering the trace was able to stay focused only on the most recently picked pages
The LRU cache replacement policy was performing extremely well.
Chart: 
Chart: 
| 64 MB | 128 MB | 256 MB | 512 MB
8 KB 512 rec | 64.38 | 64.38 | 61.22 | 62.32
16 KB 1024 rec | 61.45 | 61.45 | 60.89 | 60.51
32 KB 2048 rec | 57.6 | 59.09 | 58.91 | 59.99
64 KB 4096 rec | 58.81 | 57.83 | 57.27 | 57.39
128 KB 8192 rec | 61.21 | 63.33 | 65 | 65.67

## Slide 30
(we’re hiring)