## Slide 1: Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection
Farzad Khorasani, Rajiv Gupta, Laxmi N. Bhuyan
UC Riverside
The 48th Annual IEEE/ACM International Symposium on Microarchitecture (MICRO), 2015

## Slide 2: Thread Divergence: Problem Overview
One PC for the SIMD group (warp):
  Reduces the die size and the power consumption.
  Warp lanes must run in lockstep.
When facing intra-warp divergence:
  Mask-off inactive threads.
  Hold the re-convergence PC in a stack.
  Some execution units are reserved but not utilized until re-convergence.
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
1
Benchmark | BFS | DQG | EMIES | FF | HASH | IEFA | RT | SSSP
Warp Exec. Eff. (%) | 58 | 37 | 44 | 13 | 25 | 41 | 67 | 64

## Slide 3: Thread Divergence in Repetitive Tasks: Example
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
2
1 __global__ void CUDA_kernel_BFS(
2 const int numV, const int curr, int* levels,
3 const int* v, const int* e, bool* done ) {
4 for(
5 int vIdx = threadIdx.x + blockIdx.x * blockDim.x;
6 vIdx < numV;
7 vIdx += gridDim.x * blockDim.x ) {
8 bool p = levels[ vIdx ] == curr; // Block A.
9 if( p )
10 process_nbrs( vIdx,
11 curr, levels, v, e, done ); // Block B.
12 } }
Notes: Each thread processes some vertices.
If a vertex has been updated in the previous CUDA kernel invocation, thread has to update the vertex’s neighbors. This condition might evaluate true for some warp lanes and false for others. Threads that need not execute divergent branch must wait for other threads inside the warp to finish processing block B.

## Slide 4: Thread Divergence: Visualization
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
3
A0
A1
Lane 0
Lane 1
Lane 2
Lane 3
Lane 4
Lane 5
Lane 6
Lane 7
A2
A3
A4
A5
A6
A7
B0
B3
B6
A8
A9
A10
A11
A12
A13
A14
A15
B8
B9
B11
B12
B13
B15
A16
A17
A18
A19
A20
A21
A22
A23
B18
B20
A24
A25
A26
A27
A28
A29
A30
A31
B26
B27
B16
B22
B31
Time

## Slide 5: Collaborative Context Collection: Main Idea
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
4
Keep collecting divergent tasks until there are enough tasks to keep all warp lanes busy.
If the aggregation of collected divergent tasks and new divergent tasks equals to or exceeds the warp size, execute.
Notes: Next slide is the visualization of what I talked about.

## Slide 6: Collaborative Context Collection: Visualization
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
5
A0
A1
Lane 0
Lane 1
Lane 2
Lane 3
Lane 4
Lane 5
Lane 6
Lane 7
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
A15
B8
B9
B6
B11
B12
B13
B3
B15
A16
A17
A18
A19
A20
A21
A22
A23
A24
A25
A26
A27
A28
A29
A30
A31
B22
B20
B26
B27
B18
B16
B0
B31
AC0
AC3
AC6
Context stack
AC0
AC0
AC0
AC16
AC18
AC20
AC22
Time

## Slide 7: Collaborative Context Collection: Principles
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
6
Execution discipline: all-or-none.
Context: minimum set of variables (thread’s registers) describing the divergent task.
Context stack: a warp specific shared memory region to collect insufficient divergent task contexts.
Required assumption: repetitive divergent tasks with independent iterations.

## Slide 8: Collaborative Context Collection: Applying to CUDA Kernels (1/2)
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
7
1 __global__ void CUDA_kernel_BFS_CCC(
2 const int numV, const int curr, int* levels,
3 const int* v, const int* e, bool* done ) {
4 volatile __shared__ int cxtStack[ CTA_WIDTH ];
5 int stackTop = 0;
6 int wOffset = threadIdx.x & ( ~31 );
7 int lanemask_le = getLaneMaskLE_PTXWrapper();
8 for(
9 int vIdx = threadIdx.x + blockIdx.x * blockDim.x;
10 vIdx < numV;
11 vIdx += gridDim.x * blockDim.x ) {
12 bool p = levels[ vIdx ] == curr; // Block A.
13 int jIdx = vIdx;
14 int pthBlt = __ballot( !p );
15 int reducedNTaken = __popc( pthBlt );
. . .

## Slide 9: Collaborative Context Collection: Applying to CUDA Kernels (2/2)
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
8
. . .
16 if( stackTop >= redNTaken ) { // All take path.
17 int wScan = __popc( pthBlt & lanemask_le );
18 int pos = wOffset + stackTop – wScan;
19 if( !p ) jIdx = cxtStack[ pos ]; // Pop.
20 stackTop -= reducedNTaken;
21 process_nbrs( jIdx,
22 curr, levels, v, e, done ); // Block B.
23 } else { // None take path.
24 int wScan = __popc( ~pthBlt & lanemask_le );
25 int pos = wOffset + stackTop + wScan – 1;
26 if( p ) cxtStack[ pos ] = jIdx; // Push.
27 stackTop += warpSize – reducedNTaken; } } }
Notes: Key methods enabling CCC:
  Intra-warp binary reduction so as to count the total number of warp lanes with the false pred.
  Intra-warp binary prefix sum to realize the stack position to/from which the threads stores/restores the context.
A thread’s task context is:
  Defined prior to divergent path as a function of thread-specific special registers.
  Used inside the divergent task path.
Optimizing parallel prefix operations for the Fermi architecture. <- PAPER
Defining task context allows us to methodically define minimum set of registers that fully describe the task. This allowed us to introduce CCC as a compiler optimization.

## Slide 10: Collaborative Context Collection: Transformations
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
9
Grid-Stride Loops
  Enable task repetition over a divergent GPU kernel.
Loops with variable Trip-Count
  Reduce the largest trip-count with an intra-warp butterfly shuffle reduction.
  Select the resulting value as the uniform trip-count.
  Wrap the code inside the loop by a condition check.
Recursive Device Functions & Loops with Unknown Trip-Count
Nested and Multi-path Context Collection
  A separate and independent context stack for each divergent path.

## Slide 11: Collaborative Context Collection: Optimizations
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
10
Context Compression.
  If a context’s register can be computed from another context register simply, stack only one.
  Calculate the other one during the retrieval.
Memory Divergence Avoidance.
  Take the coalesced memory access out of the divergent path to keep it aligned.
Prioritizing the Costliest Branches.
  To avoid restricting occupancy, apply CCC only to the most expensive branches: longest branches with the least probability of traversal.

## Slide 12: Collaborative Context Collection: Automation
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
11
CCC Framework
CUDA C++ kernel with pragma-like annotations
Annotated Source Modifier
PTX Source-to-source Compiler
CUDA C++ kernel with marked regions
NVCC
CICC
PTXAS
Original PTX for kernel with marks
PTX for kernel with CCC applied
GPU Assembly with CCC applied
CUDA C++ Front-end

## Slide 13: Collaborative Context Collection: Performance Improvement
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
12
Chart: Speedup
| BFS | DQG | EMIES | FF | HASH | IEFA | RT | SSSP
Speedup | 1.13 | 1.63 | 1.34 | 3.08 | 1.2 | 2.72 | 1.38 | 1.09
Chart: Warp Exec. Eff. (%)
| BFS | DQG | EMIES | FF | HASH | IEFA | RT | SSSP
Without CCC | 64.19 | 37 | 44 | 13 | 25 | 41 | 67 | 58.72
With CCC | 97.6 | 93 | 92 | 53 | 92 | 97 | 96 | 98.4
Notes: We applied one or more transformation or optimization to each of these benchmarks. Detailed list is in the paper.
FF has the highest speedup due to being compute-intensive and branch prioritization optimization.
IEFA contains 3 long compute-only divergent paths that CCC can be applied to.
EMIES is the only benchmark that application of CCC by-default limits the occupancy of the kernel. In this case, we enforced register spillage.
HASH, BFS, and SSSP are primarily memory-bound hence application of CCC, although greatly increases the warp execution efficiency, results in smaller speedups.

## Slide 14: Collaborative Context Collection: Sensitivity on # of Diverging Warp Lanes
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
13
Chart: Divergent warp lanes
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Original | 6.5439 | 709.3545 | 673.3976 | 673.403 | 673.3997 | 673.4007 | 673.4016 | 673.3966 | 673.4021 | 673.4018 | 673.3996 | 673.4013 | 673.3981 | 673.3996 | 673.3945 | 673.396 | 673.3969 | 673.3972 | 673.4036 | 673.3961 | 673.3955 | 673.3993 | 673.398 | 673.3954 | 673.4103 | 673.4026 | 673.3963 | 673.3979 | 673.4034 | 673.404 | 673.397 | 673.404 | 673.3948
With CCC | 16.6997 | 32.5634 | 53.4847 | 74.725 | 95.7851 | 116.7366 | 137.5868 | 158.5485 | 179.3414 | 200.365 | 221.2568 | 242.2002 | 263.1646 | 284.0603 | 304.9968 | 325.9636 | 346.8795 | 367.8197 | 388.7115 | 409.6227 | 430.5371 | 451.4823 | 472.3903 | 493.2619 | 514.143 | 535.0591 | 555.9976 | 576.9668 | 597.8998 | 618.8663 | 639.8081 | 660.7298 | 678.3268
Chart: Divergent warp lanes
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Original | 99.9995 | 12.1485 | 14.875 | 17.69 | 20.417 | 23.231 | 25.959 | 28.7725 | 31.5 | 34.316 | 37.042 | 39.8575 | 42.584 | 45.3985 | 48.125 | 50.9405 | 53.667 | 56.4825 | 59.2085 | 62.022 | 64.75 | 67.565 | 70.292 | 73.105 | 75.833 | 78.6485 | 81.375 | 84.1895 | 86.917 | 89.7315 | 92.458 | 95.2735 | 98
With CCC | 100 | 91.9965 | 92.896 | 93.639 | 94.263 | 94.791 | 95.2355 | 95.615 | 95.94 | 96.215 | 96.4505 | 96.6535 | 96.8225 | 96.9665 | 97.089 | 97.1885 | 97.272 | 97.338 | 97.3885 | 97.4275 | 97.4545 | 97.47 | 97.477 | 97.4745 | 97.4635 | 97.4465 | 97.4215 | 97.39 | 97.3545 | 97.3125 | 97.265 | 97.214 | 99.4185
Notes: The divergent path contains 20 FMAD operations.
Applying CCC makes the execution time grow linearly w.r.t. the workload.
While CCC warp efficiency is always high, normal kernel’s grows linearly w.r.t. the workload.

## Slide 15: Collaborative Context Collection: Sensitivity on Divergent Path Length
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
14
Chart: Divergent path FMAD instructions (8 threads of every warp take the path)
Orig. Exec. Time | 44.453 | 84.082 | 120.851 | 146.034 | 172.852 | 205.961 | 238.518 | 272.445 | 305.311 | 338.816 | 372.199 | 406.306 | 439.803 | 472.206 | 505.944 | 538.816 | 572.415 | 605.789 | 639.959 | 673.452 | 705.805 | 739.425 | 772.023 | 805.952 | 839.301 | 873.512 | 907.057 | 939.337 | 972.838 | 1005.36 | 1039.47 | 1072.81 | 1107.07 | 1140.55 | 1172.87 | 1206.34 | 1238.78 | 1272.98 | 1306.33 | 1340.6
Exec. Time with CCC | 22.591 | 29.1 | 38.58 | 46.459 | 55.28 | 63.2 | 71.847 | 80.68 | 88.439 | 97.237 | 104.322 | 113.228 | 121.371 | 129.454 | 138.509 | 146.255 | 155.174 | 162.167 | 171.138 | 179.362 | 187.459 | 196.65 | 204.417 | 213.271 | 220.36 | 229.243 | 237.615 | 245.664 | 254.924 | 262.746 | 271.559 | 278.706 | 287.604 | 295.808 | 303.864 | 313.228 | 321.084 | 329.859 | 337.028 | 345.814
CCC Speedup | 1.9677 | 2.8894 | 3.1325 | 3.1433 | 3.1268 | 3.2589 | 3.3198 | 3.3769 | 3.4522 | 3.4844 | 3.5678 | 3.5884 | 3.6236 | 3.6477 | 3.6528 | 3.6841 | 3.6889 | 3.7356 | 3.7394 | 3.7547 | 3.7651 | 3.7601 | 3.7767 | 3.779 | 3.8088 | 3.8104 | 3.8173 | 3.8237 | 3.8162 | 3.8264 | 3.8278 | 3.8493 | 3.8493 | 3.8557 | 3.8599 | 3.8513 | 3.8581 | 3.8592 | 3.876 | 3.8767
Chart: Divergent path FMAD instructions (24 threads of every warp take the path)
Orig. Exec. Time | 38.085 | 72.035 | 104.864 | 138.417 | 172.468 | 205.92 | 238.479 | 272.406 | 305.269 | 338.781 | 372.161 | 406.271 | 439.768 | 472.17 | 505.93 | 538.783 | 572.384 | 605.743 | 639.935 | 673.409 | 705.771 | 739.395 | 771.996 | 805.934 | 839.3 | 873.512 | 907.051 | 939.336 | 972.838 | 1005.36 | 1039.46 | 1072.82 | 1107.07 | 1140.57 | 1172.87 | 1206.34 | 1238.76 | 1272.98 | 1306.33 | 1340.59
Exec. Time with CCC | 40.411 | 65.655 | 91.726 | 115.606 | 140.918 | 165.141 | 189.585 | 215.095 | 239.353 | 264.935 | 289.021 | 314.461 | 339.285 | 364.101 | 389.71 | 414.074 | 439.601 | 463.898 | 489.24 | 514.167 | 538.971 | 564.625 | 589.023 | 614.553 | 638.932 | 664.277 | 689.131 | 714.013 | 739.613 | 763.998 | 789.562 | 814.007 | 839.321 | 864.25 | 888.961 | 914.653 | 939.065 | 964.619 | 989.059 | 1014.36
CCC Speedup | 0.94244 | 1.0972 | 1.1432 | 1.1973 | 1.2239 | 1.2469 | 1.2579 | 1.2664 | 1.2754 | 1.2787 | 1.2877 | 1.292 | 1.2962 | 1.2968 | 1.2982 | 1.3012 | 1.3021 | 1.3058 | 1.308 | 1.3097 | 1.3095 | 1.3095 | 1.3106 | 1.3114 | 1.3136 | 1.315 | 1.3162 | 1.3156 | 1.3153 | 1.3159 | 1.3165 | 1.3179 | 1.319 | 1.3197 | 1.3194 | 1.3189 | 1.3191 | 1.3197 | 1.3208 | 1.3216
Notes: CCC speedups approach to the inverse of the utilized threads ratio.
To cope with CCC overhead, either the divergent path should be long or the divergent ratio should be high.

## Slide 16: Summary
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
15
Collaborative Context Collection [and Consumption] (CCC) as a software/compiler technique to overcome thread divergence.
CCC collects the context of divergent threads at a stack inside the shared memory in order to implement all-or-none principle.
Transformations enable applying CCC to wider class of applications.
Optimizations improve the performance in certain situations.
CCC can be automated as a compiler technique.
CCC results in warp execution efficiency increase and the speedup in applications with certain repetitive patterns especially for compute-intensive ones.

## Slide 17: TEMPLATE
Efficient Warp Execution in Presence of Divergence with Collaborative Context Collection|Farzad Khorasani
P