## Slide 1: Scalable SIMD-Efficient Graph Processing on GPUs
Farzad Khorasani, Rajiv Gupta, Laxmi N. Bhuyan
University of California Riverside

## Slide 2: Scalable SIMD-Efficient Graph Processing on GPUs
Graph Processing
  Building blocks of data analytics.
  Vertex-centric expression.
GPUs
  Massive parallelism.
  Traditionally demand Regular data.
SIMD-Efficiency
  Challenging due to irregularity of real-world graphs.
Scalability
  Challenging due to
    DRAM capacity
    limited GPU-GPU bandwidth.

## Slide 3: Outline
SIMD-Efficiency
  Motivation
  Our solution: Warp Segmentation
Multi-GPU Scalability
  Motivation
  Our solution: Vertex Refinement
Experimental Evaluation

## Slide 4: SIMD-efficiency: GPU programming restriction
GPU SIMT architecture
  Mainly designed for accelerating graphics pipeline.
  Groups 32 threads into a SIMD group (warp in CUDA terms).
  One PC for the whole warp.
  Load imbalance will cause thread starvation.
  Thread starvation will incur underutilization of execution elements.
Notes: AMD GPUs 64 threads form a wavefront.
Processing elements (SM cores are reserved but not utilized).

## Slide 5: SIMD-efficiency: existing graph processing approaches
Algorithm-specific solutions
  BFS [PPoPP, 2012]
  SSSP [IPDPS, 2014]
  BC [SC, 2014]
Generic solutions
  PRAM-style [HiPC, 2007]
  Virtual-Warp Centric (VWC) [PPoPP, 2011]
  CW & G-Shards in CuSha [HPDC 2014]
Notes: Since we wanted to focus on scalability and maximizing the size of a graph that can be held inside the GPU DRAM, we focus on CSR representation.
For CSR-based generic and vertex-centric graph processing, VWC is still the state-of-the-art.

## Slide 6: SIMD-efficiency: VWC
Uses CSR representation.
Group threads inside the warp into virtual warps.
  Assign each virtual warp to process one vertex.
  Virtual lanes process the neighbors.
V0
V1
V2
V3
V4
8
V0
V1
V2
V3
V4
0
1
3
3
5
0
1
0
2
0
2
E5
E0
E1
E2
E3
E4
3
1
E7
E6
VertexValues
NbrIndices
NbrVertexIndices
EdgeValues
E0
E1
E5
E2
E3
E4
E7
E6
Notes: Virtual warp size stays constant throughout the kernel execution, and can be one from the set of {2,4,8,16,32}.

## Slide 7: SIMD-efficiency: VWC drawback facing irregularity
Real-world graphs are irregular usually exhibiting power law degree distribution.
LiveJournal
69 M Edges
5 M Vertices
Pokec
30 M Edges
1.6 M Vertices

## Slide 8: SIMD-efficiency: VWC drawback facing irregularity
N0
N1
N2
N3
N4
N5
N6
N7
R
R
RF
R
RF
RF
R
RF
C0
C1
C6
C7
C2
C3
R
Lane 0
Lane 1
Lane 2
Lane 3
RF
R
RF
R
RF
C4
C5
R
RF
Time
Notes: When VWC is applied to these graphs, we face under or over subscription.
Let’s assume the first vertex has 6 neighbors and the second vertex has 2 neighbors.
The first virtual warp has to iterate over the neighbors of its assigned vertices more, and basically drag the lanes in the second virtual warp. This is an example of over-subscription.

## Slide 9: SIMD-efficiency: VWC drawback facing irregularity
N0
N1
N2
N3
N4
N5
N6
N7
R
R
R
RF
R
RF
R
RF
C0
C1
C2
C3
C6
C7
R
R
R
R
RF
RF
Lane 0
Lane 1
Lane 2
Lane 3
Lane 4
Lane 5
Lane 6
Lane 7
R
RF
C4
C5
Time
Notes: The second virtual warp has size 4 but two lanes of it do not do anything throughout the process. It is an example of under-subscription.
VWC is susceptible to undersubscription and oversubscription.
The same problem that exists for PRAM style in the 1st place appears in VWC.

## Slide 10: SIMD-efficiency: Warp Segmentation
C0
C1
C2
C3
C4
C5
C6
C7
R
R
R
R
RF
RF
R
R
N0
N1
N2
N3
N4
N5
N6
N7
R
R
R
R
R
R
RF
RF
Lane 0
Lane 1
Lane 2
Lane 3
Lane 4
Lane 5
Lane 6
Lane 7
Time
Notes: What we want is something resilient against irregularities.
Each thread processes a neighbor in multiple rounds and gets involved in a reduction with minimum number of steps. Explain figure.

## Slide 11: SIMD-efficiency: Warp Segmentation
Instead of assigning one thread (PRAM) or a fixed number of threads (VWC) inside the warp to process one vertex and its neighbors, assign one warp to 32 vertices.
Warp threads collaborate to carry out processing the group of vertices.
Eliminate intra-warp load imbalance.
No need for pre-processing or trial-and-error (unlike VWC).
Notes: Intra-warp load imbalance would be eliminated since we avoid over-subscribing or under-subscribing vertices to one or a group of threads inside the warp.

## Slide 12: SIMD-efficiency: Warp Segmentation key features
Neighbors pertained to one destination vertex form a segment.
Fast determination of the segment the neighbor belongs to by the assigned thread.
  Binary search over a shared memory buffer to discover segment size and the intra-segment index.
Parallel reduction with the threads inside the segment.

## Slide 13: SIMD-efficiency: WS segment discovery
8
V0
V1
V2
V3
V4
0
1
3
3
5
N5
N0
N1
N2
N3
N4
N7
N6
VertexValues
NbrIndices
NbrVertexIndices
Binary Search EdgeIndex inside NbrIndices
Belonging Vertex Index
Index inside Segment
Index inside Segment from right
Segment Size
Operation
N0
[0,8]
[0,4]
[0,2]
[0,1]
0
0
0
1
N1
[0,8]
[0,4]
[0,2]
[1,2]
1
0
1
2
N2
[0,8]
[0,4]
[0,2]
[1,2]
1
1
0
2
N3
[0,8]
[0,4]
[2,4]
[3,4]
3
0
1
2
N4
[0,8]
[0,4]
[2,4]
[3,4]
3
1
0
2
N5
[0,8]
[4,8]
[4,6]
[4,5]
4
0
2
3
N6
[0,8]
[4,8]
[4,6]
[4,5]
4
1
1
3
N7
[0,8]
[4,8]
[4,6]
[4,5]
4
2
0
3
Notes: Index inside the segment is calculated by comparing the EdgeIndex with the corresponding destination vertex’s NbrIndices element.

## Slide 14: SIMD-efficiency: kernel’s internal functionality
1. Fetch the content for 32 vertices to process and initialize vertex shared memory buffer with user-provided function.
2. Iterative over neighbors of assigned vertices & update the shared buffer.
  Get the neighbor content.
  Discover what vertex the neighbor belongs to (form the segments).
  Apply user-provided compute function for the fetched neighbor.
  Apply user-provided reduction function within a segment.
  Reduce with the vertex content inside the shared memory.
3. Apply user-provided comparison function signaling if the vertex is updated.
Notes: With that design, the internal functionality of the vertex-centric framework we propose becomes like this.

## Slide 15: SIMD-efficiency: Warp Segmentation
Avoids shared memory atomics for reduction.
Avoids synchronization primitives throughout the kernel.
A form of intra-warp segmented reduction.
All memory accesses are coalesced except for accessing neighbor’s content (inherent to CSR representation).
Exploits instruction-level parallelism.
Inter-warp load imbalance is negligible.
Notes: There are a few other points about WS:
- Shared memory atomics in CuSha. Imposes heavy contentions over the atomic variables and limits the expressiveness of the solution.
An alternative would be to extend the reduction across the block but it introduces CTA-wide synchronization primitives.
Our intra-warp segmented reduction does not have head flags.
All the accesses (vertex values, prefix sum of number of neighbors, the neighbor index array, and the edge array) are coalesced.
Calculation of the destination vertex the neighbor belongs to is usually independent from the content of that vertex. Non-coalesced memory access latency is possible to be covered by such operations.
Inter-warp load imbalance would be averaged out in the presence of a lot of vertices to process. (4 warp schedulers and 64 warps on an SM when 100% theoretical occupancy). We actually select a small block size so new blocks can be scheduled and introduce fresh warps.

## Slide 16: Scalability: multi-GPU computation restrictions
Limited global memory.
Limited host memory access bandwidth from GPU.
  Comparatively low PCIe bandwidth.
  Even worse transfer rate for non-coalesced direct host accesses.
Limited bandwidth between devices.
Notes: Graphics card come out with a few GB DRAM. While system RAM sizes are typically 16, 24, 32, 64, 128 GB.
One solution is to utilize UVA and extend available RAM to the host memory. However, the device is connected to the system with PCIe. Bandwidth is tens of times less than global memory access.
Transfers should be coalesced. Otherwise, the speed would be even worse (13 times).
Device paths to communicate is PCIe.
All these things tell us that the bandwidth is precious so we have to use it carefully and not to waste it.

## Slide 17: Scalability: existing approaches for inter-device vertex transfer
Transfer all the vertices belonging to one GPU to other GPUs (ALL).
  Medusa [TPDS, 2014].
Pre-select and mark boundary vertices & transfer only them (MS).
  TOTEM [PACT, 2012].
Repeat at every iteration.
Both methods waste a lot of precious inter-device bandwidth.
Graph Algorithm | Useful vertices communicated | 
 | MS | ALL
BFS | 12.21% | 10.43%
SSSP | 13.65% | 15.99%
SSWP | 3.14% | 3.68%

## Slide 18: Scalability: Vertex Refinement data structure organization
PCIe Lanes
≤M
≤M
M+1
VertexValues
Q
Q
GPU #0
NbrIndices
NbrVertexIndices
EdgeValues
Values
Indices
≤N
≤N
N+1
VertexValues
R
R
GPU #1
NbrIndices
NbrVertexIndices
EdgeValues
Values
Indices
≤P
P+1
VertexValues
T
T
GPU #2
NbrIndices
NbrVertexIndices
EdgeValues
Values
Indices
≤P
Outbox
Outbox
Outbox
M
M
M
N
N
N
P
P
P
≤M
≤N
≤P
≤M
≤N
Values
Indices
≤P
Inbox #0
Inbox #1
Inbox #2
Host Memory
≤M
≤N
≤P
≤M
≤N
Values
Indices
≤P
Inbox #0
Inbox #1
Inbox #2
Odd Buffer
Even Buffer
PCIe Lanes
PCIe Lanes
Inbox & outbox buffers.
Double buffering.
Host-as-hub.
Notes: We suggest this organization of the data structures.

## Slide 19: Scalability: Vertex Refinement data structure organization
Inbox & outbox buffers.
  Vital for fast data transfer over PCIe.
  Direct peer-device memory access will be expensive.
Host-as-hub.
  Reduces the box copy operations and consequently communication traffic.
  Reduces GPU memory consumption, allows processing bigger graphs.
Double buffering.
  Eliminates the need for additional costly inter-device synchronization barriers.
Notes: Packets over PCIe bus better be transferred in big chunks.
Double-buffering is the alternation of read and write buffers at every iteration.

## Slide 20: Scalability: Vertex Refinement
Offline Vertex Refinement
  Pre-selects and marks boundary vertices.
  Inspired by TOTEM [PACT, 2012].
  Helps finding out the maximum size for inboxes/outboxes.
Online Vertex Refinement
  Happens on-the-fly inside the CUDA kernel.
  Threads check vertices for updates, each producing a predicate.
  Intra-warp binary reduction & prefix sum employed to update the outbox.
Notes: We only elaborate online vertex refinement.

## Slide 21: Scalability: Online Vertex Refinement
O[A+0]=V0
O[A+1]=V3
O[A+2]=V7
Is (Updated & Marked)
Shuffle A
Binary Prefix Sum
Operation
V0
3
A
0
V1
3
A
1
V2
3
A
1
V3
3
A
1
V4
3
A
2
V5
3
A
2
V6
3
A
2
V7
3
A
2
Y
N
Y
Y
N
N
N
N
Binary Reduction
Reserve Outbox Region
A = atomicAdd( deviceOutboxMovingIndex, 3 );
Fill Outbox Region

## Slide 22: Scalability: Online Vertex Refinement
Online VR
  Intra-warp binary reduction with the predicate.
  Warp-aggregated atomics to reduce the contention over the outbox top variable.
  Intra-warp binary prefix sum to realize the position to write.
No syncing primitive by focusing only on the warp.
Data transfer between boxes only with the size specified by the stack tops.
Each GPU reads other GPUs’ inboxes and updates its own vertex values.
Combination of online and offline VR maximizes inter-device communication efficiency.

## Slide 23: Experimental evaluation results: WS speedup over VWC
Average across input graphs |  | Average across benchmarks | 
BFS | 1.27x – 2.60x | RM33V335E | 1.23x – 1.56x
CC | 1.33x – 2.90x | ComOrkut | 1.15x – 1.99x
CS | 1.43x – 3.34x | ER25V201E | 1.09x – 1.69x
HS | 1.27x – 2.66x | RM25V201E | 1.15x – 1.57x
NN | 1.21x – 2.70x | LiveJournal | 1.29x – 1.99x
PR | 1.22x – 2.68x | SocPokec | 1.27x – 1.77x
SSSP | 1.31x – 2.76x | RoadNetCA | 1.24x – 9.90x
SSWP | 1.28x – 2.80x | Amazon0312 | 1.53x – 2.68x
Notes: Our system is Ubuntu 14.04 64 bit, CUDA 6.5, GeForce GTX780 Kepler SM3.5, -03 flag.
We got real-world graphs from SNAP dataset. We also created RMAT graphs to imitate the behavior of real-world graphs with power law degree distribution.
Comparisons with VWC are done on a single GPU. We have only compared kernel execution duration.
Speedups for VWC are expressed in range due to various virtual warp sizes.
When averaged across all input graphs and benchmarks, speedup ranges from 1.29x to 2.80x.

## Slide 24: Experimental evaluation results: WS warp execution efficiency over VWC
Chart: Warp Execution Efficiency (%)
| RM33V335E | ComOrkut | ER25V201E | RM25V201E | RM16V201E | RM16V134E | LiveJournal | SocPokec | HiggsTwitter | RoadNetCA | WebGoogle | Amazon0312
VWC-2 | 31.2 | 23.3 | 42.7 | 29 | 30.7 | 31.8 | 24.35 | 24.6 | 8.3 | 62.75 | 14.55 | 27.55
VWC-4 | 35.6 | 25.3 | 40.8 | 33.3 | 35.1 | 36.15 | 27.8 | 27 | 12.4 | 56.8 | 20.7 | 31.85
VWC-8 | 39.6 | 29.4 | 39.6 | 37.1 | 39.4 | 39.8 | 32.4 | 31.3 | 19.4 | 42.8 | 28.55 | 36.15
VWC-16 | 40.7 | 36.4 | 41 | 39.5 | 40.8 | 40.7 | 36.4 | 36.6 | 30.3 | 33.8 | 33.3 | 37.45
VWC-32 | 39.6 | 44.6 | 33 | 40 | 39.4 | 39.4 | 36.3 | 38.4 | 40.8 | 28.65 | 34.7 | 32.85
Warp Seg. | 72.1 | 73.8 | 71.1 | 70.9 | 72.3 | 71.2 | 71.7 | 71.8 | 73.6 | 73.35 | 69.1 | 70.75
Notes: Profiled average warp execution efficiency for SSSP (predicated and non-predicated combined).
Steady warp execution efficiency for WS (71 percent).
1.75x-3.27x better warp efficiency in WS.

## Slide 25: Experimental evaluation results: WS performance comparison with CW
Input Graph | BFS | CC | CS | HS | NN | PR | SSSP | SSWP
RM33V335E | 3.41 | 3.21 | 8.44 | 14.14 | 4.02 | 5.38 | 4.36 | 4.66
ComOrkut | 5.11 | 5.91 | 1.72 | 10.76 | 5.23 | 6.85 | 7.92 | 5.72
ER25V201E | 3.47 | 3.36 | 6.2 | 10.43 | 3.72 | 2.59 | 4.46 | 4.34
RM25V201E | 3.07 | 2.76 | 7.71 | 9.65 | 3.55 | 3.54 | 3.99 | 4.14
RM16V201E | 3.45 | 3.06 | 6.53 | 8.42 | 3.87 | 4.5 | 4.63 | 4.41
RM16V134E | x | x | 3.19 | 4.97 | x | 3.93 | x | x
Average | 3.7 | 3.66 | 5.63 | 9.73 | 4.08 | 4.47 | 5.07 | 4.65
Input Graph | BFS | CC | CS | HS | NN | PR | SSSP | SSWP
RM16V134E | 0.74 | 0.8 | x | x | 0.88 | x | 0.67 | 0.56
LiveJournal | 1.06 | 1.21 | 0.74 | 1.1 | 1.03 | 0.6 | 0.86 | 0.82
SocPokec | 0.92 | 1.02 | 1.04 | 0.81 | 0.41 | 0.34 | 0.73 | 0.67
HiggsTwitter | 1.48 | 2.3 | 1.48 | 1.64 | 2.2 | 1.19 | 1.65 | 2.03
RoadNetCA | 0.67 | 1.13 | 0.98 | 0.92 | 1.02 | 1.2 | 0.76 | 0.91
WebGoogle | 0.58 | 0.82 | 0.78 | 1.74 | 1.69 | 0.59 | 0.61 | 0.74
Amazon0312 | 1.05 | 1.47 | 0.39 | 0.91 | 0.91 | 0.97 | 1.21 | 1.2
Average | 0.93 | 1.25 | 0.9 | 1.19 | 1.16 | 0.82 | 0.93 | 0.99
Notes: For the large graphs, CW representation cannot fit the whole graph inside GPU global memory. For these combinations, CuSha fails; therefore, as a straightforward workaround, we kept vertex value and small auxiliary buffers inside the GPU global memory and put shards at mapped pinned buffers inside the host.
For large graphs, CW processing time is significantly higher than our method's due to involvement of PCIe bus, limiting the scalability of CW representation.
Also for the small graphs, although CW provides fully regular access patterns, it incurs larger memory footprints. In addition, our framework covers the latency of CSR-inherent irregular accesses, therefore we observe near par performance.

## Slide 26: Experimental evaluation results: VR performance compared to MS & ALL
Input graph |  | BFS | CC | CS | HS | NN | PR | SSSP | SSWP
RM54V704E | over ALL | 1.85 | 1.81 | 2.53 | 1.64 | 1.66 | 1.48 | 1.75 | 2.03
 | over MS | 1.82 | 1.78 | 2.46 | 1.59 | 1.63 | 1.47 | 1.71 | 1.98
RM41V536E | over ALL | 1.89 | 1.84 | 2.71 | 1.62 | 1.69 | 1.44 | 1.8 | 2.1
 | over MS | 1.82 | 1.81 | 2.63 | 1.58 | 1.66 | 1.39 | 1.75 | 2.04
RM41V503E | over ALL | 1.29 | 1.29 | 1.61 | 1.23 | 1.21 | 1.18 | 1.24 | 1.35
 | over MS | 1.27 | 1.28 | 1.57 | 1.21 | 1.2 | 1.15 | 1.21 | 1.32
RM35V402E | over ALL | 1.32 | 1.31 | 1.72 | 1.28 | 1.23 | 1.21 | 1.25 | 1.41
 | over MS | 1.3 | 1.29 | 1.66 | 1.23 | 1.22 | 1.2 | 1.22 | 1.38
Notes: Compared VR with MS and ALL.
ALL is the straightforward solution that copies all the vertices belonging to one device to other devices at every iteration.
MS is the maximal subset method where vertices that belong to one device and can be accessed by another device are identified in a pre-processing stage. During the iterative execution, only these vertices are communicated to other devices.
To better realize the benefits of VR, for all the inter-device communication methods, we keep intra-device processing style intact. In other words, underlying graph processing method is WS for all experiments in this section.
More elaborated results in the paper.
Averaged across all graphs and benchmarks:
- 1.81x and 1.31x over ALL for 3 and 2 GPUs
- 1.77x and 1.28x over MS for 3 and 2 GPUs

## Slide 27: Experimental evaluation results: VR performance compared to MS & ALL
Chart: Normalized Aggregated Processing Time
| ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | BFS | CC | CS | HS | NN | PR | SSSP | SSWP
Aggregated Computation Duration | 0.80578 | 0.80406 | 0.8081 | 0.80524 | 0.80524 | 0.81022 | 0.77015 | 0.77042 | 0.77563 | 0.84798 | 0.8481 | 0.85519 | 0.81287 | 0.81267 | 0.81348 | 0.87893 | 0.87913 | 0.88732 | 0.81329 | 0.81341 | 0.82021 | 0.81316 | 0.81313 | 0.81864
Aggregated Communication Duration | 0.19422 | 0.18422 | 0.046878 | 0.19476 | 0.18515 | 0.041009 | 0.22985 | 0.21335 | 0.026436 | 0.15202 | 0.14207 | 0.065776 | 0.18713 | 0.17748 | 0.063018 | 0.12107 | 0.099059 | 0.024906 | 0.18671 | 0.17717 | 0.063085 | 0.18684 | 0.17734 | 0.021025
Chart: Normalized Aggregated Processing Time
| ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | ALL | MS | VR | BFS | CC | CS | HS | NN | PR | SSSP | SSWP
Aggregated Computation Duration | 0.68813 | 0.68736 | 0.69385 | 0.68884 | 0.68545 | 0.68991 | 0.63267 | 0.63263 | 0.63307 | 0.71131 | 0.71102 | 0.71726 | 0.69874 | 0.69855 | 0.70193 | 0.83671 | 0.8357 | 0.84889 | 0.69892 | 0.69864 | 0.70464 | 0.6984 | 0.69755 | 0.70738
Aggregated Communication Duration | 0.31187 | 0.3057 | 0.082847 | 0.31116 | 0.30504 | 0.087623 | 0.36733 | 0.35498 | 0.036922 | 0.28869 | 0.28242 | 0.083003 | 0.30126 | 0.29587 | 0.11869 | 0.15541 | 0.1643 | 0.08019 | 0.30108 | 0.29506 | 0.10835 | 0.3016 | 0.29569 | 0.036972
2 GPUs
3 GPUs
Notes: We analyzed the cost of VR inbox/outbox management versus the savings it provides.
Computation: GPU kernel.
Communication: copy, box handling.
1) MS is not that effective.
2) The overhead of our method imposed on the GPU kernel is negligible.
3) Even though VR transfers the vertices accompanying their indices, it is still much less than MS.
4) By moving from 2 GPUs to 3 GPUs the communication overhead becomes much more, signifying VR supremacy even further. (effect of host-as-hub is important).
In addition to these experimets, there are other experiments in the paper showing the effectiveness of VR when the number of GPUs are added. Also, an experiment showing how it behaves when density of the graph and its size changes.

## Slide 28: Summary
  A framework for scalable, warp-efficient and multi-GPU vertex-centric graph processing on CUDA-enabled GPUs (available at https://github.com/farkhor/WS-VR).
  Warp Segmentation for SIMD-efficient processing of vertices with irregular-sized neighbors.
  Avoids atomics & explicit syncing primitives.
  Accesses to CSR buffers are coalesced (only one exception).
  Exploits ILP.
Vertex Refinement for efficient inter-device data transfer.
  Offline and online vertex refinement.
  Inbox/outbox buffers, double-buffering, host-as-hub.
Notes: Beside being SIMD-efficient, WS … .
Offline vertex refinement recognizes boundary vertices and online VR filters in only those vertices that have been updated during the previous iteration.