## Slide 1: Chapter 4: Network Layer
Chapter goals:
understand principles behind network layer services:
  routing (path selection)
  dealing with scale
  how a router works
  advanced topics: IPv6, multicast
instantiation and implementation in the Internet
Overview:
network layer services
routing principle: path selection
hierarchical routing
IP
Internet routing protocols reliable transfer
  intra-domain
  inter-domain
what’s inside a router?
IPv6
multicast routing

## Slide 2: Quiz
What is the main role of routing?
Describe a centralized routing protocol
  Main operation functions
  Comment on complexity, robustness
Describe a table driven routing protocol
  Main functions
  Comment on complexity
How can the Internet routing scale?
  Describe the elements that make it work
  What does a router need to keep in its memory
  Describe a routing table
What happens to a packet when it arrives at a router?
  What kind of “hardware” does it go through?
  Where does the delay and loss come into play?

## Slide 3: Network layer functions
transport packet from sending to receiving hosts
network layer protocols in every host, router
three important functions:
path determination: route taken by packets from source to dest. Routing algorithms
switching: move packets from router’s input to appropriate router output
call setup: some network architectures require router call setup along path before data flows
network
data link
physical
network
data link
physical
network
data link
physical
network data
link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 4: Network service model
Q: What service model for “channel” transporting packets from sender to receiver?
guaranteed bandwidth?
preservation of inter-packet timing (no jitter)?
loss-free delivery?
in-order delivery?
congestion feedback to sender?
?
?
?
virtual circuit
or
datagram?
The most important
abstraction provided
by network layer:
service abstraction

## Slide 5: Virtual circuits
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host OD)
every router on source-dest path s maintain “state” for each passing connection
  transport-layer connection only involved two end systems
link, router resources (bandwidth, buffers) may be allocated to VC
  to get circuit-like perf.
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path

## Slide 6: Virtual circuits: signaling protocols
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 7: Datagram networks: the Internet model
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets typically routed using destination host ID
  packets between same source-dest pair may take different paths
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 8: Datagram or VC network: why?
Internet
data exchange among computers
  “elastic” service, no strict timing req.
“smart” end systems (computers)
  can adapt, perform control, error recovery
  simple inside network, complexity at “edge”
many link types
  different characteristics
  uniform service difficult
ATM
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
“dumb” end systems
  telephones
  complexity inside network

## Slide 9: Routing
Graph abstraction for routing algorithms:
graph nodes are routers
graph edges are physical links
  link cost: delay, $ cost, or congestion level
Goal: determine “good” path
(sequence of routers) thru
network from source to dest.
Routing protocol
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5
“good” path:
  typically means minimum cost path
  other def’s possible

## Slide 10: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 11: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source”) to all other nodes
  gives routing table for that node
iterative: after k iterations, know least cost path to k dest.’s

## Slide 12: Dijkstra’s algorithm, discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n*(n+1)/2 comparisons: O(n**2)
more efficient implementations possible: O(nlogn)
Oscillations possible:
e.g., link cost = amount of carried traffic
A
D
C
B
1
1+e
e
0
e
1
1
0
0
A
D
C
B
2+e
0
0
0
1+e
1
A
D
C
B
0
2+e
1+e
1
0
0
initially
… recompute
routing
… recompute

## Slide 13: Distance Vector Routing Algorithm
iterative:
continues until no nodes exchange info.
self-terminating: no “signal” to stop
asynchronous:
nodes need not exchange info/iterate in lock step!
distributed:
each node communicates only with directly-attached neighbors
Distance Table data structure
each node has its own
row for each possible destination
column for each directly-attached neighbor to node
example: in node X, for dest. Y via neighbor Z:
D (Y,Z)
X
distance from X to
Y, via Z as next hop
c(X,Z) + min {D (Y,w)}
Z
w
=
=

## Slide 14: Distance Table: example
A
E
D
C
B
7
8
1
2
1
2
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
Via
destination
D (C,D)
E
c(E,D) + min {D (C,w)}
D
w
=
=
2+2 = 4
From node E: to go to C
What is the cost thru D?

## Slide 15: Distance table gives routing table
D ()
A
B
C
D
A
1
7
6
4
B
14
8
9
11
D
5
5
4
2
E
cost to destination via
destination
A
B
C
D
A,1
D,5
D,4
D,2
Outgoing link
to use, cost
destination
Distance table
Routing table

## Slide 16: Distance Vector Routing: overview
Iterative, asynchronous: each local iteration caused by:
local link cost change
message from neighbor: its least cost path change from neighbor
Distributed:
each node notifies neighbors only when its least cost path to any destination changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute distance table
if least cost path to any dest has changed, notify neighbors
Each node:

## Slide 17: Distance Vector: link cost changes
Link cost changes:
1. node detects local link cost change
updates distance table (line 15)
2. if cost change in least cost path, notify neighbors (lines 23,24)
X
Z
1
4
50
Y
1
algorithm
terminates
“good
news
travel
fast”
Y
Z

## Slide 18: Distance Vector: link cost changes
Link cost changes:
bad news travels slow - “count to infinity” problem!
ory
ru
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 19: Distance Vector: poisoned reverse
If Z routes through Y to get to X :
Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?
X
Z
1
4
50
Y
60
algorithm
terminates

## Slide 20
Topology information is flooded within the routing domain
Best end-to-end paths are computed locally at each router.
Best end-to-end paths determine next-hops.
Advertises: link info
Works only if policy is shared and uniform
Examples: OSPF, IS-IS
Each router knows little about network topology
Only best next-hops are chosen by each router for each destination network.
Best end-to-end paths result from composition of all next-hop choices
Advertises: path info, distance
Does not require uniform policies at all routers
Examples: RIP, BGP
Link State
Vectoring
Summary: Distributed Routing Techniques

## Slide 21: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent each round
DV: exchange between neighbors only periodically
Speed of Convergence
LS: O(n**2) algorithm
  may have oscillations
DV: convergence time varies
  may have routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    errors propagate thru network

## Slide 22: Hierarchical Routing
scale: with 50 million destinations:
can’t store all dest’s in routing tables!
routing table exchange would swamp links!
administrative autonomy
internet = network of networks
each network admin may want to control routing in its own network
Our routing study thus far - idealization
all routers identical
network “flat”
… not true in practice

## Slide 23: Hierarchical Routing
aggregate routers into regions, “autonomous systems” (AS)
routers in same AS run same routing protocol
  “intra-AS” routing protocol
  routers in different AS can run different intra-AS routing protocol
special routers in AS
run intra-AS routing protocol with all other routers in AS
also responsible for routing to destinations outside AS
  run inter-AS routing protocol with other gateway routers
gateway routers

## Slide 24: IP Addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host, router and physical link
  router’s typically have multiple interfaces
  host may have multiple interfaces
  IP addresses associated with interface, not host, router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 25: IP Addressing
IP address:
  network part (high order bits)
  host part (low order bits)
What’s a network ? (from IP address perspective)
  device interfaces with same network part of IP address
  can physically reach each other without intervening router
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
network consisting of 3 IP networks
(for IP addresses starting with 223,
first 24 bits are network address)
LAN

## Slide 26: IP Addressing
How to find the networks?
Detach each interface from router, host
create “islands of isolated networks
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
Interconnected
system consisting
of six networks

## Slide 27: IP Addresses
0
network
host
10
network
host
110
network
host
1110
multicast address
A
B
C
D
class
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
32 bits
given notion of “network”, let’s re-examine IP addresses:
“class-full” addressing:

## Slide 28: IP addressing: need for change
classful addressing:
  inefficient use of address space, address space exhaustion
  e.g., class B net allocated enough addresses for 65K hosts, even if only 2K hosts in that network

## Slide 29: IP addressing: CIDR
CIDR: Classless InterDomain Routing
network portion of address of arbitrary length
address format: a.b.c.d/x, where x is # bits in network portion of address
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23

## Slide 30: IP Addresses and Prefixes
IP addresses have 32 bits: 4 octets of bits (IPv4)
A prefix is a group of IP addresses
128.32.101.5 is an IP address (32 bits)
128.32.0.0/16 is a prefix of the 16 first bits:
  128.32.0.0 – 128.32.255.255 (2^16 addresses)
128.32.4.0/24 is a prefix of the 24 first bits - longer

## Slide 31: IP addresses: how to get one?
Hosts (host portion):
hard-coded by system admin in a file
DHCP: Dynamic Host Configuration Protocol: dynamically get address: “plug-and-play”
  host broadcasts “DHCP discover” msg
  DHCP server responds with “DHCP offer” msg
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 32: IP addresses: how to get one?
Network (network portion):
get allocated portion of ISP’s address space:
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 33: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Hierarchical addressing allows efficient advertisement of routing
information:

## Slide 34: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 35: Routing is Based on Prefixes
A BGP Routing table has prefixes for entries
For a IP address of a packet, find longest match
Example: packet IP 128.32.101.1
Matching:
128.1.1.4 matches the first 8 bits – no match!
128.32.0.0/16 match for 16 bits
128.32.101.0/24 is a longer match

## Slide 36: Prefix Matching in More Detail
For a IP address of a packet, find longest match
Example: Compare
  packet IP 128.32.101.1
  With 128.32.0.0/16
  IP : 01000000. 001000000. 01100101 .00000001
  Mask : 11111111. 111111111. 00000000 .00000000
  AND : 01000000. 001000000. 00000000 .00000000
  Prefix : 01000000. 001000000. 00000000. 00000000
  Equal? Yes
  We have a match of length 16

## Slide 37: IP addressing: the last word...
Q: How does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 38: Getting a datagram from source to dest.
IP datagram:
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
misc
fields
source
IP addr
dest
IP addr
data
datagram remains unchanged, as it travels source to destination
addr fields of interest here
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
routing table in A

## Slide 39: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B
find B is on same net. as A
link layer will send datagram directly to B inside link-layer frame
  B and A are directly connected
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
misc
fields
223.1.1.1
223.1.1.3
data

## Slide 40: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Dest. Net. next router Nhops
223.1.1 1
223.1.2 223.1.1.4 2
223.1.3 223.1.1.4 2
Starting at A, dest. E:
look up network address of E
E on different network
  A, E not directly attached
routing table: next hop router to E is 223.1.1.4
link layer sends datagram to router 223.1.1.4 inside link-layer frame
datagram arrives at 223.1.1.4
continued…..
misc
fields
223.1.1.1
223.1.2.2
data

## Slide 41: Getting a datagram from source to dest.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Arriving at 223.1.4, destined for 223.1.2.2
look up network address of E
E on same network as router’s interface 223.1.2.9
  router, E directly attached
link layer sends datagram to 223.1.2.2 inside link-layer frame via interface 223.1.2.9
datagram arrives at 223.1.2.2!!! (hooray!)
misc
fields
223.1.1.1
223.1.2.2
data
network router Nhops interface
223.1.1 - 1 223.1.1.4
223.1.2 - 1 223.1.2.9
223.1.3 - 1 223.1.3.27
Dest. next

## Slide 42: Intra-AS and Inter-AS routing
Gateways:
  perform inter-AS routing amongst themselves
  perform intra-AS routers with other routers in their AS
inter-AS, intra-AS routing in
gateway A.c
network layer
link layer
physical layer
a
b
b
a
a
C
A
B
d
A.a
A.c
C.b
B.a
c
b
c

## Slide 43: Intra-AS and Inter-AS routing
Host
h2
a
b
b
a
a
C
A
B
d
c
A.a
A.c
C.b
B.a
c
b
Host
h1
Intra-AS routing
within AS A
Inter-AS
routing
between
A and B
Intra-AS routing
within AS B
We’ll examine specific inter-AS and intra-AS Internet routing protocols shortly

## Slide 44: The Internet Network layer
routing
table
Host, router network layer functions:
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 45: Measurements in the Internet
Difficulties in measuring
Measuring tools (traceroute)
Misc issues

## Slide 46: Measuring and Modeling Is not Easy
Constantly changing environment
How much data is enough
  Recently: we need to measure more than 24h!
How frewuently should I be measuring?
Are the measurements representative?

## Slide 47: Operation versus Measurements
Operators do not care about
  Measurements
  Academic Research
Why?
  Takes away resources
  Can create problems
  Complicates their lives
Luckily, there are measurement centers
  CAIDA, NLANR, routeviews, RIPE

## Slide 48: Types of Measurement Tools
Application level:
  Install application agents at two measuring entries
  REALITI tool from UCR
  More control over process
Network level:
  Use the Internet control functionality (ICMP)
  Trick the network to provide information

## Slide 49: Ping: the tool
Uses ICMP ECHO_REQUEST datagram to elicit an ICMP ECHO_RESPONSE from a host or gateway
Reports
  Round trip time
  Packets loss
Many available options: packet type, size etc
Limitation: >1sec measurement frequency
Read manual: man ping

## Slide 50: Traceroute: the tool
Traceroute measures
  the path and the round trip time
Traceroute: ingenious (ab)use of the network layer by Van Jacobson
Main ideas:
  send “bad” packets to receive ICMP: “packet died”
  Recursive probing to identify the path
  Send three packets at a time
Read manual: man traceroute

## Slide 51: The ingenuity of traceroute
Send a packet for every hop of the path
Set TTL = 1, packet expires, ICMP returns
Increase TTL by one, and repeat
At the destination, port number is wrong: return an ICMP packet, port not found

## Slide 52: Traceroute: Some Limitations
In traceroute, you may be exploring multiple paths without knowing it
Delays for each part of the path correspond to different measurements: ie they don’t sum up

## Slide 53: Identifying The Router Topology
Several efforts rely on multiple traceroute
  Govindan et al INFOCOM 2000
  Cheswick and Burch Internet Mapping Project
Main idea:
  Do thousands of traceroutes
  Collect all adjacent nodes
  Generate a graph

## Slide 54: Router Graphs: A Complication
Routers have multiple IP addresses
  One for each interface
How do we resolve this?
Only heuristics exist [Govindan]
Heuristic: Send packets to one interface and hope that they will respond with the other interface

## Slide 55: End

## Slide 56: Proposals
Overall: decent
Not enough motivation/background
  All related papers
Not enough thought on what you will do
  Spend an evening thinking what you will do and how
Try to clarify goals early and talk to me
Photocopy them, and give me the original
  It’s the contract

## Slide 57: Practical Tips
The earlier, the better
Talk to me early
Look for tools, data, previous work
  It can save you a lot of time in the long run
Try to focus on a topic

## Slide 58: Side Note
Important things in research:
  Asking the right questions
  Identifying the right topic
  Context of research
    Motivation
    Previous and related work
    Importance of problem
  Thoroughness of work