## Slide 1: Introduction to Wireless Networks
Michalis Faloutsos

## Slide 2: IEEE 802.11 Wireless LAN - 1
Wireless LANs: untethered (often mobile) networking
IEEE 802.11 standard:
  MAC protocol
  unlicensed frequency spectrum: 900Mhz, 2.4Ghz

## Slide 3: IEEE 802.11 Wireless LAN - 2
Basic Service Set (BSS) (a.k.a. “cell”) contains:
  wireless hosts
  access point (AP): base station
BSS’s combined to form distribution system (DS)

## Slide 4: IEEE 802.11 used for Ad Hoc Networks
Ad hoc network: IEEE 802.11 stations can dynamically form network without AP
Applications:
  “laptop” meeting in conference room, car
  interconnection of “personal” devices
  battlefield
IETF MANET (Mobile Ad hoc Networks) working group

## Slide 5: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 CSMA sender:
- if sense channel idle for DIFS sec.
then transmit entire frame (no collision detection)
-if sense channel busy then binary backoff
802.11 CSMA receiver:
if received OK
return ACK after SIFS

## Slide 6: IEEE 802.11 MAC Protocol
802.11 CSMA Protocol: others
NAV: Network Allocation Vector
802.11 frame has transmission time field
others (hearing data) defer access for NAV time units

## Slide 7: Ad Hoc Networks

## Slide 8: What is an ad hoc network
A collection of nodes that can communicate with each other without the use of existing infrastructure
Each node is a sender, a receiver, and a relay
There are no “special nodes” (in principal)
  No specialized routers, no DNS servers
Nodes can be static or mobile
Can be thought of us: peer-to-peer communication

## Slide 9: Example: Ad hoc network
Nodes have power range
Communication happens between nodes within range

## Slide 10: What Is Different Here?
Broadcasts of nodes can “overlap” -> collision
How do we handle this?
A MAC layer protocol could be the answer
If one node broadcasts, neighbors keeps quite
Thus, nearby nodes compete for air time
This is called contention

## Slide 11: Contention in ad hoc networks
A major difference with wireline networks
Air-time is the critical resource
Fact 1: connections that cross vertically interfere
Fact 2: connections that do not share nodes interfere
Fact 3: a single connection with itself interferes!

## Slide 12: Example of contention
Yellow connection bothers pink connection
Yellow bothers itself
When A-E is active
  E-F is silent
  F-G is silent (is it?)
A
B
C
D
E
G
F
H

## Slide 13: The Hidden Terminal Effect
hidden terminals: A, C cannot hear each other
  obstacles, signal attenuation
  collisions at B
goal: avoid collisions at B
CSMA/CA: CSMA with Collision Avoidance

## Slide 14: Collision Avoidance: RTS-CTS exchange - 1
CSMA/CA: explicit channel reservation
  sender: send short RTS: request to send
  receiver: reply with short CTS: clear to send
CTS reserves channel for sender, notifying (possibly hidden) stations
Avoid hidden station collisions

## Slide 15: Collision Avoidance: RTS-CTS exchange - 2
RTS and CTS short:
  collisions less likely, of shorter duration
  end result similar to collision detection
IEEE 802.11 allows:
  CSMA
  CSMA/CA: reservations
  polling from AP

## Slide 16: The 802.11 MAC protocol
Introduced to reduce collisions
Sender sends Request To Send (RTS): ask permission
Case A: Receiver gives permission Clear To Send (CTS)
Sender sends Data
Receiver sends ACK, if received correctly
Case B: Receiver does not respond
  Sender waits, times out, exponential back-off, and tries again
A
D
C
B
RTS
CTS
RTS
CTS

## Slide 17: Why is this necessary?
A: RTS, and B replies with a CTS
C hears RTS and avoids sending anything
  C could have been near B (not shown here)
D hears CTS so it does not send anything to B
A
D
C
B
RTS
CTS

## Slide 18: Some numbers for 802.11
Typical radius of power-range: 250m
Interference range: 500m
  At 500m one can not hear, but they are bothered!
RTS packet 40 bytes
CTS and ACK 39 bytes
MAC header is 47 bytes

## Slide 19: Typical Simulation Environment
A 2-dimensional rectangle
Fixed number of nodes
Static: uniformly distributed
Dynamic: way-point model
  Pick location, move with speed v, pause
Power range: fixed or variable
Sender-receivers uniformly distributed

## Slide 20: Various Communication Paradigms
Broadcasting:
  one nodes reaches everybody
Multicasting:
  One node reaches some nodes
Anycasting:
  One node reaches a subset of some target nodes (one)
Application Layer protocols and overlays
  Applications like peer-to-peer