## Slide 1: The Data Link Layer
Based on slides by Shiv. Kalyanaraman and B. Sidkar

## Slide 2
Understand principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
  reliable data transfer, flow control
Instantiation and implementation of various link layer technologies
Goals

## Slide 3
link layer services
error detection, correction
multiple access protocols and LANs
link layer addressing, ARP
specific link layer technologies:
  Ethernet
  IEEE 802.11 LANs
  PPP
  ATM
  hubs, bridges, switches
Overview

## Slide 4: Link Layer: setting the context - 1

## Slide 5: Link Layer: setting the context - 2
two physically connected devices:
  host-router, router-router, host-host
unit of data: frame
M
adapter card
application
transport
network
link
physical
network
link
physical
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
H
t
H
n
H
l
frame
phys. link
data link
protocol

## Slide 6: Link Layer Services - 1
Framing, link access:
  encapsulate datagram into frame, adding header, trailer
  implement channel access if shared medium,
  ‘physical addresses’ used in frame headers to identify source, dest
    different from IP address!

## Slide 7: Link Layer Services - 2
Reliable delivery between two physically connected devices:
  seldom used on low bit error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 8: Link Layer Services - 3
Flow Control:
  pacing between sender and receivers
Error Detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
Error Correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission

## Slide 9: Link Layer: Implementation
Implemented in “adapter”
  e.g., PCMCIA card, Ethernet card
  typically includes: RAM, DSP chips, host bus interface, and link interface
application
transport
network
link
physical
network
link
physical
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
H
t
H
n
H
l
frame
phys. link
data link
protocol
adapter card

## Slide 10: Some basic concepts
Bandwidth and throughput
Link capacity limits
Bandwidth delay product

## Slide 11: Bandwidth and Throughput
See PetDav p.40
Bandwidth: the range of frequencies a channel can use
  Tel. Line: 300 - 3300Hz -> 3000Hz
Bandwidth commonly used as number of bits per sec that can be transmitted
Throughput: the number of bits that can be delivered successfully defined per layer
  For Link level, same as bandwidth
  For application level, information that can go through
Goodput: useful throughput
  throughput - overhead

## Slide 12: Link Capacity
How much capacity (data rate) can a link support?
Shannon’s theorem - classic theorem:
  C = B log2 (1 + S/N)
Where
  C is link capacity
  B is the bandwidth of the line
  S is average signal power
  N is average noise power
S/N is the signal to noise ratio
  Expressed in decibels: db = 10 log10 (S/N)
  Signal strength is reported relative to noise
For db = 30, and B = 3300 - 300Hz -> C = 30Kbps

## Slide 13: Bandwidth delay product
B, Bandwidth is how fast I can push bits on the link
D, Delay is the time it takes for information to arrive at the destination
B x D is the amount of bits that can be in flight on a link before the receiver is aware of anything
Often this is used for D = round trip time
  Amount of information that is on the link before sender is informed that something arrived at the receiver

## Slide 14: Error Detection - 1
EDC= Error Detection and Correction bits (redundancy)
D = Data protected by error checking, may include header fields
Error detection not 100% reliable!
  protocol may miss some errors, but rarely
  larger EDC field yields better detection and correction

## Slide 15: Error Detection - 2

## Slide 16: Parity Checking
Single Bit Parity:
Detect single bit errors
Two Dimensional Bit Parity:
Detect and correct single bit errors
0
0

## Slide 17: Internet checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment (note: used at transport layer only)

## Slide 18: Checksumming: Cyclic Redundancy Check
View data bits, D, as a binary number
Choose r+1 bit pattern (generator), G
Goal: choose r CRC bits, R, such that
  <D,R> exactly divisible by G (modulo 2)
  receiver knows G, divides <D,R> by G. If non-zero remainder: error detected!
  can detect all burst errors less than r+1 bits
Widely used in practice (ATM, HDCL)

## Slide 19: CRC Example
Want:
  D.2r XOR R = nG
equivalently:
  D.2r = nG XOR R
equivalently:
if we divide D.2r by G, want reminder R
R = remainder[ ]
D.2r
G
See picture from book (this is weird)

## Slide 20: Multiple Access Links and Protocols
Three types of “links”:
Point-to-point (single wire, e.g. PPP, SLIP)
Broadcast (shared wire or medium; e.g, Ethernet, Wavelan, etc.)
Switched (e.g., switched Ethernet, ATM etc)

## Slide 21: Multiple Access Protocols - 1
single shared communication channel
two or more simultaneous transmissions by nodes: interference
  only one node can send successfully at a time
multiple access protocol:
  distributed algorithm that determines how stations share channel, i.e., determine when station can transmit

## Slide 22: Multiple Access protocols - 2
multiple access protocol (cont.):
  communication about channel sharing must use channel itself!
  What to look for in multiple access protocols:
    synchronous or asynchronous
    information needed about other stations
    robustness (e.g., to channel errors)
    performance

## Slide 23: Multiple Access protocols - 3
claim: humans use multiple access protocols all the time
How do we share?

## Slide 24: MAC Protocols: a taxonomy
Three broad classes:
Channel Partitioning
  divide channel into smaller “pieces” (time slots, frequency)
  allocate piece to node for exclusive use
Random Access
  allow collisions
  “recover” from collisions
“Taking turns”
  tightly coordinate shared access to avoid collisions
Goal: efficient, fair, simple, decentralized

## Slide 25: Channel Partitioning MAC protocols: TDMA - 1
TDMA: time division multiple access
Access to channel in "rounds"
Each station gets fixed length slot (length = pkt trans time) in each round
Unused slots go idle
Example: 6-station LAN, 1,3,4 have pkt, slots 2,5,6 idle

## Slide 26: Channel Partitioning MAC protocols: FDMA - 2
Example: 6-station LAN, 1,3,4 have pkt, frequency bands 2,5,6 idle
frequency bands
time

## Slide 27: Channel Partitioning (CDMA) - 1
CDMA (Code Division Multiple Access)
unique “code” assigned to each user; ie, code set partitioning
used mostly in wireless broadcast channels (cellular, satellite, etc)
all users share same frequency, but each user has own “chipping” sequence (ie, code) to encode data

## Slide 28: Channel Partitioning (CDMA) - 2
Encoded signal = (original data) X (chipping sequence)
Decoding: inner-product of encoded signal and chipping sequence
allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
Not in Peterson Davie!

## Slide 29: CDMA Encode/Decode

## Slide 30: CDMA: two-sender interference

## Slide 31: Performance of Fixed Assignment Protocols - 1
Fixed assignment protocols are ideal for continuous streams such as video or audio
What about for packet switched data?
A “perfect” multiple access scheme would always use the channel when there are packets waiting (statistical multiplexing)
The mean delay for statistical multiplexing is just like for the M / M / 1 queue:
where  is the arrival rate and  is the service rate

## Slide 32: Performance of Fixed Assignment Protocols - 2
OTOH fixed assignment protocols divide the channel into N separate independent, /N identical subchannels
If each user has arrival rate /N, each user/subchannel pair can be modeled as a separate M / M / 1 queue
And the mean delay for a packet is
So, if we use fixed assignment protocols for packet switched data, mean delay goes up by a factor of N!!

## Slide 33: Random Access Protocols - 1
When node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
Two or more transmitting nodes -> “collision”,
Random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)

## Slide 34: Random Access Protocols - 2
Examples of random access MAC protocols:
  ALOHA (not in PetDavie)
  slotted ALOHA (not in PetDavie)
  CSMA and CSMA/CD

## Slide 35: Pure (unslotted) ALOHA - 1
Unslotted Aloha: simpler, no synchronization
pkt needs transmission:
  send when you have a packet
Collision probability increases:
  pkt sent at t0 collide with other pkts sent in [t0-1, t0+1]

## Slide 36: Pure (unslotted) ALOHA - 2
Success if none starts right before or right after:
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0,t0+1]
= p . (1-p)(N-1) . (1-p)(N-1)
P(success by any of N nodes) = N p . (1-p)(N-1) .
(1-p)(N-1)
… choosing optimum p as N -> infty ...
= 1/(2e) = .18

## Slide 37: Slotted Aloha
time is divided into equal size slots (= pkt trans. time)
node with new arriving pkt: transmit at beginning of next slot
if collision: retransmit pkt in future slots with probability p, until successful.
Success (S), Collision (C), Empty (E) slots

## Slide 38: Slotted Aloha Efficiency
Q: What is max fraction slots successful?
A: Suppose N stations have packets to send
  each transmits in slot with probability p
  prob. successful transmission S is:
by single node: S= p (1-p)(N-1)
by any of N nodes
S = Prob (only one transmits)
= N p (1-p)(N-1)
… choosing optimum p as n -> infty ...
= 1/e = .37 as N -> infty
At best: channel
use for useful
transmissions 37% of time!

## Slide 39: Performance Comparison
S = throughput = “goodput”
(success rate)
G = offered load = Np
0.5
1.0
1.5
2.0
0.1
0.2
0.3
0.4
Pure Aloha
Slotted Aloha
protocol constrains
effective channel
throughput!

## Slide 40: The Rules of Sharing
CSMA: Collision Sensing Multiple Access
  Sense the channel before sending
CSMA/CD: CSMA with Collision Detection
  Sense the channel before sending
  Sense the channel WHILE sending too

## Slide 41: Carrier Sensing Multiple Access (CSMA) - 1
In some shorter distance networks, it is possible to listen to the channel before transmitting
In radio networks, this is called “ sensing the carrier”
The CSMA protocol works just like Aloha except: If the channel is sensed busy, then the user waits to transmit its packet, and a collision is avoided
This really improves the performance in short distance networks!

## Slide 42: Carrier Sensing Multiple Access (CSMA) - 2
How long does a blocked user wait before trying again to transmit its packet? Three basic variants:
1-persistent: Blocked user continuously senses channel until its idle, then transmits
0-persistent: Blocked user waits a randomly chosen amount of time before sensing channel again

## Slide 43: Carrier Sensing Multiple Access (CSMA) - 3
P-persistent: Let T = end-to-end propagation delay
  If channel is idle then transmit packet
  If channel busy then toss coin [with P(heads) = P]
  Heads: Transmit at first idle
  Tails: wait until first idle plus T, sense, repeat
Human analogy: Don’t interrupt others

## Slide 44: CSMA collisions
collisions can occur:
propagation delay means two nodes may not year hear each other’s transmission
collision: entire packet transmission time wasted
spatial layout of nodes along ethernet
note: role of distance and propagation delay in determining collision prob.

## Slide 45: CSMA/CD (Collision Detection)
CSMA improves performance, but still it wastes the channel during collisions
In some very short distance networks (e.g. coax LANs), it is possible to listen while transmitting (in addition to listening before transmitting)
If we detect a collision while transmitting, we can abort the transmission and free up the channel sooner
This idea was proposed by R. Metcalfe and Boggs at Xerox PARC in the mid 1970s under the name Ethernet.
Human analogy: the polite conversationalist

## Slide 46: CSMA/CD collision detection

## Slide 47: “Taking Turns” MAC protocols - 1
Channel partitioning MAC protocols:
  share channel efficiently at high load
  inefficient at low load: delay in channel access, 1/N bandwidth allocated even if only 1 active node!
Random access MAC protocols
  efficient at low load: single node can fully utilize channel
  high load: collision overhead
“Taking turns” protocols
  look for best of both worlds!

## Slide 48: “Taking Turns” MAC protocols - 2
Polling:
Master node “invites” slave nodes to transmit in turn
Request to Send, Clear to Send messages
Concerns:
  polling overhead
  latency
  single point of failure (master)
Token passing:
Control token passed from one node to next sequentially.
Token message
Concerns:
  token overhead
  latency
  single point of failure (token)

## Slide 49: Reservation-based protocols - 1
Distributed Polling:
Time divided into slots
Begins with N short reservation slots
  reservation slot time equal to channel end-end propagation delay
  station with message to send posts reservation
  reservation seen by all stations

## Slide 50: Reservation-based protocols - 2
After reservation slots, message transmissions ordered by known priority