## Slide 1: Data Link Layer
Ethernet
Bridges
Token Ring

## Slide 2: Summary of MAC protocols
What do you do with a shared media?
  Channel Partitioning: time, frequency or code
    Time Division,Code Division, Frequency Division
  Random partitioning (dynamic),
    ALOHA, S-ALOHA, CSMA, CSMA/CD
    carrier sensing: easy in some technologies (wire), hard in others (wireless)
    CSMA/CD used in Ethernet
  Taking Turns
    polling from a central cite, token passing

## Slide 3: LAN technologies
Data link layer so far:
  services, error detection/correction, multiple access
Next: LAN technologies
  addressing
  Ethernet
  hubs, bridges, switches
  802.11
  PPP
  ATM

## Slide 4: LAN Addresses and ARP - 1
32-bit IP address:
network-layer address
used to get datagram to destination network (recall IP network definition)
LAN (or MAC or physical) address:
used to get datagram from one interface to another physically-connected interface (same network)
48 bit MAC address (for most LANs) burned in the adapter ROM

## Slide 5: LAN Addresses and ARP - 2
Each adapter on LAN has unique LAN address

## Slide 6: LAN Address (more)
MAC address allocation administered by IEEE
manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
(a) MAC address: like Social Security Number
(b) IP address: like postal address
MAC flat address => portability
  can move LAN card from one LAN to another
IP hierarchical address NOT portable
  depends on network to which one attaches

## Slide 7: Data Link and Routing
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Starting at A, given IP datagram addressed to B:
look up net. address of B, find B on same net. as A
link layer send datagram to B inside link-layer frame
B’s MAC
addr
A’s MAC
addr
A’s IP
addr
B’s IP
addr
IP payload
datagram
frame
frame source,
dest address
datagram source,
dest address

## Slide 8: ARP: Address Resolution Protocol
Each IP node (Host, Router) on LAN has ARP module, table
ARP Table: IP/MAC address mappings for some LAN nodes
< IP address; MAC address; TTL>
< ………………………….. >
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
MAC address of B
given B’s IP address?

## Slide 9: ARP protocol
A knows B's IP address, wants to learn physical address of B
A broadcasts ARP query pkt, containing B's IP address
  all machines on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) physical layer address
A caches (saves) IP-to-physical address pairs until information becomes old (times out)
  soft state: information that times out (goes away) unless refreshed

## Slide 10: Routing to another LAN - 1
Walkthrough: routing from A to B via R

## Slide 11: Routing to another LAN - 2
A creates IP packet with source A, destination B
A uses ARP to get R’s physical layer address for 111.111.111.110
A creates Ethernet frame with R's physical address as dest, Ethernet frame contains A-to-B IP datagram
A’s data link layer sends Ethernet frame

## Slide 12: Routing to another LAN - 3
R’s data link layer receives Ethernet frame
R removes IP datagram from Ethernet frame, sees its destined to B
R uses ARP to get B’s physical layer address
R creates frame containing A-to-B IP datagram sends to B

## Slide 13: Ethernet
“Dominant” LAN technology:
Cheap $20 for 100Mbs!
First widely used LAN technology
Simpler, cheaper than token LANs and ATM
Kept up with speed race: 10, 100, 1000 Mbps
Metcalfe’s Ethernet
sketch

## Slide 14: Ethernet Frame Structure - 1
Sending adapter encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
Preamble:
7 bytes with pattern 10101010 followed by one byte with pattern 10101011
Used to synchronize receiver, sender clock rates

## Slide 15: Ethernet Frame Structure - 2
Addresses: 6 bytes, frame is received by all adapters on a LAN and dropped if address does not match
Type: indicates the higher layer protocol, mostly IP but others may be supported such as Novell IPX and AppleTalk)
CRC: checked at receiver, if error is detected, the frame is simply dropped

## Slide 16: Ethernet
Ethernet uses 1-persistent CSMA/CD on coaxial cable at 10 Mbps (802.3 allows other speeds & media)
The maximum cable length allowed: 500m
Longer distances covered using repeaters to connect multiple “segments” of cable
No two stations can be separated by more than 2500 meters and 4 repeaters
Including the propagation delay for 2500m and the store and forward delay in 4 repeaters, the maximum time for a bit to travel between any two stations is max=25.6se (one way)

## Slide 17: Ethernet: uses CSMA/CD
A: sense channel, if idle
  then {
  transmit and monitor the channel;
      If detect another transmission
      then {
      abort and send jam signal;
        update # collisions;
        delay as required by exponential backoff algorithm;
        goto A
        }
      else {done with the frame; set collisions to zero}
    }
  else {wait until ongoing transmission is over and goto A}

## Slide 18: Ethernet’s CSMA/CD
In order to ensure that every collision is “heard" by all stations, when a station detects a collision , it jams the channel
Example
  Two stations, A and B, are close together
  A third station, C, is far away
  A and B will detect each other’s transmission very quickly and shut off
  This will only cause a short blip which may not be detected by C but will still cause enough errors to destroy C’s packet

## Slide 19: Ethernet’s CSMA/CD
When collisions occur, Ethernet uses a random retransmission scheme called exponential backoff:
  If your packet is in a collision, set K=2
  Pick a number k at random from {0, 1,..,K-1}
  After k* seconds, sense channel, transmit if idle
  If collision occurs, let K=2 x K, go to step 2
After 10 repeats, stop doubling K
After 16, give up and tell layer above “I give up”
“Fixes” random access stability problem by passing it to the layer above!

## Slide 20: Ethernet Technologies: 10Base2
10: 10Mbps; 2: under 200 meters max cable length
Thin coaxial cable in a bus topology
Repeaters used to connect up to multiple segments
Repeater repeats bits it hears on one interface to its other interfaces: physical layer device!

## Slide 21: 10BaseT and 100BaseT - 1
10/100 Mbps rate; latter called “fast ethernet”
T stands for Twisted Pair
Hub to which nodes are connected by twisted pair, thus “star topology”
Notes: CSMA/CD implemented at hub?

## Slide 22: 10BaseT and 100BaseT - 1
Max distance from node to Hub is 100 meters
Hub can gather monitoring information, statistics for display to LAN administrators

## Slide 23: Gbit Ethernet
Use standard Ethernet frame format
Allows for point-to-point links and shared broadcast channels
In shared mode, CSMA/CD is used; short distances between nodes to be efficient
Uses hubs, called here “Buffered Distributors”
Full-Duplex at 1 Gbps for point-to-point links

## Slide 24: Token Rings (IEEE 802.5)
A ring topology is a single unidirectional loop connecting a series of stations in sequence
Each bit is stored and forwarded by each station’s network interface

## Slide 25: Token Rings: IEEE 802.5 -1
Versions that operate at 1, 4, and 16 Mbps over shielded twisted pair copper wire
Max token holding time: 10 ms, limiting frame length
SD, ED mark start, end of packet

## Slide 26: Token Ring: IEEE 802.5 - 2
AC: access control byte:
  Token bit: value 0 means token can be seized, value 1 means data follows FC
  Priority bits: priority of packet
  Reservation bits: station can write these bits to prevent stations with lower priority packet from seizing token after token becomes free

## Slide 27: Token Ring: IEEE 802.5 - 3
FC: frame control used for monitoring and maintenance
Source, destination address: 48 bit physical address, as in Ethernet
Data: packet from network layer
Checksum: CRC
FS: frame status: set by dest., read by sender
  set to indicate destination up, frame copied OK from ring
  DLC-level ACKing

## Slide 28: Token Ring: IEEE 802.5 - 4
After transmitting one or more packets (depending on the rules of the protocol), the node transmits a new token to the next node in one of 3 ways:
  Single Packet Mode: Token is transmitted after receiving the last bit of transmitted packet(s)
  Multiple Token Mode: Token is transmitted immediately after the last bit of the packet(s) is transmitted
In small rings, the last two are the same

## Slide 29: Interconnecting LANs
Q: Why not just one big LAN?
Limited amount of supportable traffic: on single LAN, all stations must share bandwidth
Limited length: 802.3 specifies maximum cable length
Large “collision domain” (can collide with many stations)
Limited number of stations: 802.5 have token passing delays at each station

## Slide 30: Hubs - 1
Physical Layer devices: essentially repeaters operating at bit levels: repeat received bits on one interface to all other interfaces
Hubs can be arranged in a hierarchy (or multi-tier design), with backbone hub at its top

## Slide 31: Hubs - 2
Each connected LAN referred to as LAN segment
Hubs do not isolate collision domains: node may collide with any node residing at any segment in LAN
Hub Advantages:
  simple, inexpensive device
  Multi-tier provides graceful degradation: portions of the LAN continue to operate if one hub malfunctions
  extends maximum distance between node pairs (100m per Hub)

## Slide 32: Hub limitations
Single collision domain results in no increase in max throughput
  multi-tier throughput same as single segment throughput
Individual LAN restrictions pose limits on number of nodes in same collision domain and on total allowed geographical coverage
Cannot connect different Ethernet types (e.g., 10BaseT and 100baseT)

## Slide 33: Bridges - 1
Link Layer devices: operate on Ethernet frames, examining frame header and selectively forwarding frame based on its destination
Bridge isolates collision domains since it buffers frames
When frame is to be forwarded on segment, bridge uses CSMA/CD to access segment and transmit

## Slide 34: Bridges - 2
Bridge advantages:
  Isolates collision domains resulting in higher total max throughput, and does not limit the number of nodes nor geographical coverage
  Can connect different type Ethernet since it is a store and forward device
  Transparent: no need for any change to hosts LAN adapters

## Slide 35: Bridges: frame filtering, forwarding
Bridges filter packets
  Same-LAN -segment frames not forwarded onto other LAN segments
Forwarding:
  How to know which LAN segment on which to forward frame?
  Looks like a routing problem (more shortly!)

## Slide 36: Backbone Bridge

## Slide 37: Interconnection Without Backbone
Not recommended for two reasons:
  - Single point of failure at Computer Science hub
  - All traffic between EE and SE must path over CS segment

## Slide 38: Bridge Filtering - 1
Bridges learn which hosts can be reached through which interfaces: maintain filtering tables
  when frame received, bridge “learns” location of sender: incoming LAN segment
  records sender location in filtering table
Filtering table entry:
  (Node LAN Address, Bridge Interface, Time Stamp)
  stale entries in Filtering Table dropped (TTL can be 60 minutes)

## Slide 39: Bridge Filtering - 2
Filtering procedure:
  if destination is on LAN on which frame was received
    then drop the frame
    else { lookup filtering table
    if entry found for destination
        then forward the frame on interface indicated;
        else flood; /* forward on all but the interface on which the frame arrived*/
      }

## Slide 40: Bridge Learning: example - 1
Suppose C sends frame to D and D replies back with frame to C
C sends frame, bridge has no info about D, so floods to both LANs
  bridge notes that C is on port 1
  frame ignored on upper LAN
  frame received by D

## Slide 41: Bridge Learning: example - 2
D generates reply to C, sends
  bridge sees frame from D
  bridge notes that D is on interface 2
  bridge knows C on interface 1, so selectively forwards frame out via interface 1

## Slide 42: Bridges Spanning Tree
For increased reliability, desirable to have redundant, alternate paths from source to dest
With multiple simultaneous paths, cycles result - bridges may multiply and forward frame forever
Solution: organize bridges in a spanning tree by disabling subset of interfaces
Disabled

## Slide 43: WWF Bridges vs. Routers
Both store-and-forward devices
  routers: network layer devices (examine network layer headers)
  bridges are Link Layer devices
Routers maintain routing tables, implement routing algorithms
Bridges maintain filtering tables, implement filtering, learning and spanning tree algorithms

## Slide 44: Routers vs. Bridges - 1
Bridges + and -
+ Bridge operation is simpler requiring less processing bandwidth
- Topologies are restricted with bridges: a spanning tree must be built to avoid cycles
- Bridges do not offer protection from broadcast storms (endless broadcasting by a host will be forwarded by a bridge)

## Slide 45: Routers vs. Bridges - 2
Routers + and -
+ arbitrary topologies can be supported, cycling is limited by TTL counters (and good routing protocols)
+ provide firewall protection against broadcast storms
- require IP address configuration (not plug and play)
- require higher processing bandwidth
Bridges do well in small (few hundred hosts) while routers used in large networks (thousands of hosts)