## Slide 1: Internet and Stuff:The Basics
What is the Internet?
What does it consist of?
Main terminology and lingo
Fundamental Concepts
Re-using some slides from Kurose and Ross book

## Slide 2: The Internet
A network of networks
Hierarchical structure
  Multiple possible levels
  Two official levels
    Intra-domain: within an Autonomous System (AS)
    Inter-domain: between Autonomous Systems
    AS: autonomously administered part of the Internet
    ASes are identified by their AS number

## Slide 3: Visualizing the Internet
millions of connected computing devices: hosts, end-systems
  pc’s workstations, servers
  PDA’s phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
routers: forward packets (chunks) of data thru network
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 4: “Cool” Internet Appliances
IP picture frame
http://www.ceiva.com/
Web-enabled toaster+weather forecaster
http://dancing-man.com/robin/toasty/

## Slide 5: Some Internet Lingo
A packet switched best effort network
TCP or Transmission Control Protocol:
  Communication between end-points
IP or Internet Protocol:
  How things are routed
Packets are similar to postal letters
  From, to, content
  Postman handles all packets similarly
  Addressing is hierarchical
IETF: Internet Engineering Task Force: the body
RFC: Request For Comments: (pseudo)-standards

## Slide 6: What’s a protocol?
The definition of a behavior
Here: the format of a communication exchange:
Sequence of actions, format of information, predefined interpretation
Hi
Hi
Got the
time?
2:00
TCP connection
req.
TCP connection
reply.
Get http://gaia.cs.umass.edu/index.htm
<file>
time

## Slide 7: Faloutsos’ Golden Rules of Networking
Nothing is absolute in networks research
This applies for the first rule
There are no complicated concepts, just obscure jargon

## Slide 8: Centralised versus Distributed Protocols
Centralised: all information is collected in one place and then processed
Distributed: decisions are taken locally with partial or summary of the information

## Slide 9: The Principles of the Internet
Goal: Interconnect existing net technologies
  ARPA packet radio, and ARPANET
  Packet switching? Felxibility
  Trade-off: poorer non-guaranteed performance
“The Design Philosophy of The DARPA Internet Protocols”, David Clark, MIT.

## Slide 10: Secondary Internet Principles
Fault-tolerance to component failures
Support multiple types of services
Interoperate with different technologies
Allow distributed management
Be cost effective (ie sharing)
Be easily extendible
Resources and entities must be accountable (for security purpose)

## Slide 11: Internet Architecture Characteristics
Scalability to millions of users
  Hierarchical structure combined with address aggregation
  Stateless routing: Routers do not keep detailed info per connection
Best-effort service: no guarantees
Decentralized control
Self-configuration

## Slide 12: Internet protocol stack
application: supporting network applications
  ftp, smtp, http
transport: host-host data transfer
  tcp, udp
network: routing of datagrams from source to destination
  ip, routing protocols
link: data transfer between neighboring network elements
  ppp, ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 13: Roles of Layers
application: support application
  HTTP, ftp,
transport: end-to-end issues
  TCP, UDP
network: pick the route (delays, QoS)
  OSPF, BGP, PIM
link: given a link transfer a packet
  Ethernet, PPP
physical: bits “on the wire”, ie. Voltage modulation
application
transport
network
link
physical
Notes: This is were we stopped 2006

## Slide 14: Basic Routing Concepts
Packet = postal letter
Router receives packet
Needs to decide which link to send it to
Scalability: decide on local information
Routers keep “summary” of information
Exploit the hierarchy in the IP address

## Slide 15: IP Addresses
IPv4 addresses have 32 bits: 4 octets of bits
  128.32.101.5 is an IP address (32 bits)
An IP prefix is a group of IP addresses
  128.32.0.0/16 is a prefix of the first 16 bits
  = 128.32.0.0 – 128.32.255.255 (2^16 addresses)
  128.32.4.0/24 is a longer prefix 24 bits
Routing: find the longest match:
  IP prefix in table that matches most bits of the address

## Slide 16: Types of Communications
Circuit Switching (reserve a slice of resources)
  Frequency division multiplexing
  Time division multiplexing
Packet switching
  Virtual Circuits: routers keep per connection info
  Datagrams: no per conn. Information
    Connection oriented (state at end points, handshake - TCP)
    Connectionless (no state at end points - UDP)

## Slide 17: Types of Communications
Advantage of packet switching:
  Resource sharing
  No need for reservations
  Easier to implement distributedly
Advantage of circuit switching:
  Can guarantee performance (Quality of Service)

## Slide 18: In more detail…

## Slide 19: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 20: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 21: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 22: Circuit Switching: FDMA and TDMA
FDMA
frequency
time
TDMA
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 23: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed,
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  transmit over link
  wait turn at next link
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 24: Network Core: Packet Switching
Packet-switching versus circuit switching: postal service versus telephone or FAX service
A
B
C
10 Mbs
Ethernet
1.5 Mbs
45 Mbs
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 25: Packet switching versus circuit switching
1 Mbit link
each user:
  100Kbps when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less than .0004
Packet switching allows more users to use network!
N users
1 Mbps link

## Slide 26: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (see QoS, multimedia)
Is packet switching a “slam dunk winner?”

## Slide 27: Classification of the Types of Communication
Things are more fuzzy in practice
Circuit Switching
Packet Switching
Datagrams
(IP)
Virtual Circuits
(ATM)
Connectionless
(UDP, endpoints
don’t keep- much state)
Connection-
Oriented
(TCP, end points
Keep state)
(no per flow
State in routers)
(per flow state
in routers -
resource
reservation)
Dedicated
hardware
Dedicated
Shared
hardware
Time
Division
Multiplexing
Frequency
Division
Multiplexing

## Slide 28: Packet-switched networks: routing
Goal: move packets among routers from source to destination
  we’ll study several path selection algorithms (chapter 4)
datagram network:
  destination address determines next hop
  routes may change during session
  analogy: driving, asking directions
virtual circuit network:
  each packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time, remains fixed thru call
  routers maintain per-call state

## Slide 29: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 30: Institutional access: local area networks
company/univ local area network (LAN) connects end system to edge router
Ethernet:
  shared or dedicated cable connects end system and router
  10 Mbs, 100Mbps, Gigabit Ethernet
deployment: institutions, home LANs happening now

## Slide 31: Wireless access networks
shared wireless access network connects end system to router
wireless LANs:
  radio spectrum replaces wire
  Commonly used link layer IEEE 802.11
base
station
mobile
hosts
router

## Slide 32: Home networks
Typical home network components:
ADSL or cable modem
router/firewall
Ethernet
wireless access
point
wireless
access
point
wireless
laptops
router/
firewall
cable
modem
to/from
cable
headend
Ethernet
(switched)

## Slide 33: Performance Issues

## Slide 34: Delay in packet-switched networks
packets experience delay on end-to-end path
four sources of delay at each hop
nodal processing:
  check bit errors
  determine output link
queueing
  time waiting at output link for transmission
  depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing

## Slide 35: Delay in packet-switched networks
Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 36: Queueing delay
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 37: Network Core: Packet Switching
Packet-switching:
store and forward behavior
break message into smaller chunks: “packets”
Store-and-forward: switch waits until chunk has completely arrived, then forwards/routes
Q: what if message was sent as single unit?

## Slide 38: Small versus large packets
Big Packet 2 Mbits
Small packets: 2Mb/5000 = 400bits
Transmission delay: 400bits/sec
Transmission delay over one link:
  Small: 1 sec
  Big: 5000 sec
To go over 3 links:
  Small 5004 sec
  Big 3 x 5000 = 15000 sec!
Why the difference: parallelism!

## Slide 39: Why layering?
Dealing with complex systems:
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
Isolating “functions” and interactions components
  layered reference model for discussion
layering considered harmful?

## Slide 40: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Each layer:
distributed
“entities” implement layer functions at each node
entities perform actions, exchange messages with peers

## Slide 41: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
take data from app
add addressing, reliability check info to form “datagram”
send datagram to peer
wait for peer to ack receipt
analogy: post office
data
transport
transport
ack

## Slide 42: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 43: Protocol layering and data
Each layer takes data from above
adds header information to create new data unit
passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
message
segment
datagram
frame

## Slide 44: Internet structure: network of networks
roughly hierarchical
national/international backbone providers (NBPs)
  e.g. BBN/GTE, Sprint, AT&T, IBM, UUNet
  interconnect (peer) with each other privately, or at public Network Access Point (NAPs)
regional ISPs
  connect into NBPs
local ISP, company
  connect into regional ISPs
NBP A
NBP B
NAP
NAP
regional ISP
regional ISP
local
ISP
local
ISP

## Slide 45: National Backbone Provider
e.g. Sprint US backbone network

## Slide 46: Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet demonstrated publicly
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 47: Internet History
1970: ALOHAnet satellite network in Hawaii
  Faloutsos is born 26 May ‘70
1973: Metcalfe’s PhD thesis proposes Ethernet
1974: Cerf and Kahn - architecture for interconnecting networks
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 48: Internet History
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 49: Internet History
Early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: WWW
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, http: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the WWW
Late 1990’s:
est. 50 million computers on Internet
est. 100 million+ users
backbone links running at 1 Gbps
1990’s: commercialization, the WWW

## Slide 50: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
performance: loss, delay
layering and service models
backbones, NAPs, ISPs
history
You now have:
context, overview, “feel” of networking
more depth, detail later in course