## Slide 1: Internet and Stuff
What is Internet?
What does it consist of?
Main terminology and lingo
Fundamental Concepts
Re-using slides from Kurose and Ross

## Slide 2: The Internet
A network of networks
Hierarchical structure
  Multiple possible levels
  Two official levels
    Intra-domain: within an Autonomous System (AS)
    Inter-domain: between Autonomous Systems
    AS: autonomously administered part of the Internet
    ASes are identified by their AS number

## Slide 3: Visualizing the Internet
millions of connected computing devices: hosts, end-systems
  pc’s workstations, servers
  PDA’s phones, toasters
  running network apps
communication links
  fiber, copper, radio, satellite
routers: forward packets (chunks) of data thru network
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 4: “Cool” internet appliances
World’s smallest web server
http://www-ccs.cs.umass.edu/~shri/iPic.html
IP picture frame
http://www.ceiva.com/
Web-enabled toaster+weather forecaster
http://dancing-man.com/robin/toasty/

## Slide 5: Some Internet Lingo
A packet switched best effort network
TCP or Transmission Control Protocol:
  Communication between end-points
IP or Internet Protocol:
  How things are routed
Packets are similar to postal letters
  From, to, content
  Postman handles all packets the similarly
  Addressing is hierarchical
IETF: Internet Engineering Task Force: the body
RFC: Request For Comments: (pseudo)-standards

## Slide 6: What’s a protocol?
The definition of a behavior
Here: the format of a communication exchange:
Sequence of actions, format of information, predefined interpretation
Hi
Hi
Got the
time?
2:00
TCP connection
req.
TCP connection
reply.
Get http://gaia.cs.umass.edu/index.htm
<file>
time

## Slide 7: Golden Rules of Networking
Nothing is absolute in networks research
This applies for first rule
There are no complicated concepts, just obscure jargon

## Slide 8: Centralised versus Distributed Protocols
Centralised: all information is collected in one place and then processed
Distributed: decisions are taken locally with partial or summary of the information

## Slide 9: The Principle of the Internet
Interconnect existing net technologies
  ARPA packet radio, and ARPANET
  Packet switching? Felxibility
  Trade-off: poorer non-guaranteed performance
“The Desing Philosophy of The DARPA Internet Protocols”, David Clark, MIT.

## Slide 10: Secondary Internet Principles
Fault-tolerance to component failures
Support multiple types of services
Interoperate with different technologies
Allow distributed management
Be cost effective (ie sharing)
Be easily extendible
Resources and entities must be accountable (for security purpose)

## Slide 11: Internet Architecture Characteristics
Scalabbility to millions of users
  Stateless routing: Routers cannot keep detailed info per connection
Best-effort service: no guarantees
Decentralized control
Self-configuration

## Slide 12: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 13: Organization of air travel: a different view
Layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 14: Internet protocol stack
application: supporting network applications
  ftp, smtp, http
transport: host-host data transfer
  tcp, udp
network: routing of datagrams from source to destination
  ip, routing protocols
link: data transfer between neighboring network elements
  ppp, ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 15: Roles of Layers
application: support application
transport: end-to-end issues
network: pick the route (delays, QoS)
link: given a link transfer a packet
physical: bits “on the wire”, ie. Voltage modulation
application
transport
network
link
physical

## Slide 16: Types of Communications
Circuit Switching (reserve a slice of resources)
  Frequency division multiplexing
  Time division multiplexing
Packet switching
  Virtual Circuits: routers keep per connection info
  Datagrams: no per conn. Information
    Connection oriented (state at end points, handshake - TCP)
    Connectionless (no state at end points - UDP)

## Slide 17: Types of Communications
Advantage of packet switching:
  Resource sharing
  No need for reservations
  Easier to implement distributedly
Advantage of circuit switching:
  Can guarantee performance (Quality of Service)

## Slide 18: Basic Routing Concepts
Packet = postal letter
Router receives packet
Needs to decide which link to send it to
Scabality: decide on local information
Routers keep “summmary” of information
Exploit the hiearchy in the IP address

## Slide 19: IP Addresses
IPv4 addresses have 32 bits: 4 octets of bits
  128.32.101.5 is an IP address (32 bits)
An IP prefix is a group of IP addresses
  128.32.0.0/16 is a prefix of the first 16 bits
  = 128.32.0.0 – 128.32.255.255 (2^16 addresses)
  128.32.4.0/24 is a longer prefix 24 bits
Routing: find the longest match:
  IP prefix in table that matches most bits of the address

## Slide 20: A

## Slide 22: Part I: Introduction
Our goal:
get context, overview, “feel” of networking
more depth, detail later in course
approach:
  descriptive
  use Internet as example
Overview:
what’s the Internet
what’s a protocol?
network edge
network core
access net, physical media
performance: loss, delay
protocol layers, service models
backbones, NAPs, ISPs
history
Assignment: read
chapter 1 in text

## Slide 23: What’s the Internet: “nuts and bolts” view
protocols: control sending, receiving of msgs
  e.g., TCP, IP, HTTP, FTP, PPP
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
local ISP
company
network
regional ISP
router
workstation
server
mobile

## Slide 24: What’s the Internet: a service view
communication infrastructure enables distributed applications:
  WWW, email, games, e-commerce, database., voting, file (MP3) sharing
communication services provided:
  connectionless
  connection-oriented
cyberspace [Gibson]:
  “a consensual hallucination experienced daily by billions of operators, in every nation, ...."

## Slide 25: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 26: A closer look at network structure:
network edge: applications and hosts
network core:
  routers
  network of networks
access networks, physical media: communication links

## Slide 27: The network edge:
end systems (hosts):
  run application programs
  e.g., WWW, email
  at “edge of network”
client/server model
  client host requests, receives service from server
  e.g., WWW client (browser)/ server; email client/server
peer-peer model:
  host interaction symmetric
  e.g.: Gnutella, KaZaA

## Slide 28: Network edge: connection-oriented service
Goal: data transfer between end sys.
handshaking: setup (prepare for) data transfer ahead of time
  Hello, hello back human protocol
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
reliable, in-order byte-stream data transfer
  loss: acknowledgements and retransmissions
flow control:
  sender won’t overwhelm receiver
congestion control:
  senders “slow down sending rate” when network congested

## Slide 29: Network edge: connectionless service
Goal: data transfer between end systems
  same as before!
UDP - User Datagram Protocol [RFC 768]: Internet’s connectionless service
  unreliable data transfer
  no flow control
  no congestion control
App’s using TCP:
HTTP (WWW), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
streaming media, teleconferencing, Internet telephony

## Slide 30: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 31: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 32: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 33: Circuit Switching: TDMA and TDMA
FDMA
frequency
time
TDMA
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 34: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed,
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  transmit over link
  wait turn at next link
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 35: Network Core: Packet Switching
Packet-switching versus circuit switching: human restaurant analogy
other human analogies?
A
B
C
10 Mbs
Ethernet
1.5 Mbs
45 Mbs
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 36: Network Core: Packet Switching
Packet-switching:
store and forward behavior
break message into smaller chunks: “packets”
Store-and-forward: switch waits until chunk has completely arrived, then forwards/routes
Q: what if message was sent as single unit?

## Slide 37: Packet switching versus circuit switching
1 Mbit link
each user:
  100Kbps when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less than .0004
Packet switching allows more users to use network!
N users
1 Mbps link

## Slide 38: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 6)
Is packet switching a “slam dunk winner?”

## Slide 39: Packet-switched networks: routing
Goal: move packets among routers from source to destination
  we’ll study several path selection algorithms (chapter 4)
datagram network:
  destination address determines next hop
  routes may change during session
  analogy: driving, asking directions
virtual circuit network:
  each packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time, remains fixed thru call
  routers maintain per-call state

## Slide 40: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 41: Residential access: point to point access
Dialup via modem
  up to 56Kbps direct access to router (conceptually)
ISDN: integrated services digital network: 128Kbps all-digital connect to router
ADSL: asymmetric digital subscriber line
  up to 1 Mbps home-to-router
  up to 8 Mbps router-to-home
  ADSL deployment: happening

## Slide 42: Residential access: cable modems
HFC: hybrid fiber coax
  asymmetric: up to 10Mbps upstream, 1 Mbps downstream
network of cable and fiber attaches homes to ISP router
  shared access to router among home
  issues: congestion, dimensioning
deployment: available via cable companies, e.g., MediaOne

## Slide 43: Residential access: cable modems
Diagram: http://www.cabledatacomnews.com/cmic/diagram.html

## Slide 44: Institutional access: local area networks
company/univ local area network (LAN) connects end system to edge router
Ethernet:
  shared or dedicated cable connects end system and router
  10 Mbs, 100Mbps, Gigabit Ethernet
deployment: institutions, home LANs happening now
LANs: chapter 5

## Slide 45: Wireless access networks
shared wireless access network connects end system to router
wireless LANs:
  radio spectrum replaces wire
  e.g., Lucent Wavelan 11 Mbps
wider-area wireless access
  CDPD: wireless access to ISP router via cellular network
base
station
mobile
hosts
router

## Slide 46: Home networks
Typical home network components:
ADSL or cable modem
router/firewall
Ethernet
wireless access
point
wireless
access
point
wireless
laptops
router/
firewall
cable
modem
to/from
cable
headend
Ethernet
(switched)

## Slide 47: Physical Media
physical link: transmitted data bit propagates across link
guided media:
  signals propagate in solid media: copper, fiber
unguided media:
  signals propagate freely, e.g., radio
Twisted Pair (TP)
two insulated copper wires
  Category 3: traditional phone wires, 10 Mbps Ethernet
  Category 5 TP: 100Mbps Ethernet

## Slide 48: Physical Media: coax, fiber
Coaxial cable:
wire (signal carrier) within a wire (shield)
  baseband: single channel on cable
  broadband: multiple channel on cable
bidirectional
common use in 10Mbs Ethernet
Fiber optic cable:
glass fiber carrying light pulses
high-speed operation:
  100Mbps Ethernet
  high-speed point-to-point transmission (e.g., 5 Gps)
low error rate

## Slide 49: Physical media: radio
signal carried in electromagnetic spectrum
no physical “wire”
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
Radio link types:
microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WaveLAN)
  2Mbps, 11Mbps
wide-area (e.g., cellular)
  e.g. CDPD, 10’s Kbps
satellite
  up to 50Mbps channel (or multiple smaller channels)
  270 Msec end-end delay
  geosynchronous versus LEOS

## Slide 50: Delay in packet-switched networks
packets experience delay on end-to-end path
four sources of delay at each hop
nodal processing:
  check bit errors
  determine output link
queueing
  time waiting at output link for transmission
  depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing

## Slide 51: Delay in packet-switched networks
Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 52: Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 53: “Real” Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: routers, rt delays on source-dest path
also: pingplotter, various windows programs

## Slide 54: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 55: Layered air travel: services
Counter-to-counter delivery of person+bags
baggage-claim-to-baggage-claim delivery
people transfer: loading gate to arrival gate
runway-to-runway delivery of plane
airplane routing from source to destination

## Slide 56: Distributed implementation of layer functionality
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Departing airport
arriving airport
intermediate air traffic sites
airplane routing
airplane routing

## Slide 57: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 58: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Each layer:
distributed
“entities” implement layer functions at each node
entities perform actions, exchange messages with peers

## Slide 59: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
take data from app
add addressing, reliability check info to form “datagram”
send datagram to peer
wait for peer to ack receipt
analogy: post office
data
transport
transport
ack

## Slide 60: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 61: Protocol layering and data
Each layer takes data from above
adds header information to create new data unit
passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
message
segment
datagram
frame

## Slide 62: Internet structure: network of networks
roughly hierarchical
national/international backbone providers (NBPs)
  e.g. BBN/GTE, Sprint, AT&T, IBM, UUNet
  interconnect (peer) with each other privately, or at public Network Access Point (NAPs)
regional ISPs
  connect into NBPs
local ISP, company
  connect into regional ISPs
NBP A
NBP B
NAP
NAP
regional ISP
regional ISP
local
ISP
local
ISP

## Slide 63: National Backbone Provider
e.g. Sprint US backbone network

## Slide 64: Internet History
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Research Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet demonstrated publicly
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 65: Internet History
1970: ALOHAnet satellite network in Hawaii
1973: Metcalfe’s PhD thesis proposes Ethernet
1974: Cerf and Kahn - architecture for interconnecting networks
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets

## Slide 66: Internet History
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks

## Slide 67: Internet History
Early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: WWW
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, http: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the WWW
Late 1990’s:
est. 50 million computers on Internet
est. 100 million+ users
backbone links running at 1 Gbps
1990’s: commercialization, the WWW

## Slide 68: Introduction: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
performance: loss, delay
layering and service models
backbones, NAPs, ISPs
history
You now have:
context, overview, “feel” of networking
more depth, detail later in course