## Slide 1: Internet Multicasting
Copyright M. Faloutsos

## Slide 3: The Multicast Problem
U. of Toronto
2
Michalis Faloutsos
GIVEN: Network
GIVEN: User Requests (and quality requirements)
ESTABLISH: Efficient distribution trees
?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: What is The Need for Multicasting?
Use bandwidth efficiently
  Duplicate packets only when necessary
Simply put:
  Some links can not support multiple flows of the same data
3 times the
traffic

## Slide 5: What Is Efficient?
Scalable
  Multicast state
  Number of control messages
Use network bandwidth efficiently
Meet end-to-end performance requirements
  E2e Delay: from source to destinations

## Slide 6: Some Theory on Multicast Routing

## Slide 7: Multicast Routing Algorithms
U. of Toronto
4
Michalis Faloutsos
NP-complete problem [Dreyfus72]
Related to the Steiner tree problem
Approximation algorithms have practical interest
Shortest Paths
Greedy
Optimal
source
destinations
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: A Greedy Variation
Known as KMB [Kou Markowski Berman 81]
Greedy: connect to nearest point on the tree
KMB: connect to nearest group member
Seemingly: KMB is less efficient that Greedy
Surprisingly: KMB is just as efficient!

## Slide 9: Multicast Bounds
Bounds for Greedy and Sh. Paths w.r.t.:
  Maximum asymmetry: A
  Number of join requests: M
  Competitive Ratio of tree cost: Algorithm/Optimal
Problem Variations:
  Static: members know ahead of time
  Join-Only: members join randomly
  Join-Leave: members join and leave randomly
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Performance of Algorithms
Shortest Path: tighlty bounded by M
  Where M the number of destinations
Greedy and KMB:
  Static: bounded by 2
  Join-only: log M
  Join-leave: 2^M (or N)

## Slide 11: Multicasting on Directed Graphs
U. of Toronto
7
Michalis Faloutsos
Real Networks: Directed
Maximum Asymmetry:
  A = max(e(v,w)/e(w,v))
FIND Min. Cost Tree
Joint work: R. Pankaj, K.C. Sevcik
c
Ac
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Overview of Theoretical Results
U. of Toronto
9
Michalis Faloutsos
Short. Paths:
  tight bound in all variations
Greedy:
  Static: Tight bound
  Join-Only: Near-optimal online bound
  Join-Leave: Large lower bound
[Faloutsos et al SIROCCO’97]
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Our Results in Detail
U. of Toronto
10
Michalis Faloutsos
Lower bound for any online algorithm
Greedy at most log(M) to any online algorithm
Join-Only:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Our Results: Graphical Overview
U. of Toronto
11
Michalis Faloutsos
Static and Join-only:
  Greedy is good (near-optimal)
Join-leave:
  Greedy bad in worst case
Why not combine into an adaptive algorithm?
2A
M
A,2^M
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15
U. of Toronto
13
Michalis Faloutsos
“This is just not effective…We need to get some chains”
The Far Side -- G. Larson
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Desirable Protocol Properties
15
Michalis Faloutsos
Scalable
Easy to implement and deploy
Provide high QoS
Use network resources efficiently
  Create efficient trees
  Use little bandwidth
  Minimize required state
Adaptive - Flexible
Notes: <number>
<footer>
<header>
<date/time>
15
Limit pre-configuration needs
Robustness
Loop freedom

## Slide 17: Internet Multicasting: Protocols

## Slide 18: Breaking the Rules
Internet: no state per flow
Multicasting has state per each multicast group!

## Slide 19: What Are The Issues?
Routing
  Intra-domain
  Inter-domain
Reliable multicasting
Secure multicasting
Address space allocation
Multicast state aggregation
Modeling and Simulating: realistic models

## Slide 20: What Is The Real Issue
ISPs do not want/care to deploy multicast
Chicken and egg problem
  Customers do not ask for multicasting,
  because there are no multicast applications,
  because there is no support for multicasting
Multicast researchers:
  Be careful on what topic you choose

## Slide 21: MBone: The multicast backbone
Some routers are multicast enabled
These routers connect to each other with virtual edges (encapsulation)
Mutlicast protocols and applications can be deployed on the MBone

## Slide 22: Multicast Routing
Router Assisted: routers duplicate packets
  DVMRP: flood and prune
  PIM/CBT: core based, shared tree
  Source Specific Multicast: each source creates a tree
  QoS aware protocols: QoSMIC, QMRP
Application-level
  Only end-points (members) are aware of the tree
  Packets are duplicated at the members only!

## Slide 23: The PIM Protocol
More deployed protocol
Based on a Core – Rendez-vous Point
Based on Shortest Path Routing
Issue: selecting the core
Not adaptive
New
source
core

## Slide 24: Border Gateway Multicast Protocol
16
Michalis Faloutsos
Designed to be interdomain
Border Gateway Multicast Protocol [Thaler 97]
  Reverse Shortest Paths Routing
  Domains “own” multicast addresses
New
Shortest Path
source
Notes: <number>
<footer>
<header>
<date/time>
16
Superceeded: PIM [Estrin 96], CBT [Ballarardie 93]

## Slide 25: Yet Another Multicast Protocol: YAM
U. of Toronto
17
Michalis Faloutsos
Yet Another Multicast protocol [Carlberg97]
Multiple paths
Use of static information
Non scalable:
  “flood” of control messages
New
Notes: <number>
<footer>
<header>
<date/time>
17
Superceeded: PIM [Estrin 96], CBT [Ballarardie 93]

## Slide 26: Our Protocol: QoSMIC
18
Michalis Faloutsos
QoS Multicast Internet protoCol [SIGCOMM’98]
Supports QoS
Uses dynamic information
Scalable
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: QoSMIC: The Overview
U. of Toronto
19
Michalis Faloutsos
Manager Router
1. Search: for Candidates
2. Bid: Candidates “Bid”
3. Select: New chooses path
  using dynamic QoS info.
Joint work with A. Banerjea, R. Pankaj
Manager
New
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: QoSMIC: Search and Bid
U. of Toronto
20
Michalis Faloutsos
I. Local Search (costly)
II. Multicast Tree Search
Bid messages collect dynamic information
Manager
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29: QoSMIC: Flexible-Adaptable
U. of Toronto
21
Michalis Faloutsos
In Searching:
  Local and/or M. Tree Search
In Routing:
  Greedy and/or Short. Paths
In run time according to application needs
Manager
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Some Simulations
U. of Toronto
24
Michalis Faloutsos
Compare routing efficiency with BGMP
  Tree cost = Sum of link-weights
Compare message complexity with YAM
  Number of control messages of search phase
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: The Simulation Set-up
U. of Toronto
25
Michalis Faloutsos
Build a simulator
Real Graph: Major Internet routers [Casner93]
Weighted asymmetric graph
Simulation Precision:
  95%-confidence interval <10% of shown values
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: The Simulated Algorithms
U. of Toronto
26
Michalis Faloutsos
Offline: greedy for reference
SP: Shortest Paths
BGMP: Reverse Shortest Paths
QoSMIC
Notes: <number>
<footer>
<header>
<date/time>

## Slide 33: Tree Cost Vs Group Size
U. of Toronto
27
Michalis Faloutsos
QoSMIC up to 40% better than BGMP
Asym = 10
Notes: <number>
<footer>
<header>
<date/time>
27

## Slide 34: Tree Cost Vs Asymmetry
U. of Toronto
28
Michalis Faloutsos
QoSMIC up to 60% better than BGMP
Notes: <number>
<footer>
<header>
<date/time>
28

## Slide 35: Joinning Distance Distribution
U. of Toronto
29
Michalis Faloutsos
Even small Local Search is good (2 h - 55% joins)
Large Local Search (8 h) to cover for ALL cases
Group Density:
1-15 %
Notes: <number>
<footer>
<header>
<date/time>
29

## Slide 36: Search Message Complexity
U. of Toronto
30
Michalis Faloutsos
YAM has to have large Local Search
QoSMIC can keep LS small  scalable
Over-estimate of both protocols
Notes: <number>
<footer>
<header>
<date/time>

## Slide 37: QoSMIC: The Claim
U. of Toronto
23
Michalis Faloutsos
<< QoSMIC routes in a QoS-sensitive way,
and is more efficient even than the
non QoS-sensitive protocols >>
Notes: <number>
<footer>
<header>
<date/time>

## Slide 38: Why Isn’t QoSMIC the Standard?
Implementation complexity
Scalability and message complexity
Needs industry and IETF support
Timeliness:
  Now people look at other issues

## Slide 39: Generalizing QoSMIC
QoSMIC as a set of searching procedures
  Local flooding
  Indirect search
A mechanism to search for points of interest
  Servers, caches etc
Possible applications
  Web server location
  Ad-hoc networks: searching for a destination

## Slide 41: QoSMIC: More QoS support
U. of Toronto
22
Michalis Faloutsos
Multiple sources per group
Connect directly to the source to improve end-to-end QoS
source-1
source-2
s-1 only
stop s-1
source-1
source-2
Notes: <number>
<footer>
<header>
<date/time>