## Slide 1: Multimedia and Quality of Service

## Slide 2: Chapter 6: Multimedia Networking
Chapter goals:
understand service requirements for multimedia networking
  delay
  bandwidth
  loss
learn about how to make the best of the best-effort Internet
learn about how the Internet might evolve to better support multimedia
Chapter Overview:
multimedia networking apps
streaming stored audio and video
  RTSP
interactive real-time apps
  Internet phone example
RTP
H.323 and SIP
beyond best effort
  scheduling and policing
  integrated services
  differentiated services

## Slide 3: Multimedia in Networks
Fundamental characteristics:
Typically delay sensitive delay.
But loss tolerant: infrequent losses cause minor glitches that can be concealed.
Antithesis of data (programs, banking info, etc.), which are loss intolerant but delay tolerant.
Multimedia is also called “continuous media”
Classes of MM applications:
Streaming stored audio and video
Streaming live audio and video
Real-time interactive video

## Slide 4: Multimedia And Streaming Requirements
Streaming stored MM
Clients request audio/video files from servers and pipeline reception over the network and display
Interactive: user can control operation (similar to VCR: pause, resume, fast forward, rewind, etc.)
Delay: from client request until display start can be 1 to 10 seconds

## Slide 5: Realtime Requirements
Unidirectional Real-Time:
similar to existing TV and radio stations, but delivery over the Internet (stock quotes)
Non-interactive, just listen/view
Interactive Real-Time :
Phone or video conference
More stringent requirements
Video: < 150 msec acceptable
Audio: < 150 msec good, <400 msec acceptable
Loss < 10%
Delay Jitter < 50msec

## Slide 6: The Challenge of Multimedia
Internet is best effort
  No guarantees on delay
  Packets can be lost and reordered
  Performance is not predictable

## Slide 7: Making the best of best effort
To mitigate impact of “best-effort” Internet:
Use UDP to avoid TCP and its slow-start phase…
Buffer content at client to aleviate jitter
We can timestamp packets, so that receiver knows when the packets should be played back.
Adapt compression level to available bandwidth
We can send redundant packets to mitigate the effects of packet loss.

## Slide 8: How should the Internet evolve to better support multimedia?
Integrated services philosophy:
Change Internet protocols so that applications can reserve end-to-end bandwidth
  Need to deploy protocol that reserves bandwidth
  Must modify scheduling policies in routers to honor reservations
  Application must provide the network with a description of its traffic, and must further abide to this description.
Requires new, complex software in hosts & routers
Differentiated services philosophy:
Fewer changes to Internet infrastructure, yet provide 1st and 2nd class service.
Datagrams are marked.
User pays more to send/receive 1st class packets.
ISPs pay more to backbones to send/receive 1st class packets.

## Slide 9: To Control or not to Control?
Laissez-faire philosophy
No reservations, no datagram marking
As demand increases, provision more bandwidth
Place stored content at edge of network:
  ISPs & backbones add caches
  Content providers put content in CDN nodes
  P2P: choose nearby peer with content
Virtual private networks (VPNs)
Reserve permanent blocks of bandwidth for enterprises.
Routers distinguish VPN traffic using IP addresses
Routers use special scheduling policies to provide reserved bandwidth.

## Slide 10: Streaming Stored Audio & Video
Streaming stored media:
Audio/video file is stored in a server
Users request audio/video file on demand.
Audio/video is rendered within, say, 10 s after request.
Interactivity (pause, re-positioning, etc.) is allowed.
Media player:
  removes jitter
  decompresses
  error correction
  graphical user interface with controls for interactivity
Plug-ins may be used to imbed the media player into the browser window.

## Slide 11: Streaming from Web server (1)
Audio and video files stored in Web servers
naïve approach
browser requests file with HTTP request message
Web server sends file in HTTP response message
content-type header line indicates an audio/video encoding
browser launches media player, and passes file to media player
media player renders file
Major drawback: media player interacts with server through intermediary of a Web browser

## Slide 12: Streaming from Web server (2)
Alternative: set up connection between server and player
Web browser requests and receives a meta file (a file describing the object) instead of receiving the file itself;
Content-type header indicates specific audio/video application
Browser launches media player and passes it the meta file
Player sets up a TCP connection with server and sends HTTP request.
Some concerns:
Media player communicates over HTTP, which is not designed with pause, ff, rwnd commands
May want to stream over UDP

## Slide 13: Streaming from a streaming server
This architecture allows for non-HTTP protocol between server and media player
Can also use UDP instead of TCP.

## Slide 14: Using a Jitter or Playback Buffer
Send at constant rate over UDP.
Buffer and delay playback for 1-10 s To mitigate the effects of jitter,.

## Slide 15: Real Time Streaming Protocol: RTSP
RTSP: RFC 2326
Client-server application layer protocol.
For user to control display: rewind, fast forward, pause, resume, repositioning, etc…
Why not use HTTP?
Designers of HTTP had fixed media in mind: HTML, images, applets, etc.
HTTP does not target stored continuous media (i.e., audio, video, SMIL presentations, etc.)

## Slide 16: Real Time Streaming Protocol: RTSP
What it doesn’t do:
does not define how audio/video is encapsulated for streaming over network
does not restrict how streamed media is transported; it can be transported over UDP or TCP
does not specify how the media player buffers audio/video
RealNetworks
Server and player use RTSP to send control info to each other

## Slide 17: Real-time interactive applications
PC-2-PC phone
PC-2-phone
  Dialpad
  Net2phone
videoconference
Webcams
Going to now look at a PC-2-PC Internet phone example in detail

## Slide 18: Internet phone over best-effort (1)
Best effort
packet delay, loss and jitter
Internet phone example
now examine how packet delay, loss and jitter are often handled in the context of an IP phone example.
Internet phone applications generate packets during talk spurts
bit rate is 64 kbps during talk spurt
during talk spurt, every 20 msec app generates a chunk of 160 bytes = 8 kbytes/sec * 20 msec
header is added to chunk; then chunk+header is encapsulated into a UDP packet and sent out
some packets can be lost and packet delay will fluctuate.
receiver must determine when to playback a chunk, and determine what do with missing chunk

## Slide 19: Internet phone (2)
packet loss
UDP segment is encapsulated in IP datagram
datagram may overflow a router queue
TCP can eliminate loss, but
  retransmissions add delay
  TCP congestion control limits transmission rate
Redundant packets can help
end-to-end delay
accumulation of transmission, propagation, and queuing delays
more than 400 msec of end-to-end delay seriously hinders interactivity; the smaller the better
delay jitter
consider two consecutive packets in talk spurt
initial spacing is 20 msec, but spacing at receiver can be more or less than 20 msec
removing jitter
sequence numbers
timestamps
delaying playout

## Slide 20: Internet phone (3): fixed playout delay
Receiver attempts to playout each chunk at exactly q msecs after the chunk is generated.
  If chunk is time stamped t, receiver plays out chunk at t+q .
  If chunk arrives after time t+q, receiver discards it.
Sequence numbers not necessary.
Strategy allows for lost packets.
Tradeoff for q:
  large q: less packet loss
  small q: better interactive experience

## Slide 21: Internet phone (4): fixed playout delay
Sender generates packets every 20 msec during talk spurt.
First packet received at time r
First playout schedule: begins at p
Second playout schedule: begins at p’

## Slide 22: Adaptive playout delay (1)
Estimate network delay and adjust playout delay at the beginning of each talk spurt.
Chunks still played out every 20 msec during talk spurt.

## Slide 23: Estimating the Delay
Dynamic estimate of average delay at receiver:
Use the exponential weighted moving average (again!)
where u is a fixed constant (e.g., u = .01).
Also useful to estimate the average deviation of the delay, vi :

## Slide 24: Adaptive playout delay for a talk spurt
The estimates di and vi are calculated for every received packet, although they are only used at the beginning of a talk spurt.
For first packet in talk spurt, playout time is:
where K is a positive constant. For this same packet, the play out delay is:
For packet j in the same talk spurt, play packet out at

## Slide 25: When does a Talk Spurt Begins?
If there were never loss, receiver could simply look at the successive time stamps.
  Difference of successive stamps > 20 msec, talk spurt begins.
But because loss is possible, receiver must look at both time stamps and sequence numbers.
  Difference of successive stamps > 20 msec and sequence numbers without gaps, talk spurt begins.

## Slide 26: Recovering From Loss
Loss happens
How can you deal with loss and move on with your life?
Loss: packet never arrives or arrives later than its scheduled play-out time

## Slide 27: Comment on Types of Losses
Packet loss vs partial loss (bit errors)
Typically in the Internet, we have packet loss
Partial loss is unlikely but not impossible (sigcomm 2000)

## Slide 28: Dealing With Loss
Redundancy is the answer
  Send more so that if something gets lost we are still ok
Issue; maximize improvement for given overhead
Important concept 1: data is loss tolerant
Important concept 2: target user perception

## Slide 29: Recovery from packet loss (1)
forward error correction (FEC): simple scheme
for every group of n chunks create a redundant chunk by exclusive OR-ing the n original chunks
send out n+1 chunks, increasing the bandwidth by factor 1/n.
can reconstruct the original n chunks if there is at most one lost chunk from the n+1 chunks
Playout delay needs to fixed to the time to receive all n+1 packets

## Slide 30: Recovery from packet loss (1)
What is the right value of n?
Tradeoff:
  increase n, less bandwidth waste
  increase n, longer playout delay
  increase n, higher probability that 2 or more chunks will be lost

## Slide 31: Recovery from packet loss (2)
2nd FEC scheme
“piggyback lower quality stream”
send lower resolution audio stream as the redundant information
for example, nominal stream PCM at 64 kbps and redundant stream GSM at 13 kbps.
Sender creates packet by taking the nth chunk from nominal stream and appending to it the (n-1)st chunk from redundant stream.
Whenever there is non-consecutive loss, the receiver can conceal the loss.
Only two packets need to be received before playback
Can also append (n-1)st and (n-2)nd low-bit rate chunk

## Slide 32: Losses: Let’s Ask the User
Consecutive loss is more noticeable and annoying to people
Many small glitches are better than one big black-out

## Slide 33: Recovery from packet loss (3)
Interleaving
Spread the effect of loss
chunks are broken up into smaller units
for example, 4 5 msec units per chunk
interleave the chunks as shown in diagram
packet now contains small units from different chunks
Reassemble chunks at receiver
if a packet is lost, still have most of every chunk

## Slide 34: Recovery from packet loss (4)
Receiver-based repair of damaged audio streams
produce a replacement for a lost packet that is similar to the original
can give good performance for low loss rates and small packets
simplest: repetition
more complicated: interpolation
  To smooth transition from previous and next frame

## Slide 35: Current Multimedia Protocols
RTP: Real-Time Protocol
RTCP: Real-Time Control Protocol
H.323: Protocol for establishing audio-video calls
  I.e. IP telephony

## Slide 36: Real-Time Protocol (RTP)
RTP specifies a packet structure for packets carrying audio and video data: RFC 1889.
RTP packet provides
  payload type identification
  packet sequence numbering
  timestamping
RTP runs in the end systems.
RTP packets are encapsulated in UDP segments
Interoperability: If two Internet phone applications run RTP, then they may be able to work together

## Slide 37: RTP runs on top of UDP
RTP libraries provide a transport-layer interface
that extend UDP:
  port numbers, IP addresses
  error checking across segment
  payload type identification
  packet sequence numbering
  time-stamping

## Slide 38: RTP Example
Consider sending 64 kbps PCM-encoded voice over RTP.
Application collects the encoded data in chunks, e.g., every 20 msec = 160 bytes in a chunk.
The audio chunk along with the RTP header form the RTP packet, which is encapsulated into a UDP segment.
RTP header indicates type of audio encoding in each packet; senders can change encoding during a conference. RTP header also contains sequence numbers and timestamps.

## Slide 39: RTP and QoS
RTP does not provide any mechanism to ensure timely delivery of data or provide other quality of service guarantees.
RTP encapsulation is only seen at the end systems -- it is not seen by intermediate routers.
  Routers provide the Internet's traditional best-effort service
To support Quality of Service, we need additional mechanisms

## Slide 40: RTP Streams
RTP allows each source (for example, a camera or a microphone) to be assigned its own independent RTP stream of packets.
  For example, for a videoconference between two participants, four RTP streams could be opened: two streams for transmitting the audio (one in each direction) and two streams for the video (again, one in each direction).
However, some popular encoding techniques -- including MPEG1 and MPEG2 -- bundle the audio and video into a single stream during the encoding process. When the audio and video are bundled by the encoder, then only one RTP stream is generated in each direction.
For a many-to-many multicast session, all of the senders and sources typically send their RTP streams into the same multicast tree with the same multicast address.

## Slide 41: Real-Time Control Protocol (RTCP)
Providing feedback in an RTP session.
Each participant in an RTP session periodically transmits RTCP control packets to all other participants.
Each RTCP packet contains sender and/or receiver reports that report statistics useful to the application.
Statistics include number of packets sent, number of packets lost, interarrival jitter, etc.
This feedback of information to the application can be used to control performance and for diagnostic purposes.
  The sender may modify its transmissions based on the feedback.

## Slide 42: RTCP - Continued
- For an RTP session there is typically a single multicast address; all RTP and RTCP packets belonging to the session use the multicast address.
- RTP and RTCP packets are distinguished from each other through the use of
distinct port numbers.
- To limit traffic, each participant reduces his RTCP traffic as the number of conference participants increases.

## Slide 43: RTCP Packets
Receiver report packets:
fraction of packets lost, last sequence number, average interarrival jitter.
Sender report packets:
SSRC of the RTP stream, the current time, the number of packets sent, and the number of bytes sent.
Source description packets:
e-mail address of the sender, the sender's name, the SSRC of the associated RTP stream. Packets provide a mapping between the SSRC and the user/host name.

## Slide 44: Overview of H.323
Foundation for audio and video conferencing across IP networks.
Targets real-time communication (rather than on-demand)
Broad in scope:
  stand-alone devices (e.g., Web phones, )
  applications in PCs
  point-to-point and multipoint conferences

## Slide 45: What does H.323 specify?
H.323 specification includes:
  How endpoints make and receive calls.
  How endpoints negotiate common audio/video encodings.
  How audio and video chunks are encapsulated and sent over network.
  How audio and video are synchronized (lipsync).
  How endpoints communicate with their respective gatekeepers.
  How Internet phones and PSTN/ISDN phones communicate.

## Slide 46: H.323 Endpoints Must Support:
G.711 - ITU standard for speech compression
RTP - protocol for encapsulating media chunks into packets
H.245 - “Out-of-band” control protocol for controlling media between H.323 endpoints.
Q.931 - A signalling protocol for establishing and terminating calls.
RAS (Registration/Admission/Status) channel protocol - Protocol for communicating with a gatekeeper (if gatekeeper is present)

## Slide 47: Overview (2)
Telephone calls
Video calls
Conferences
Whiteboards
All terminals supporting H.323

## Slide 48: Overview (3)
H.323
SS7, Inband

## Slide 50: RTP Header
Payload Type (7 bits): Used to indicate the type of encoding that is
currently being used.
If a sender changes the encoding in the middle of a conference, the
sender informs the receiver through this payload type field.
  Payload type 0: PCM mu-law, 64 Kbps
  Payload type 3, GSM, 13 Kbps
  Payload type 7, LPC, 2.4 Kbps
  Payload type 26, Motion JPEG
  Payload type 31. H.261
  Payload type 33, MPEG2 video
Sequence Number (16 bits): The sequence number increments by one for each RTP packet sent; may be used to detect packet loss
and to restore packet sequence.

## Slide 51: RTP Header (2)
Timestamp field (32 bytes long). Reflects the sampling instant of the first byte in the RTP data packet. The receiver can use the timestamps to remove packet jitter and provide synchronous playout. The timestamp is derived from a sampling clock at the sender.
  As an example, for audio the timestamp clock increments by one for each sampling period (for example, each 125 usecs for a 8 KHz sampling clock); if the audio application generates chunks consisiting of 160 encoded samples, then the timestamp increases by 160 for each RTP packet when the source is active. The timestamp clock continues to increase at a constant rate even the source is inactive.
SSRC field (32 bits long). Identifies the source of the RTP stream. Each stream in a RTP session should have a distinct SSRC.

## Slide 52: Synchronization of Streams
RTCP can be used to synchronize different media streams within a RTP session.
Consider a videoconferencing application for which each sender generates one RTP stream for video and one for audio.
The timestamps in these RTP packets are tied to the video and audio sampling clocks, and are not tied to the wall-clock time (i.e., to real time).
Each RTCP sender-report packet contains, for the most recently generated packet in the associated RTP stream, the timestamp of the RTP packet and the wall-clock time for when the packet was created. Thus the RTCP sender-report packets associate the sampling clock to the real-time clock.
Receivers can use this association to synchronize the playout of audio and video.

## Slide 53: RTCP Bandwidth Scaling
RTCP attempts to limit its traffic to 5% of the session bandwidth.
For example, suppose there is one sender, sending video at a rate of 2 Mbps. Then RTCP attempts to limit its traffic to 100 Kbps.
The protocol gives 75% of this rate, or 75 kbps, to the receivers; it gives the remaining 25% of the rate, or 25 kbps, to the sender.
The 75 kbps devoted to the receivers is equally shared among the receivers. Thus, if there are R receivers, then each receiver gets to send RTCP traffic at a rate of 75/R kbps and the sender gets to send RTCP traffic at a rate of 25 kbps.
A participant (a sender or receiver) determines the RTCP packet transmission period by dynamically calculating the the average RTCP packet size (across the entire session) and dividing the average RTCP packet size by its allocated rate.

## Slide 54: H.323
Overview
H.323 terminal
H. 323 encoding
Gatekeeper
Gateway
Audio codecs
Video codecs

## Slide 55: H.323 Terminal

## Slide 56: H.323 Encoding
Audio:
H.323 endpoints must support G.711 standard for speech compression. G.711 transmits voice at 56/64 kbps.
H.323 is considering requiring G.723 = G.723.1, which operates at 5.3/6.3 kbps.
Optional: G.722, G.728, G.729
Video
Video capabilities for an H.323 endpoint are optional.
Any video-enabled H.323 endpoint must support the QCIF H.261 (176x144 pixels).
Optionally supports other H.261 schemes: CIF, 4CIF and 16CIF.
H.261 is used with communication channels that are multiples of 64 kbps.

## Slide 57: Generating audio packet stream in H.323
Audio
Source
Encoding:
e.g., G.711
or G.723.1
RTP packet
encapsulation
UDP
socket
Internet or
Gatekeeper

## Slide 58: H.245 Control Channel
H.323 stream may contain multiple channels for different media types.
One H.245 control channel per H.323 session.
H.245 control channel is a reliable (TCP) channel that carries control messages.
Principle tasks:
  Open and closing media channels.
  Capability exchange: before sending media, endpoints agree on encoding algorithm
Note: H.245 for multimedia conferencing is analogous with RTSP for media streaming

## Slide 59: Information flows

## Slide 60: Gatekeeper 1/2
The gatekeeper is optional. Can provides to terminals:
  address translation to IP addresses
  bandwidth management: can limit amount of bandwidth consumed by real-time conferences
Optionally, H.323 calls can be routed through gatekeeper. Useful for billing.
RAS protocol (over TCP) for terminal-gatekeeper communication.
H.323 terminals
Gatekeeper
Router
Internet
LAN = “Zone”
RAS

## Slide 61: Gatekeeper 2/2
H.323 terminal must register itself with the gatekeeper in its zone.
  When the H.323 application is invoked at the terminal, the terminal uses RAS to send its IP address and alias (provided by user) to the gatekeeper.
If gatekeeper is present in a zone, each terminal in zone must contact gatekeeper to ask permission to make a call.
Once it has permission, the terminal can send the gatekeeper an e-mail address, alias string or phone extension. The gatekeeper translates the alias to an IP address.
  If necessary, a gatekeeper will poll other gatekeepers in other zones to resolve an IP address. Process varies by vendor.

## Slide 62: Gateway
H.323 terminals
Gatekeeper
Router
Internet
LAN = “Zone”
RAS
Gateway
PSTN
Bridge between IP Zone and PSTN (or ISDN) network.
Terminals communicate with gateways using H.245 and Q.931

## Slide 63: Audio codecs
MOS (Mean Opinion Score)

## Slide 64: Video codecs
H.261 (p x 64 kbit/s)
  Video over ISDN
  Resolutions : QCIF, CIF
H.263 (< 64 kbit/s)
  Low bit rate communication
  Resolutions: SQCIF, QCIF, CIF,4CIF, 16CIF
(128 x 96) (176 x 144) (352 x 288) (704 x 576) (1408 x 1152)
SQCIF QCIF CIF 4CIF 16CIF

## Slide 65: RTSP: out of band control
FTP uses an “out-of-band” control channel:
A file is transferred over one channel.
Control information (directory changes, file deletion, file renaming, etc.) is sent over a separate TCP connection.
The “out-of-band” and “in-band” channels use different port numbers.
RTSP messages are also sent out-of-band:
The RTSP control messages use different port numbers than the media stream, and are therefore sent out-of-band.
The media stream, whose packet structure is not defined by RTSP, is considered “in-band”.
If the RTSP messages were to use the same port numbers as the media stream, then RTSP messages would be said to be “interleaved” with the media stream.

## Slide 66: RTSP initiates and controls delivery
Client obtains a description of the multimedia presentation, which can consist of several media streams.
The browser invokes media player (helper application) based on the content type of the presentation description.
Presentation description includes references to media streams, using the URL method rtsp://
Player sends RTSP SETUP request; server sends RTSP SETUP response.
Player sends RTSP PLAY request; server sends RTSP PLAY response.
Media server pumps media stream.
Player sends RTSP PAUSE request; server sends RTSP PAUSE response.
Player sends RTSP TEARDOWN request; server sends RTSP TEARDOWN response.

## Slide 67: Meta file example
<title>Twister</title>
<session>
<group language=en lipsync>
<switch>
<track type=audio
e="PCMU/8000/1"
src = "rtsp://audio.example.com/twister/audio.en/lofi">
<track type=audio
e="DVI4/16000/2" pt="90 DVI4/8000/1"
src="rtsp://audio.example.com/twister/audio.en/hifi">
</switch>
<track type="video/jpeg"
src="rtsp://video.example.com/twister/video">
</group>
</session>

## Slide 68: RTSP session
Each RTSP has a session identifier, which is chosen by the server.
The client initiates the session with the SETUP request, and the server responds to the request with an identifier.
The client repeats the session identifier for each request, until the client closes the session with the TEARDOWN request.
RTSP port number is 554.
RTSP can be sent over UDP or TCP. Each RTSP message can be sent over a separate TCP connection.

## Slide 69: RTSP: exchange example
C: SETUP rtsp://audio.example.com/twister/audio RTSP/1.0
Transport: rtp/udp; compression; port=3056; mode=PLAY
S: RTSP/1.0 200 1 OK
Session 4231
C: PLAY rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
Range: npt=0-
C: PAUSE rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
Range: npt=37
C: TEARDOWN rtsp://audio.example.com/twister/audio.en/lofi RTSP/1.0
Session: 4231
S: 200 3 OK

## Slide 70: RTSP: streaming caching
Caching of RTSP response messages makes little sense.
But desirable to cache media streams closer to client.
Much of HTTP/1.1 cache control has been adopted by RTSP.
  Cache control headers can be put in RTSP SETUP requests and responses:
    If-modified-since: , Expires: , Via: , Cache-Control:
Proxy cache may hold only segments of a given media stream.
  Proxy cache may start serving a client from its local cache, and then have to connect to origin server and fill missing material, hopefully without introducing gaps at client.
When origin server is sending a stream through client, and stream passes through a proxy, proxy can use TCP to obtain the stream; but proxy still sends RTSP control messages to origin server.