## Slide 1: Providing Quality of Service in the Internet

## Slide 2: The QoS Problem Illustrated
Simple model for sharing and congestion studies:
  Competing for a scarce resource
The aspects of the problem
  Who is allowed? Admission Control
  Which packets are which? Packet classification
  How do I share? Scheduling
  Use resources efficiently

## Slide 3: Principles for QOS Guarantees
Consider a phone application at 1Mbps and an FTP application sharing a 1.5 Mbps link.
  bursts of FTP can congest the router and cause audio packets to be dropped.
  want to give priority to audio over FTP
PRINCIPLE 1: Marking of packets is needed for router to distinguish between different classes; and new router policy to treat packets accordingly

## Slide 4: Principles for QOS Guarantees (more)
Applications misbehave (audio sends packets at a rate higher than 1Mbps assumed above);
PRINCIPLE 2: provide protection (isolation) for one class from other classes
Require Policing Mechanisms to ensure sources adhere to bandwidth requirements; Marking and Policing need to be done at the edges:

## Slide 5: Principles for QOS Guarantees (more)
Alternative to Marking and Policing: allocate a set portion of bandwidth to each application flow; can lead to inefficient use of bandwidth if one of the flows does not use its allocation
PRINCIPLE 3: While providing isolation, it is desirable to use resources as efficiently as possible

## Slide 6: Principles for QOS Guarantees (more)
Cannot support traffic beyond link capacity
PRINCIPLE 4: Need a Call Admission Process; application flow declares its needs, network may block call if it cannot satisfy the needs

## Slide 7: The QoS “Architecture”

## Slide 8: Overview of Current QoS Trends
RSVP: Resource reservation Protocol
  Receivers back-propagate their QoS needs for resources
  Not scalable, more meaningful in multicasting
DiffServ: Differentiated Services
  “Colour” packets on entrance, treat different colours
  Per Hop Behavior: packets carry with the “routing state”
  namely how the expect to be treated.
IntServ: Integrated Services
  Routers maintain state per flow (!!!)

## Slide 9: Scheduling And Policing Mechanisms
Scheduling: choosing the next packet for transmission on a link can be done following a number of policies;
FIFO: in order of arrival to the queue; packets that arrive to a full buffer are either discarded, or a discard policy is used to determine which packet to discard among the arrival and those already queued

## Slide 10: Scheduling Policies
Priority Queuing: classes have different priorities; class may depend on explicit marking or other header info, eg IP source or destination, TCP Port numbers, etc.
Transmit a packet from the highest priority class with a non-empty queue
Preemptive and non-preemptive versions

## Slide 11: Scheduling Policies (more)
Round Robin: scan class queues serving one from each class that has a non-empty queue

## Slide 12: Scheduling Policies (more)
Weighted Fair Queuing: is a generalized Round Robin in which an attempt is made to provide a class with a differentiated amount of service over a given period of time

## Slide 13: Policing Mechanisms
Three criteria:
  (Long term) Average Rate (100 packets per sec or 6000 packets per min??), crucial aspect is the interval length
  Peak Rate: e.g., 6000 p p minute Avg and 1500 p p sec Peak
  (Max.) Burst Size: Max. number of packets sent consecutively, ie over a short period of time

## Slide 14: Policing Mechanisms
Token Bucket mechanism, provides a means for limiting input to specified Burst Size and Average Rate.

## Slide 15: Policing Mechanisms (more)
Bucket can hold b tokens; token are generated at a rate of r token/sec unless bucket is full of tokens.
Over an interval of length t, the number of packets that are admitted is less than or equal to (r t + b).
Token bucket and WFQ can be combined to provide upper bound on delay.

## Slide 16: Integrated Services
An architecture for providing QOS guarantees in IP networks for individual application sessions
relies on resource reservation, and routers need to maintain state info (Virtual Circuit??), maintaining records of allocated resources and responding to new Call setup requests on that basis

## Slide 17: Call Admission
Session must first declare its QOS requirement and characterize the traffic it will send through the network
R-spec: defines the QOS being requested
T-spec: defines the traffic characteristics
A signaling protocol is needed to carry the R-spec and T-spec to the routers where reservation is required; RSVP is a leading candidate for such signaling protocol

## Slide 18: Call Admission
Call Admission: routers will admit calls based on their R-spec and T-spec and base on the current resource allocated at the routers to other calls.

## Slide 19: Integrated Services: Classes
Guaranteed QOS: this class is provided with firm bounds on queuing delay at a router; envisioned for hard real-time applications that are highly sensitive to end-to-end delay expectation and variance
Controlled Load: this class is provided a QOS closely approximating that provided by an unloaded router; envisioned for today’s IP network real-time applications which perform well in an unloaded network

## Slide 20: Differentiated Services
Intended to address the following difficulties with Intserv and RSVP;
Scalability: maintaining states by routers in high speed networks is difficult sue to the very large number of flows
Flexible Service Models: Intserv has only two classes, want to provide more qualitative service classes; want to provide ‘relative’ service distinction (Platinum, Gold, Silver, …)
Simpler signaling: (than RSVP) many applications and users may only w ant to specify a more qualitative notion of service

## Slide 21: Differentiated Services
Approach:
  Only simple functions in the core, and relatively complex functions at edge routers (or hosts)
  Do not define service classes, instead provides functional components with which service classes can be built

## Slide 22: Edge Functions
At DS-capable host or first DS-capable router
Classification: edge node marks packets according to classification rules to be specified (manually by admin, or by some TBD protocol)
Traffic Conditioning: edge node may delay and then forward or may discard

## Slide 23: Core Functions
Forwarding: according to “Per-Hop-Behavior” or PHB specified for the particular packet class; such PHB is strictly based on class marking (no other header fields can be used to influence PHB)
BIG ADVANTAGE:
No state info to be maintained by routers!

## Slide 24: Classification and Conditioning
Packet is marked in the Type of Service (TOS) in IPv4, and Traffic Class in IPv6
6 bits used for Differentiated Service Code Point (DSCP) and determine PHB that the packet will receive
2 bits are currently unused

## Slide 25: Classification and Conditioning
It may be desirable to limit traffic injection rate of some class; user declares traffic profile (eg, rate and burst size); traffic is metered and shaped if non-conforming

## Slide 26: Forwarding (PHB)
PHB result in a different observable (measurable) forwarding performance behavior
PHB does not specify what mechanisms to use to ensure required PHB performance behavior
Examples:
  Class A gets x% of outgoing link bandwidth over time intervals of a specified length
  Class A packets leave first before packets from class B

## Slide 27: Forwarding (PHB)
PHBs under consideration:
  Expedited Forwarding: departure rate of packets from a class equals or exceeds a specified rate (logical link with a minimum guaranteed rate)
  Assured Forwarding: 4 classes, each guaranteed a minimum amount of bandwidth and buffering; each with three drop preference partitions

## Slide 28: Differentiated Services Issues
AF and EF are not even in a standard track yet… research ongoing
“Virtual Leased lines” and “Olympic” services are being discussed
Impact of crossing multiple ASs and routers that are not DS-capable

## Slide 29: QoS: Summary
Internet was not designed with QoS in mind
Adding QoS over best-effort is not easy
QoS also requires access limitations
  Admission control
  Traffic shaping
No final solution exists yet

## Slide 30: Real-Time Protocol (RTP)
Provides standard packet format for real-time application
Typically runs over UDP
Specifies header fields below
Payload Type: 7 bits, providing 128 possible different types of encoding; eg PCM, MPEG2 video, etc.
Sequence Number: 16 bits; used to detect packet loss

## Slide 31: Real-Time Protocol (RTP)
Timestamp: 32 bytes; gives the sampling instant of the first audio/video byte in the packet; used to remove jitter introduced by the network
Synchronization Source identifier (SSRC): 32 bits; an id for the source of a stream; assigned randomly by the source

## Slide 32: RTP Control Protocol (RTCP)
Protocol specifies report packets exchanged between sources and destinations of multimedia information
Three reports are defined: Receiver reception, Sender, and Source description
Reports contain statistics such as the number of packets sent, number of packets lost, inter-arrival jitter
Used to modify sender transmission rates and for diagnostics purposes

## Slide 33: RTCP Bandwidth Scaling
If each receiver sends RTCP packets to all other receivers, the traffic load resulting can be large
RTCP adjusts the interval between reports based on the number of participating receivers
Typically, limit the RTCP bandwidth to 5% of the session bandwidth, divided between the sender reports (25%) and the receivers reports (75%)