## Slide 1: Automatic Detection of Excessive Glycemic Variability for Diabetes Management
Matthew Wiley, Razvan Bunescu, Cindy Marling,
Jay Shubrook and Frank Schwartz
School of Electrical Engineering and Computer Science
Appalachian Rural Health Institute Diabetes and Endocrine Center
Athens, Ohio, USA

## Slide 2: Diabetes
Body fails to effectively produce and/or use insulin
Treated and managed with blood glucose control

## Slide 3: Diabetes
Body fails to effectively produce and/or use insulin
Treated and managed with blood glucose control
346 million people world wide
Two major types:
  Type I
  Type II

## Slide 4: Poor Control Increases Risk of Complications
CONTROL
Foot Ulcers
Angina
Heart Attack
Coronary Bypass
Surgery
Stroke
Blindness
Amputation
Dialysis
Kidney
Transplant
Microalbuminuria
Mild Retinopathy
Mild Neuropathy
Albuminuria
Macular Edema
Proliferative
Retinopathy
Periodontal Disease
Impotence
Gastroparesis
Depression
RISK
Good
Poor

## Slide 5: Administering Insulin
Type I patients must administer insulin
  Injection
  Insulin Pump
Insulin Pump

## Slide 6: Continuous Glucose Monitoring
Two approaches to monitoring:
  Fingersticks
  Continuous Glucose Monitoring (CGM) sensors
CGM Sensor
Fingerstick

## Slide 7: Data Overload
CGM sensors record values every 5 or 10 minutes

## Slide 8: Excessive Glycemic Variability
Characterized by fluctuations in blood glucose
Patients are not yet routinely screened
Acceptable Glycemic Variability
Excessive Glycemic Variability

## Slide 9: Background
Preliminary work:
  Two physicians individually classified 400 plots
  Naïve Bayes classifier: 85% accuracy

## Slide 10: Background
Preliminary work:
  Two physicians individually classified 400 plots
  Naïve Bayes classifier: 85% accuracy
Three orthogonal directions:
  Smoothing of blood glucose data
  Feature engineering
  Evaluation of other classifiers

## Slide 11: Smoothing Blood Glucose Data
Sensors record at ±20% accuracy
  Physicians implicitly smooth noise

## Slide 12: Smoothing Blood Glucose Data
Several smoothing methods were investigated:
  Moving averages
  Polynomial regression
  Discrete Fourier transform filter
  Cubic spline interpolation
Cubic spline identified as the best match

## Slide 13: Cubic Spline Interpolation
Two reasons:
  Smooth curves
  Significant points
Doctor
Spline

## Slide 14: Feature Engineering
Several features were investigated in this work:
Mean Amplitude of Glycemic Excursions (MAGE)
Distance Traveled
Excursion Frequency
Standard Deviation
Area Under the Curve
Roundness Ratio
Bending Energy
Eccentricity
Amplitudes of DFT frequencies
Two dimensional central moments
Direction Codes

## Slide 15: Feature Selection
Two methods are reported:
  t-Test filter
  Greedy backward elimination
Both raw and smooth data

## Slide 16: Feature Selection
Two methods are reported:
  t-Test filter
  Greedy backward elimination
Both raw and smooth data
Out of the four feature sets selected:
  No feature appeared in all four sets
  Eccentricity and bending energy were never selected

## Slide 17: Experimental Evaluation
Three classifiers compared:
  Naïve Bayes (NB)
  Support Vector Machines (SVM)
  Multilayer Perceptron (MP)

## Slide 18: Experimental Evaluation
Three classifiers compared:
  Naïve Bayes (NB)
  Support Vector Machines (SVM)
  Multilayer Perceptron (MP)
Evaluated with 10-fold cross validation
  Tuned with development dataset
  Features from feature selection
  Both raw and smooth data

## Slide 19: Visual Overview of Evaluation

## Slide 20: Results
NB with raw data: 87.1%
  Same settings as preliminary work – the baseline
t-test filter:
  SVM with smoothed data: 92.8%
Greedy backward elimination:
  MP with smoothed data: 93.8%

## Slide 21: Results
NB with raw data: 87.1%
  Same settings as preliminary work – the baseline
t-test filter:
  SVM with smoothed data: 92.8%
Greedy backward elimination:
  MP with smoothed data: 93.8%
Overall:
  Additional features helped
  Smoothed data helped

## Slide 22: Comparison of ROC Curves for Best Classifiers

## Slide 23: Future Work
This experiment was constrained by the dataset size
  Potentially suboptimal parameters and features
  Collecting more data is a high priority

## Slide 24: Future Work
This experiment was constrained by the dataset size
  Potentially suboptimal parameters and features
  Collecting more data is a high priority
Plans for a “5-star” ordinal scheme
  Alleviate disagreements between annotators
  Opportunity to further improve accuracy

## Slide 25: From Bench to Bedside
Integration with current CGM management systems
  Glucose sensors are in common use as a diagnostic tool
  Some patients use glucose sensors year round
  Manufacturers already provide reporting

## Slide 26: From Bench to Bedside
Integration with current CGM management systems
  Glucose sensors are in common use as a diagnostic tool
  Some patients use glucose sensors year round
  Manufacturers already provide reporting
Development of a screen for routine clinical use
  Identify at risk patients in the clinical setting
  Completion of the intended application

## Slide 27: Acknowledgements
National Science Foundation
Medtronic
Ohio University
Our Dedicated Research Nurses
My Fellow Graduate Research Assistants
Over 50 Anonymous Patients with Type 1 Diabetes on Insulin Pump Therapy

## Slide 28: Thanks!
Questions?