## Slide 1: CS/EE 217: GPU Architecture and Parallel Programming Tiled Convolution

## Slide 2: Objective
To learn about tiled convolution algorithms
  Some intricate aspects of tiling algorithms
  Output tiles versus input tiles

## Slide 3: Tiled 1D Convolution Basic Idea
ghost
ghost
N
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
15
1
2
3
4
5
8
9
10
11
12
13
0
7
6
Tile 0
Tile 2
2
3
4
5
6
7
8
9
Tile 1
10
11
12
13
14
15
Tile 3
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
15
P
halo
Notes: Elements that are involved in multiple tiles and loaded by multiple blocks are commonly referred to as halo elements. In this example, n = 2, the mask window size is 2n+1.

## Slide 4: Loading the left halo
int n = Mask_Width/2;
int halo_index_left = (blockIdx.x - 1)*blockDim.x + threadIdx.x;
if (threadIdx.x >= blockDim.x - n) {
N_ds[threadIdx.x - (blockDim.x - n)] =
(halo_index_left < 0) ? 0 : N[halo_index_left];
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
15
i =6
halo_index_left = 2
n = 2
2
3
4
5
6
7
8
9
N
N_ds
Notes: n is the half of the tile width n = Mask_width/2.
In the first statement, we map the thread index to the element index into the previous tile with the expression (blockIdx.x-1)*blockDim. x1+ threadIdx.x.
We then pick only the last n threads to load the needed left halo elements using the condition in the if statement. For example, In Figure 8.6, blockDim.x equals 4 and n equals 2;only threads 2 and 3 will be used. Threads 0 and 1 will not load any thing due to the failed condition.

## Slide 5: Loading the internal elements
N_ds[n + threadIdx.x] = N[blockIdx.x*blockDim.x + threadIdx.x];
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
15
i =6
halo = 2
n = 2
2
3
4
5
6
7
8
9
N
N_ds
Notes: n is the half of the tile width n = Mask_width/2. So for internal elements, we need to shift the position by n.

## Slide 6: Loading the right halo
int halo_index_right = (blockIdx.x + 1)*blockDim.x + threadIdx.x;
if (threadIdx.x < n) {
N_ds[n + blockDim.x + threadIdx.x] =
(halo_index_right >= Width) ? 0 : N[halo_index_right];
}
1
2
3
4
5
6
7
8
9
10
11
12
13
14
0
15
i =6
halo_index_right = 10
n = 2
2
3
4
5
6
7
8
9
N
N_ds
Notes: For the the right halo element, the position is shifted to n + blockDim, which is the mask width,.

## Slide 7
__global__ void convolution_1D_basic_kernel(float *N, float *P, int Mask_Width,
int Width) {
int i = blockIdx.x*blockDim.x + threadIdx.x;
__shared__ float N_ds[TILE_SIZE + MAX_MASK_WIDTH - 1];
int n = Mask_Width/2;
int halo_index_left = (blockIdx.x - 1)*blockDim.x + threadIdx.x;
if (threadIdx.x >= blockDim.x - n) {
N_ds[threadIdx.x - (blockDim.x - n)] =
(halo_index_left < 0) ? 0 : N[halo_index_left];
}
N_ds[n + threadIdx.x] = N[blockIdx.x*blockDim.x + threadIdx.x];
int halo_index_right = (blockIdx.x + 1)*blockDim.x + threadIdx.x;
if (threadIdx.x < n) {
N_ds[n + blockDim.x + threadIdx.x] =
(halo_index_right >= Width) ? 0 : N[halo_index_right];
}
__syncthreads();
float Pvalue = 0;
for(int j = 0; j < Mask_Width; j++) {
Pvalue += N_ds[threadIdx.x + j]*M[j];
}
P[i] = Pvalue;
}
Notes: Now, each thread will use the use N_ds[threadIdx.x] through N_ds[thread[Idx.x+Mask_Width-1]. Note that the halo elements has shift the N_ds element position by n already.

## Slide 8: Shared Memory Data Reuse
Element 2 is used by thread 4 (1X)
Element 3 is used by threads 4, 5 (2X)
Element 4 is used by threads 4, 5, 6 (3X)
Element 5 is used by threads 4, 5, 6, 7 (4X)
Element 6 is used by threads 4, 5, 6, 7 (4X)
Element 7 is used by threads 5, 6, 7 (3X)
Element 8 is used by threads 6, 7 (2X)
Element 9 is used by thread 7 (1X)
2
3
4
5
6
7
8
9
N_ds
Mask_Width is 5

## Slide 9: Ghost Cells
N
0
N[0]
N[3]
N[1]
N[2]
N[5]
N[4]
N[6]
0
0
0
P[0]
P[1]
P[2]
P[3]
P[4]
P[5]
P[6]

## Slide 10
__global__ void convolution_1D_basic_kernel(float *N, float *P, int Mask_Width,
int Width) {
int i = blockIdx.x*blockDim.x + threadIdx.x;
__shared__ float N_ds[TILE_SIZE];
N_ds[threadIdx.x] = N[i];
__syncthreads();
int This_tile_start_point = blockIdx.x * blockDim.x;
int Next_tile_start_point = (blockIdx.x + 1) * blockDim.x;
int N_start_point = i - (Mask_Width/2);
float Pvalue = 0;
for (int j = 0; j < Mask_Width; j ++) {
int N_index = N_start_point + j;
if (N_index >= 0 && N_index < Width) {
if ((N_index >= This_tile_start_point)
&& (N_index < Next_tile_start_point)) {
Value += N_ds[threadIdx.x+j-(Mask_Width/2)]*M[j];
} else {
Pvalue += N[N_index] * M[j];
}
}
}
P[i] = Pvalue;
}
Notes: Simple tiled 1D convolution – general caching or using L2 cache to avoid using halo elements. In this case, you need to read from both shared memory (N_ds) and the global memory N[] directly and hope N[] is cached in L2.
For statement: Value += N_ds[threadIdx.x+j-(Mask_Width/2)]*M[j]; the offset (Mask_Width/2) is needed as we compute the convolution from i–n to i+n for the N[i]

## Slide 11: 2D convolution with Tiling P
Use a thread block to calculate a tile of P
  Thread Block size determined by the TILE_SIZE

## Slide 12: Tiling N
Each element in the tile is used in calculating up to MASK_SIZE * MASK_SIZE P elements (all elements in the tile)
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
Notes: For instance, element 3 are used in the 6 examples (should include more). So in general, it is KERNEL_SIZE*KERNEL_SIZE

## Slide 13: High-Level Tiling Strategy
Load a tile of N into shared memory (SM)
  All threads participate in loading
  A subset of threads then use each N element in SM
TILE_SIZE
TILE_SIZE
KERNEL_SIZE
KERNEL_SIZE

## Slide 14: Output Tiling and Thread Index (P)
Use a thread block to calculate a tile of P
  Each output tile is of TILE_SIZE for both x and y
col_o = blockIdx.x * TILE_SIZE + tx;
row_o = blockIdx.y*TILE_SIZE + ty;

## Slide 15: Input tiles need to be larger than output tiles.
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
Output Tile
Input Tile
Notes: The reason for this is that we don’t use ghost elements in this case. Instead, we use concept of input tiles

## Slide 16: Dealing with Mismatch
Use a thread block that matches input tile
  Each thread loads one element of the input tile
  Some threads do not participate in calculating output
    There will be if statements and control divergence

## Slide 17: Setting up blocks
#define O_TILE_WIDTH 12
#define BLOCK_WIDTH (O_TILE_WIDTH + 4)
dim3 dimBlock (BLOCK_WIDTH, BLOCK_WIDTH);
dim3 dimGrid ((imageWidth – 1)/O_TILE_WIDTH + 1,
(imageHeight-1)/O_TILE_WIDTH+1, 1);
In general, block width = Tile width + mask width – 1;

## Slide 18: Using constant memory for mask
Since mask is used by all threads and not modified:
  All threads in a warp access the same locations at every time
  Take advantage of the cachable constant memory!
  Magnify memory bandwidth without consuming shared memory
Syntax:
__global__ void convolution_2D_kernel (float *P,
*float N, height, width, channels,
const float __restrict__ *M) {

## Slide 19: Shifting from output coordinates to input coordinates
Input tile
for thread (0,0)
Output tile
for thread (0,0)
Notes: So the input tiles will cover the output tiles with mask_width/2 as the green boundary size.

## Slide 20: Shifting from output coordinates to input coordinate
int tx = threadIdx.x;
int ty = threadIdx.y;
int row_o = blockIdx.y * TILE_SIZE + ty;
int col_o = blockIdx.x * TILE_SIZE + tx;
int row_i = row_o - 2; //MASK_SIZE/2
int col_i = col_o - 2; //MASK_SIZE/2

## Slide 21: Threads that loads halos outside N should return 0.0

## Slide 22: Taking Care of Boundaries
float output = 0.0f;
if((row_i >= 0) && (row_i < N.height) &&
(col_i >= 0) && (col_i < N.width) ) {
Ns[ty][tx] = N.elements[row_i*N.width + col_i];
}
else{
Ns[ty][tx] = 0.0f;
}

## Slide 23: Some threads do not participate in calculating output.
if(ty < TILE_SIZE && tx < TILE_SIZE){
for(i = 0; i < MASK_SIZE; i++) {
for(j = 0; j < MASK_SIZE; j++) {
output += Mc[i][j] * Ns[i+ty][j+tx];
}
}

## Slide 24: Some threads do not write output
if(row_o < P.height && col_o < P.width)
P.elements[row_o * P.width + col_o] = output;

## Slide 25: In General
BLOCK_SIZE is limited by the maximum number of threads in a thread block
Input tile sizes could be could be k*TILE_SIZE + (MASK_SIZE-1)
  For 1D convolution – what is it for 2D convolution?
  By having each thread to calculate k input points (thread coarsening)
  k is limited by the shared memory size
MASK_SIZE is decided by application needs

## Slide 26: CS/EE 217 GPU Architecture and Parallel Programming Tiled Convolution Analysis

## Slide 27: Objective
To learn more about the analysis of tiled algorithms

## Slide 28: If we used a larger (8 element) tile
6
7
8
9
10
11
16
17
N_ds
Mask_Width is 5
For Mask_Width = 5, we load 8+5-1 = 12 elements (12 memory loads)
12
13
14
15
8
9
10
11
12
13
14
15
P

## Slide 29: Each output P element uses 5 N elements (in N_ds)
6
7
8
9
10
11
16
17
N_ds
Mask_Width is 5
P[8] uses N[6], N[7], N[8], N[9], N[10]
P[9] uses N[7], N[8], N[9], N[10], N[11]
P[10] uses N[8], N[9], N[10], N[11], N[12]
…
P[14] uses N[12], N[13], N[14], N[15],N[16]
P[15] uses N[13], N[14], N[15], N[16], N[17]
12
13
14
15
8
9
10
11
12
13
14
15
P

## Slide 30: A simple way to calculate tiling benefit
(8+5-1)=12 elements loaded
8*5 global memory accesses replaced by shared memory accesses
This gives a bandwidth reduction of 40/12=3.3

## Slide 31: In General
Tile_Width + Mask_Width -1 elements loaded
Tile_Width * Mask_Width global memory accesses replaced by shared memory access
This gives a reduction of bandwidth by
(Tile_Width *Mask_Width)/(Tile_Width+Mask_Width-1)

## Slide 32: Another Way to Look at Reuse
6
7
8
9
10
11
16
17
N_ds
Mask_Width is 5
N[6] is used by P[8] (1X)
N[7] is used by P[8], P[9] (2X)
N[8] is used by P[8], P[9], P[10] (3X)
N[9] is used by P[8], P[9], P[10], P[11] (4X)
N[10] is used by P[8], P[9], P[10], P[11], P[12] (5X)
… (5X)
N[14] is uses by P[12], P[13], P[14], P[15] (4X)
N[15] is used by P[13], P[14], P[15] (3X)
12
13
14
15
8
9
10
11
12
13
14
15
P

## Slide 33: Another Way to Look at Reuse
The total number of global memory accesses (to the (8+5-1)=12 N elements) replaced by shared memory accesses is
1 + 2 + 3 + 4 + 5 * (8-5+1) + 4 + 3 + 2 + 1
= 10 + 20 + 10
= 40
So the reduction is
40/12 = 3.3

## Slide 34: Ghost elements change ratios
For a boundary tile, we load Tile_Width + (Mask_Width-1)/2 elements
  10 in our example of Tile_Width =8 and Mask_Width=5
Computing boundary elements do not access global memory for ghost cells
  Total accesses is 3 + 4+ 6*5 = 37 accesses
The reduction is 37/10 = 3.7

## Slide 35: In General for 1D
The total number of global memory accesses to the (Tile_Width+Mask_Width-1) N elements replaced by shared memory accesses is
1 + 2 + … + Mask_Width-1+ Mask_Width * (Tile_Width -Mask_Width+1) + Mask_Width-1+… + 2 + 1
= (Mask_Width-1) *Mask_Width+ Mask_Width*(Tile_Width-Mask_Width+1)
= Mask_Width*(Tile_Width)

## Slide 36: Bandwidth Reduction for 1D
The reduction is
Mask_Width * (Tile_Width)/(Tile_Width+Mask_Size-1)
Tile_Width | 16 | 32 | 64 | 128 | 256
Reduction Mask_Width = 5 | 4.0 | 4.4 | 4.7 | 4.9 | 4.9
Reduction Mask_Width = 9 | 6.0 | 7.2 | 8.0 | 8.5 | 8.7

## Slide 37: 2D Output Tiling and Indexin (P)
Use a thread block to calculate a tile of P
  Each output tile is of TILE_SIZE for both x and y
col_o = blockIdx.x * TILE_WIDTH + tx;
row_o = blockIdx.y*TILE_WIDTH + ty;

## Slide 38: Input tiles need to cover halo elements.
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
3
4
5
6
7
2
3
4
5
6
1
2
3
4
5
2
3
5
6
7
0
1
1
3
1
Output Tile
Input Tile
Mask_Width = 5

## Slide 39: A Simple Analysis for a small 8X8 output tile example
12X12=144 N elements need to be loaded into shared memory
The calculation of each P element needs to access 25 N elements
8X8X25 = 1600 global memory accesses are converted into shared memory accesses
A reduction of 1600/144 = 11X

## Slide 40: In General
(Tile_Width+Mask_Width-1) 2 elements from N need to be loaded into shared memory for each tile
The calculation of each P element needs to access Mask_Width 2 elements
  Tile_Width 2 * Mask_Width 2 global memory accesses are converted into shared memory accesses
The reduction is
Tile_Width 2 * Mask_Width 2 / (Tile_Width+Mask_Width-1) 2

## Slide 41: Bandwidth Reduction for 2D
The reduction is
Mask_Width 2 * (Tile_Width) 2 /(Tile_Width+Mask_Size-1) 2
Tile_Width | 8 | 16 | 32 | 64
Reduction Mask_Width = 5 | 11.1 | 16 | 19.7 | 22.1
Reduction Mask_Width = 9 | 20.3 | 36 | 51.8 | 64

## Slide 42: Ghost elements change ratios
Left as homewok.

## Slide 43: Any MORE QUESTIONS? Read Chapter 8