## Slide 1: CSE 153 Design of Operating Systems Winter 2023
Lecture 14/15: Memory Management (1)
Some slides from Dave O’Hallaron

## Slide 2: OS Abstractions
Operating System
Hardware
Applications
CPU
Disk
RAM
Process
File system
Virtual memory

## Slide 3: Our plan of action
Memory/storage technologies and trends
  Memory wall!
Locality of reference to the rescue
  Caching in the memory hierarchy
Abstraction: Address spaces and memory sharing
Virtual memory
Today: background and bird’s eye view – more details to follow later

## Slide 4: Random-Access Memory (RAM)
Key features
  RAM is traditionally packaged as a chip.
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
Static RAM (SRAM)
  Each cell stores a bit with a four or six-transistor circuit.
  Retains value indefinitely, as long as it is kept powered.
  Relatively insensitive to electrical noise (EMI), radiation, etc.
  Faster and more expensive than DRAM.
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor. One transistor is used for access
  Value must be refreshed every 10-100 ms.
  More sensitive to disturbances (EMI, radiation,…) than SRAM.
  Slower and cheaper than SRAM.

## Slide 5: SRAM vs DRAM Summary
Trans. Access Needs Needs
per bit time refresh? EDC? Cost Applications
SRAM 4 or 6 1X No Maybe 100x Cache memories
DRAM 1 10X Yes Yes 1X Main memories,
frame buffers

## Slide 6: Conventional DRAM Organization
d x w DRAM:
  dw total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 7: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 8: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU

## Slide 9: Memory Modules
: supercell (i,j)
64 MB
memory module
consisting of
eight 8Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 10: Enhanced DRAMs
Basic DRAM cell has not changed since its invention in 1966.
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR4 (8 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports only DDR3 SDRAM

## Slide 11: Nonvolatile Memories
DRAM and SRAM are volatile – lose info without power
Nonvolatile memories (NVMs) retain value
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase
  Flash memory: EEPROMs with partial (sector) erase capability
    Wears out after about 100,000 erasings.
  Phase Change Memories (PCMs): also wear out
  Many exciting NVMs at various stages of development

## Slide 12: NVM Uses
Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
Caches in high end systems
Getting better -- many expect Universal memory to come
  i.e., large replace both DRAM and disk drives

## Slide 13: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 14: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%eax
Load operation: movl A, %eax

## Slide 15: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
Register file
Bus interface
x
0
A
x
Main memory
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 16: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %eax.
x
ALU
Register file
Bus interface
x
Main memory
0
A
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 17: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
Register file
Bus interface
A
Main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 18: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 19: Memory Write Transaction (3)
Main memory reads data word y from the bus and stores it at address A.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %eax, A

## Slide 20: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1980 | 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010
Disk seek time | 87000000 | 75000000 | 28000000 | 10000000 | 8000000 | 8000000 | 8000000 | 8000000
Flash SSD access time | 75000
DRAM access time | 375 | 200 | 100 | 70 | 60 | 55 | 50 | 40
SRAM access time | 300 | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5
CPU cycle time | 1000 | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4
Effective CPU cycle time | 0.3 | 0.25 | 0.1
Disk
DRAM
CPU
SSD

## Slide 21: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 22: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy
Virtual memory and memory sharing

## Slide 23: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 24: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 25: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 26: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 27: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 28: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 29: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy
Virtual memory and memory sharing

## Slide 30: An Example Memory Hierarchy
Registers
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
Remote secondary storage
(tapes, distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
costlier
per byte

## Slide 31: Memory hierarchy
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each layer, faster, smaller device caches larger, slower device
  .
Why do memory hierarchies work?
  Because of locality!
    Hit fast memory much more frequently even though its smaller
  Thus, the storage at level k+1 can be slower (but larger and cheaper!)
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 32: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 33: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 34: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 35: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 36: Examples of Caching in the Hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
64-bytes block
64-bytes block
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
1
On-Chip L1
Hardware
10
On/Off-Chip L2
AFS/NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 37: Summary so far
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.

## Slide 38: Sharing Memory
Rewind to the days of “second-generation” computers
  Programs use physical addresses directly
  OS loads job, runs it, unloads it
Multiprogramming changes all of this
  Want multiple processes in memory at once
    Overlap I/O and CPU of multiple jobs
  How to share physical memory across multiple processes?
    Many programs do not need all of their code and data at once (or ever) – no need to allocate memory for it
    A program can run on machine with less memory than it “needs”

## Slide 39: Virtual Addresses
To make it easier to manage the memory of processes running in the system, we’re going to make them use virtual addresses (logical addresses)
  Virtual addresses are independent of the actual physical location of the data referenced
  OS determines location of data in physical memory
Instructions executed by the CPU issue virtual addresses
  Virtual addresses are translated by hardware into physical addresses (with help from OS)
  The set of virtual addresses that can be used by a process comprises its virtual address space

## Slide 40: Virtual Addresses
Many ways to do this translation…
  Need hardware support and OS management algorithms
Requirements
  Need protection – restrict which addresses jobs can use
  Fast translation – lookups need to be fast
  Fast change – updating memory hardware on context switch
vmap
processor
physical memory
virtual addresses
physical addresses

## Slide 41: Fixed Partitions
Physical memory is broken up into fixed partitions
  Size of each partition is the same and fixed
  Hardware requirements: base register
  Physical address = virtual address + base register
  Base register loaded by OS when it switches to a process
Physical Memory
P1
P2
P3
P4
P5

## Slide 42: Fixed Partitions
P4’s Base
+
Offset
Virtual Address
Physical Memory
Base Register
P1
P2
P3
P4
P5
  How do we provide protection?

## Slide 43: Fixed Partitions
Advantages
  Easy to implement
    Need base register
    Verify that offset is less than fixed partition size
  Fast context switch
Problems?
  Internal fragmentation: memory in a partition not used by a process is not available to other processes
  Partition size: one size does not fit all (very large processes?)

## Slide 44: Variable Partitions
Natural extension – physical memory is broken up into variable sized partitions
  Hardware requirements: base register and limit register
  Physical address = virtual address + base register
Why do we need the limit register?
  Protection: if (virtual address > limit) then fault

## Slide 45: Variable Partitions
P3’s Base
+
Offset
Virtual Address
Base Register
P2
P3
<
Protection Fault
Yes?
No?
P3’s Limit
Limit Register
P1

## Slide 46: Variable Partitions
Advantages
  No internal fragmentation: allocate just enough for process
Problems?
  External fragmentation: job loading and unloading produces empty holes scattered throughout memory
P2
P3
P1
P4

## Slide 47: Paging
New Idea: split virtual address space into multiple partitions
  Each can go anywhere!
Virtual Memory
Page 1
Page 2
Page 3
Page N
Physical Memory
Paging solves the external fragmentation problem by
using fixed sized units in both physical and virtual memory
But need to keep track
of where things are!

## Slide 48: Process Perspective
Processes view memory as one contiguous address space from 0 through N
  Virtual address space (VAS)
In reality, pages are scattered throughout physical storage
The mapping is invisible to the program
Protection is provided because a program cannot reference memory outside of its VAS
  The address “0x1000” maps to different physical addresses in different processes

## Slide 49: Paging
Translating addresses
  Virtual address has two parts: virtual page number and offset
  Virtual page number (VPN) is an index into a page table
  Page table determines page frame number (PFN)
  Physical address is PFN::offset
Page tables
  Map virtual page number (VPN) to page frame number (PFN)
    VPN is the index into the table that determines PFN
  One page table entry (PTE) per page in virtual address space
    Or, one PTE per VPN

## Slide 50: Page Lookups
Page frame
Page number
Offset
Virtual Address
Page Table
Page frame
Offset
Physical Address
Physical Memory

## Slide 51: Paging Example
Pages are 4KB
  Offset is 12 bits (because 4KB = 212 bytes)
  VPN is 20 bits (32 bits is the length of every virtual address)
Virtual address is 0x7468
  Virtual page is 0x7, offset is 0x468
Page table entry 0x7 contains 0x2000
  Page frame number is 0x2000
  Seventh virtual page is at address 0x2000 (2nd physical page)
Physical address = 0x2000 + 0x468 = 0x2468

## Slide 52: Page Table Entries (PTEs)
Page table entries control mapping
  The Modify bit says whether or not the page has been written
    It is set when a write to the page occurs
  The Reference bit says whether the page has been accessed
    It is set when a read or write to the page occurs
  The Valid bit says whether or not the PTE can be used
    It is checked each time the virtual address is used (Why?)
  The Protection bits say what operations are allowed on page
    Read, write, execute (Why do we need these?)
  The page frame number (PFN) determines physical page
R
V
M
Prot
Page Frame Number
1
1
1
2
20

## Slide 53: Paging Advantages
Easy to allocate memory
  Memory comes from a free list of fixed size chunks
  Allocating a page is just removing it from the list
  External fragmentation not a problem
    All pages of the same size
Simplifies protection
  All chunks are the same size
  Like fixed partitions, don’t need a limit register
Simplifies virtual memory – later

## Slide 54: Paging Limitations
Can still have internal fragmentation
  Process may not use memory in multiples of a page
Memory reference overhead
  2 references per address lookup (page table, then memory)
  What can we do?
Memory required to hold page table can be significant
  Need one PTE per page
  32 bit address space w/ 4KB pages = 220 PTEs
  4 bytes/PTE = 4MB/page table
  25 processes = 100MB just for page tables!
  What can we do?

## Slide 55: Segmentation
Segmentation: partition memory into logically related units
  Module, procedure, stack, data, file, etc.
  Units of memory from user’s perspective
Natural extension of variable-sized partitions
  Variable-sized partitions = 1 segment/process
  Segmentation = many segments/process
  Fixed partition : Paging :: Variable partition : Segmentation
Hardware support
  Multiple base/limit pairs, one per segment (segment table)
  Segments named by #, used to index into table
  Virtual addresses become <segment #, offset>

## Slide 56: Segment Lookups
limit
base
+
<
Protection Fault
Segment #
Offset
Virtual Address
Segment Table
Yes?
No?
Physical Memory