## Slide 1: Reference Monitors/Information Flow Tracking
Slide credits: Raksha presentation based on that original authors

## Slide 2: Reference Monitors
A class of analyses that monitors application code to enforce some invariants
What kinds of invariants? We’ve seen at least one
  Control Flow Integrity—what was that for?
But there are many other reference monitors that have been proposed – a versatile model
  Not just for security
Classical implementation: inlined reference monitor (IRM)
  Software only implementation

## Slide 3: Inline reference monitors
Software implementation advantages
  Flexible in terms of policy
  Amenable to compiler optimizations – for example, selectively monitor
  Don’t need hardware support
Disadvantages:
  Performance tends to be terrible
  Coverage
  Legacy binaries
  …

## Slide 4: Today
Look at some reference monitors because
  Some that are important and that have had commercial impact
  But also, to think about this class of computation in general
Hopefully discover that:
  There are many monitors, but they share a common (or at least similar) computation model
  Each particular monitor can be implemented in a variety of ways from software only, to hardware only to something in between
    With different implications – not just performance
How do we provide hardware support for this class of computation?
How do we think about implementation tradeoffs
  Can this be automated?

## Slide 5: RAKSHA A Flexible Information Flow Architecture for Software Security
Michael Dalton Hari Kannan Christos Kozyrakis
Computer Systems Laboratory
Stanford University

## Slide 6: Motivation
Software security is in a crisis
  Far-reaching financial & social implications
Worms now mixing different kinds of attacks
  No longer just simple buffer overflows
High-level semantic vulnerabilities now most common threats
  SQL Injection, Cross Site Scripting, Directory Traversal, etc
  Easy to exploit; often architecture & OS independent
Need a new approach that is
  Robust, End-to-end, Practical, Flexible, Fast

## Slide 7: Motivation
High-level semantic vulnerabilities are prevalent in web-based attacks
  SQL injection – code inserted into entry field
  Cross-Site Scripting (XSS)
    Injected website sends malicious code to client
Real-World Examples:
  Website database breach
    The Wall Street Journal database in July 2014
  Twitter worms
statement = "SELECT * FROM users WHERE name ='" + userName + "';"
SELECT * FROM users WHERE name = ‘bob' OR '1'='1';
‘bob’ OR '1'='1
userName:
ERROR!

## Slide 8: Dynamic Information Flow Tracking
DIFT tags (taints) data from untrusted sources
  Each byte or word of memory, register has a taint bit
Taint status is propagated across instructions
  If any source operand is tainted, destination becomes tainted
Trap to OS if tainted data used unsafely
  Tainted pointer dereference
  Tainted jump address
  Tainted code
Can prevent memory corruption on unmodified binaries
Potential: Protect from low-level & high level threats

## Slide 9: What is DIFT?
DIFT – Dynamic Information Flow Tracking
  Associates a tag with every word of memory
  Tag is used to mark tainted data from untrusted sources
    Data produced from tainted data is also tainted
    Check tag when data is used for potentially unsafe operations (ex. Code Execution)
  Detects both low and high-level attacks
 | userName=
X | ‘bob’
X | OR
X | ‘1’=‘1
Tag
Data
'bob' OR '1'='1
userName:
User input
(untrusted)
Tag Check
SECURITY TRAP

## Slide 10: Limitations of Current DIFT Systems
Software-based DIFT
  On source code (incomplete coverage)
  Or transparently through dynamic binary instrumentation
Advantages
  Runs on existing hardware
  Flexible security policies
Disadvantages
  High overhead
  Cannot protect O/S
  Cannot protect self-modifying binaries
  Does not work well with multi-threaded applications

## Slide 11: Limitations of Current DIFT Systems
Hardware-based DIFT uses one, fixed security policy
  Can only solve one problem (e.g., memory corruption)  unsafe
    High-level attacks cannot be addressed
  Cannot adapt to code that violates policy assumptions  impactical
    E.g. glib uses alternate bounds checking instructions (index & 0x00FF)
  Vulnerable to attacks that exploit inflexibility of policies
BUT really fast
Hardware security exceptions generate OS traps
  Cannot protect OS  not end-to-end
  Cannot combine HW and SW to cover difficult cases  inflexible
    On a trap, just terminate the program…

## Slide 12: Raksha (Protection) Overview
Get the best of both worlds
  From H/W: fast check and propagation, work with any binary
  From S/W: flexible policies, high-level analysis & decisions
Goals
  Protect against high-level & low-level attacks
  Protect against multiple concurrent attacks
  Protect O/S code
    At least a major part of it

## Slide 13: RAKSHA Overview
Raksha follows the general DIFT model
  All state is extended by a 4-bit tag (registers & memory)
    4 independent 1-bit states
  Operations propagate tags from sources to destinations
  Operations check tags to identify security traps
New features
  Software-controlled check & propagate policies  flexibility
    Specify policy using check, propagate registers
    Fine-grain software control to avoid common pitfalls
    Flexibility allows us to catch wide range of bugs
  Up to 4 concurrently active policies  robustness
    One policy per tag bit
    Provide comprehensive protection against many bugs
  Low-overhead, user-level, security traps  end-to-end, flexibility
    Can extend with software; can check operating system

## Slide 14: Raksha Architecture and Features

## Slide 15: Policy Specification
Up to 4 1-bit policies in parallel
One check & propagate register per active security policy
Policies specified at granularity of primitive operation
  Int/FP Arithmetic, Move, Logical, Comparison, Execute
Instructions are decoded into ≥1 primitive operations
  Apply rules specified by check/prop regs to each operation
  Addresses basic pitfalls of previous designs
  Conditional Move is logic and move
  Good for CISC

## Slide 16
Memory address AND data tainted
Load address is tainted
Store address is tainted
Jump destination is tainted*
Branch condition is tainted*
System call arguments are tainted*
Return address register is tainted
Stack pointer is tainted
Memory address OR data tainted*
Security Checking Policies
Notes: undesired code is not executed

## Slide 17: Policy Specification Registers

## Slide 18: Check Policy: LOAD
Load r2,M[r1+offset]
Check Enables
  Check source address
    If Tagged(r1) then security trap
  Check source
    If Tagged(M[r1+offset]) then security trap
  Both Checks can be running simultaneously
Propagate Enables
  Propagate only from source address
  Propagate only from source
  Propagate both tags
    AND or OR mode

## Slide 19: Low Overhead Security Traps
On security Trap invoke pre-registered handler
  Handler in same address space as code under inspection
    Fast switch to S/W
  Handler invocation triggers a special “trusted mode”
  Trusted mode is orthogonal to user/kernel mode
Untrusted Mode
  Transparent tags
  Normal Checks and Propagations
Trusted Mode
  Visible tags, Tag Access & Manipulation Instructions
  No Checks / No Propagations

## Slide 20: Low Overhead Security Traps
Benefits
  Can check security of (most of the) OS
    Reduce the amount of code you really trust
  Coupling HW and SW security analysis is practical
    Low performance overhead
Drawback: A memory corruption can corrupt the security handler
  Solution: A security policy used to protect handler code & data
  Handler Code & data are tainted on initialization
  Policy does not allow access outside of trusted mode
  3 bits remaining…

## Slide 21: Tag Granulariity & Storage
Tag granularity
  HW maintains per word tag bits
  What if SW wants byte or bit granularity for some data?
  Maintain in SW using sandboxing & fast user-level traps
    Acceptable performance if not common case…
Tag storage
  Initial HW ⇒ +4 bits/word in registers, caches, memory
    12.5% storage overhead
  Multi-granularity tag storage scheme [Suh’04]
    Exploit tag similarity to reduce storage overhead
    Page-level tags ⇒ cache line-level tags ⇒ word-level tags

## Slide 22: Raksha-based LEON3

## Slide 23: Raksha Prototype System
Full-featured Linux system
  On-line since October 2006…
HW: modified Leon-3 processor
  Open-source, Sparc V8 processor, RISC
  Single-issue, in-order, 7-stage pipeline
  Modified RTL for processor & system
  First DIFT system on FPGA

## Slide 24: Raksha Software Infrastructure
Goal: run real-world software stack
  Running a full-featured Linux 2.6 on Raksha hardware
    Custom distribution booting over NFS
  Full GNU toolchain + glibc
    Over 120 packages total
  Set HW policies using preloaded shared libraries
Support enterprise software
  SSH
  Postgresql
  wu-ftpd
  Apache
  …

## Slide 25: Raksha Implementation Summary
Full-system prototype based on LEON 3
  Open source processor from Gaisler Research
  SPARC V8 compliant
Synthesized on Virtex 2 FPGA board
Parameter | Specification
Pipeline depth | 7 stages
Instruction Cache | 8KB
Data Cache | 32KB
Clock frequency | 20 Mhz
Block RAM utilization | 22%
4 input LUT utilization | 42%
Total increase in gates due to tags | 7.17%

## Slide 26: Raksha Implementation Summary
Overhead over original
  Logic: 7%
  Storage: 12.5%
  Clock frequency: none
Application performance
  Check/propagate tags ⇒ no slowdown
  Overhead depends on SW analysis
    Frequency of traps, SW complexity, …
Worst-case example from experiments
  Filtering low-level false positives/negatives
  Bzip2: +33% with Raksha’s user-level traps
  Bzip2: +280% with OS traps
Memory Speed???

## Slide 27: Performance Results
Overhead is analysis-dependent
  Proportional to exceptions frequency and handler duration
  Many analyses are very cheap
    Most high-level analyses invoked infrequently
  Buffer overflow protection can be most expensive
    If software is used to correctly filter false-positives/negatives
    AND with 2n-1 is bounds checking
Buffer overflow overhead
Program | Exception | OS trap
gcc | 1.01x | 1.04x
crafty | 1.01x | 1.02x
gzip | 1.31x | 3.60x
bzip2 | 2.99x | 18.80x
vortex | 1.34x | 3.41x

## Slide 28: Performance Results

## Slide 29: Performance – O/S and S/W traps

## Slide 30: H/W Policies for Security Experiments
Concurrent protection using 4 policies
Memory corruption (LL attacks)
  Propagate on arithmetic, load/store, logical
  Check on tainted pointer/PC use
  Trap handler untaints data validated by user code
String tainting (LL & HL attacks)
  Propagate on arithmetic, load/store, logical
  No checks
System call interposition (HL attacks)
  No propagation
  Check on system call in untrusted mode
  Trap handler invokes proper SW analysis
Sandboxing policy (for trap handler protection)
  Handler taints its own code & data
  Check on fetch/loads/stores in untrusted mode

## Slide 31: Security Experiments
Program | Lang. | Attack | Detected Vulnerability
Traceroute | C | Double Free | Tainted data ptr
Polymorph | C | Buffer Overflow | Tainted Code ptr
Wu-FTPD | C | Format String | Tainted”%n” in vfprintf string
Gzip | C | Directory Traversal | Open tainted dir
Wabbit | PHP | Directory Traversal | Escape Apache root w/ tainted ‘..’
OpenSSH | C | Command Injection | Excve tainted file
ProFTPD | C | SQL Injection | Tainted SQL command
Htdig | C++ | Cross-site Scripting | Tainted <script> tag
PhpSysInfo | PHP | Cross-site Scripting | Tainted <script> tag
Scry | PHP | Cross-site Scripting | Tainted <script> tag
Unmodified Sparc binaries from real-world programs
  Basic/net utilities, servers, web apps, search engine
Protection against low-level memory corruptions
  Both Control & non-control data attacks
1st DIFT architecture to detect semantic attacks
  Without needing to recompile applications
Protection is independent of programming language
  Catch suspicious behavior, regardless of language choice

## Slide 32: Lessons Learned
HW support for fine-grain tainting is crucial
  For both high-level and low-level attacks
  Provides fine-grain info to separate legal uses from attacks
Lesson from high-level attacks
  Check for attacks at system calls
  Provides complete mediation, independent language/library
Lessons from low-level attack
  Fixed policies from previous DIFT systems are broken
False positives & negatives even within glibc
  Problem: what constitutes validation of tainted data?
  Need new SW analysis to couple with HW tainting
    Raksha’s flexibility and extensibility are crucial

## Slide 33: SIFT: SMT based Information Flow Tracking

## Slide 34: Another design point
New ideas (to us):
  Parallelize the reference monitor thread
    Checking in parallel with execution – what are the implications?
  Hardware support for reference monitor generation
    Little hardware support for execution
    Use normal instructions and a spare SMT hardware context
  Some optimizations…

## Slide 35: Existing DIFT Schemes and Limitations
Hardware solutions:
  Taint propagation with extra busses
  Additional checking units
  Limitations
  intrusive changes to datapath design
Software solutions:
  More instructions to propagate and check taint
  Limitations
  High performance cost
  Source code recompilation

## Slide 36
t
r5
0
IFQ
1
0
r1
r4
r0
r2
r3
Instruction Decode
0
1
0
add r3,r1,r4
Exception Checking Logic
WriteBack
0
0
0
0
data
1
data
1
data
1
data
1
add r3 r1 r4
r4
r1
r1
r4
r1+r4
r1+r4
1
RF
ALU
MEM
+
t
1
0
1
Taint Computation Logic
Hardware –based DIFT
Existing
DIFT

## Slide 37
add r3 r1 r4
add r3 r1 r4
compiler
add r3 r1 r4
shr r2 r5 2
shl r0 r5 1
or r0 r2 r0
MEM
ALU
RF
IFQ
r1
r4
r0
r2
r3
Instruction Decode
WriteBack
data
data
data
data
00111100
01100000
or r5 r5 r0
and r2 r2 16
and r0 r0 16
r5 is used for storing taint information of remaining register file
A small region of memory is used to store taint information of memory
Software –based DIFT
Existing
DIFT

## Slide 38: SIFT (SMT-based DIFT)
Execute two threads on SMT processor
  Primary thread executes real program
  Security thread executes taint tracking instructions
Committed instructions from main thread generate taint checking instruction(s) for security thread
Instruction generation is done in hardware
Taint tracking instructions are stored into a buffer from where they are fed to the second thread context
Threads are synchronized at system calls

## Slide 39
Instruction Flow in SIFT

## Slide 40
SMT Datapath with SIFT Logic

## Slide 41
ALU
MEM
r1
r4
r0
r2
r3
Instruction Decode
add r3 r1 r4
WriteBack
0
0
1
1
1
1
0
data
data
data
data
0
r5
SIFT Generator
add r3 r1 r4
or r3 r1 r4
or r3 r1 r4
RF 1
IFQ 1
IFQ 2
1
0
0
1
0
0
RF 2
r1+r4
r1
r1+r4
1
0
1
1
r1
r1
r4
r4
r4
or
+
add r3 r1 r4
SIFT Example
Context-2
DIFT
Context-1
Shared Resources

## Slide 42
SIFT Instruction Generation Logic
1. Taint Code Generation
2. Secutiry Instruction Opcodes are read from COT
3. Rest of the instructions are taken from Register Organizer and stored Instruction Buffer
4. Load and Store Instruction’s memory addresses are stored in Address Buffer

## Slide 43
Die Floorplan with SIFT Logic
SUN T1 Open Source Core
IGL synthesized using Synopsys Design Compiler using a TSMC 90nm standard cell library
COT, IB and AB implemented using Cadence Virtuoso
The integrated processor netlist placed and routed using Cadence SoC Encounter
Cost 4.5% of whole processor area

## Slide 44
Software is not involved, transparent to user and applications (although the checking code can also be generated in software)
Hardware instruction generation is faster than software generation
Additional hardware is at the back end of the pipeline, it is not on the critical path
No inter-core communication
Benefits of Taint Checking with SMT

## Slide 45: Number of Security Instructions per Primary Thread Instruction
Chart: Checking Inst per Main Inst
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
 | 1.756 | 1.7975 | 2.1452 | 1.8317 | 1.5077 | 1.8358 | 1.786 | 1.6329 | 1.6813 | 2.1314 | 1.7302 | 1.795 | 2.6199 | 2.0098 | 1.6755 | 1.8172 | 2.2698 | 1.7111 | 1.5923 | 1.8931 | 1.6174 | 1.7194 | 2.0838 | 1.8539

## Slide 46
Chart: Performance Loss
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
 | 0.33301 | 0.56368 | 0.4541 | 0.4172 | 0.37607 | 0.45761 | 0.41744 | 0.25947 | 0.48004 | 0.59128 | 0.53281 | 0.32011 | 0.45827 | 0.37956 | 0.51208 | 0.33316 | 0.41075 | 0.45444 | 0.43398 | 0.35414 | 0.32278 | 0.43805 | 0.4928 | 0.42578
SIFT Performance Overhead

## Slide 47
Reduce the number of checking instructions by eliminating the ones that never change the taint state.
Reduce data dependencies in the checker by preloading taint values into its cache once the main program encounters the corresponding address
Reduce the number of security instructions depending on taint state of registers and TLB
SIFT Performance Optimizations

## Slide 48
lda r0,24176(r0)
xor r9,3,r2
addq r0,r9,r0
ldah r16,8191(r29)
ldq_u r1,0(r0)
lda r16,-26816(r16)
lda r0,1(r0)
lda r18,8(r16)
extqh r1,r0,r1
sra r1,56,r10
bne r2,0x14
and r9,255,r9
stl r3,32(r30)
ldl r2,64(r2)
lda r16,48(r30)
bic r2,255,r2
bis r3,r2,r2
bis r0,r0,r0
bis r9,r9,r2
bis r0,r9,r0
bis r29,r29,r16
ldq_u r1,0(r0)
bis r1,r0,r1
bne r1,0xfffffffffffff080
bis r16,r16,r16
bis r0,r0,r0
bis r16,r16,r18
bis r1,r0,r1
bis r1,r1,r10
bne r2,0xfffffffffffff080
bis r9,r9,r9
bis r3,r30,r3
bne r3,0xfffffffffffff080
stl r3,32(r30)
ldl r2,64(r2)
bis r2,r2,r2
bne r2,0xfffffffffffff080
bis r30,r30,r16
bis r2,r2,r2
bis r3,r2,r2
bis r9,r9,r2
bis r0,r9,r0
bis r29,r29,r16
ldq_u r1,0(r0)
bis r1,r0,r1
bne r1,0xfffffffffffff080
bis r16,r16,r18
bis r1,r0,r1
bis r1,r1,r10
bne r2,0xfffffffffffff080
bis r3,r30,r3
bne r3,0xfffffffffffff080
stl r3,32(r30)
ldl r2,64(r30)
bne r2,0xfffffffffffff080
bis r30,r30,r16
bis r3,r2,r2
Primary Thread
SIFT Security Thread
SIFT – F Security Thread
Eliminating Checking Instructions

## Slide 49
SIFT Logic with Instruction Elimination

## Slide 50
Chart: SIFT and SIFT-F Performance
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
SIFT | 0.33301 | 0.56368 | 0.4541 | 0.4172 | 0.37607 | 0.45761 | 0.41744 | 0.25947 | 0.48004 | 0.59128 | 0.53281 | 0.32011 | 0.45827 | 0.37956 | 0.51208 | 0.33316 | 0.41075 | 0.45444 | 0.43398 | 0.35414 | 0.32278 | 0.43805 | 0.4928 | 0.42578
SIFT-F | 0.25652 | 0.52407 | 0.39714 | 0.3887 | 0.33187 | 0.39902 | 0.41171 | 0.17467 | 0.4513 | 0.53896 | 0.49374 | 0.28266 | 0.43669 | 0.30386 | 0.47538 | 0.30015 | 0.36914 | 0.37446 | 0.34498 | 0.27972 | 0.25743 | 0.37118 | 0.46686 | 0.37523
Chart: Percentage of Instructions Filtered by SIFT-F
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
 | 0.25986 | 0.1853 | 0.16877 | 0.28799 | 0.16737 | 0.19658 | 0.17407 | 0.4456 | 0.22937 | 0.2479 | 0.18896 | 0.18091 | 0.21186 | 0.19104 | 0.26154 | 0.22791 | 0.17811 | 0.24431 | 0.33867 | 0.22837 | 0.3011 | 0.24602 | 0.17943 | 0.23222
Performance Impact of Eliminating Security Instructions

## Slide 51
Chart: SIFT and SIFT-P Performance
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
SIFT | 0.33301 | 0.56368 | 0.4541 | 0.4172 | 0.37607 | 0.45761 | 0.41744 | 0.25947 | 0.48004 | 0.59128 | 0.53281 | 0.32011 | 0.45827 | 0.37956 | 0.51208 | 0.33316 | 0.41075 | 0.45444 | 0.43398 | 0.35414 | 0.32278 | 0.43805 | 0.4928 | 0.42578
SIFT-P | 0.29329 | 0.42275 | 0.40239 | 0.1929 | 0.36599 | 0.45429 | 0.26816 | 0.10177 | 0.4318 | 0.5134 | 0.48441 | 0.27093 | 0.15313 | 0.093777 | 0.284 | 0.033938 | 0.07591 | 0.44331 | 0.35769 | 0.34703 | 0.27671 | 0.4209 | 0.49135 | 0.31217
Chart: SIFT L1 Cache Misses
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
SIFT | 3.3498 | 8.0658 | 1.8992 | 4.0018 | 8.9434 | 7.9017 | 75.1781 | 4.9802 | 6.2873 | 3.6678 | 2.7207 | 6.4981 | 46.6814 | 33.3038 | 7.7464 | 70.8842 | 17.3112 | 0.23669 | 5.7389 | 13.7855 | 2.4704 | 0.81154 | 0.00782 | 14.4553
SIFT-F | 0.00576 | 0.09777 | 0.00118 | 0.00889 | 0.03013 | 0.1656 | 0.0283 | 8e-05 | 0.01605 | 0.00229 | 0.01222 | 0.03026 | 6e-05 | 0.13672 | 0.00072 | 0.11443 | 0.1874 | 0.0086 | 0.02135 | 0.08628 | 0.00336 | 0.00013 | 0 | 0.041634
Performance Impact of Cache Prefetching

## Slide 52
Chart: PErformance Loss
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
SIFT | 0.33301 | 0.56368 | 0.4541 | 0.4172 | 0.37607 | 0.45761 | 0.41744 | 0.25947 | 0.48004 | 0.59128 | 0.53281 | 0.32011 | 0.45827 | 0.37956 | 0.51208 | 0.33316 | 0.41075 | 0.45444 | 0.43398 | 0.35414 | 0.32278 | 0.43805 | 0.4928 | 0.42578
SIFT-F | 0.25652 | 0.52407 | 0.39714 | 0.3887 | 0.33187 | 0.39902 | 0.41171 | 0.17467 | 0.4513 | 0.53896 | 0.49374 | 0.28266 | 0.43669 | 0.30386 | 0.47538 | 0.30015 | 0.36914 | 0.37446 | 0.34498 | 0.27972 | 0.25743 | 0.37118 | 0.46686 | 0.37523
SIFT-P | 0.29329 | 0.42275 | 0.40239 | 0.1929 | 0.36599 | 0.45429 | 0.26816 | 0.10177 | 0.4318 | 0.5134 | 0.48441 | 0.27093 | 0.15313 | 0.093777 | 0.284 | 0.033938 | 0.07591 | 0.44331 | 0.35769 | 0.34703 | 0.27671 | 0.4209 | 0.49135 | 0.31217
SIFT-FP | 0.21168 | 0.38735 | 0.35759 | 0.13851 | 0.31359 | 0.39683 | 0.26258 | 0.050051 | 0.40446 | 0.43388 | 0.44124 | 0.22786 | 0.095973 | 0.072005 | 0.20754 | 0.030989 | 0.064253 | 0.35906 | 0.26545 | 0.27296 | 0.20374 | 0.35052 | 0.47242 | 0.26176
SIFT Performance on a 8-way Issue Processor

## Slide 53
Chart: PErformance Loss
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
SIFT-FP | 0.21168 | 0.38735 | 0.35759 | 0.13851 | 0.31359 | 0.39683 | 0.26258 | 0.050051 | 0.40446 | 0.43388 | 0.44124 | 0.22786 | 0.095973 | 0.072005 | 0.20754 | 0.030989 | 0.064253 | 0.35906 | 0.26545 | 0.27296 | 0.20374 | 0.35052 | 0.47242 | 0.26176
SIFT-FP (ISA Support) | 0.11083 | 0.32143 | 0.33801 | 0.088251 | 0.28857 | 0.32041 | 0.23426 | 0.028469 | 0.36845 | 0.33213 | 0.34941 | 0.12474 | 0.032807 | 0.049425 | 0.10749 | 0.026537 | 0.038891 | 0.22043 | 0.19561 | 0.18599 | 0.13363 | 0.23073 | 0.42957 | 0.19809
Performance Effect of ISA Support

## Slide 54
Chart: PErformance Loss
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
SIFT-FP | 0.21168 | 0.38735 | 0.35759 | 0.13851 | 0.31359 | 0.39683 | 0.26258 | 0.050051 | 0.40446 | 0.43388 | 0.44124 | 0.22786 | 0.095973 | 0.072005 | 0.20754 | 0.030989 | 0.064253 | 0.35906 | 0.26545 | 0.27296 | 0.20374 | 0.35052 | 0.47242 | 0.26176
SIFT-FP(Separate Cache) | 0.20597 | 0.38104 | 0.35728 | 0.1373 | 0.31209 | 0.39544 | 0.26083 | 0.050039 | 0.40449 | 0.42356 | 0.44045 | 0.23059 | 0.09595 | 0.068576 | 0.20725 | 0.029915 | 0.062923 | 0.35889 | 0.26357 | 0.26147 | 0.20287 | 0.34726 | 0.47239 | 0.25957
SIFT-FP(Separate Perfect Cache) | 0.17366 | 0.27616 | 0.34514 | 0.10476 | 0.29168 | 0.37847 | 0.03062 | 0.049949 | 0.17159 | 0.31616 | 0.37084 | 0.20626 | 0.089831 | 0.063331 | 0.20666 | 0.011916 | 0.062509 | 0.35886 | 0.24363 | 0.24752 | 0.17943 | 0.34469 | 0.461 | 0.21672
Performance Effect of Cache Sharing

## Slide 55
Chart: PErformance Loss
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
policy 1 | 0.13217 | 0.34017 | 0.34659 | 0.10305 | 0.30407 | 0.36832 | 0.22648 | 0.023764 | 0.37725 | 0.4202 | 0.38168 | 0.15922 | 0.094198 | 0.071843 | 0.13054 | 0.027495 | 0.064301 | 0.25311 | 0.177 | 0.21642 | 0.14949 | 0.25478 | 0.45202 | 0.22062
policy 2 | 0.13424 | 0.34059 | 0.34659 | 0.10305 | 0.30452 | 0.36997 | 0.22703 | 0.023764 | 0.37784 | 0.42403 | 0.38482 | 0.15925 | 0.094198 | 0.071843 | 0.13055 | 0.027646 | 0.064314 | 0.26136 | 0.18367 | 0.22705 | 0.15167 | 0.26072 | 0.45651 | 0.22284
policy 3 | 0.21168 | 0.38735 | 0.35759 | 0.13851 | 0.31359 | 0.39683 | 0.26258 | 0.050051 | 0.40446 | 0.43388 | 0.44124 | 0.22786 | 0.095973 | 0.072005 | 0.20754 | 0.030989 | 0.064253 | 0.35906 | 0.26545 | 0.27296 | 0.20374 | 0.35052 | 0.47242 | 0.26176
Policy 1 – No Checking only propagation
Policy 2 – Jump Targets, Return Address, Stack Pointer
Policy 3 – Jump Targets, Branch Conditions, System Call Arguments, Memory data and address
SIFT-FP with Different Policies

## Slide 56
Multicore SIFT

## Slide 57
Chart: Performance Loss
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
MSIFT | 0.090504 | 0.38601 | 0.364 | 0.36885 | 0.23361 | 0.31773 | 0.32418 | 0.19687 | 0.12177 | 0.37395 | 0.2787 | 0.21771 | 0.45817 | 0.42163 | 0.42236 | 0.21814 | 0.41692 | 0.27432 | 0.31378 | 0.17911 | 0.135 | 0.26035 | 0.31846 | 0.29096
MSIFT-FP | 0.055615 | 0.22742 | 0.20248 | 0.070845 | 0.17077 | 0.23695 | 0.02749 | 0.037428 | 0.071345 | 0.23493 | 0.19485 | 0.19859 | 0.073747 | 0.074543 | 0.00015236 | 0.019857 | 0.039053 | 0.21343 | 0.21174 | 0.11114 | 0.071687 | 0.21 | 0.22567 | 0.12955
Multicore SIFT Performance

## Slide 58
Chart: Performance Loss
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
MSIFT | 0.090504 | 0.38601 | 0.364 | 0.36885 | 0.23361 | 0.31773 | 0.32418 | 0.19687 | 0.12177 | 0.37395 | 0.2787 | 0.21771 | 0.45817 | 0.42163 | 0.42236 | 0.21814 | 0.41692 | 0.27432 | 0.31378 | 0.17911 | 0.135 | 0.26035 | 0.31846 | 0.29096
MSIFT-FP | 0.055615 | 0.22742 | 0.20248 | 0.070845 | 0.17077 | 0.23695 | 0.02749 | 0.037428 | 0.071345 | 0.23493 | 0.19485 | 0.19859 | 0.073747 | 0.074543 | 0.00015236 | 0.019857 | 0.039053 | 0.21343 | 0.21174 | 0.11114 | 0.071687 | 0.21 | 0.22567 | 0.12955
MSIFT-FP 32 Entry Buffer | 0.069254 | 0.22638 | 0.24213 | 0.08548 | 0.039701 | 0.21137 | 0.031694 | 0.026697 | 0.080586 | 0.16716 | 0.21218 | 0.18446 | 0.068938 | 0.054272 | 3.6277e-05 | 0.019897 | 0.03711 | 0.20564 | 0.1794 | 0.14087 | 0.086019 | 0.21717 | 0.2684 | 0.12412
MSIFT-FP 128 Entry Buffer | 0.01369 | 0.18162 | 0.12691 | 0.020445 | 0.0041909 | 0.088474 | 0.024153 | 0.0067271 | 0.038521 | 0.11093 | 0.1501 | 0.10836 | 0.015061 | 0.041204 | 7.2553e-06 | 0.016815 | 0.013949 | 0.14334 | 0.14885 | 0.031427 | 0.037347 | 0.1442 | 0.17715 | 0.071455
MSIFT-FP Inf. Buffer | 0.0037743 | 0.073676 | 0.14814 | 0.013673 | 2.6609e-05 | 0.0014743 | 0.0040137 | 0.006711 | 0.0037589 | -0.00044596 | 0.012431 | 0.04379 | 1.2456e-06 | 0.034659 | 7.2553e-06 | 0.015898 | 0.0034461 | 0.064465 | 0.14526 | -0.027073 | 0.021248 | 0.01395 | 0.15282 | 0.031987
MSIFT with Different Buffer Sizes

## Slide 59
Chart: Performance Loss
| astar | bzip2 | cactusADM | calculix | dealII | gamess | gcc | GemsFDTD | gobmk | gromacs | h264ref | hmmer | lbm | leslie3d | libquantum | mcf | milc | namd | omnetpp | povray | sjeng | sphinx3 | zeusmp | avg
MSIFT-FP | 0.055615 | 0.22742 | 0.20248 | 0.070845 | 0.17077 | 0.23695 | 0.02749 | 0.037428 | 0.071345 | 0.23493 | 0.19485 | 0.19859 | 0.073747 | 0.074543 | 0.00015236 | 0.019857 | 0.039053 | 0.21343 | 0.21174 | 0.11114 | 0.071687 | 0.21 | 0.22567 | 0.12955
MSIFT-FP Perfect Cache | 0.049128 | 0.22449 | 0.18898 | 0.0696 | 0.16812 | 0.23387 | 0.020654 | 0.037427 | 0.069555 | 0.22185 | 0.19399 | 0.18767 | 0.073746 | 0.074525 | 0.00015236 | 0.019845 | 0.039053 | 0.21322 | 0.21108 | 0.10998 | 0.069818 | 0.20973 | 0.22541 | 0.1266
MSIFT-FP Perfect Cache (32 Entry) | 0.062395 | 0.22377 | 0.23054 | 0.084321 | 0.022032 | 0.20729 | 0.025296 | 0.026695 | 0.079042 | 0.12887 | 0.21125 | 0.18079 | 0.063287 | 0.053573 | 2.1766e-05 | 0.019868 | 0.026237 | 0.2051 | 0.1788 | 0.13885 | 0.084364 | 0.21713 | 0.26816 | 0.11903
MSIFT-FP Perfect Cache (128 Entry) | 0.0087126 | 0.18006 | 0.11813 | 0.019543 | 2.6609e-05 | 0.083704 | 0.017791 | 0.0067271 | 0.037313 | 0.071412 | 0.14916 | 0.10436 | 0.0001121 | 0.040816 | 7.2553e-06 | 0.016751 | 0.016899 | 0.14324 | 0.14836 | 0.028196 | 0.035912 | 0.14399 | 0.17678 | 0.067305
MSIFT-FP Perfect Cache Inf. Buffer | 0.0037743 | 0.057461 | 0.033251 | 0.013673 | 2.6609e-05 | 0.0014743 | 0.0040137 | 0.006711 | 0.0037589 | -0.00044596 | 0.012431 | 0.04379 | 1.2456e-06 | 0.034659 | 7.2553e-06 | 0.015898 | 0.0034461 | 0.064437 | 0.032995 | -0.027073 | 0.021248 | 0.0177 | 0.15282 | 0.021568
Multicore SIFT with Perfect Cache

## Slide 60
Discussion
Collapse multiple checking instructions via ISA?
Optimize resource sharing between two threads?
Provide additional execution units for the checker?
Using memory page granularity taint?

## Slide 61: General RM Hardware support
Is this a good idea?
  What are the benefits
What would it look like? Parallel checking model? Custom Hardware?
How do you retask it for different reference monitors?
Can we benefit from both software optimizations and hardware acceleration?