## Slide 1: Code Reuse Attacks (II)
Slide credits: some slides and figures adapted from David Brumley, AC Chen, and others

## Slide 2: Signature-Based Detection
CRAs have a distinctive signature
  Gadgets-gadgets-gadgets
Some early work attempted to detect anomalies in the branch predictor
“DROP: Detecting ROP malicious code”
  P. Chen et al. ICISS 2009
    if (# instructions between returns <= 5) then it is a gadget
    if (# consecutive gadgets >= 3) then it is a ROP attack

## Slide 3: DROP
Gadget Length
max tolerable gadget length for CRA
min # gadgets to launch a CRA
Consecutive Gadgets
Regular workloads
CRAs
N=5
S=3
Implemented in software
5x slowdown
Can we do better?

## Slide 4: Building on DROP
Apply the same idea to
  Indirect jumps
  Indirect calls
Adjust the thresholds

## Slide 5: Extending DROP for JOP
max tolerable gadget length for CRA
min # gadgets to launch a CRA
Regular workloads
CRAs
Indirect jumps/calls are not that frequent
Added dispatcher gadgets

## Slide 6: Case of Long Gadgets
Side effects
  Overwrite registers/memory locations
  May cause exceptions
    adc [ebx-0x74EBDBAC], cl
  Limited number of registers
    One for the dispatcher
    One for jumping back to the dispatcher
    Only 6 left (in x86)

## Slide 7: Gadget Length and State Changes
Chart: Gadget Length
| 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0
State Changes ≤ 2 | 0.29907 | 0.1759 | 0.065362 | 0.01856 | 0.0043804 | 0.00095317 | 0.00019972 | 7.0053e-05 | 0 | 0
State Changes ≤ 1 | 0.19815 | 0.05724 | 0.014821 | 0.0026987 | 0.00042004 | 6.3545e-05 | 0 | 0 | 0 | 0

## Slide 8: Defeating DROP
Make the attack pattern less predictable
  Perform some unnecessary computation
  Without harming attack state
Call a function
  Execute many instructions
  Return to the same point in the attack
  Caller saved registers stay intact
    ebx, esi, edi, esp, ebp

## Slide 9: Delay Gadgets
call [ecx-0x56000a00]
add bl, bh
inc ebx
add dh, bh
jmp edi
Dispatcher
Gadget
Functional
Gadget
Delay
Gadget
add [ebx], edx
jmp esi
pop eax
jmp eax
atoi()

## Slide 10: Summary of DROP Limitations
Implemented in software
  5x slowdown
Tight margin for detecting ROP
  False positives/negatives
Easily defeated by using delay gadgets

## Slide 11: Another proposal: SCRAP
Signature-Based CRA Protection
Detects CRAs with delay gadgets
No false positives for regular workloads
Implemented in hardware
  Low overhead
  Protects legacy binaries

## Slide 12: Attack Signatures
Symbol | Instruction
w | Indirect Jump
x | Indirect Call
y | Call
z | Return
a | All Other
DROP-like Signature Definition:
Up to N instructions
S or more gadgets

## Slide 13: SCRAP Attack Signatures
Symbol | Instruction
w | Indirect Jump
x | Indirect Call
y | Call
z | Return
a | All Other
Signatures with delay gadgets (N=5, S=3):
Attack has 3 parts
Each part has a Gadget and Delays
A Gadget has up to 5 instructions
Delay is a function call
A function call can be a Delay as long as it is not an Attack itself

## Slide 14: Example Signatures
Signature | Detected by DROP-like? | Detected by SCRAP?
aaawaawaaw
awaaxaaaaw
awaxaaaaaazaxaw
awaxaayaazaaaazaxaw
✔ | ✔
✘ | ✔
✔ | ✔
✘ | ✔

## Slide 15: Pushdown Automata

## Slide 16: Simple Implementation
Augment the stack of PDA with Secure Call Stack
  Save the PDA state for calls
  Restore for returns
  Modify for indirect jumps
Commit throttling
  Only one stack operation for a commit window
  Negligible slowdown
  Simplifies the circuitry

## Slide 17: SCRAP Hardware

## Slide 18: False Positives for SCRAP
CRAs
Gadget Length
Consecutive Gadgets
5
6
7
8
9
10
11
12
13
1
2
3
4
5
6
SPEC 2006 benchmarks
140 Shell-storm CRA exploits

## Slide 19: Performance of SCRAP

## Slide 20: Conclusions
Signature-based detection of CRAs is promising
  No source code, simple, low-overhead, effective
Naïve approaches can be defeated
  Delay gadgets
But is SCRAP really more secure?
  Are there other ways to hide?
  Paper introduces another detector that tolerates longer gadgets
    Becomes harder to avoid false positives
  Attacks can be short

## Slide 21: Gadget Length
Long gadget means more intermediate instructions
Chart: Gadget Length
| 1.0 | 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 35.0 | 40.0 | 45.0 | 50.0
 | 0.30361 | 0.4747 | 0.56867 | 0.64819 | 0.68916 | 0.71807 | 0.73494 | 0.75663 | 0.7759 | 0.78554 | 0.79759 | 0.80482 | 0.81928 | 0.83133 | 0.84096 | 0.8506 | 0.85301 | 0.86265 | 0.86988 | 0.87711 | 0.88434 | 0.89157 | 0.89398 | 0.89639 | 0.9012 | 0.91325 | 0.92048 | 0.9253 | 0.93253 | 0.93494 | 0.93735 | 0.93976 | 0.94217 | 0.94458 | 0.95181 | 0.95422 | 0.95904 | 0.96386 | 0.96627 | 0.97108 | 0.97831 | 0.98795 | 0.99277 | 0.99277 | 0.99518 | 0.99518 | 1 | 1 | 1 | 1

## Slide 22: Two threshold SCRAP

## Slide 23: Our story so far…
Unauthorized Control Information Tampering
http://propercourse.blogspot.com/2010/05/i-believe-in-duct-tape.html
Notes: We have conducted analysis on the 107 CERT advisories from 2000 to 2003.
Our survey of the CERT advisories indicates that UCIT vulnerabilities account for 65% of advisory entries.
http://research.microsoft.com/en-us/um/people/shuochen/papers/ieee-proc.pdf
Journal version of “XKI03” in CFI slides from Princeton.

## Slide 24: How to really solve the problem?
Prevent buffer overflows? How? Later
Prevent illegal control flow? Hmm….
Control Flow Integrity (CFI), Abadi et al, CCS 2005
  Important paper in security
  Control flow: how your program counter changes
  Control flow altering instructions: branches, calls, returns, …
  CFI: How to specify and preserve legal control flow in a program
    How does this help with CRAs?
    Discussion: how do we approach this problem?

## Slide 25: CFI: Control-Flow Integrity
Main idea: pre-determine control flow graph (CFG) of an application
  Static analysis of source code
  Static binary analysis  CFI
  Execution profiling
  Explicit specification of security policy
Execution must follow the pre-determined control flow graph
[Abadi et al.]

## Slide 26: Control Flow Integrity
protects against powerful adversary
  with full control over entire data memory
widely-applicable
  language-neutral; requires binary only
provably-correct & trustworthy
  formal semantics; small verifier
efficient
  hmm… 0-45% in experiments; average 16%
Notes: The box around “data memory” is to highlight we’re going to limit the power of the attacker for memory with instructions.

## Slide 27: CFI Adversary Model
CAN
Overwrite any data memory at any time
  stack, heap, data segs
Overwrite registers in current context
CANNOT
Execute Data
  NX takes care of that
Modify Code
  text seg usually read-only
Write to %ip
  true in x86
Overwrite registers in other contexts
  kernel will restore regs

## Slide 28: CFI Overview
Invariant: Execution must follow a path in a control flow graph (CFG) created ahead of run time.
Method:
build CFG statically, e.g., at compile time
instrument (rewrite) binary, e.g., at install time
  add IDs and ID checks; maintain ID uniqueness
verify CFI instrumentation at load time
  direct jump targets, presence of IDs and ID checks, ID uniqueness
perform ID checks at run time
  indirect jumps have matching IDs
“static”
Notes: source code analysis, or even security automata

## Slide 29: CFI: Binary Instrumentation
Use binary rewriting to instrument code with runtime checks
Inserted checks ensure that the execution always stays within the statically determined CFG
  Whenever an instruction transfers control, destination must be valid according to the CFG
Goal: prevent injection of arbitrary code and invalid control transfers (e.g., return-to-libc)
  Secure even if the attacker has complete control over the thread’s address space

## Slide 30: CFG Example

## Slide 31: CFI: Control Flow Enforcement
For each control transfer, determine statically its possible destination(s)
Insert a unique bit pattern at every destination
  Two destinations are equivalent if CFG contains edges to each from the same source
    This is imprecise (why?)
  Use same bit pattern for equivalent destinations
Insert binary code that at runtime will check whether the bit pattern of the target instruction matches the pattern of possible destinations

## Slide 32: CFI: Example of Instrumentation
Original code
Instrumented code
Abuse an x86 assembly instruction to
insert “12345678” tag into the binary
Jump to the destination only if
the tag is equal to “12345678”

## Slide 33: CFI: Preventing Circumvention
Unique IDs
  Bit patterns chosen as destination IDs must not appear anywhere else in the code memory except ID checks
Non-writable code
  Program should not modify code memory at runtime
    What about run-time code generation and self-modification?
Non-executable data
  Program should not execute data as if it were code
Enforcement: hardware support + prohibit system calls that change protection state + verification at load-time

## Slide 34: Improving CFI Precision
Suppose a call from A goes to C, and a call from B goes to either C, or D (when can this happen?)
  CFI will use the same tag for C and D, but this allows an “invalid” call from A to D
  Possible solution: duplicate code or inline
  Possible solution: multiple tags
Function F is called first from A, then from B; what’s a valid destination for its return?
  CFI will use the same tag for both call sites, but this allows F to return to B after being called from A
  Solution: shadow call stack

## Slide 35: CFI: Security Guarantees
Effective against attacks based on illegitimate control-flow transfer
  Stack-based buffer overflow, return-to-libc exploits, pointer subterfuge, code reuse attacks
Does not protect against attacks that do not violate the program’s original CFG
  Incorrect arguments to system calls
  Substitution of file names
  Other data-only attacks

## Slide 36: Possible Execution of Memory
[Erlingsson]

## Slide 37: Control Flow Integrity
Generate Control Flow Graph
  Unique labels for edges
Instrument the code with checks
  Each indirect branch checks target for a label
...
cmp [ecx], 12345678h
jne error_label
lea ecx, [ecx+4]
jmp ecx
...
...
mov eax, [esp+4]
...
...
jmp ecx
...
...
<data 12345678h>
mov eax, [esp+4]
...
Source
Destination
CFI
instrumentation
Added instructions

## Slide 38: CFI Limitations
Need to construct Control Flow Graph
  Sometimes difficult; especially for obfuscated code
  No publicly available tools for constructing CFG from binaries
    This is changing
Runtime performance overhead due to extra instructions
  About 20% for SPEC 2K6 Benchmarks
Problems with dynamic linking
Indirect branches are a headache
Does not handle unintended instructions
Imprecise

## Slide 39: Where Do Jump Targets Go?
Typical use of indirect jump instruction
  To efficiently implement switch-case statements
    Target is in the same function
  To support dynamic linking
    Target is a function entry point
Key Observation:
Legitimate jump targets ARE NOT in the middle of another function

## Slide 40: Branch Regulation
Enforce the following rules:
  Returns go to the correct addresses
  Jumps target same functions or function entry points
  Calls target function entry points
Use hardware checks for enforcement
  Low performance overhead (around 2%)
  Unintended instructions are handled
  No CFG needed
  Requires minimal binary annotations
Security shown for common libraries

## Slide 41: How Does BR Mitigate JOP Attacks?
0x0000
0xFFFF
Stack growth
Stack frame for main()
Stack frame for vulnerable()
xor ecx, ecx
mul ecx
lea ebx, [esp+8] mov al, 11
int 0x80
malicious return
pop edi
jmp edi
lea ebx, [esp+8]
jmp esi
mov al, 11
int 0x80
mul ecx
jmp esi
<register values>
<C>
<D>
<F>
<E>
<B>
xor ecx, ecx
jmp esi
popa
jmp esi
function1()
function2()
NOT ALLOWED

## Slide 42: Implementing Branch Regulation
Use a Secure Call Stack
Annotate function entry points with function size info
Compare jump targets with function bounds and allow if checks pass
Store bounds in secure call stack
Cache a few secure stack entries for performance

## Slide 43: Inserting Code Annotations
080483e4 <main>:
80483e4: push ebp
80483e5: mov ebp, esp
...
80483f9: mov eax, 0
80483fe: leave
80483ff: ret
...
08048410 g F .text 005a __libc_csu_init
080483e4 g F .text 001c main
080482b8 g F .init 0000 _init
...
080483d2 <main>:
80483d2: <annotation> <size=001c>
80483e4: push ebp
80483e5: mov ebp, esp
...
80483f9: mov eax, 0
80483fe: leave
80483ff: ret
Original Code
Annotated Code
Symbol Table

## Slide 44: Executing Call Instruction
call
eax
.
.
.
8048232: call eax
.
.
.
80482bc: <annotation> 0x98
80482be: push esp
80482C0: …
.
.
.
8048300: jmp ecx
.
.
.
8048354: ret
.
.
.
Fetch
Decode
Execute
Commit
Instruction Cache
call eax
… | … | …
Base | Bound | Return
… | … | …
BR Check
Function Bounds Stack
<annotation> 0098
80482bc
80482bc
<annotation>
0098
(function size)
80482bc | 8048354 | 8048236

## Slide 45: Executing Jump Instruction
jmp
ecx
.
.
.
0x8048232: call eax
.
.
.
0x80482BC: <annotation> 0x98
0x80482BE: push esp
0x80482C0: …
.
.
.
0x8048300: jmp ecx
.
.
.
0x8048354: ret
.
.
.
Fetch
Decode
Execute
Commit
Instruction Cache
jmp ecx
… | … | …
Base | Bound | Return
… | … | …
BR Check
Function Bounds Stack
0x80483AA
0x80482BC| 0x8048354 | 0x8048236
0x80482BC
>
0x8048354
>

## Slide 46: Executing Return Instruction
ret
.
.
.
0x8048232: call eax
.
.
.
0x80482BC: <annotation> 0x98
0x80482BE: push esp
0x80482C0: …
.
.
.
0x8048300: jmp ecx
.
.
.
0x8048354: ret
.
.
.
Fetch
Decode
Execute
Commit
Instruction Cache
ret
… | … | …
Base | Bound | Return
… | … | …
BR Check
Function Bounds Stack
0x8048236
0x80482BC| 0x8048354 | 0x8048236
0x8048236
=
Return Address
from Stack

## Slide 47: Security of Branch Regulation
Effectively reduces the exploitable code base to the current function
An attacker needs to find in same function:
  A vulnerability to exploit
  Sufficient functional gadgets
  Dispatcher gadget
  A system call instruction

## Slide 48: Number of Vulnerable Functions
Library
libc
libm
libcrypto
libgcrypt
libssl
Functions with Dispatcher Gadget and System Call
0
0
0
0
0
Functions with Dispatcher Gadget
12
0
3
2
0
Total Number of Functions
7775
1077
7991
1135
1017

## Slide 49: Unintended Instructions
Mostly garbage instructions
Usually more side effects than intentional
Chart: Number of Gadgets
| NO-BR | DGP | DGC | DGC-SSE | DGC-SYS
intended | 4925 | 458 | 419 | 62 | 0
unintended | 19764 | 972 | 850 | 353 | 0
24689
4925

## Slide 50: Additional Security Analysis in the Paper
Analysis of available gadgets
Dispatcher gadget discovery algorithms
Analysis of gadget side effects
  Gadget length
  Impact of unintended gadgets

## Slide 51: Increase of Executable Size
Chart: Executable Size Increase
| perlbench | bzip2 | gcc | mcf | gobmk | hmmer | sjeng | libquantum | h264ref | omnetpp | xalancbmk | milc | namd | dealII | soplex | povray | lbm | sphinx3 | avg
Control Flow Integrity | 0.047992 | 0 | 0.042984 | 0 | 0.015593 | 0.048079 | 0.027867 | 0.045535 | 0.024365 | 0.079616 | 0.094149 | 0.033008 | 0.0082248 | 0.044626 | 0.075102 | 0.044156 | 0.021363 | 0.040633 | 0.038516
Branch Regulation | 0.011836 | 0 | 0.010178 | 0 | 0.0036894 | 0.012049 | 0.0034833 | 0.013065 | 0.0078036 | 0.02266 | 0.019437 | 0.0060015 | 8.5973e-05 | 0.013166 | 0.020902 | 0.016065 | 0.0053408 | 0.012276 | 0.009891

## Slide 52: Impact of Secure Stack Cache Size
Chart: Cache size
 | 0.1573 | 0.059007 | 0.040245 | 0.021376 | 0.011411 | 0.011463 | 0.010449 | 0.01098 | 0.010378

## Slide 53: BR Performance with 4-Entry Cache
Chart: Slowdown
| perlbench | bzip2 | gcc | mcf | gobmk | hmmer | sjeng | libquantum | h264ref | omnetpp | xalancbmk | milc | namd | dealII | soplex | povray | lbm | sphinx3 | avg
Control Flow Integrity | 0.37394 | 0.024096 | 0.15129 | 0.060374 | 0.25873 | 0.043458 | 0.24326 | 0.0037068 | 0.39172 | 0.52639 | 0.48166 | 0.024606 | 0.023985 | 0.13573 | 0.15401 | 0.57763 | 0.070118 | 0.53863 | 0.22685
Branch Regulation | 0.045282 | 0.0065976 | 0.047162 | 0.042024 | 0.020465 | -9.1764e-05 | 0.00061203 | 3.0783e-05 | 0.00085264 | 0.052898 | 0.067376 | 0.0066017 | 0.019566 | -0.0029307 | 0.037769 | 0.031494 | 4.3588e-06 | 0.016411 | 0.021785

## Slide 54: Another CFI Solution point: CFI Mon
Some solutions try to reuse existing hardware
  Use performance monitoring unit on x86
  kBouncer: use Last Branch Record (LBR)
  CFIMon: use the branch target store to implement a CFI reference monitor

## Slide 55: Precision Mode of Intel CPU ---Branch Trace Store (BTS) Mechanism
Record all control transfer precisely into a predefined buffer
  jump, call, return, interrupt and exception
  also record the addresses of branch source and target
Let a monitor get the trace in a batch
  an interrupt will be delivered when the buffer is nearly full
Obtain all the branch information of a running application, help users locate the vulnerabilities
Notes: To accurately and effectively identify an attack, CFIMon needs precise information of every branch at runtime for detection
since the monitor can obtain
all the branch information of a running application, it
can not only detect security attacks, but also identify the
control flow of the execution of malicious code, thus
help users locate the vulnerabilities

## Slide 56: Main Idea
The CFI of an application can be maintained if we can
  get a legal set of branch target addresses for every branch
  check whether the target address of every branch is within the corresponding legal set at runtime

## Slide 57: Branch Classification in X86 ISA ---Direct Branch & Its Target Address
Direct Branch
  Direct jump
    jnz c2ef0 <__write>
  Direct call
    callq 34df0 <abort>
Since the code is read-only and cannot be modified during runtime, both the direct jump and direct call are considered safe one
(safe branch) √

## Slide 58: Branch Classification in X86 ISA ---Indirect Branch & Its Target Address
Indirect Branch
  Indirect jump
    jmpq *%rdx
    not possible to gain the whole target address set just by static analysis
  Indirect call
    callq *%rax
    its target address could be obtained by statically scanning the binary code of the application and the libraries it uses
  Return
    retq
    its target address could also be obtained by scanning the binary code.
(unsafe branch) √
A call can only transfer control to the
start of a function.
In general, the target address of a return has to be the one next to a call
Dynamic Training
Notes: A return instruction branches to an address popped from the stack, which could only be determined during
runtime. Since a function maybe be invoked through a function pointer, we cannot know exactly all of its callers. Fortunately, we finds that in most cases, a return follows a call instruction

## Slide 59: CFIMon: 2 Phases
Offline phase
  build a legal set of target addresses for each branch instruction
Online phase
  diagnose possible attacks with legal sets following a number of rules
    determine the status of the branch as legal, illegal or suspicious

## Slide 60: Offline Analysis --- obtain legal set: ret_set, call_set
Scans the binary of application and dynamic libraries to get
  ret_set
    contains all addresses of the instructions next to each call
    special cases
  call_set
    contains all addresses of the first instruction of each function
.
.
add(3,4);
printf(“TEST!”);
.
.
ret_set
int add
(int a, int b){
printf(“1st inst.”);
.
.
}
call_set

## Slide 61: Online Detection
<source,target>
special case?
<source> is direct
branch?
legal
illegal
suspicious
ret_set
call_set
train_set
yes
no
yes
no
yes
yes
no
yes
no
no
<source> is indirect call
<source> is return
<source> is indirect jump
Consider the state of a branch depending on <target>
switch into
different cases
based on <source>
slide-window
mechanism

## Slide 62: Architecture
A kernel extension
A user-level tool with 2 modules

## Slide 63: Slide-Window Mechanism ---For Suspicious Branches
The diagnose module makes a flexible decision depending on the pattern of the branches
  maintain a window of the states of recent n branches
  apply a rule of tolerating at most m suspicious branches in the recent n ones
    i.e., at most m suspicious branches are accepted in recent n branches

## Slide 64: Summarizing CFI
Need to construct the CFG
  Binary analysis, based on source, based on profiling (CFIMon), etc…
Need to enforce legal control flow
  Does not completely solve the problem but makes it much harder
  Imprecise and therefore attackable (papers last year and this year show how to construct CRAs that bypass CFI approximations)
More precise but requires significantly more work/information than the two other defense categories.

## Slide 65: Discussion/Consolidation
CRAs are an open problem
  Almost every solution has weaknesses
  Assumptions (spoken or unspoken) typically become the target of the attack
Three general approaches
  Moving target
  Signature detection
  CFI – our first example of a reference monitor
We focused on implementations that had a hardware component
  Advantages include: overhead; unintended branches; binary compatibility …