## Slide 1: Exploiting modern architectures
Slide credit: some slides from Lucas Davi and others

## Slide 2
Introduction
Read the kernel memory
Bypass security mechanism (ASLR)
Bypass sandboxing
Critical vulnerabilities in modern processors
Vulnerability originates in architecture
  Difficult to fix!

## Slide 3: Outline
First we will set the table
  Ingredient 1: Side channel and covert channel attacks
  Ingredient 2: Speculation and branch predictor
Meltdown and Spectre
  Spectre (Branch target injection)
  Spectre (Bypassing bound check)
  Meltdown
  What else is out there?
Possible defenses
  Software defenses
  New architectures

## Slide 4: Ingredient 1: Covert/Side channels

## Slide 5
Microarchitecture side channels
Program security relies on isolation
  Process boundary
  Process vs. kernel
  Sandboxing
  Virtual machines, …
Modern processors support multiple programs running at the same time
    Isolation broken at architecture level
  Side channels galore!!
    What one process does can affect others
  What are examples?

## Slide 6: Cache Side-Channel Attack
f2 85 5c 06
6a 91 4e 0c
c4 fc da a8
d5 37 e9 9c
28 1e 4c 24
09 bf 15 82
30 6f 53 d9
a4 49 2d 0e
S-Box
SubBytes
Set-associative cache
ways
sets

## Slide 7: Flush+Reload Attack
Cache
L2
L1-I
Victim
1- Flush each line in the critical data
2- Victim accesses critical data
3- Reload critical data (measure time)
Evicted
Time
CPU1
ways
sets
L1-D
L2
L1-I
Attacker
L1-D
Shared L3
CPU2

## Slide 8: Prime+Probe: L1 Attack
L1 Cache
ways
sets
L2
L1-I
L1-D
Attacker
Victim
2-way SMT core
1- Prime each cache set
2- Victim accesses critical data
3- Probe each cache set (measure time)
Evicted
Time

## Slide 9: Attack on Critical Table

## Slide 10: Its not just the CPU

## Slide 11: Side and covert channels are everywhere!
Paper under review– vulnerability reported to Nvidia

## Slide 12: Ingredient 2: Speculative Execution

## Slide 13: First lets start with pipelining
Fetch
Reg
Read
ALU
Data
Memory
Reg
Write
Notes: Modern times – available on netflix

## Slide 14: Control hazards!

## Slide 15: Enter branch predictors

## Slide 16: Putting it all together– Attacks!

## Slide 17: Some observations about speculation
Speculated instructions can be any old nonsense
  We’ll clean up later
No checks of permissions.
  Permissions not ready to check
  No danger – we will squash instructions if wrong
  Even security extensions do not work
Speculation causes exposure
  Through side channels
  Through physical exposure (e.g., memory bus)

## Slide 18: General Idea of all attacks
Fool the processor to speculatively execute some instructions such that:
  The instructions access sensitive data without permission
    (basically a covert transmitter)
  The data is exposed through a side channel
We read it from the side channel  broke isolation
Can read kernel memory; memory out of a sandbox; basically break software isolation based on permissions

## Slide 19
Three published variants of attack
Spectre : bounds check bypass (CVE-2017-5753)
Spectre: branch target injection (CVE-2017-5715)
Meltdown: rogue data cache load (CVE-2017-5754)

## Slide 20: Spectre: Variant 1 : bounds check bypass

## Slide 21: Variant 1: bypassing bound check
Read out of bound memory

## Slide 22: Variant 1: bypassing bound check
Assumption:
These value are not cached:
arr1->length
arr2->data[0x200]
arr2->data[0x300]

## Slide 23: Variant 1: bypassing bound check
Assumption:
The branch conditions are predicted as true
Speculatively:
  load value = arr1->data[untrusted_offset_from_caller]
  start a load from a data-dependent offset in arr2->data, loading the corresponding cache line into the L1 cache

## Slide 24: Variant 1: bypassing bound check
measuring the time required to load arr2->data[0x200] andarr2->data[0x300]
Discloses whether arr1->data[untrusted_offset_from_caller]&1 is 0 or 1

## Slide 25: Spectre: Variant 2 : branch target injection

## Slide 26: Jump-over-ASLR: Attack Overview
Use Branch Target Buffer (BTB) to recover random address bits
Two scenarios:
  One user space process attacking another
  User process attacking Kernel ASLR
Attack capabilities:
  Control speculation of another process
  Recover all random bits in Linux Kernel and KVM*
  Recover part of random bits in User Process making brute force attack much faster
* https://github.com/felixwilhelm/mario_baslr/

## Slide 27: Branch Target Prediction Mechanism
Virtual Address space
jmp
A:
B:
Address tag | Target
Branch Target Buffer
A
B

## Slide 28: User-Level Attack
Spy
Victim
jmp
Address tag | Target
A:
B:
A
B
jmp
A:
B:
C:
Branch Target Buffer
Observation: HIT
Observation: MISPREDICTION

## Slide 29: Latencies Observed by the Spy on Haswell Processor

## Slide 30: Variant 2: branch target injection background(Branch Target Buffer)
V
BIA
BTA
Branch PC
Branch Target
Address
=
Valid Bit
Hit?
Branch Instruction
Address (Tag)
Next Fetch PC

## Slide 31: Big Picture
Data Area
Code Area
Victim process
Chosen
Payload
2
Adversary can inject address of ROP gadget into the BTB
3
CPU run the ROP payload speculatively
1
Adversary knows the binary of the app
4
ROP payload leaks the data through side channel

## Slide 32: Meltdown: Variant 3: rogue data cache load

## Slide 33: Variant 3: rogue data cache load background

## Slide 34: Variant 3: rogue data cache load background

## Slide 35: Variant 3: rogue data cache load background
Instruction decoder reads bytes from memory, parse the buffer and output instructions
Map architectural register to physical register
Insert instruction into reservation stations after renaming
Keep track of readiness of source values of an instruction

## Slide 36: Variant 3: rogue data cache load background
  When all source values of an instruction are ready, dispatch the instruction to functional unit (FU)
  When a micro op is finished executing the result and exception status are added to the entry in the reorder buffer thus resolving dependencies of other micro ops

## Slide 37: Variant 3: rogue data cache load background
  An instruction updates the register alias table (essentially a future file for other instruction in the pipeline) when it completes execution
  An instruction updates the architectural register file when it is the oldest in the machine(oldest in reorder buffer) and has completed execution

## Slide 38: Variant 3: rogue data cache load explanation
Idea:
The permission check for accessing an address might not be on the critical path for reading data from memory to a register (permission check could have significant performance impact)
Memory read could make the result of the read available to following instructions immediately
Setting a flag in the reorder buffer that causes an exception to be raised if the permission check fails

## Slide 39: Variant 3: rogue data cache load explanation
1 rcx = kernel address
2 rbx = prob array
3
4
5
6
7
Step 1 The content of an attacker-chosen memory location, which is inaccessible to the attacker, is loaded into a register.
Executes instructions in the small time window between the illegal memory access and the raising of the exception
Notes: The instruction sequence from step 1 which is executed out of order has to be chosen in a way that it becomes a transient instruction sequence. If this transient instruction sequence is executed before the MOV instruction is retired (i.e., raises the exception), and the transient instruction sequence performed computations based on the secret, it can be utilized to transmit the secret to the attacker

## Slide 40: Variant 3: rogue data cache load explanation
1 rcx = kernel address
2 rbx = prob array
3
4
5
6
7
Step 2 A transient instruction accesses a cache line based on the secret content of the register
(line 5-7)
Notes: The instruction sequence from step 1 which is executed out of order has to be chosen in a way that it becomes a transient instruction sequence. If this transient instruction sequence is executed before the MOV instruction is retired (i.e., raises the exception), and the transient instruction sequence performed computations based on the secret, it can be utilized to transmit the secret to the attacker

## Slide 41: Variant 3: rogue data cache load explanation
1 rcx = kernel address
2 rbx = prob array
3
4
5
6
7
Step 3 The attacker uses Flush+Reload to determine the accessed cache line and hence the secret stored at the chosen memory location.
Notes: The instruction sequence from step 1 which is executed out of order has to be chosen in a way that it becomes a transient instruction sequence. If this transient instruction sequence is executed before the MOV instruction is retired (i.e., raises the exception), and the transient instruction sequence performed computations based on the secret, it can be utilized to transmit the secret to the attacker

## Slide 42: Defenses (short term/software)

## Slide 43: Kernel Page Table Isolation (KPTI)
Key Idea: Separate user space and kernel space
Each application has two sets of pages tables rather than one and switches between them on every kernel-to-user and user-to-kernel transition
Overhead on every system call, interrupt, etc..
Does not work for software sandboxes, or variant 2

## Slide 44: Retpoline:(return + trampoline)
Retpoline:(return + trampoline)
Google’s defense against Spectre variant 2
  Variant 2 is super dangerous for the cloud
  Allows one application to disclose information of another
Uses another feature of modern processors called the Return Address Stack
  Instead of predicting the return address through the branch target buffer, we keep the return value on a stack
  When we retrun, we read it from the stack
Replace indirect branches with a return

## Slide 45: Retpoline:(return + trampoline)
Background:
Subroutine Calls
A: 0xFC34: CALL printf
B: 0xFD08: CALL printf
C: 0xFFB0: CALL printf
P: 0x1000: (start of printf)
0x1000
FC3
1
0x1000
FD0
1
0x1000
FFB
1
  BTB can easily predict target of calls

## Slide 46: Retpoline:(return + trampoline)
Background:
Subroutine Returns
  BTB can easily predict target of calls
P: 0x1000: ST $RA  [$sp]
0x1B98: LD $tmp  [$sp]
A: 0xFC34: CALL printf
B: 0xFD08: CALL printf
A’:0xFC38: CMP $ret, 0
B’:0xFD0C: CMP $ret, 0
0x1B9C: RETN $tmp
0xFC38
1B9
0
1
X
  BTB can’t predict return for multiple call sites

## Slide 47: Retpoline:(return + trampoline)
Background: Return Address Stack (RAS)
Keep track of call stack
A: 0xFC34: CALL printf
FC38
D004
P: 0x1000: ST $RA  [$sp]
…
0x1B9C: RETN $tmp
FC38
BTB
A’:0xFC38: CMP $ret, 0
FC38

## Slide 48: Variant 2: branch target injection Defenses: Retpoline
Retpoline:(return + trampoline)
Make a direct call to set_up_target.
  Generates distinct stack and RSB entries with a return target of capture_spec.
Notes: Make a direct call to set_up_target; this is known at compile time and will not trigger speculative target resolution. This generates distinct stack and RSB entries with a return target of capture_spec.

## Slide 49: Variant 2: branch target injection Defenses: Retpoline
Retpoline:(return + trampoline)
2. Modify the on-stack entry generated by (1), to instead direct to %r11.
Notes: Make a direct call to set_up_target; this is known at compile time and will not trigger speculative target resolution. This generates distinct stack and RSB entries with a return target of capture_spec.

## Slide 50: Variant 2: branch target injection Defenses: Retpoline
Retpoline:(return + trampoline)
3. Return against our original call
Speculative execution consumes the RSB entry generated by (1), and is captured within the pause loop at (4). These instructions are only executed by the speculative path.
Our return is ultimately retired, the on-stack value is used to locate the actual new instruction pointer and the benign results of any speculative execution in the loop at (4) are discarded
Notes: Make a direct call to set_up_target; this is known at compile time and will not trigger speculative target resolution. This generates distinct stack and RSB entries with a return target of capture_spec.

## Slide 51: Thinking ahead – what is next?

## Slide 52: Things that make you go hmmm…
Speculation is very old
  Architectures have been vulnerable for over 30 years
  But then only discovered now? Why?
    Suspected for a long time; 1992 paper
    Discovered concurrently by at least 4 teams!
    “things we don’t know we don’t know” – Donald Rumsfled 
Offensive security research is important
  Sometimes not considered seriously
What else is out there?
How can we fix it?

## Slide 53: New Attacks
Unfortunately, many more variants are appearing
  New side channels: attacks through the L1 cache, and the TLBs
  New applications: Other attacks demonstrated on SGX
Branchscope? Attack on the directional part of the branch predictor
SpectreRSB/ret2spec: use the return stack buffer
SpectrePrime and MeltdownPrime
  New attacks from Princeton/Nvidia using the cache coherence/memory consistency protocol

## Slide 54: Principled/comprehensive solutions
One proposal – disable speculation
  Use parallelism instead
  Ugh…back to the dark ages of computer architecture
Keep speculation, but make it safe
  New ways of designing architectures
  SafeSpec (our proposal)
  Poison Ivy (Micro 2016)
  Safe branch predictors:
    Decorrelated/private branch predictors
    Control Flow Integrity based branch predictors

## Slide 55: Principled/comprehensive solutions
One proposal – disable speculation
  Use parallelism instead
  Ugh…back to the dark ages of computer architecture
Software patches
  Often address one aspect of the attack (not all variants)
  High overhead: 10%-30% (Netflix reported 800% slowdown for Meltdown patches)
Intel Microcode updates
  Stops speculation where dangerous (problems similar to disable speculation solution)
Future/principled fixes
  Keep speculation, but make it safe: SafeSpec
  Randomization?

## Slide 56: SafeSpec
Use temporary structures (Shadow) to hold any state that is produced speculatively
Notes: State the limitations

## Slide 57: Implementation and Results
Integrated SafeSpec to MARSSx86
Evaluated the performance using SPEC2017

## Slide 58: Conclusions/Summary
Security traditionally considered a software problem to be solved in software
…but we see that architectures can be a source of vulnerability
  Architectures must be designed with security in mind
  …but they can also offer security mechanisms for software
Meltdown/Spectre will force a seismic rethinking of how to design architectures
  Will be played out over the next few years…