## Slide 1: Adversarial Evasion-Resilient Hardware Malware Detectors
Nael Abu-Ghazaleh
Joint work with Khaled Khasawneh, Dmitry Ponomarev and Lei Yu

## Slide 2: Malware is Everywhere!

## Slide 3: Malware is Everywhere!
Over 250,000 malware registered every day!

## Slide 4: Hardware Malware Detectors (HMDs)
Use Machine Learning: detect malware as computational anomaly
Use low-level features collected from the hardware
Can be always-on without adding performance overhead
Many research papers including ISCA’13, HPCA’15 and MICRO’16

## Slide 5: Overview
Reverse-engineer HMDs
Develop evasive malware
Evade detection after re-training
Can malware evade detection?

## Slide 6: Overview
Reverse-engineer HMDs
Develop evasive malware
Evade detection after re-training
Can malware evade detection?
If yes
Can we make HMDs robust to evasion?
Yes! using RHMD
1- Provably harder to reverse-engineer
2- Robust to evasion

## Slide 7: Reverse Engineering

## Slide 8: How to Reverse Engineer HMDs?
Challenges:
  We don’t know the detection period
  We don’t know the features used
  We don’t know the detection algorithm
Approach:
  Train different classifiers
  Derive specific parameters as an optimization problem

## Slide 9: Reverse Engineering HMDs
Attacker Training Data
_________________________

## Slide 10: Reverse Engineering HMDs
Victim HMD
Black box
output
10100
Attacker Training Data
_________________________

## Slide 11: Reverse Engineering HMDs
Victim HMD
Black box
output
10100
Attacker Training Data
_________________________
Training model
Labels
Data

## Slide 12: Reverse Engineering HMDs
Victim HMD
Black box
output
10100
Attacker Training Data
_________________________
Training model
Reverse-engineered HMD
Data
Labels

## Slide 13: We Can Guess Detectors Parameters!
Victim HMD parameters:
  - 10K detection period - Instructions features vector

## Slide 14: We Can Guess Detectors Parameters!
Victim HMD parameters:
  - 10K detection period - Instructions features vector
Guessing detection period:
LR: Logistic Regression
DT: Decision Tree
SVM: Support Vector Machines

## Slide 15: We Can Guess Detectors Parameters!
Victim HMD parameters:
  - 10K detection period - Instructions features vector
Guessing feature vector:
LR: Logistic Regression
DT: Decision Tree
SVM: Support Vector Machines

## Slide 16: Reverse Engineering Effectiveness
Logistic Regression
Neural Networks
Victim HMD

## Slide 17: Reverse Engineering Effectiveness
Logistic Regression
Neural Networks
Current generation of HMDs can be reverse engineered

## Slide 18: Evading HMDs

## Slide 19: How to Create Evasive Malware?
Challenges:
  - We don’t have malware source code
  - We can’t decompile malware because its obfuscated
  Our approach:
Dynamic Control Flow Graph
PIN

## Slide 20: What we Should Add to Evade?
Logistic Regression (LR)
  LR is defined by a weight vector θ
  Add instructions whose weights are negative

## Slide 21: What we Should Add to Evade?
Neural Network (NN)
  Collapse the description of the NN into a single vector
  Add instructions whose weights are negative

## Slide 22: What we Should Add to Evade?
Neural Network (NN)
  Collapse the description of the NN into a single vector
  Add instructions whose weights are negative
Current generation of HMDs are vulnerable to evasion attacks!

## Slide 23: Does re-training Help?

## Slide 24: Can we Retrain with Samples of Evasive Malware?
Linear Model (LR)

## Slide 25: Can we Retrain with Samples of Evasive Malware?
Linear Model (LR)
  Non-Linear Model (NN)

## Slide 26: Explaining Retraining Performance
Linear Model (LR)

## Slide 27: Explaining Retraining Performance
Non-Linear Model (NN)

## Slide 28: What if we Keep Retraining?

## Slide 29: What if we Keep Retraining?

## Slide 30: What if we Keep Retraining?

## Slide 31: What if we Keep Retraining?

## Slide 32: What if we Keep Retraining?
Re-training is not a general solution

## Slide 33: Can we Build Detectors that Resist Evasion?

## Slide 34: Overview of RHMDs
HMD
1
HMD
2
HMD
n
.
.
.
RHMD
Pool of diverse
HMDs

## Slide 35: Overview of RHMDs
HMD
1
HMD
2
HMD
n
.
.
.
Selector
Output
Input
RHMD

## Slide 36: Overview of RHMDs
Number of committed instructions
Detection period
0
…
Features vector
HMD
1
HMD
2
HMD
n
.
.
.
Selector
Output
Input
RHMD

## Slide 37: Overview of RHMDs
Number of committed instructions
Detection period
0
…
…
Features vector
HMD
1
HMD
2
HMD
n
.
.
.
Selector
Output
Input
RHMD

## Slide 38: Overview of RHMDs
Number of committed instructions
Detection period
0
…
…
…
Features vector
HMD
1
HMD
2
HMD
n
.
.
.
Selector
Output
Input
RHMD

## Slide 39: Overview of RHMDs
Number of committed instructions
Detection period
0
…
…
…
Features vector
HMD
1
HMD
2
HMD
n
.
.
.
Selector
RHMD
Diversify by Different:
1- Features
2- Detection periods

## Slide 40: Reverse Engineer RHMDs
2 feature vectors
3 feature vectors
Randomizing the features

## Slide 41: Reverse Engineer RHMDs
Randomizing the features & detection period
2 feature vectors & 2 periods
3 feature vectors & 2 periods

## Slide 42: RHMD is Resilient to Evasion

## Slide 43: Hardware Overhead
FPGA prototype on open core (AO486):
RHMD with three detectors:
  Area increase 1.72%
  Power increase 0.78%

## Slide 44: Transferability
Given an evasive malware crafted to evade Detector A how likely would it evade Detector B
Detector A
Detector B
Craft evasive
malware
Target
How likely it
will evade?

## Slide 45: Impact on RHMDs?
RHMD resilient to black-box attacks
  Making reverse engineering is not accurate
Transferability help understanding resilience to
  White-box attack: attacker knows some/all base detectors
  Gray-box attacks: attacker has access to training data

## Slide 46: Intra-algorithm Transferability

## Slide 47: Cross-algorithm Transferability

## Slide 48: Combined Transferability

## Slide 49: Final thoughts
Machine learning will be prevalent in systems
  Already used in a number of predictors
Especially true as systems and applications continue to evolve
Important to understand implications and design for resilience against adversarial attacks

## Slide 50: Thank you!
Questions?

## Slide 51: Can’t Just Randomly Add Instructions

## Slide 52: Evasion Overhead