## Slide 1: A High-Resolution Side-Channel Attack on Last-Level Cache
Mehmet Kayaalp, IBM Research
Nael Abu-Ghazaleh, University of California Riverside
Dmitry Ponomarev, State University of New York at Binghamton
Aamer Jaleel, Nvidia Research
The 53rd Design Automation Conference (DAC), Austin, TX, June 8, 2016

## Slide 2: Cache Side-Channel
f2 85 5c 06
6a 91 4e 0c
c4 fc da a8
d5 37 e9 9c
28 1e 4c 24
09 bf 15 82
30 6f 53 d9
a4 49 2d 0e
S-Box
SubBytes
Set-associative cache
ways
sets

## Slide 3: Flush+Reload Attack
Cache
L2
L1-I
Victim
1- Flush each line in the critical data
2- Victim accesses critical data
3- Reload critical data (measure time)
Evicted
Time
CPU1
ways
sets
L1-D
L2
L1-I
Attacker
L1-D
Shared L3
CPU2

## Slide 4: Prime+Probe: L1 Attack
L1 Cache
ways
sets
L2
L1-I
L1-D
Attacker
Victim
2-way SMT core
1- Prime each cache set
2- Victim accesses critical data
3- Probe each cache set (measure time)
Evicted
Time

## Slide 5: Prime+Probe: LLC Attack
L2
L1-I
Victim
2- Victim accesses critical data
CPU1
L1-D
L2
L1-I
Attacker
L1-D
Shared L3
CPU2
1- Prime each cache set
3- Probe each cache set (measure time)
Inclusive
Evict critical data
Back-invalidations
Challenges:
Find collision groups for each cache set
  Discover hardware details
  Identify a minimal set of addresses per cache set
Find which are the critical cache sets
  Find which cache sets incur the most slowdown for the victim
  Among those, look for the expected access pattern

## Slide 6: Discovering LLC Details
Intel Sandy Bridge die
4x Cores
4x 2MB
LLC Banks
virtual page number
page offset
Virtual Address
0
12
63
tag
set index
L1 Access
0
12
63
line offset
physical page number
page offset
Physical Address
0
12
35
tag
LLC Access
17
35
6
set index
0
line offset
6
Hash
bank select

## Slide 7: Bank Selection and Cavity Sets
tag
17
35
set index
0
line offset
6
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
●
XOR
H0
H1
<H0, H1>:
<00>
<11>
<01>
<10>
Number of ways:
15
16
16
16
cavity
sets

## Slide 8: Finding Collision Groups
…
number of ways
Memory Page
same set index
same set index
x N = Cache Size
N = (8 MB / 4 KB / 16)
= 128
ɸ = { }
Add page ρ to ɸ
Measure ∆t = t( ɸ ) - t( ɸ - ρ )
If ∆t is high
For each ρi∈ ɸ
Measure ∆ti = t( ɸ ) - t( ɸ - ρi )
Add ρi to the new group if ∆ti is high
Remove the group from ɸ
Repeat until N groups are found
ways
N

## Slide 9: Finding Critical Sets

## Slide 10: Attack on Instructions
for round = 1:9
if round is even
/* even rounds */
else
/* odd rounds */
/* last round */
sets
time

## Slide 11: Attack on Critical Table

## Slide 12: Attack Analysis
True Positive Rate
# true critical accesses observed
# all critical accesses of the victim
False Discovery Rate (FDR)
# false critical accesses observed
# all measurements of the attacker
Cache Side-Channel Vulnerability (CSV)
CSV = Pearson-correlation (Attacker trace, Victim trace)
TPR =
FDR =

## Slide 13: Comparison to Flush+Reload

## Slide 14: Summary
A new high-resolution Prime+Probe LLC attack is proposed
It does not rely on large pages or the sharing of cryptographic data between the victim and the attacker
Mechanisms to discover precise groups of addresses that map into the same LLC set in the presence of:
  Physical indexing
  Index hashing
  Varying cache associativity across the LLC sets
Concurrent attack on the instruction and data tp improve the signal and reduce the noise
Not limited to AES and can be applied to attacking any ciphers that rely on pre-computed cryptographic tables (e.g. Blowfish, Twofish)