## Slide 1: Impala: Algorithm/Architecture Co-Design for In-Memory Multi-Stride Pattern Matching
Elaheh Sadredini*, Reza Rahimi*, Marzieh Lenjani,
Mircea Stan, and Kevin Skadron
The 26th IEEE International Symposium on High-Performance Computer Architecture (HPCA 2020)
* Equal contribution
** This work is funded, in part, by the NSF (CCF-1629450) and CRISP, one of six centers in JUMP, a Semiconductor Research Corporation (SRC) program sponsored by MARCO and DARPA.
I am in the academic job market this year!

## Slide 3: Pattern Processing Is the Performance Bottleneck in Many Big-Data Applications
Network Security
Bioinformatics
Marketing
Virus Scanning
Natural Language Processing
Database

## Slide 4: Motivating Example: Network Security
Snort Rule Set
Rule 1
Rule 2
. . .
Rule N
Network Intrusion Detection System
Packet
Malicious
or
Non-malicious
Demand for high-throughput pattern matching
Rule size or complexity
Increasing network line rate

## Slide 5: Finite Automata for Pattern Recognition Languages
Regular expression: (ab+|ba+) c
Non-deterministic Finite Automata (NFA)
Non-deterministic
Finite Automata (NFA)
Deterministic
Finite Automata (DFA)

## Slide 6: Finite Automata for Pattern Recognition Languages
Regular expression: (ab+|ba+) c
Input:
a |  |  | 
Non-deterministic Finite Automata (NFA)

## Slide 7: Finite Automata for Pattern Recognition Languages
Regular expression: (ab+|ba+) c
Input:
a |  |  | 
Non-deterministic Finite Automata (NFA)

## Slide 8: Finite Automata for Pattern Recognition Languages
Regular expression: (ab+|ba+) c
Input:
a | b |  | 
Non-deterministic Finite Automata (NFA)

## Slide 9: Finite Automata for Pattern Recognition Languages
Regular expression: (ab+|ba+) c
Input:
a | b | c | ...
Non-deterministic Finite Automata (NFA)

## Slide 10: Challenges: von Neumann Processors Easily Become Memory Bound
Unpredictable behavior (branch misprediction)
Irregular access pattern (cache miss)
Many parallel patterns (saturate memory bandwidth)

## Slide 11: Why In-Memory Processing is Suitable for Pattern Matching?
Significance and Generality
Parallelism
Simplicity
Memory Bound

## Slide 12
Non-deterministic finite automata processing
with
Processing in-memory architecture

## Slide 13
Regular expression:
Equivalent
Homogenous model aligns well with HW implementation

## Slide 14
Potential next states
1 | 1 | 1 | 0
State match vector
1 | 1 | 0 | 0
Next Active States
1 | 1 | 0 | 0
Bitwise AND
C

## Slide 15
Potential next states
1 | 1 | 1 | 0
State match vector
1 | 1 | 0 | 0
Next Active States
1 | 1 | 0 | 0
Bitwise AND
C

## Slide 16
Potential next states
1 | 1 | 1 | 0
State match vector
1 | 1 | 0 | 0
Next Active States
1 | 1 | 0 | 0
Bitwise AND
C
(10)

## Slide 17
Potential next states
1 | 1 | 1 | 0
State match vector
1 | 1 | 0 | 0
Next Active States
1 | 1 | 0 | 0
Bitwise AND
C
(10)

## Slide 18
Potential next states
1 | 1 | 1 | 0
State match vector
1 | 1 | 0 | 0
Next Active States
1 | 1 | 0 | 0
Bitwise AND
C
(10)

## Slide 19: Challenges in PIM Solutions
Symbol Sparsity
8-bit processing
Algorithm PIM Architecture
Throughput
Area Efficiency
Energy Efficiency

## Slide 20: Overview of Our Solution
8-bit NFA
FlexAmata
Engine
4-bit NFA
Squashing
Area Efficiency
Energy Efficiency
Architecture Implication
Reducing sparsity

## Slide 21: Overview of Our solution
4-bit NFA
FlexAmata
Engine
16-bit NFA
Vectorized Striding
Throughput Gain
8-bit NFA
FlexAmata
Engine
4-bit NFA
Squashing
Area Efficiency
Energy Efficiency
Architecture Implication
Longer and Serial  Shorter and Parallel

## Slide 22: Vectorized Temporal Squashing and Striding (V-TeSS)

## Slide 23: Vectorized Temporal Squashing and Striding (V-TeSS)

## Slide 24: Vectorized Temporal Squashing and Striding (V-TeSS)
Average 1.68X state overhead
(1X – 5.11x)

## Slide 25: Vectorized Temporal Squashing and Striding (V-TeSS)

## Slide 26: Vectorized Temporal Squashing and Striding (V-TeSS)
False positive:
\xF, \xC, \xF, \xB

## Slide 27: Vectorized Temporal Squashing and Striding (V-TeSS)
Broader impact: minimizing multi-value variables in PIM solutions

## Slide 28: Hardware Support: Impala
Area-efficiency: One 256× 256  four 16×256 blocks
Throughput efficiency: 8-bit processing  16-bit processing
Lower energy: smaller subarray size

## Slide 29: Hardware Support: Impala
Area-efficiency: One 256× 256  four 16×256 blocks
Throughput efficiency: 8-bit processing  16-bit processing
Lower energy: smaller subarray size
At the expense of higher one time pre-processing time

## Slide 30: Scalable Interconnect
State Matching Subarrays
State Matching Subarrays
State Matching Subarrays
State Matching Subarrays
Tuesday, 4:10pm, Best of CAL Session

## Slide 31: Scalable Interconnect
Source State
Destination State
Visualization of interconnect resources
A
B
C
D
A
B
C
D

## Slide 32: Scalable Interconnect
Source State
Destination State
Visualization of interconnect resources
Breadth first labeling

## Slide 33: Scalable Interconnect
Source State
Destination State
Visualization of interconnect resources
Genetic Algorithm

## Slide 34: Comparison Across Architectures
 |  | Memory | Processing Rate | Throughput (Gbps) | Area () | Throughput/area (Gbps/)
von Neumann | XeonPhi | NA | 8 bits/cycle | 0.13 | ~400 | <0.001
 | GPU | NA | 8 bits/cycle | 0.5 | ~300 | 0.002
 | ASIC (HARE) | NA | 8 bits/cycle | 3.9 | 80 | 0.04
Memory-Centric | FPGA | LUT/BRAM | 16 bits/cycle | 3.47 | 45 | 0.07
 | Automata Processor | DRAM | 8 bits/cycle | 1 | 38 | 0.03
 | Cache Automaton | SRAM | 8 bits/cycle | 28.8 | 4.3 | 6.7
 | Impala (our solution) | SRAM | 16 bits/cycle | 80 | 3.2 | 25
 |  | Memory | Processing Rate | Throughput (Gbps) |  | 
von Neumann | XeonPhi | NA | 8 bits/cycle | 0.13 | ~400 | <0.001
 | GPU | NA | 8 bits/cycle | 0.5 | ~300 | 0.002
 | ASIC (HARE) | NA | 8 bits/cycle | 3.9 | 80 | 0.04
Memory-Centric | FPGA | LUT/BRAM | 16 bits/cycle | 3.47 | 45 | 0.07
 | Automata Processor | DRAM | 8 bits/cycle | 1 | 38 | 0.03
 | Cache Automaton | SRAM | 8 bits/cycle | 28.8 | 4.3 | 6.7
 | Impala (our solution) | SRAM | 16 bits/cycle | 80 | 3.2 | 25
Performance factors: Throughput and Density
Benchmark: 1000 Regexes, 40,000 states

## Slide 35: Comparison Across Architectures
 |  | Memory | Processing Rate | Throughput (Gbps) | Area () | Throughput/area (Gbps/)
von Neumann | XeonPhi | NA | 8 bits/cycle | 0.13 | ~400 | <0.001
 | GPU | NA | 8 bits/cycle | 0.5 | ~300 | 0.002
 | ASIC (HARE) | NA | 8 bits/cycle | 3.9 | 80 | 0.04
Memory-Centric | FPGA | LUT/BRAM | 16 bits/cycle | 3.47 | 45 | 0.07
 | Automata Processor | DRAM | 8 bits/cycle | 1 | 38 | 0.03
 | Cache Automaton | SRAM | 8 bits/cycle | 28.8 | 4.3 | 6.7
 | Impala (our solution) | SRAM | 16 bits/cycle | 80 | 3.2 | 25
 |  | Memory | Processing Rate | Throughput (Gbps) |  | 
von Neumann | XeonPhi | NA | 8 bits/cycle | 0.13 | ~400 | <0.001
 | GPU | NA | 8 bits/cycle | 0.5 | ~300 | 0.002
 | ASIC (HARE) | NA | 8 bits/cycle | 3.9 | 80 | 0.04
Memory-Centric | FPGA | LUT/BRAM | 16 bits/cycle | 3.47 | 45 | 0.07
 | Automata Processor | DRAM | 8 bits/cycle | 1 | 38 | 0.03
 | Cache Automaton | SRAM | 8 bits/cycle | 28.8 | 4.3 | 6.7
 | Impala (our solution) | SRAM | 16 bits/cycle | 80 | 3.2 | 25
Performance factors: Throughput and Density
Benchmark: 1000 Regexes, 40,000 states

## Slide 36: Comparison Across Architectures
 |  | Memory | Processing Rate | Throughput (Gbps) | Area () | Throughput/area (Gbps/)
von Neumann | XeonPhi | NA | 8 bits/cycle | 0.13 | ~400 | <0.001
 | GPU | NA | 8 bits/cycle | 0.5 | ~300 | 0.002
 | ASIC (HARE) | NA | 8 bits/cycle | 3.9 | 80 | 0.04
Memory-Centric | FPGA | LUT/BRAM | 16 bits/cycle | 3.47 | 45 | 0.07
 | Automata Processor | DRAM | 8 bits/cycle | 1 | 38 | 0.03
 | Cache Automaton | SRAM | 8 bits/cycle | 28.8 | 4.3 | 6.7
 | Impala (our solution) | SRAM | 16 bits/cycle | 80 | 3.2 | 25
 |  | Memory | Processing Rate | Throughput (Gbps) |  | 
von Neumann | XeonPhi | NA | 8 bits/cycle | 0.13 | ~400 | <0.001
 | GPU | NA | 8 bits/cycle | 0.5 | ~300 | 0.002
 | ASIC (HARE) | NA | 8 bits/cycle | 3.9 | 80 | 0.04
Memory-Centric | FPGA | LUT/BRAM | 16 bits/cycle | 3.47 | 45 | 0.07
 | Automata Processor | DRAM | 8 bits/cycle | 1 | 38 | 0.03
 | Cache Automaton | SRAM | 8 bits/cycle | 28.8 | 4.3 | 6.7
 | Impala (our solution) | SRAM | 16 bits/cycle | 80 | 3.2 | 25
Performance factors: Throughput and Density
Benchmark: 1000 Regexes, 40,000 states
Impala provides a general, flexible, efficient, and scalable solution!

## Slide 37: Impala: Main Takeaways
https://github.com/gr-rahimi/APSim
Analyzing application properties for a more efficient architecture
Tall arrays and serial processing  short and parallel arrays
Three-fold throughput, area, energy benefits
Co-designing across the hierarchy for a better PIM solution