## Slide 1: Exploring Speed and Energy Tradeoffs in Droplet Transport for Digital Microfluidic Biochips
Johnathan Fiske, *Dan Grissom, Philip Brisk
University of California, Riverside
19th Asia & South PacificDesign Automation Conference
Singapore, January 21, 2014

## Slide 2: The Bottom Line
Microfluidics will replace traditional bench-top chemistry

## Slide 3: The Future of Chemistry
Discrete Droplet Based
“Digital”
Microfluidics
Miniaturization + Automation
of Biochemistry

## Slide 4: Applications
Biochemical reactions and immunoassays
  Clinical pathology
Drug discovery and testing
  Rapid assay prototyping
Biochemical terror and hazard detection
DNA extraction & sequencing

## Slide 5: Digital Microfluidic Biochips (DMFB) 101
Basic Microfluidic Operations
A Digital Microfluidic Biochip (DMFB)
http://microfluidics.ee.duke.edu/
Droplet
Ground Electrode
CE1
CE3
CE2
Control Electrodes
Bottom
Plate
Top
Plate
Hydrophobic
Layer

## Slide 6: Digital Microfluidic Biochips (DMFB) 101
Droplet Actuation on a Prototype DMFB
at the University of Tennessee

## Slide 7: DMFB Mapping
How do I make a reaction run on a DMFB?

## Slide 8: CAD Synthesis Flow
Synthesis: The process of mapping an application to hardware
  Similar to how applications are mapped to ICs
Electrode Sequence

## Slide 9: Synthesis Example
1.) Schedule
2.) Place
3.) Route

## Slide 10: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 11: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 12: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 13: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 14: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 15: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 16: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 17: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 18: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 19: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 20: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 21: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 22: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 23: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 24: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 25: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 26: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 27: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 28: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 29: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 30: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 31: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 32: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 33: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 34: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 35: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 36: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 37: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 38: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 39: Compaction Example
Electrode Activations
Corresponding Droplet Motion

## Slide 40: Discrete Perspective
Increase Voltage  Increase Velocity
Compaction treated as discrete problem
  Single voltage used for all droplet movements
  All droplets move at same speed (requires halts)
Pollack, M. G., Shenderov, A. D., and Fair, R. B. 2002. Electrowetting-based actuation of droplets for integrated microfluidics. Lab-on-a-Chip 2, 2 (Mar. 2002), 96-101.
D2 WAITS

## Slide 41: Continuous-Time Perspective
Voltages can be changed
  Abandons synchronous droplet movement
Reduce energy usage; maintain timing
Compaction treated as continuous problem
  Multiple voltages used for droplet movements
  Droplets move at different speeds (avoid halts)

## Slide 42: Formal Problem Formation
Details In Paper

## Slide 43: General Problem Formation
Droplet paths broken into segments
  Max-length contiguous subsequence in one direction
Droplet motion:
  Constant velocity/voltage along entire segment
  Only stops at beginning/end of segments
  Interference constraints at continuous-time positions
Static Constraints
Dynamic Constraints
Interference Regions (IR) Prevent Droplet Collisions

## Slide 44: Algorithmic Description
Step 1: Route computation
  Roy’s maze-based droplet router (greedy)
    Computes routes that could overlap
  Never re-visit/re-compute routes

## Slide 45: Algorithmic Description
Step 2: Time-constrained, energy-aware compaction
  Given timing constraint
  For each droplet path:
    Compute initial path velocity
      Minimum Voltage for velocity derived from graph
Noh, J. H., Noh, J., Kreit, E., Heikenfeld, J., and Rack, P. D. 2012. Toward active-matrix lab-on-a-chip: programmable electrofluidic control enabled by arrayed oxide thin film transistors. Lab-on-a-Chip 12, 2 (Jan. 2012), 353-360.
Least-squares-fit equation

## Slide 46: Algorithmic Description
Step 2: Compaction (continued)
  Compute all segment timings from
  initial velocities
  For each droplet path
    For each electrode position in
      Compare against each previously compacted path
        If no interference along segment:
          Accept segment
        If interference along segment:
          Speedup current droplet along its segment
          Adjust remaining segments to conserve energy
          Re-compute path timings for that droplet
(0,8]
(7,14]
(8,13]
(0,7]
Example Coming!

## Slide 47: Simple Example
d1
d2
s2
s1
D1
Compact D1.
D2
(0,8]
(7,14]
(8,13]
(0,7]

## Slide 48: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  |  |  | 12 | 
 |  |  |  |  |  |  |  | 11 | 
 |  |  |  |  |  |  |  | 10 | 
 |  |  |  |  |  |  |  | 9 | 
 |  |  |  |  |  |  |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
No previous paths; D1 routes with no problems.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
(0,8]
(7,14]
(8,13]
(0,7]

## Slide 49: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  |  |  | 12 | 
 |  |  |  |  |  |  |  | 11 | 
 |  |  |  |  |  |  |  | 10 | 
 |  |  |  |  |  |  |  | 9 | 
 |  |  |  |  |  |  |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
Now compact D2 against all previous droplet paths (D1).
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 1 electrodes/s

## Slide 50: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | 1 |  | 12 | 
 |  |  |  |  |  |  |  | 11 | 
 |  |  |  |  |  |  |  | 10 | 
 |  |  |  |  |  |  |  | 9 | 
 |  |  |  |  |  |  |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
Now compact D2 against all previous droplet paths (D1).
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 1 electrodes/s

## Slide 51: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | 1 |  | 12 | 
 |  |  |  |  |  | 2 |  | 11 | 
 |  |  |  |  |  |  |  | 10 | 
 |  |  |  |  |  |  |  | 9 | 
 |  |  |  |  |  |  |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
Now compact D2 against all previous droplet paths (D1).
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 1 electrodes/s

## Slide 52: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | 1 |  | 12 | 
 |  |  |  |  |  | 2 |  | 11 | 
 |  |  |  |  |  | 3 |  | 10 | 
 |  |  |  |  |  |  |  | 9 | 
 |  |  |  |  |  |  |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
Now compact D2 against all previous droplet paths (D1).
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 1 electrodes/s

## Slide 53: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | 1 |  | 12 | 
 |  |  |  |  |  | 2 |  | 11 | 
 |  |  |  |  |  | 3 |  | 10 | 
 |  |  |  |  |  | 4 |  | 9 | 
 |  |  |  |  |  |  |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
Now compact D2 against all previous droplet paths (D1).
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 1 electrodes/s

## Slide 54: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | 1 |  | 12 | 
 |  |  |  |  |  | 2 |  | 11 | 
 |  |  |  |  |  | 3 |  | 10 | 
 |  |  |  |  |  | 4 |  | 9 | 
 |  |  |  |  |  | 5 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5/6 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
While compacting D2, detected interference at time 5 between D1 and D2.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 1 electrodes/s

## Slide 55: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  |  |  | 12 | 
 |  |  |  |  |  |  |  | 11 | 
 |  |  |  |  |  |  |  | 10 | 
 |  |  |  |  |  |  |  | 9 | 
 |  |  |  |  |  |  |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
Increases D2’s velocity/voltage (2.5x) and restart compaction for D2.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s

## Slide 56: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .8 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  |  |  | 9 | 
 |  |  |  |  |  |  |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
Re-compact D2 at 2.5x speed against all previous droplet paths (D1).
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s

## Slide 57: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .8 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 5 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 
d1
d2
s2
s1
D2
D1
Re-compact D2 at 2.5x speed against all previous droplet paths (D1).
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s

## Slide 58: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  |  |  |  |  | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 reached end of segment.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s

## Slide 59: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  |  |  |  |  | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 60: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  |  |  |  | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 61: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  |  |  |  | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 62: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  |  |  | 7.4 | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 63: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  |  |  | 7.4 | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 64: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  |  | 9.5 | 7.4 | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 65: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  |  | 9.5 | 7.4 | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 66: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  | 11.6 | 9.5 | 7.4 | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 67: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  | 11.6 | 9.5 | 7.4 | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 68: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  | 11.6 | 9.5 | 7.4 | 5.3 | 3.2 |  |  | 
d1
d2
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 69: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  | 11.6 | 9.5 | 7.4 | 5.3 | 3.2 |  |  | 
d1
d1
s2
s1
D2
D1
D2 does not need to get there before D1; save energy and slow D2 down to 0.46 electrodes/sec.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 70: Simple Example
 |  |  |  |  |  |  |  | 13 | 
 |  |  |  |  |  | .4 |  | 12 | 
 |  |  |  |  |  | .6 |  | 11 | 
 |  |  |  |  |  | 1.2 |  | 10 | 
 |  |  |  |  |  | 1.6 |  | 9 | 
 |  |  |  |  |  | 2 |  | 8 | 
 |  | 1 | 2 | 3 | 4 | 5 / 2.4 | 6 | 7 | 
 |  |  |  |  |  | 2.8 |  |  | 
 |  | 11.6 | 9.5 | 7.4 | 5.3 | 3.2 |  |  | 
d1
d1
s2
s1
D2
D1
D2 compacted against D2 with no interference.
Numbers on electrodes indicate the time the droplet arrives at the electrode.
Segment 1: 1 electrode/s
Segment 2: 1 electrode/s
Segment 3: 2.5 electrodes/s
Segment 4: 0.46 electrodes/s

## Slide 71: Simulation Details
DMFB modeled after University of Tennessee’s active matrix design1
  Electrode resistance = 1GΩ
  Electrode pitch (dimension) = 2.54mm
  Voltagemin = 13V, Voltagemax = 70V
  Voltage/velocity relationship:
1 Noh, J. H., Noh, J., Kreit, E., Heikenfeld, J., and Rack, P. D. 2012. Toward active-matrix lab-on-a-chip: programmable electrofluidic control enabled by arrayed oxide thin film transistors. Lab-on-a-Chip 12, 2 (Jan. 2012), 353-360.

## Slide 72: Simulation Details
Benchmarks
  PCR, In-Vitro Diagnostics, Protein, ProteinSplit assays (common benchmarks)
Base Routing Flow2
  Step 1: Roy maze router (same as proposed)
  Step 2: Constant voltage
    Add stalls at beginning of routes to avoid interference
Setup
  Schedules and placements same for both route compactors
2 Grissom, D., and Brisk, P. Fast online synthesis of generally programmable digital microfluidic biochips. In Proceedings of the ACM/IEEE International Conference on Hardware Software Codesign and System Synthesis (Tampere, Finland, October 07 - 12, 2012). CODES-ISSS '12, 413-422.

## Slide 73: Results: Energy Savings
Base flow performed at 30V, 50V and 70V
  Time constraints for continuous-time compaction derived from these runs
Energy savings vary greatly between sub-problems
  Due to amount and complexity of droplets being routed
Routing
Sub-problem #

## Slide 74: Results: Energy Savings
Higher voltages  Better energy usage across platforms
More V for less time can lead to energy savings
30V sees greatest savings because slower paths provide more opportunities for route speedups

## Slide 75: Results: Energy Savings
Threshold exists where Increasing Voltage  Decreases Energy becomes not true
Threshold depends on device characteristics
Large savings can be incurred by decreasing voltage on halts
  Wait for 0.5s:
    @ 30V  450 V2s/GΩ
    @ 70V  2450 V2s/GΩ
Energy Decreasing
Energy Increasing

## Slide 76: Conclusion
Base flow performed at 30V, 50V and 70V
  Time constraints derived from these runs
More savings seen when compared to lower-voltage base cases
First model for continuous-time domain droplet routing (compaction)
  Varying voltage  varying velocity
Multiple speeds allow for energy savings
  Higher voltages can have better energy usage
  Continuous-time domain droplet compaction can achieve energy savings across range of voltage
Tradeoffs may vary based on characteristics of DMFB

## Slide 77: Thank You
http://microfluidics.cs.ucr.edu/