## Slide 1: GPU Architecture

## Slide 2
Notes: Poll Title: How do you feel today? https://www.polleverywhere.com/multiple_choice_polls/1dDXUPAIrphlTz7LGV2eI?flow=Default&onscreen=persist

## Slide 3: Software informs Hardware
Efficiency through understanding how each level interacts
Design hardware for common case applications
This is hardware specialization

## Slide 4: Graphics Applications – The pipeline
Many stages for graphics applications
Involve many different operations

## Slide 5: Graphics Applications – Vertex Transformation
Transform defined through matrix multiplication
A single operation is then applied to all affected vertices

## Slide 6: Single Instruction Multiple Data
Matrix Multiplication can be classified as SIMD paradigm
A single instruction stream is applied to multiple separate data structures
How do we handle multiple data threads within hardware?

## Slide 8: Jacquard Loom
Multiple Vertical Threads are grouped into a Warp
Horizontal Weft is weaved through the warp in a single operation

## Slide 10: Jacquard Loom
Complex patterns are created by selecting which threads are lifted
Jacquard Loom shows the efficiency of operating on multiple threads in one cycle

## Slide 11: Back to Modern Computers
Threads are executing the same instruction but on different data

## Slide 12: Vector Processors
Increase the number of ALU hardware units
Increasing the number of datapaths per functional unit reduces the execution time, as more element operations can be processed concurrently.

## Slide 13: Vector Processors
Increase size (width) of registers
Increasing number of datapaths requires more data to be accessed within a single cycle

## Slide 14: The Von-Neumann Model with SIMD units
Single Instruction Multiple Data
(SIMD)
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Single Instruction Multiple Data
(SIMD)
Duplicate Processing Unit to support vector instructions
Still share a single control unit
Notes: Insert von-neumann schematic here

## Slide 15: Handling multiple Warps
A single SIMD unit can handle multiple Warps
Scheduling policy tells which one will be executed next
Fine-Grained Scheduling (Round Robin)
Course-Grained Scheduling (Greedy than Oldest)

## Slide 16: Key Takeaways
Vector processor are SIMD units
Increasing number of datapaths requires more data to be accessed within a single cycle
Unit of execution and scheduling is a vector instruction with multiple data
Therefore threads are grouped into a single warp
Proccing units are duplicated but share a control unit

## Slide 17
Notes: Poll Title: Are there any drawback other than area from having a larger SIMD unit? i.e. a SIMD unit with 32, 64, or 128 ALUs https://www.polleverywhere.com/free_text_polls/ffU7blNcVenZXV0ySdewj

## Slide 18: GPU Microarchitecture Overview
Single-Instruction, Multiple-Threads
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 19: Streaming Multiprocessors are SIMD Processors
Control unit for instruction fetch, decode, and control is shared among multiple processing units
  Control overhead is minimized
Memory
Processing Unit
I/O
ALU
Processor (SM)
Shared Memory
Register
File
Control Unit
PC
IR
Notes: Insert von-neumann schematic here

## Slide 20: SIMD Execution Among Threads in a Warp
All threads in a warp must execute the same instruction at any point in time
  Also called SIMT execution model
This works efficiently if all threads follow the same control flow path
  All if-then-else statements make the same decision
  All loops iterate the same number of times
Notes: WARP_SIZE

## Slide 21: GPU Microarchitecture Overview
GPU
Interconnection Network
SIMT Core Cluster
SIMT
Core
SIMT
Core
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Memory
Partition
GDDR3/GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core

## Slide 22: Inside a SIMT Core
SIMT front end / SIMD backend
Fine-grained multithreading
  Interleave warp execution to hide latency
  Register values of all threads stays in core
SIMT
Front End
SIMD Datapath
Fetch
Decode
Schedule
Branch
Memory Subsystem
Icnt.
Network
SMem
L1 D$
Tex $
Const$
Reg
File

## Slide 23: Inside a pipelined SIMT Core
SIMT Front End
SIMD Datapath
ALU
ALU
ALU
I-Cache
Decode
I-Buffer
Score
Board
Issue
Operand
Collector
MEM
ALU
Fetch
SIMT-Stack
Done (WID)
Valid[1:N]
Branch Target PC
Pred.
Active
Mask
Three decoupled warp schedulers
Scoreboard
Large register file
Multiple SIMD functional units
Scheduler 1
Scheduler 2
Scheduler 3

## Slide 24: Fetch + Decode
Arbitrate the I-cache among warps
  Cache miss handled by fetching again later
Fetched instruction is decoded and then stored in the I-Buffer
  1 or more entries / warp
  Only warp with vacant entries are considered in fetch
Inst. W1
r
Inst. W2
Inst. W3
v
r
v
r
v
To
Fetch
Issue
Decode
Score-
Board
Issue
ARB
PC
1
PC
2
PC
3
A
R
B
Selection
T
o
I
-
C
a
c
h
e
Valid[1:N]
I-Cache
Decode
I-Buffer
Fetch
Valid[1:N]

## Slide 25: Instruction Issue
Select a warp and issue an instruction from its I-Buffer for execution
  Scheduling: Greedy-Then-Oldest (GTO)
  GT200/later Fermi/Kepler: Allow dual issue (superscalar)
  Fermi: Odd/Even scheduler
  To avoid stalling pipeline might
  keep instruction in I-buffer until
  know it can complete (replay)

## Slide 26: Execution
SIMD Datapath
ALU
ALU
ALU
Issue
Operand
Collector
MEM
ALU
SIMT-Stack
Active
Mask
Multiple SIMD units
Separate Warps can be executing in-flight simultaneously

## Slide 27: Key Takeaways
Streaming Multiprocessors are “Core” blocks of GPUs
They contain multiple SIMD units
Support for Multithreading of warps
SIMT
Front End
SIMD Datapath
Fetch
Decode
Schedule
Branch
Memory Subsystem
Icnt.
Network
SMem
L1 D$
Tex $
Const$
Reg
File

## Slide 28
Notes: Poll Title: What are the benefits from multiple smaller SMs over a single large SM? https://www.polleverywhere.com/free_text_polls/1aPXXHp3VOulAIHzpewFE

## Slide 29: How should we program for this architecture?
GPU
Interconnection Network
SIMT Core Cluster
SM
SIMT
Core
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Memory
Partition
GDDR5
Off-chip DRAM
SIMT Core Cluster
SIMT
Core
SIMT
Core
SIMT Core Cluster
SIMT
Core
SIMT
Core
How do we organize thread execution?

## Slide 30: Vector Operations
A[0]
vector A
vector B
vector C
A[1]
A[2]
A[N-1]
B[0]
B[1]
B[2]
…
…
B[N-1]
C[0]
C[1]
C[2]
C[N-1]
…
op
op
op
op
Assign a thread to each element of an array
One thread operates on a single element
Tid 0
Tid 1
Tid 2
Tid N-1

## Slide 31: Arrays of Parallel Threads
A CUDA kernel is executed by a grid (array) of threads
  All threads in a grid run the same kernel code (Single Program Multiple Data)‏
  Each thread has indexes that it uses to compute memory addresses and make control decision
However this is not scalable with large arrays or matricies
Nothing inherent with id to map to a specific SM to execute
…
0
1
2
254
255
…
C[i] = A[i] + B[i];
i = threadIdx.x;

## Slide 32: Thread Blocks: Scalable Cooperation
Divide thread array into multiple blocks
Thread Blocks become Unit of scheduling to an SM
Can easily scale to different number of SMs
Thread Block 0
Thread Block 1
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
0
1
2
254
255
…
1
2
254
255
0
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
1
2
254
255
Thread Block N-1
0
i = blockIdx.x * blockDim.x + threadIdx.x;
C[i] = A[i] + B[i];
…
…
…
…

## Slide 33: Transparent Scalability
Each block can execute in any order relative to others.
Hardware is free to assign blocks to any processor at any time
  A kernel scales to any number of parallel processors
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Thread grid
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
time
time

## Slide 34: blockIdx and threadIdx
Each thread uses indices to decide what data to work on
  blockIdx: 1D, 2D, or 3D
  threadIdx: 1D, 2D, or 3D
Simplifies memory addressing when processing multidimensional data
  Image processing
  Solving PDEs on volumes
  …
device
Grid
Block (0, 0)
Block (1, 1)
Block (1, 0)
Block (0, 1)
Block (1,1)
Thread
(0,0,0)
Thread
(0,1,3)
Thread
(0,1,0)
Thread
(0,1,1)
Thread
(0,1,2)
Thread
(0,0,0)
Thread
(0,0,1)
Thread
(0,0,2)
Thread
(0,0,3)
(1,0,0)
(1,0,1)
(1,0,2)
(1,0,3)

## Slide 35: Executing Thread Blocks
Threads are assigned to Streaming Multiprocessors (SM) in block granularity
SM maintains thread/block idx #s
SM manages/schedules thread execution
t0 t1 t2 … tm
Blocks
SP
Shared
Memory
SM

## Slide 36: Warps as Scheduling Units
Each Block is executed as 32-thread Warps
  An implementation decision, not part of the CUDA programming model
  Warps are scheduling units in SM
  Threads in a warp execute in SIMD
If 3 blocks are assigned to an SM and each block has 256 threads, how many Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps

## Slide 37: Key Takeaways
Threads are grouped into Thread blocks
ThreadID and Block ID can be 3 dimensional
Thread Blocks are the unit of scheduling at the SM level
device
Grid
Block (0, 0)
Block (1, 1)
Block (1, 0)
Block (0, 1)
Block (1,1)
Thread
(0,0,0)
Thread
(0,1,3)
Thread
(0,1,0)
Thread
(0,1,1)
Thread
(0,1,2)
Thread
(0,0,0)
Thread
(0,0,1)
Thread
(0,0,2)
Thread
(0,0,3)
(1,0,0)
(1,0,1)
(1,0,2)
(1,0,3)