## Slide 1: Control Divergence and Memory coalescing

## Slide 2: Objective
To learn to analyze the performance impact of control divergence
  Boundary condition checking
  Control divergence is data-dependent

## Slide 3: Performance Impact of Control Divergence
Boundary condition checks are vital for complete functionality and robustness of parallel code
  The tiled matrix multiplication kernel has many boundary condition checks
  The concern is that these checks may cause significant performance degradation
  For example, see the tile loading code below:
if(Row < Width && t * TILE_WIDTH+tx < Width) {
ds_M[ty][tx] = M[Row * Width + p * TILE_WIDTH + tx];
} else {
ds_M[ty][tx] = 0.0;
}
if (p*TILE_WIDTH+ty < Width && Col < Width) {
ds_N[ty][tx] = N[(p*TILE_WIDTH + ty) * Width + Col];
} else {
ds_N[ty][tx] = 0.0;
}

## Slide 4: Two types of blocks in loading M Tiles
1. Blocks whose tiles are all within valid range until the last phase.
2. Blocks whose tiles are partially outside the valid range all the way
M
TILE_WIDTH
Type 1
Type 2

## Slide 5: Analysis of Control Divergence Impact
Assume 16x16 tiles and thread blocks
Each thread block has 8 warps (256/32)
Assume square matrices of 100x100
There are 49 thread blocks (7 in each dimension)

## Slide 6: Control Divergence in Loading M Tiles
Assume 16x16 tiles and thread blocks
Each thread block has 8 warps (256/32)
Assume square matrices of 100x100
There are 42 (6*1) Type 1 blocks, with a total of 48 (8*6) warps
Only the warps on the edge of control divergence

## Slide 7: Control Divergence in Loading M Tiles (Type 2)
Type 2: the 7 block assigned to load the bottom tiles, with a total of 56 (8*7) warps
The first 2 warps in each Type 2 block will stay within the valid range until the last phase
The 6 remaining warps stay outside the valid range
So, only 2 warp have control divergence

## Slide 8: Overall Impact of Control Divergence
Type 1 Blocks: 49 out of 392 warp-phases have control divergence
Type 2 Blocks: 2 out of 392 warp-phases have control divergence
The performance impact is expected to be ~13% (51/392)
M
TILE_WIDTH
Type 1
Type 2

## Slide 9: Additional Comments
The estimated performance impact is data dependent.
  For larger matrices, the impact will be significantly smaller
In general, the impact of control divergence for boundary condition checking for large input data sets should be insignificant
  One should not hesitate to use boundary checks to ensure full functionality
The fact that a kernel is full of control flow constructs does not mean that there will be heavy occurrence of control divergence
We will cover some algorithm patterns that naturally incur control divergence (such as parallel reduction) in the Parallel Algorithm Patterns modules

## Slide 10: Memory Coalescing
To learn that memory coalescing is important for effectively utilizing memory bandwidth in CUDA
  Its origin in DRAM burst
  Checking if a CUDA memory access is coalesced
  Techniques for improving memory coalescing in CUDA code

## Slide 11: DRAM Burst – A System View
Each address space is partitioned into burst sections
  Whenever a location is accessed, all other locations in the same section are also delivered to the processor
Basic example: a 16-byte address space, 4-byte burst sections
  In practice, we have at least 4GB address space, burst section sizes of 128-bytes or more
2
1
0
3
5
4
6
7
9
8
10
11
13
12
14
15
Burst section
Burst section
Burst section
Burst section

## Slide 12: Memory Coalescing
When all threads of a warp execute a load instruction, if all accessed locations fall into the same burst section, only one DRAM request will be made and the access is fully coalesced.
2
1
0
3
5
4
6
7
9
8
10
11
13
12
14
15
Burst section
Burst section
Burst section
Burst section
T0
T1
T2
T3
Coalesced Loads
T0
T1
T2
T3
Coalesced Loads

## Slide 13: Un-coalesced Accesses
When the accessed locations spread across burst section boundaries:
  Coalescing fails
  Multiple DRAM requests are made
  The access is not fully coalesced.
Some of the bytes accessed and transferred are not used by the threads
2
1
0
3
5
4
6
7
9
8
10
11
13
12
14
15
Burst section
Burst section
Burst section
Burst section
T0
T1
T2
T3
Un-coalesced Loads
T0
T1
T2
T3
Un-coalesced Loads

## Slide 14: How to judge if an access is coalesced?
Accesses in a warp are to consecutive locations if the index in an array access is in the form of
  A[(expression with terms independent of threadIdx.x) + threadIdx.x];

## Slide 15: A 2D C Array in Linear Memory Space
M0,2
M1,1
M0,1
M0,0
M1,0
M0,3
M1,2
M1,3
M0,2
M0,1
M0,0
M0,3
M1,1
M1,0
M1,2
M1,3
M2,1
M2,0
M2,2
M2,3
M2,1
M2,0
M2,2
M2,3
M3,1
M3,0
M3,2
M3,3
M3,1
M3,0
M3,2
M3,3
M
linearized order in increasing address

## Slide 16: Two Access Patterns of Basic Matrix Multiplication
A
B
WIDTH
Thread 1
Thread 2
A[Row*n+i]
B[i*k+Col]
i is the loop counter in the inner product loop of the kernel code
A is m n, B is n k
Col = blockIdx.x*blockDim.x + threadIdx.x
HEIGHT

## Slide 17: B accesses are coalesced
N
T0
T1
T2
T3
Load iteration 0
T0
T1
T2
T3
Load iteration 1
Access direction in kernel code
B0,2
B1,1
B0,1
B0,0
B1,0
B0,3
B1,2
B1,3
B2,1
B2,0
B2,2
B2,3
B3,1
B3,0
B3,2
B3,3
B0,2
B0,1
B0,0
B0,3
B1,1
B1,0
B1,2
B1,3
B2,1
B2,0
B2,2
B2,3
B3,1
B3,0
B3,2
B3,3

## Slide 18: A Accesses are Not Coalesced
T0
T1
T2
T3
Load iteration 0
T0
T1
T2
T3
Load iteration 1
Access direction in kernel code
…
A0,2
A1,1
A0,1
A0,0
A1,0
A0,3
A1,2
A1,3
A2,1
A2,0
A2,2
A2,3
A3,1
A3,0
A3,2
A3,3
A0,2
A0,1
A0,0
A0,3
A1,1
A1,0
A1,2
A1,3
A2,1
A2,0
A2,2
A2,3
A3,1
A3,0
A3,2
A3,3

## Slide 19: Loading an Input Tile
A
B
C
WIDTH
Row
Col
n
m
n
k
k
m
int tx = threadIdx.x
int ty = threadIdx.y
Accessing tile 0 2D indexing:
A[Row][tx]
B[ty][Col]
Have each thread load an A element
and a B element at the same relative
position as its C element.
Notes: Point out that I and j will become global thread indices.

## Slide 20: Corner Turning
d_M
d_N
W
I
D
T
H
WIDTH
d_M
d_N
Original
Access
Pattern
Tiled
Access
Pattern
Copy into
shared
memory
Perform
multiplication
with shared memory
values