## Slide 1: Warp Scheduling Basics

## Slide 2: Loose Round Robin (LRR)
Goes around to every warp and issue if ready (R)
If warp is not ready (W), skip and issue next ready warp
Issue: Warps all run at the same speed, potentially all reaching memory access phase together and stalling.
R
R
W
R
R
R
R
Select
All Warps
Execution Units
W
. . .

## Slide 3: Two-level (TL)
Warps are grouped into two groups:
  Pending warps (potentially waiting on long latency instr.)
  Active warps (Ready to execute)
  Warps move between Pending and Active groups
Within the Active group, issue LRR
Goal: Overlap warps performing computation with warps performing memory access
P
P
P
P
P
P
P
A
A
A
A
Select
Pending Warps
Active Warps
Execution Units
P
. . .
. . .

## Slide 4: Greedy-then-oldest (GTO)
Schedule from a single warp until it stalls
Then pick the oldest warp (time warp assigned to core)
Goal: Improve cache locality for greedy warp
R
R
W
R
R
R
R
Select
All Warps
Execution Units
W
. . .

## Slide 5
Cache-Conscious Wavefront Scheduling
Timothy G. Rogers1
Mike O’Connor2
Tor M. Aamodt1
1The University of British Columbia
2AMD Research

## Slide 6
Compute Unit
DRAM
DRAM
Wavefronts and Caches
Threads in Wavefront
Compute Unit
W1
…
…
Wavefront Scheduler
W2
DRAM
…
10’s of thousands concurrent threads
High bandwidth memory system
Include data caches
…
ALU
ALU
ALU
…
…
L2 cache
Memory Unit
L1D
High Level Overview of a GPU

## Slide 7
Motivation
Improve performance of highly parallel applications with irregular or data dependent access patterns on GPU
These workloads can be highly cache-sensitive
Increase 32k L1D to 8M
  Minimum 3x speedup
  Mean speedup >5x
Breadth First Search (BFS)
K-Means (KMN)
Memcached-GPU (MEMC)
Parallel Garbage Collection (GC)

## Slide 8
Data Cache
Data Cache
Where does the locality come from?
Classify two types of locality
Intra-wavefront locality
Inter-wavefront locality
LD $line (X)
LD $line (X)
LD $line (X)
LD $line (X)
Wave0
Hit
Wave0
Wave1
Hit

## Slide 9
0
20
40
60
80
100
120
AVG-Highly Cache Sensitive
(Hits/Miss) PKI
Misses PKI
Inter-Wavefront Hits PKI
Intra-Wavefront Hits PKI
Quantifying intra-/inter-wavefront locality

## Slide 10
Observation
Issue-level scheduler chooses the access stream
Memory System
Wavefront Scheduler
Wavefront Scheduler
Round Robin Scheduler
Memory System
Greedy then Oldest Scheduler
ld A
,B,C,D…
DC
B
A
ld Z,Y,X,W
ld A,B,C,D
WX
Y
Z
...
...
ld Z,Y,X,W
DC
B
A
DC
B
A
ld A,B,C,D…
...
Wave0
Wave1
Wave0
Wave1
ld A,B,C,D…

## Slide 11
A,B,C,D
E,F,G,H
I,J,K,L
A,B,C,D
E,F,G,H
I,J,K,L
W0
W1
W2
W0
W1
W2
Optimal Replacement using RR scheduler
LRU replacement
A,B,C,D
W0
A,B,C,D
W0
E,F,G,H
W1
E,F,G,H
W1
I,J,K,L
W2
I,J,K,L
W2
A
B
C
D
4 hits
12 hits
E
F
L
Difficult Access Stream
Need a better replacement Policy?

## Slide 12
Why miss rate is more sensitive to scheduling than replacement
…
1024 threads = thousands of memory accesses
…
…
…
1
2
A
Wavefront Scheduler
Replacement Policy
Ld A
Ld A
Ld B
Ld C
Ld C
Ld D
Ld E
Ld E
Ld F
W0
W1
W31
Decision picks from thousands of potential accesses
Decision limited to one of A possible ways
…

## Slide 13
0
10
20
30
40
50
60
70
80
90
AVG-Highly Cache-Sensitive
Does this ever Happen?
Loose Round Robin with LRU
  Belady Optimal
Greedy Then Oldest with LRU
Consider two simple schedulers
MPKI
Chart: MPKI

## Slide 14
Key Idea
Use the wavefront scheduler to shape the access pattern
Memory System
Wavefront Scheduler
Wavefront Scheduler
Greedy then Oldest Scheduler
Memory System
Cache-Conscious Wavefront Scheduler
ld A,B,C,D
DC
B
A
ld Z,Y,X,W
ld A,B,C,D
WX
Y
Z
...
...
ld Z,Y,X,W
DC
B
A
DC
B
A
ld Z,Y,X,W…
ld A,B,C,D…
...
...
ld Z,Y,X,W…
Wave0
Wave1
Wave0
Wave1
ld A,B,C,D…
WX
Y
Z
WX
Y
Z

## Slide 15
Time
CCWS Components
Locality Scoring System
Balances cache miss rate and overall throughput
Lost Locality Detector
W0
W1
W2
W0
W1
W2
Victim Tags
Tag
Tag
Tag
Tag
Tag
Tag
W0
W1
W2
Detects when wavefronts have lost intra-wavefront locality
L1 victim tags organized by wavefront ID
More Details in the Paper
Score

## Slide 16
CCWS Implementation
Memory Unit
Cache
Victim Tags
Locality Scoring System
Wave Scheduler
W0
W1
W2
Tag
WID
Data
Tag
Tag
Tag
Tag
Tag
Tag
W0
W1
W2
Time
Score
Tag
WID
Data
…
W0
W1
W2
No W2 loads
W0
W1
W2
…
W0: ld X
X
0
W0,X
X
W0 detected lost locality
W2: ld Y
W0: ld X
ProbeW0,X
Y
2
More Details in the Paper

## Slide 17
Methodology
GPGPU-Sim (version 3.1.0)
30 Compute Units (1.3 GHz)
  32 wavefront contexts (1024 threads total)
32k L1D cache per compute unit
  8-way
  128B lines
  LRU replacement
1M L2 unified cache
Stand Alone GPGPU-Sim Cache Simulator
Trace-based cache simulator
Fed GPGPU-Sim traces
Used for oracle replacement

## Slide 18
Performance Results
Also Compared Against
A 2-LVL scheduler
  Similar to GTO performance
A profile-based oracle scheduler
  Application and input data dependent
  CCWS captures 86% of oracle scheduler performance
Variety of cache-insensitive benchmarks
  No performance degradation
0
0.5
1
1.5
2
HMEAN-Highly Cache-Sensitive
Speedup
LRR
GTO
CCWS

## Slide 19
0
10
20
30
40
50
60
70
80
90
AVG-Highly Cache-Sensitive
Cache Miss Rate
CCWS less cache misses than other schedulers optimally replaced
Full Sensitivity Study in Paper
MPKI
Chart: MPKI

## Slide 20
Related Work
Wavefront Scheduling
Gerogia Tech - GPGPU Workshop 2010
UBC - HPCA 2011
UT Austin - MICRO 2011
UT Austin/NVIDIA/UIUC/Virginia - ISCA 2011
OS-Level Scheduling
SFU – ASPLOPS 2010
Intel/MIT – ASPLOPS 2012

## Slide 21
Conclusion
Different approach to fine-grained cache management
Good for power and performance
High level insight not tied specifics of a GPU
  Any system with many threads sharing a cache can potentially benefit
Questions?