## Slide 1
Warped Gates: Gating Aware Scheduling
and Power Gating for GPGPUs
Mohammad Abdel-Majeed* Daniel Wong*
Murali Annavaram
Ming Hsieh Department of Electrical Engineering
University of Southern California
MICRO-2013
* Equal Contribution
Supported by

## Slide 2: Problem Overview
Execution unit accounts for majority of energy consumption in GPGPU, even more than Mem and Reg!
Leakage energy is becoming a greater concern with technology scaling
Traditional microprocessor power gating techniques are ineffective in GPGPUs
Component Energy Breakdown for GTX480[1]
[1] J. Leng, T. Hetherington, A. ElTantawy, S. Gilani, N. S. Kim, T. M. Aamodt, and V. J. Reddi, “GPUWattch: enabling energy optimizations in GPGPUs,” presented at the ISCA '13: Proceedings of the 40th Annual International Symposium on Computer Architecture, 2013.
Overview | 2

## Slide 3: GPGPU Overview (GTX480)
V | Dec_INST | R
V | Dec_INST | R
V | Dec_INST | R
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
SFU
SFU
SFU
SFU
SFU LD/ST SP0 SP1
INT Unit
Operands
Result Queue
FP Unit
Warp Scheduler
(2-level)
Register File
128KB
Execution Units
64KB shared Memory/L1 cache
SM
Instruction Cache
Fetch and decode
I_Buffer
Overview | 3
SP accounts for 98% of Execution Unit Leakage Energy
Execution units account for 68% of total on chip area

## Slide 4: Power Gating Overview
Cuts off leakage current that flows through a circuit block
Power gate at SP granularity
Important Parameters:
  Wakeup Delay – Time to return to Vdd (3 cycles)
  Breakeven Time – # of consecutive power gated cycles required to compensate PG energy overhead (9-24 cycles)
  Idle Detect - # of idle cycles before power gating[2]
Time
Static Energy
t2
t0
t1
t3
t4
Eoverhead
Overhead to sleep
and Wakeup
Overhead to Sleep
Cumulative energy savings
Wakeup
Cycles>wakeup_delay
Uncompensated
Cycle 1
Cycle 1+BET
Cycles>idle_detect
Compensated
Cycles>BET time
Idle_detect
Busy
Overview | 4
Breakeven Time
[2] Z. Hu, et. al. Microarchitectural techniques for power gating of execution units. In ISLPED ’04.

## Slide 5
Power Gating Challenges in GPGPUs
Challenges | 5

## Slide 6: Power Gating Challenges in GPGPUs
Traditional microprocessors experience idle periods many 10s of cycles long[3]
Int. Unit Idle period length distribution for hotspot
  Assume 5 idle detect, 14 BET
Lost Opportunity
Energy Loss or Neutral
Energy Savings
[3] S. Dropsho, et. al. Managing static leakage energy in microprocessor functional units. In Proceedings of the MICRO 35, 2012
Challenges | 6
Need to increase idle period length

## Slide 7: Warp Scheduler Effect on Power Gating
Idle periods interrupted by instructions that are greedily scheduled
INT
FP
FP
INT
INT
FP
INT
Ready Warps
INT
Need to coalesce warp issues by resource type
Challenges | 7
Idle Periods

## Slide 8
GATES:
Gating Aware Two-level Scheduler
Issue warps based on execution unit resource type
GATES | 8

## Slide 9: Gating Aware Two-level Scheduler (GATES)
INT
FP
INT
INT
INT
FP
FP
Ready Warps
INT
GATES | 9
Idle Period
Idle periods are coalesced

## Slide 10: Gating Aware Two-level Scheduler (GATES)
Per instruction type active warps subset
Instruction Issue Priority
Dynamic priority switching
  Switch highest priority when it out of ready warps
Two-level
GATES
GATES | 10

## Slide 11: Effect of GATES on Idle Period Length
~3x increase in positive power gating events
~2x increase in negative power gating events
Need to further stretch idle periods
Two-level
GATES
GATES | 11

## Slide 12
Blackout Power Gating
Forced idleness of execution units to meet BET
Blackout | 12

## Slide 13: Blackout Power Gating
Force idleness until break even time has passed
  Even when there are pending instructions
Would this not cause performance loss?
  No, because of GPGPU-specific large heterogeneity of execution units and good mix of instruction types
Blackout | 13
Wakeup
Cycles>wakeup_delay
Uncompensated
Cycle 1
Cycle 1+BET
Cycles>idle_detect
Compensated
Cycles>BET time
Idle_detect
Busy
X
X

## Slide 14: Blackout Power Gating
~2.4x increase in positive PG events over GATES (GATES ~3x w.r.t. baseline)
GATES
GATES + Blackout
Blackout | 14

## Slide 15: Blackout Policies
Naïve Blackout
  GATES and Blackout is independent
Can lead to overaggressive power gating
Blackout | 15
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
SP0 SP1
Warp Scheduler
(GATES)
Idle Detect
INT
X

## Slide 16: Blackout Policies
Coordinated Blackout
PG only when active warps count = 0
Blackout | 16
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
C
SP0 SP1
Warp Scheduler
(GATES)
Idle Detect
Dynamic priority switching is Blackout aware
Active Warp Count Based
INT
✓

## Slide 17: Impact of Blackout
Some benchmarks still show poor performance
  Not enough active warps to hide forced idleness
Goal is as close to 0% overhead as possible

## Slide 18
Adaptive Idle Detect
Reducing Worst Case Blackout Impact
Adaptive Idle Detect | 18

## Slide 19: Adaptive Idle Detect
Dynamically change idle detect to avoid aggressive PG
Infer performance loss due to Blackout
  “Critical Wakeup” – Wakeup that occur the moment blackout period ends
High Correlation vs Runtime
Adaptive Idle Detect | 19

## Slide 20: Adaptive Idle Detect
Independent idle detect values for INT and FP pipelines
Break execution time into epoch (1000 cycles)
If critical wakeup > threshold, idleDetect++
Conservatively decrement idleDetect every 4 epochs
Bound idle detect between 5 – 10 cycles
GATES
Blackout
Adaptive Idle Detect
Warped Gates
Adaptive Idle Detect | 20

## Slide 21: Architectural Support
2-bit type indicator
2 counters keep track of number of INT/FP instr in active subset. Used to determine dynamic priority
Architectural Support | 21

## Slide 22
Evaluation
Evaluation | 22

## Slide 23: Evaluation Methodology
GPGPU-Sim v3.0.2
  Nvidia GTX480
GPUWattch and McPAT for Energy and Area estimation
18 Benchmarks from ISPASS, Rodinia, Parboil
Power Gating parameters
  Wakeup delay – 3 cycles
  Breakeven time – 14 cycles
  Idle detect – 5 cycles
Evaluation | 23

## Slide 24: Power Gating Wakeups / Overhead
Coalescing idle periods – fewer, but longer, idle periods
Blackout reduces PG overhead by 26%
Warped Gates reduces PG overhead by 46%
Evaluation | 24

## Slide 25: Integer Unit Static Energy Savings
Blackout/Warped Gates is able to save energy when ConvPG cannot
Warped Gates saves ~1.5x static energy w.r.t. ConvPG
Evaluation | 25

## Slide 26: FP Unit Static Energy Savings
Warped Gates save ~1.5x static energy w.r.t. ConvPG
  (Ignores Integer only benchmarks)
Evaluation | 26

## Slide 27: Performance Impact
Naïve Blackout has high overhead due to aggressive PG
Both ConvPG and Warped Gates has ~1% overhead
Evaluation | 27

## Slide 28: Conclusion
Execution units – largest energy usage in GPGPUs
Static energy becoming increasingly important
Traditional microprocessor power gating techniques ineffective in GPGPUs due to short idle periods
GATES – Scheduler level technique to increase idle periods by coalescing instruction type issues
Blackout – Forced idleness of execution unit to avoid negative power gating events
Adaptive Idle Detect – Limit performance impact
Warped Gates able to save 1.5x more static power than traditional microprocessor techniques, with negligible performance loss
Conclusion | 28

## Slide 29
Thank you!
Questions?
Conclusion | 29