## Slide 1: GPU Architecture Research Directions

## Slide 2
Advancing Computer Systems without Technology Progress
DARPA/ISAT Workshop, March 26-27, 2012
Mark Hill & Christos Kozyrakis
Decreasing cost per unit computation
1971: Intel 4004
2012: Datacenter
1981: IBM 5150
2007: iPhone
Notes: Increasing transistor density has led to decreasing cost per unit computation… or what is equivalent increased capability per unit cost.
This leads to a rather famous exponential growth curve.
A quick review of the impact of this curve is in order:
- First microprocessor had 2300 transistors basically designed for a souped up calculator
- Today we carry around smartphones that have half a billion transistors in them. A large part of what makes them useful is the computing capability that resulted from technology scaling.
- Of course, not all computation takes place somewhere you can see it. A large amount of computation happens in datacenters that are hidden away out of sight behind the internet.
However, the traditional CMOS scaling that gave us all this is ending. ITRS projects we’ll end at the 7 nm process node. Others may put it at 5 nm. But either way this is happening really soon and likely within the next 10 years.
Of course, there are other technologies being proposed. However, none of them are ready for prime time.
Open question: can we continue increasing function per unit cost without CMOS scaling?

## Slide 3
Ease of
Programming
Hardware Efficiency
Single Core OoO Superscalar CPU
Brawny (OoO) Multicore
ASIC
Better
16K thread, SIMT Accelerator
Wimpy (In-order) Multicore
(how to get here?)
Notes: Approach 1: Start with easy to program hardware and improve HW efficiency
Approach 2: Start with efficient HW and make it easier to program

## Slide 4
Ease of
Programming
Hardware Efficiency
Start by using right tool for each job…
Notes: Approach 1: Start with easy to program hardware and improve HW efficiency
Approach 2: Start with efficient HW and make it easier to program

## Slide 5: Amdahl’s Law Limits this Approach
Easy to accelerate
Hard to accelerate

## Slide 6: Question: Can dividing line be moved?
easy to accelerate (Acc. Arch1)
easy to accelerate (Acc. Arch2)

## Slide 7: Forward-Looking GPU Software
Still Massively Parallel
Less Structured
  Memory access and control flow patterns are less predictable
Execute efficiently on a GPU today
Graphics Shaders
Matrix Multiply
…
Less efficient on today’s GPU
Raytracing
Molecular Dynamics
Object Classification
…

## Slide 8
Ease of
Programming
Energy Efficiency
Better
Two Routes to “Better”
Notes: Approach 1: Start with easy to program hardware and improve HW efficiency
Approach 2: Start with efficient HW and make it easier to program

## Slide 9: Research Direction 1: Mitigating SIMT Control Divergence

## Slide 10: Recall: SIMT Hardware Stack
-
G
1111
TOS
B
C
D
E
F
A
G
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B/1111
C/1001
D/0110
E/1111
A/1111
G/1111
-
A
1111
TOS
E
D
0110
E
C
1001
TOS
-
E
1111
E
D
0110
TOS
-
E
1111
A
D
G
A
Time
C
B
E
-
B
1111
TOS
-
E
1111
TOS
Reconv. PC
Next PC
Active Mask
Stack
E
D
0110
E
E
1001
TOS
-
E
1111
Potential for significant loss of throughput when control flow diverged!

## Slide 11: Performance vs. Warp Size
Chart: IPC normalized to warp size 32
Convergent Applications
Warp-Size Insensitive Applications
Divergent Applications
165 Applications

## Slide 12: Dynamic Warp Formation (Fung MICRO’07)
Time
1 2 3 4
A
1 2 -- --
C
-- -- 3 4
D
1 2 3 4
E
1 2 3 4
B
Warp 0
5 6 7 8
A
5 -- 7 8
C
-- 6 -- --
D
5 6 7 8
E
5 6 7 8
B
Warp 1
9 10 11 12
A
-- -- 11 12
C
9 10 -- --
D
9 10 11 12
E
9 10 11 12
B
Warp 2
Reissue/Memory
Latency
SIMD Efficiency  88%
1 2 7 8
C
5 -- 11 12
C
Pack
How to pick threads to pack into warps?
Notes: Multiple warps interleave execution in core to hide pipeline/memory latency
Breaks up the “static warps”, pack the threads running this instruction into fewer warps to improve efficiency
How should we decide which threads to pack together?

## Slide 13: Dynamic Warp Formation: Hardware Implementation
Thread Scheduler
PC-Warp LUT
Warp Pool
I
s
s
u
e
L
o
g
i
c
Warp Allocator
TID x N
PC A
TID x N
PC B
H
H
TID x N
PC
Prio
TID x N
PC
Prio
OCC
PC
IDX
OCC
PC
IDX
Warp Update Register T
Warp Update Register NT
REQ
REQ
TID x N
PC
Prio
A
5
6
7
8
A
1
2
3
4
5
7
8
6
B
C
1011
0100
B
2
3
0110
B
0
B
5
2
3
8
B
0010
B
2
7
1
3
4
2
B
C
0110
1001
C
1
1001
C
1
4
C
6
1101
C
1
No Lane Conflict
A: BEQ R2, B
C: …
X
1
2
3
4
Y
5
6
7
8
X
1
2
3
4
X
1
2
3
4
X
1
2
3
4
X
1
2
3
4
Y
5
6
7
8
Y
5
6
7
8
Y
5
6
7
8
Y
5
6
7
8
Z
5
2
3
8
Z
5
2
3
8
Z
5
2
3
8

## Slide 14: DWF Pathologies: Starvation
9 6 3 4
D
-- 10 -- --
D
1 2 3 4
E
5 6 7 8
E
9 10 11 12
E
Majority Scheduling
  Best Performing
  Prioritize largest group of threads with same PC
Starvation
  LOWER SIMD Efficiency!
Other Warp Scheduler?
  Tricky: Variable Memory Latency
Time
1 2 7 8
C
5 -- 11 12
C
9 6 3 4
D
-- 10 -- --
D
1 2 7 8
E
5 -- 11 12
E
9 6 3 4
E
-- 10 -- --
E
B: if (K > 10)
C: K = 10;
else
D: K = 0;
E: B = C[tid.x] + K;
1000s cycles
Notes: 12:17 – 13:00 – 14:23

## Slide 15: DWF Pathologies: Extra Uncoalesced Accesses
Coalesced Memory Access = Memory SIMD
  1st Order CUDA Programmer Optimization
Not preserved by DWF
E: B = C[tid.x] + K;
1 2 3 4
E
5 6 7 8
E
9 10 11 12
E
Memory
0x100
0x140
0x180
1 2 7 12
E
9 6 3 8
E
5 10 11 4
E
Memory
0x100
0x140
0x180
#Acc = 3
#Acc = 9
No DWF
With DWF
L1 Cache Absorbs
Redundant
Memory Traffic
L1$ Port Conflict
Notes: 14:23 – 16:15
Coalesced Memory Access = Grouping individual word accesses from threads inside a warp into a wide access to a chunk of memory
- Serviced by a single wide access

## Slide 16: DWF Pathologies: Implicit Warp Sync.
Some CUDA applications depend on the lockstep execution of “static warps”
  E.g. Task Queue in Ray Tracing
Thread 0 ... 31
Thread 32 ... 63
Thread 64 ... 95
Warp 0
Warp 1
Warp 2
int wid = tid.x / 32;
if (tid.x % 32 == 0) {
sharedTaskID[wid] = atomicAdd(g_TaskID, 32);
}
my_TaskID = sharedTaskID[wid] + tid.x % 32;
ProcessTask(my_TaskID);
Implicit
Warp
Sync.
Notes: 16:15 – 17:22
A single thread in each warp branches off to fetch task for the rest of the warp.

## Slide 17: Observation
Static
Warp
Dynamic
Warp
Static
Warp
Compute kernels usually contain divergent and non-divergent (coherent) code segments
Coalesced memory access usually in coherent code segments
  DWF no benefit there
Coherent
Divergent
Coherent
Reset Warps
Divergence
Recvg
Pt.
Coales. LD/ST
Notes: 17:22 – 18:37

## Slide 18: Thread Block Compaction
Run a thread block like a warp
  Whole block move between coherent/divergent code
  Block-wide stack to track exec. paths reconvg.
Barrier @ Branch/reconverge pt.
  All avail. threads arrive at branch
  Insensitive to warp scheduling
Warp compaction
  Regrouping with all avail. threads
  If no divergence, gives static warp arrangement
Starvation
Implicit
Warp Sync.
Extra Uncoalesced
Memory Access
Notes: 18:37 – 20:03

## Slide 19: Thread Block Compaction
PC
RPC
Active Threads
A
-
1
2
3
4
5
6
7
8
9
10
11
12
D
E
--
--
3
4
--
6
--
--
9
10
--
--
C
E
1
2
--
--
5
--
7
8
--
--
11
12
E
-
1
2
3
4
5
6
7
8
9
10
11
12
Time
1 2 7 8
C
5 -- 11 12
C
9 6 3 4
D
-- 10 -- --
D
5 6 7 8
A
9 10 11 12
A
1 2 3 4
A
5 6 7 8
E
9 10 11 12
E
1 2 3 4
E
A: K = A[tid.x];
B: if (K > 10)
C: K = 10;
else
D: K = 0;
E: B = C[tid.x] + K;
5 6 7 8
A
9 10 11 12
A
1 2 3 4
A
5 -- 7 8
C
-- -- 11 12
C
1 2 -- --
C
-- 6 -- --
D
9 10 -- --
D
-- -- 3 4
D
5 6 7 8
E
9 10 11 12
E
1 2 7 8
E
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
--
Notes: 20:03 – 21:45
Here is the same example as before with the block-wide stack.
Clarify that in HW, the active threads are represented as a block-wide active mask.

## Slide 20: Thread Compactor
Convert activemask from block-wide stack to thread IDs in warp buffer
Array of Priority-Encoder
P-Enc
P-Enc
P-Enc
P-Enc
1
2
7
8
5
--
11
12
1
2
--
--
5
--
7
8
--
--
11
12
C
E
1
2
--
--
5
--
7
8
--
--
11
12
1 2 7 8
C
5 -- 11 12
C
Warp Buffer

## Slide 21: Experimental Results
0.6
0.7
0.8
0.9
1
1.1
1.2
1.3
TBC
DWF
IPC Relative to Baseline
COHE
DIVG
2 Benchmark Groups:
  COHE = Non-Divergent CUDA applications
  DIVG = Divergent CUDA applications
Serious Slowdown from
pathologies
No Penalty for COHE
22% Speedup on DIVG
Per-Warp Stack
Notes: 26:53 – 27:50
We group our benchmarks according to how much they suffer from branch divergence in the first place.

## Slide 22: Recent work on warp divergence
Intel [MICRO 2011]: Thread Frontiers – early reconvergence for unstructured control flow.
UT-Austin/NVIDIA [MICRO 2011]: Large Warps – similar to TBC except decouple size of thread stack from thread block size.
NVIDIA [ISCA 2012]: Simultaneous branch and warp interweaving. Enable SIMD to execute two paths at once.
Intel [ISCA 2013]: Intra-warp compaction – extends Xeon Phi uarch to enable compaction.
NVIDIA: Temporal SIMT [described briefly in IEEE Micro article and in more detail in CGO 2013 paper]
NVIDIA [ISCA 2015]: Variable Warp-Size Architecture – merge small warps (4 threads) into “gangs”.

## Slide 23: Thread Frontiers [Diamos et al., MICRO 2011]
+

## Slide 24: Temporal SIMT
32-wide datapath
time
1 cyc
1 warp instruction = 32 threads
thread
0
thread
31
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ld
ml
ml
ml
ml
ad
ad
ad
ad
st
st
st
st
ml
ml
ml
ml
ad
ad
ad
ad
st
st
st
st
ml
ml
ml
ml
ad
ad
ad
ad
st
st
st
st
ml
ml
ml
ml
ad
ad
ad
ad
st
st
st
st
ml
ml
ml
ml
ad
ad
ad
ad
st
st
st
st
ml
ml
ml
ml
ad
ad
ad
ad
st
st
st
st
ml
ml
ml
ml
ad
ad
ad
ad
st
st
st
st
ml
ml
ml
ml
ad
ad
ad
ad
st
st
st
st
Spatial SIMT (current GPUs)
1-wide
time
1 cyc
ld
ld
ld
ld
ld
ld
ld
0
(threads)
1
2
3
4
5
6
7
ld
ld
ld
8
9
ld
10
Pure Temporal SIMT
[slide courtesy of Bill Dally]

## Slide 25: Temporal SIMT Optimizations
Control divergence — hybrid MIMD/SIMT
Scalarization
  Factor common instructions from multiple threads
  Execute once – place results in common registers
  [See: SIMT Affine Value Structure (ISCA 2013)]
32-wide
(41%)
4-wide
(65%)
1-wide
(100%)
[slide courtesy of Bill Dally]

## Slide 26: Scalar Instructions in SIMT Lanes
Scalar instruction spanning warp
Scalar register visible to all threads
Temporal execution of Warp
Multiple lanes/warps
Y. Lee, CGO 2013
[slide courtesy of Bill Dally]

## Slide 27: Variable Warp-Size Architecture
Most recent work by NVIDIA [ISCA 2015]
Split the SM datapath into narrow slices.
  Extensively studied 4-thread slices
Gang slice execution to gain efficiencies of wider warp.
Slices can execute independently
Slices share an L1
I-Cache and Memory Unit

## Slide 28: Divergent Application Performance
Chart: IPC normalized to warp size 32
| CoMD | Lighting | GamePhysics | ObjClassifier | Raytracing | HMEAN-DIV | Divergent Applications
WS 32 | 1 | 1 | 1 | 1 | 1 | 1
WS 4 | 1.28 | 1.32 | 1.2 | 1.63 | 1.62 | 1.3878
I-VWS | 1.27 | 1.28 | 1.13 | 1.57 | 1.6 | 1.3457
E-VWS | 1.17 | 1.16 | 1.13 | 1.54 | 1.51 | 1.2777
Warp Size 4
I-VWS: Break on CF Only
E-VWS: Break + Reform

## Slide 29: Convergent Application Performance
Chart: IPC normalized to warp size 32
| Game 1 | MatrixMultiply | Game 2 | FeatureDetect | Radix Sort | HMEAN-CON | Convergent Applications
WS 32 | 1 | 1 | 1 | 1 | 1 | 1
WS 4 | 0.79 | 0.81 | 0.58 | 0.82 | 0.75 | 0.73775
I-VWS | 1.01 | 1 | 1 | 0.99 | 0.99 | 0.99794
E-VWS | 1 | 1 | 1 | 0.99 | 0.99 | 0.99598
Warp Size 4
I-VWS: Break on CF Only
Warp-Size Insensitive Applications Unaffected
E-VWS: Break + Reform

## Slide 30: Research Direction 2: Mitigating High GPGPU Memory Bandwidth Demands

## Slide 31: Reducing Off-Chip Access / Divergence
Re-writing software to use “shared memory” and avoid uncoalesced global accesses is bane of GPU programmer existence.
Recent GPUs introduce caches, but large number of warps/wavefronts lead to thrashing.

## Slide 32
NVIDIA: Register file cache (ISCA 2011, MICRO)
  Register file burns significant energy
  Many values read once soon after written
  Small register file cache captures locality and saves energy but does not help performance
  Recent follow on work from academia
Prefetching (Kim, MICRO 2010)
Interconnect (Bakhoda, MICRO 2010)
Lee & Kim (HPCA 2012) CPU/GPU cache sharing

## Slide 33: Thread Scheduling Analogy [MICRO 2012]
Human Multitasking
  Humans have limited attention capacity
  GPUs have limited cache capacity
Chart: Tasks at Once
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0
HMEAN Normalized IPC | 0.59323 | 1.0289 | 1.44 | 1.6252 | 1.33 | 1.1 | 0.87 | 1.0339 | 1.0192 | 1.0174 | 1.0121
GPU Core
Processor
Cache
Chart: Threads Actively Scheduled
| 1.0 | 2.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 32.0
HMEAN Normalized IPC | 0.59323 | 1.0289 | 1.5339 | 1.6252 | 1.5399 | 1.3292 | 1.2002 | 1.1149 | 1.0808 | 1.052 | 1.0393 | 1.0339 | 1.0192 | 1.0174 | 1.0121 | 1

## Slide 34: Use Memory System Feedback [MICRO 2012]
Chart: Threads Actively Scheduled
| 1.0 | 2.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 32.0
MPKI | 10.9922 | 11.7746 | 15.0311 | 17.8012 | 21.8722 | 26.8669 | 30.8744 | 33.0259 | 34.1718 | 34.7411 | 35.1755 | 35.366 | 35.5353 | 35.7157 | 35.7679 | 36.1863
HMEAN Normalized IPC | 0.59323 | 1.0289 | 1.5339 | 1.6252 | 1.5399 | 1.3292 | 1.2002 | 1.1149 | 1.0808 | 1.052 | 1.0393 | 1.0339 | 1.0192 | 1.0174 | 1.0121 | 1
Performance
Cache Misses
GPU Core
Processor
Cache
Thread Scheduler
Feedback

## Slide 35
Data Cache
Data Cache
Sources of Locality
Intra-wavefront locality
Inter-wavefront locality
LD $line (X)
LD $line (X)
LD $line (X)
LD $line (X)
Wave0
Hit
Wave0
Wave1
Hit

## Slide 36
0
20
40
60
80
100
120
AVG-Highly Cache Sensitive
(Hits/Miss) PKI
Misses PKI
Inter-Wavefront Hits PKI
Intra-Wavefront Hits PKI

## Slide 37
Scheduler affects access pattern
Memory System
Wavefront Scheduler
Wavefront Scheduler
Round Robin Scheduler
Memory System
Greedy then Oldest Scheduler
ld A
,B,C,D…
DC
B
A
ld Z,Y,X,W
ld A,B,C,D
WX
Y
Z
...
...
ld Z,Y,X,W
DC
B
A
DC
B
A
ld A,B,C,D…
...
Wave0
Wave1
Wave0
Wave1
ld A,B,C,D…

## Slide 38
Use scheduler to shape access pattern
Memory System
Wavefront Scheduler
Wavefront Scheduler
Greedy then Oldest Scheduler
Memory System
Cache-Conscious Wavefront Scheduling
[MICRO 2012 best paper runner up,
Top Picks 2013, CACM Research Highlight]
ld A,B,C,D
DC
B
A
ld A,B,C,D
WX
Y
Z
...
ld Z,Y,X,W
DC
B
A
DC
B
A
ld A,B,C,D…
...
ld Z,Y,X,W…
Wave0
Wave1
Wave0
Wave1
ld A,B,C,D…

## Slide 39
Memory Unit
Cache
Victim Tags
Locality Scoring System
Wave Scheduler
W0
W1
W2
Tag
WID
Data
Tag
Tag
Tag
Tag
Tag
Tag
W0
W1
W2
Time
Score
Tag
WID
Data
…
W0
W1
W2
No W2 loads
W0
W1
W2
…
W0: ld X
X
0
W0,X
X
W0 detected lost locality
W2: ld Y
W0: ld X
ProbeW0,X
Y
2

## Slide 40
0
0.5
1
1.5
2
HMEAN-Highly Cache-Sensitive
Speedup
LRR
GTO
CCWS
Notes: A 2-LVL scheduler
  Similar to GTO performance
A profile-based oracle scheduler
  Application and input data dependent
  CCWS captures 86% of oracle scheduler performance
Variety of cache-insensitive benchmarks
  No performance degradation

## Slide 41: Static Wavefront Limiting [Rogers et al., MICRO 2012]
Profiling an application we can find an optimal number of wavefronts to execute
Does a little better than CCWS.
Limitations: Requires profiling, input dependent, does not exploit phase behavior.

## Slide 42: Improve upon CCWS?
CCWS detects bad scheduling decisions and avoids them in future.
Would be better if we could “think ahead” / “be proactive” instead of “being reactive”

## Slide 43: Programmability case study [MICRO 2013]
Sparse Vector-Matrix Multiply
Simple Version
GPU-Optimized Version
SHOC Benchmark Suite
(Oakridge National Labs)
Added Complication
Dependent on Warp Size
Parallel Reduction
Explicit Scratchpad Use
Divergence
Each thread has locality
Using DAWS scheduling
within 4% of optimized with no programmer input

## Slide 44: Observations [Rogers et al., MICRO 2013]
Memory divergence in static instructions is predictable
Data touched by divergent loads dependent on active mask
Warp 0
Warp 1
…
load
…
Divergence
Divergence
Warp
Main Memory
Main Memory
Main Memory
Divergence
Both Used To Create Cache Footprint Prediction
4 accesses
2 accesses
1
0
1
0
Warp
1
1
1
1

## Slide 45: Footprint Prediction
Detect loops with locality
Classify loads in the loop
Compute footprint from active mask
Some loops have locality
Some don’t
Limit multithreading here
while(…) {
load 1
…
load 2
}
Diverged
Not Diverged
while(…) {
load 1
…
load 2
}
Warp 0
1
1
1
1
1
1
Loop with locality
Loop with locality
Diverged
Not Diverged
4 accesses
1 access
+
Warp 0’s Footprint
= 5 cache lines

## Slide 46
int C[]={0,64,96,128,160,160,192,224,256};
void sum_row_csr(float* A, …) {
float sum = 0;
int i =C[tid];
while(i < C[tid+1]) {
sum += A[ i ];
++i;
}
…
Example Compressed Sparse Row Kernel
Time1
Time0
Time2
Cache
A[0]
A[64]
A[96]
A[128]
Cache
A[0]
A[64]
A[96]
A[128]
Cache
A[32]
A[160]
A[192]
A[224]
Warp0
1
1
1
1
2nd Iter.
Warp0
1
0
0
0
33rd Iter.
Warp1
0
1
1
1
1st Iter.
Memory Divergence
Divergent Branch
Go
Go
Warp1
Warp0
Warp1
Warp0
No Footprint
DAWS Operation Example
Cache Footprint
4
4
4
Want to capture spatial locality
Hit
Hit
Hit
Hit
Go
Hit x30
Hit x30
Hit x30
Hit x30
Loop
Stop
Go
No locality detected = no footprint
Locality Detected
1 Diverged Load Detected
Footprint = 4X1
Footprint = 3X1
Early warps profile loop for later warps
Warp 0 has branch divergence
Both warps capture spatial locality together
4 Active threads
Stop
Footprint decreased

## Slide 47
Sparse MM Case Study Results
Within 4% of optimized with no programmer input
Divergent Code Execution time
Performance (normalized to optimized version)

## Slide 48: Memory Request Prioritization Buffer [Jia et al., HPCA 2014]
Reorder requests by sorting by Warp ID.
Bypass when too many accesses to same cache set.
W3
W2
W1
W3
W2
W1
W3
W3
W2
W2
W1
W1
Bypass accesses to hot set
Reorder requests by warp ID

## Slide 49: Priority-Based Cache Allocation in Throughput Processors [Li et al., HPCA 2015]
CCWS leaves L2 and DRAM underutilized.
Allow some additional warps to execute but do not allow them to allocate space in cache:
Warp 0
Warp 1
Normal Warps
Warp 2
Warp 3
Non-Polluting
Warps
Warp 4
Schedule and allocate in L1
Schedule and bypass L1
Warp 5
Throttled Warps
Warp n-1
Not scheduled

## Slide 50: Coordinated criticality-Aware Warp Acceleration (CAWA) [Lee et al., ISCA 2015]
Some warps execute longer than others due to lack of uniformity in underlying workload.
Give these warps more space in cache and more scheduling slots.
Estimate critical path by observing amount of branch divergence and memory stalls.
Also, predict if line inserted in line will be used by a warp that is critical using modified version of SHiP cache replacement algorithm.

## Slide 51: Other Memory System Performance Considerations
TLB Design for GPUs.
  Current GPUs have translation look aside buffers (makes managing multiple graphics application surfaces easier; does not support paging)
  How does large number of threads impact TLB design?
  E.g., Power et al., Supporting x86-64 Address Translation for 100s of GPU Lanes, HPCA 2014. Importance of multithreaded page table walker + page walk cache.

## Slide 52: Research Direction 3: Coherent Memory for Accelerators

## Slide 53: Why GPU Coding Difficult?
Manual data movement CPU  GPU
Lack of generic I/O , system support on GPU
Need for performance tuning to reduce
  off-chip accesses
  memory divergence
  control divergence
For complex algorithms, synchronization
Non-deterministic behavior for buggy code
Lack of good performance analysis tools

## Slide 54: Manual CPU  GPU Data Movement
Problem #1: Programmer needs to identify data needed in a kernel and insert calls to move it to GPU
Problem #2: Pointer on CPU does not work on GPU since different address spaces
Problem #3: Bandwidth connecting CPU and GPU is order of magnitude smaller than GPU off-chip
Problem #4: Latency to transfer data from CPU to GPU is order of magnitude higher than GPU off-chip
Problem #5: Size of GPU DRAM memory much smaller than size of CPU main memory

## Slide 55: Identifying data to move CPU  GPU
CUDA/OpenCL: Job of programmer 
C++AMP passes job to compiler.
OpenACC uses pragmas to indicate loops that should be offloaded to GPU.

## Slide 56: Memory Model
Rapid change (making programming easier)
Late 1990’s: fixed function graphics only
2003: programmable graphics shaders
2006: + global/local/shared (GeForce 8)
2009: + caching of global/local
2011: + unified virtual addressing
2014: + unified memory / coherence

## Slide 57: Caching
Scratchpad uses explicit data movement. Extra work. Beneficial when reuse pattern statically predictable.
NVIDIA Fermi / AMD Southern Island add caches for accesses to global memory space.

## Slide 58: CPU memory vs. GPU global memory
Prior to CUDA: input data is texture map.
CUDA 1.0 introduces cudaMemcpy
  Allows copy of data between CPU memory space to global memory on GPU
Still has problems:
  #1: Programmer still has to think about it!
  #2: Communicate only at kernel grid boundaries
  #3: Different virtual address space
    pointer on CPU not a pointer on GPU => cannot easily share complex data structures between CPU and GPU

## Slide 59: Fusion / Integrated GPUs
Why integrate?
  One chip versus two (cf. Moore’s Law, VLSI)
  Latency and bandwidth of communication: shared physical address space, even if off-chip, eliminates copy: AMD Fusion. 1st iteration 2011. Same DRAM
  Shared virtual address space? (AMD Kavari 2014)
  Reduce latency to spawn kernel means kernel needs to do less to justify cost of launching

## Slide 60: CPU Pointer not a GPU Pointer
NVIDIA Unified Virtual Memory partially solves the problem but in a bad way:
  GPU kernel reads from CPU memory space
NVIDIA Uniform Memory (CUDA 6) improves by enabling automatic migration of data
Limited academic work. Gelado et al. ASPLOS 2010.

## Slide 61: CPU  GPU Bandwidth
Shared DRAM as found in AMD Fusion (recent Core i7) enables the elimination of copies from CPU to GPU. Painful coding as of 2013.
One question how much benefit versus good coding. Our limit study (WDDD 2008) found only ~50% gain. Lustig & Martonosi HPCA 2013.
Algorithm design—MummerGPU++

## Slide 62: CPU  GPU Latency
NVIDIA’s solution: CUDA Streams. Overlap GPU kernel computation with memory transfer. Stream = ordered sequence of data movement commands and kernels. Streams scheduled independently. Very painful programming.
Academic work: Limit Study (WDDD 2008), Lustig & Martonosi HPCA 2013, Compiler data movement (August, PLDI 2011).

## Slide 63: GPU Memory Size
CUDA Streams
Academic work: Treat GPU memory as cache on CPU memory (Kim et al., ScaleGPU, IEEE CAL early access).

## Slide 64: Solution to all these sub-issues?
Heterogeneous System Architecture: Integrated CPU and GPU with coherence memory address space.
Need to figure out how to provide coherence between CPU and GPU.
Really two problems: Coherence within GPU and then between CPU and GPU.

## Slide 65: Research Direction 4: Easier Programming with Synchronization

## Slide 66: Synchronization
Locks are not encouraged in current GPGPU programming manuals.
Interaction with SIMT stack can easily cause deadlocks:
while( atomicCAS(&lock[a[tid]],0,1) != 0 )
; // deadlock here if a[i] = a[j] for any i,j = tid in warp
// critical section goes here
atomicExch (&lock[a[tid]], 0) ;

## Slide 67
Correct way to write critical section for GPGPU:
done = false;
while( !done ) {
if( atomicCAS (&lock[a[tid]], 0 , 1 )==0 ) {
// critical section goes here
atomicExch(&lock[a[tid]], 0 ) ;
}
}
Most current GPGPU programs use barriers within thread blocks and/or lock-free data structures.
This leads to the following picture…

## Slide 68
Lifetime of GPU Application Development
Time
Functionality
Performance
Wilson Fung, Inderpeet Singh, Andrew Brownsword, Tor Aamodt
?
Time
Fine-Grained Locking/Lock-Free
Time
Transactional Memory
E.g. N-Body with 5M bodies CUDA SDK: O(n2) – 1640 s (barrier) Barnes Hut: O(nLogn) – 5.2 s (locks)
Notes: Usually, developers can get the application running on GPU after a little bit of initial effort, and spend the rest of their time tuning the application for performance.
For application that require (or benefit from) fine-grained data synchronization, the developer may spend significant effort just to get the code working. As in the usual case, the first working code performs poorly, so effort to tune the application is still required. If the developers spend the effort to tune the code, the reward can be great. For example, O(nLogn) implementation of N-Body is orders of magnitude faster than the naïve implementation, but it is harder to get right because of locks.
Hypothesis 1: For applications that require fine-grained communication between tasks, developers will give up long before the code is working on a GPU, and even if they manage to get the application to run correctly, the performance will initially be bad and they may then decide they have wasted too much time for too little progress.
Hypothesis 2: With TM, the developer will get working code sooner, leaving time to tune the code for performance.
Even if there is a performance overhead for using TM it is a gain for the developer (better performing code with same effort).

## Slide 69: Transactional Memory
Programmer specifies atomic code blocks called transactions [Herlihy’93]
TM Version:
atomic {
X[c] = X[a]+X[b];
}
Lock Version:
Lock(X[a]);
Lock(X[b]);
Lock(X[c]);
X[c] = X[a]+X[b];
Unlock(X[c]);
Unlock(X[b]);
Unlock(X[a]);
Potential Deadlock!

## Slide 70: Transactional Memory
Commit
Commit
TX1
Non-conflicting transactions may run in parallel
TX2
A
B
C
D
Memory
Conflicting transactions automatically serialized
TX1
A
B
C
D
Memory
TX2
Commit
Abort
Commit
TX2
Programmers’ View:
TX1
TX2
TX1
TX2
OR
Time
Time
Notes: In the programmers’ view, transactions are executed atomically in some order.
The underlying runtime system can optimistically run non-conflicting transactions in parallel.
Conflicting transactions may be resolved by aborting one of the transaction and restarting it later.

## Slide 71: Are TM and GPUs Incompatible?
Hardware TM for GPU Architectures
71
GPU uarch very different from multicore CPU…
KILO TM [MICRO’11, IEEE Micro Top Picks]
Hardware TM for GPUs
Half performance of fine grained locking
  Chip area overhead of 0.5%
Notes: For those who know something about both TM and GPU, the two may seem to be incompatible concepts.
Yes, GPUs are different from multi core CPUs.
These differences lead to a set of challenges for supporting TM on GPU.
For each of these challenges, I will show you how KILO TM, our hardware TM for GPUs, addresses the challenge.

## Slide 72: Research Direction 5: GPU Power Efficiency

## Slide 73: GPU power
More efficient than CPU but
  Consumes a lot of power
  Much less efficient than ASIC or FPGAs
  What can be done to reduce power consumption?
Look at the most power hungry components
  What can be duty cycled/power gated?
  Can we make GPUs more energy elastic?
  GPUWattch to evaluate ideas

## Slide 74: Other Research Directions….
Non-deterministic behavior for buggy code
  GPUDet ASPLOS 2013
Lack of good performance analysis tools
  NVIDIA Profiler/Parallel NSight
  AerialVision [ISPASS 2010]
  GPU analytical perf/power models (Hyesoon Kim)
Chart: Result Variation (Kepler)
| 20000.0 | 21000.0 | 22000.0 | 23000.0 | 24000.0 | 25000.0 | 26000.0 | 27000.0 | 28000.0 | 29000.0 | 30000.0 | 31000.0 | 32000.0 | 33000.0 | 34000.0 | 35000.0 | 36000.0 | 37000.0 | 38000.0 | 39000.0 | 40000.0 | 41000.0 | 42000.0 | 43000.0 | 44000.0 | 45000.0 | 46000.0 | 47000.0 | 48000.0 | 49000.0 | 50000.0
 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.02 | 0.022 | 0.02 | 0.026 | 0.032 | 0.044 | 0.066 | 0.082 | 0.2 | 0.216 | 0.41 | 0.492 | 0.66 | 0.818 | 0.968 | 0.978 | 1 | 1 | 0.998 | 1 | 1 | 1 | 1

## Slide 75: Lack of I/O and System Support…
Support for printf, malloc from kernel in CUDA
File system I/O?
GPUfs (ASPLOS 2013):
  POSIX-like file system API
  One file per warp to avoid control divergence
  Weak file system consistency model (close->open)
  Performance API: O_GWRONCE, O_GWRONCE
  Eliminate seek pointer
GPUnet (OSDI 2014): Posix like API for sockets programming on GPGPU.

## Slide 76: Conclusions
GPU Computing is growing in importance due to energy efficiency concerns
GPU architecture has evolved quickly and likely to continue to do so
We discussed some of the important microarchitecture bottlenecks and recent research.
Also discussed some directions for improving programming model