## Slide 1: Advanced Operating Systems (CS 202) Synchronization
(some cache coherence slides adapted from Ian Watson)

## Slide 2: Classic Example
Suppose we have to implement a function to handle withdrawals from a bank account:
  withdraw (account, amount) {
    balance = get_balance(account);
    balance = balance – amount;
    put_balance(account, balance);
    return balance;
  }
Now suppose that you and your father share a bank account with a balance of $1000
Then you each go to separate ATM machines and simultaneously withdraw $100 from the account

## Slide 3: Interleaved Schedules
The problem is that the execution of the two threads can be interleaved:
What is the balance of the account now?
balance = get_balance(account);
balance = balance – amount;
balance = get_balance(account);
balance = balance – amount;
put_balance(account, balance);
put_balance(account, balance);
Execution sequence seen by CPU
Context switch
Notes: Is the bank happy with our implementation?

## Slide 4: How Interleaved Can It Get?
............... get_balance(account);
put_balance(account, balance);
put_balance(account, balance);
balance = balance – amount;
balance = balance – amount;
balance = get_balance(account);
balance = ...................................
How contorted can the interleavings be?
We'll assume that the only atomic operations are reads and writes of individual memory locations
  Some architectures don't even give you that!
We'll assume that a context switch can occur at any time
We'll assume that you can delay a thread as long as you like as long as it's not delayed forever

## Slide 5: Mutual Exclusion
Mutual exclusion to synchronize access to shared resources
  This allows us to have larger atomic blocks
  What does atomic mean?
Code that uses mutual called a critical section
  Only one thread at a time can execute in the critical section
  All other threads are forced to wait on entry
  When a thread leaves a critical section, another can enter
  Example: sharing an ATM with others
What requirements would you place on a critical section?

## Slide 6: Using Locks
  Why is the “return” outside the critical section? Is this ok?
  What happens when a third thread calls acquire?
withdraw (account, amount) {
acquire(lock);
balance = get_balance(account);
balance = balance – amount;
put_balance(account, balance);
release(lock);
return balance;
}
acquire(lock);
balance = get_balance(account);
balance = balance – amount;
balance = get_balance(account);
balance = balance – amount;
put_balance(account, balance);
release(lock);
acquire(lock);
put_balance(account, balance);
release(lock);
Critical Section
Notes:   What happens when blue tries to acquire the lock?

## Slide 7: Stepping back
What does the OS need to support?
  And why? Isnt this an application/programming problem?
Synchronization is hard – why?
Synchronization can be a performance problem – why?
Other semantics than mutual exclusion possible.

## Slide 8: Implementing locks
Software implementations possible
  You should have seen Dekker’s algorithm and possibly Peterson’s algorithm
  They are difficult to get right
  They make assumptions on the system that may no longer hold
    (e.g., memory consistency as we will see shortly)
Most systems offer hardware support

## Slide 9: Using Test-And-Set
Here is our lock implementation with test-and-set:
When will the while return? What is the value of held?
struct lock {
int held = 0;
}
void acquire (lock) {
while (test-and-set(&lock->held));
}
void release (lock) {
lock->held = 0;
}

## Slide 10: Overview
Before we talk deeply about synchronization
  Need to get an idea about the memory model in shared memory systems
  Is synchronization only an issue in multi-processor systems?
What is a shared memory processor (SMP)?
Shared memory processors
  Two primary architectures:
    Bus-based/local network shared-memory machines (small-scale)
    Directory-based shared-memory machines (large-scale)

## Slide 11: Plan…
Introduce and discuss cache coherence
Discuss basic synchronization, up to MCS locks (from the paper we are reading)
Introduce memory consistency and implications
Is this an architecture class???
  The same issues manifest in large scale distributed systems

## Slide 12: Crash course on cache coherence

## Slide 13: Bus-based Shared Memory Organization
Basic picture is simple :-
CPU
Cache
CPU
Cache
CPU
Cache
Shared Bus
Shared
Memory

## Slide 14: Organization
Bus is usually simple physical connection (wires)
Bus bandwidth limits no. of CPUs
Could be multiple memory elements
For now, assume that each CPU has only a single level of cache
Other organizations (e.g., with a network) have NUMA issues

## Slide 15: Problem of Memory Coherence
Assume just single level caches and main memory
Processor writes to location in its cache
Other caches may hold shared copies - these will be out of date
Updating main memory alone is not enough
What happens if two updates happen at (nearly) the same time?
  Can two different processors see them out of order?

## Slide 16: Example
CPU
Cache
CPU
Cache
CPU
Cache
Shared Bus
Shared
Memory
X: 24
Processor 1 reads X: obtains 24 from memory and caches it
Processor 2 reads X: obtains 24 from memory and caches it
Processor 1 writes 32 to X: its locally cached copy is updated
Processor 3 reads X: what value should it get?
Memory and processor 2 think it is 24
Processor 1 thinks it is 32
Notice that having write-through caches is not good enough
1
2
3

## Slide 17: Cache Coherence
Try to make the system behave as if there are no caches!
How? Idea: Try to make every CPU know who has a copy of its cached data?
    too complex!
More practical:
  Snoopy caches
    Each CPU snoops memory bus
    Looks for read/write activity concerned with data addresses which it has cached.
      What does it do with them?
    This assumes a bus structure where all communication can be seen by all.
More scalable solution: ‘directory based’ coherence schemes

## Slide 18: Snooping Protocols
Write Invalidate
  CPU with write operation sends invalidate message
  Snooping caches invalidate their copy
  CPU writes to its cached copy
    Write through or write back?
  Any shared read in other CPUs will now miss in cache and re-fetch new data.

## Slide 19: Snooping Protocols
Write Update
  CPU with write updates its own copy
  All snooping caches update their copy
Note that in both schemes, problem of simultaneous writes is taken care of by bus arbitration - only one CPU can use the bus at any one time.
Harder problem for arbitrary networks

## Slide 20: Update or Invalidate?
Which should we use?
Bus bandwidth is a precious commodity in shared memory multi-processors
  Contention/cache interrogation can lead to 10x or more drop in performance
  (also important to minimize false sharing)
Therefore, invalidate protocols used in most commercial SMPs

## Slide 21: Implementation Issues
In both schemes, knowing if a cached value is not shared (copy in another cache) can avoid sending any messages.
Invalidate description assumed that a cache value update was written through to memory. If we used a ‘copy back’ scheme other processors could re-fetch old value on a cache miss.
We need a protocol to handle all this.

## Slide 22: MESI – locally initiated accesses
Invalid
Modified
Exclusive
Shared
Read
Hit
Read
Hit
Read
Hit
Read
Miss(sh)
Read
Miss(ex)
Write
Hit
Write
Hit
Write
Hit
Write
Miss
RWITM
Invalidate
Mem Read
Mem Read
= bus transaction

## Slide 23: MESI – remotely initiated accesses
Invalid
Modified
Exclusive
Shared
Mem Read
Mem Read
Mem Read
Invalidate
RWITM
RWITM
= copy back

## Slide 24: Both together
Image credit: Wiki page on MESI
By Jugones55 - Own work, GFDL, https://commons.wikimedia.org/w/index.php?curid=7136764
Notes: Image from Wiki page on MESI

## Slide 25: MESI notes
There are other protocols and minor variations (particularly to do with write miss)
Normal ‘write back’ when cache line is evicted is done if line state is M
Multi-level caches
  If caches are inclusive, only the lowest level cache needs to snoop on the bus
    Most modern CPUs have inclusive caches
    But they don’t perform as well as non-inclusive caches

## Slide 26: Cache Coherence summary
Reads and writes are atomic
  What does atomic mean?
    As if there is no cache
Some magic to make things work
  Have performance implications
  …and therefore, have implications on performance of programs

## Slide 27: Directory Schemes
Snoopy schemes do not scale because they rely on broadcast
Directory-based schemes allow scaling.
  avoid broadcasts by keeping track of all PEs caching a memory block, and then using point-to-point messages to maintain coherence
  they allow the flexibility to use any scalable point-to-point network

## Slide 28: Basic Scheme (Censier & Feautrier)
• Assume "k" processors.
• With each cache-block in memory: k presence-bits, and 1 dirty-bit
• With each cache-block in cache: 1valid bit, and 1 dirty (owner) bit
  Read from main memory by PE-i:
    If dirty-bit is OFF then { read from main memory; turn p[i] ON; }
    if dirty-bit is ON then { recall line from dirty PE (cache state to shared); update memory; turn dirty-bit OFF; turn p[i] ON; supply recalled data to PE-i; }
  Write to main memory:
    If dirty-bit OFF then { send invalidations to all PEs caching that block; turn dirty-bit ON; turn P[i] ON; ... }
    ...

## Slide 29: Key Issues
Scaling of memory and directory bandwidth
  Can not have main memory or directory memory centralized
  Need a distributed memory and directory structure
Directory memory requirements do not scale well
  Number of presence bits grows with number of PEs
  Many ways to get around this problem
    limited pointer schemes of many flavors
Industry standard
  SCI: Scalable Coherent Interface