## Slide 1: Designing Secure Processors in the Age of Spectre and Meltdown Nael Abu-Ghazaleh University of California, Riverside nael@cs.ucr.edu

## Slide 2: Architecture support for security
What hardware
Vulnerabilities are
Exploitable by software?
What support can we
offer to improve software
Security?

## Slide 3: Malware is Everywhere!
Over 350,000 malware registered every day!
Notes: The problem is that there is a lot of malware
These are what we see these days, but they are not always visible
Lets jump to what attackers really wants?

## Slide 4: What motivates attackers? One cross-section

## Slide 7
Installs: 80-100 USD per 1000 machines (US); 7-8 USD per 1000 machines (Asia)
  Source: Cabalerro et al. “Measuring pay-per-install...” Usenix 2011

## Slide 8: Underground Malware Economy
Segmented supply chain
E.g., pay-per-exploit ~2013:
  Good guys/bug bounty programs (Google, pwn2own, iDefense, Zdi, …): 2-25K
  Black market: 250K+ for a good zero day
Good guys pay more now, but probably also black market
Bad guys motivated to protect their investments
  Malware continues to become more sophisticated
  …making defense more difficult

## Slide 9: New application spaces
Security no longer just about information
Cloud is ubiquitous
Machine learning everywhere
New threat models

## Slide 12: What’s going on in Architecture? Circa 2010
Moore’s law still here
  barely (10nm->7nm->?)
Dennard’s scaling ended
  Power wall
We have transistors, but we can’t power them
  Dark silicon
  Can be used for important applications such as security

## Slide 13: Opportunities: Architecture & Security?
Vulnerabilities originating in architecture
  Side and covert channels
  Speculation attacks
  Fault injection
  Hardware trojans, …
Defenses rooted in architecture
  Do no harm
    Avoid vulnerabilities in architecture/HW
  Help software
    Security abstractions/mechanisms
    Computational support for expensive defenses
Attacks
Defenses

## Slide 14: Overview—Spectulative execution attacks
Attack flavor--Speculation attacks
  Overview, and SpectreRSB
Defense flavor
  Do no harm: Keep speculation, but prevent vulnerability
    SafeSpec: close the speculative side channels
    SpecCFI: prevent malicious speculation

## Slide 15: New Vulnerabilities in Modern Processors
Spectre v1/v2/Meltdown(v3)
Jan 2018
May 2018
July 2018
Spectre v1.1
Spectre v1.2
SGXpectre
Speculative store bypass (v4)
SpectreRSB(v5?) / ret2spec
NetSpectre
Aug 2018
SpectreNG
May 2019
MDS/RIDL/Zombieload

## Slide 16: Attack Ingredients
Speculative Execution
Side Channel
Fetch
Reg
Read
ALU
Data
Memory
Reg
Write
Notes: Speculative executions which occers on pipelined processors.. And if you are curious this is a picture from a move called Charly chapplen modern time  it is a good movie that you can watch on netflix

## Slide 17: Side Channel Attacks
Running programs share resources
What one process does can affect the other

## Slide 18: Cache Side Channel Attacks
Access to the data inside the cache is fast
Loading data from memory is slow
Exploits timing differences that are introduced by the caches
  Flush and reload
  Prime and probe
  …

## Slide 19
Side Channel: Flush and Reload Attack
Cache
L2
L1-I
Victim
1- Flush each line in the critical data
2- Victim accesses critical data
3- Reload critical data (measure time)
Evicted
Time
CPU1
ways
sets
L1-D
L2
L1-I
Attacker
L1-D
Shared L3
CPU2

## Slide 20: Ingredient 2: Speculative Execution

## Slide 21: Speculative Execution
Fetch
Decode
Execute
Memory
Write back
Fetch
Decode
Execute
Memory
Write back
Fetch
Decode
Execute
Memory
Write back
add $r1,r2
beq $r1,$r3,#16
add $r3,$r2
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
stall?
Modern processors are super-pipelined and superscalar
  May take up to several hundred cycles to resolve a branch

## Slide 22: Speculative Execution (Correct guess)
Fetch
Decode
Execute
Memory
Write back
Fetch
Decode
Execute
Memory
Write back
Fetch
Decode
Execute
Memory
Write back
add $r1,r2
beq $r1,$r3,#16
add $r3,$r2
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Speculative
Right guess

## Slide 23
Fetch
Decode
Execute
Memory
Write back
Fetch
Decode
Execute
Memory
Write back
Fetch
Decode
Execute
Memory
Write back
add $r1,r2
beq $r1,$r3,#16
sub $r3,$r2
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
Cycle 6
Cycle 7
Cycle 8
Speculative
Wrong guess
Fetch
Decode
Execute
Memory
Write back
add $r3,$r2
Cleaning up for miss-speculation:
- Remove squashed instructions affect on architectural state
- Doesn't remove squashed instructions affects on microarchitectural state
Speculative Execution (Wrong guess) .
Notes: In fact when we wait the lost opportunity could be 200 cycles or more.. Threrefore, to take advantage of this oprrutunity we use speculation
What is spculaiton ? We simply guess what is the results of the branch -- > if we guess correctly then we manage to fill the pipline and if we do not guess correctly then we romve the effect and we havent lose anything because anyway we would have been waiting .
(20-25 stages on intel's processors)

## Slide 24: Microarchitectural Prediction Structures
Target
Predictor
Directional
Predictor
Return Address
Predictor
RSB
Jump over ASLR: Micro 2016
BranchScope, ASPLOS 2018
SpectreRSB (Spectre v5), WOOT’18
Notes: You don’t really have to know the details
BTB: for branches that are indirect (means the location that they jump to is a variable not an imidate )
then I use something called the target predictor
PHT: try to guess wither we are taking a branch or not taking it, this is called directional predctor
RSB: Finally for return instructions, becouase they don’t follow privouse history .. So think about a printf statement , just beucae it return to the current palace at this call does not mean that it will return to it in the next call. So we use something called the resturn stack buffer which keeps the address of the call to use as prediction.
The original spectre paper showld attacks on the first two companents and my attack actually targets the last component the RSB.

## Slide 25: Return Stack Buffers (RSB)
Software Stack
RSB
main(){
call fun1;
add r2,r3;
return; }
fun1(){
call fun2;
add r2,r3;
return;}
fun2(){
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000043
0X00000055
0X00000056
fun1
0X00000080
0X00000012
0X00000080
0X00000012
arguments
arguments
0X00000042
0X00000042
arguments
fun2

## Slide 26: Return Stack Buffers (RSB)
Software Stack
RSB
main(){
call fun1;
add r2,r3;
return;
}
fun1(){
call fun2;
add r2,r3;
return;
}
fun2(){
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000043
0X00000055
0X00000056
fun1
0X00000080
0X00000012
0X00000080
0X00000012
arguments
arguments
0X00000042
0X00000042
arguments
fun2
popRSB
Memory request

## Slide 27: Return Stack Buffers (RSB)
Software Stack
RSB
main(){
call fun1;
add r2,r3;
return;
}
fun1(){
call fun2;
add r2,r3;
return;
}
fun2(){
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000043
0X00000055
0X00000056
fun1
0X00000080
0X00000012
0X00000080
0X00000012
arguments
arguments
0X00000042
arguments
fun2
Memory response
0X00000042
?=

## Slide 28: Return Stack Buffers (RSB)
Software Stack
RSB
main(){
call fun1;
add r2,r3;
return;
}
fun1(){
call fun2;
add r2,r3;
return;
}
fun2(){
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000043
0X00000055
0X00000056
fun1
0X00000080
0X00000012
0X00000080
0X00000012
arguments
arguments
Memory response
0X00000042
?=
if predicted (RSB value) == actual (software stack value)
Continue execution  gained performance
else
Squash speculative instructions  No performance loss
0X00000042

## Slide 29: Putting all Together– Attacks!

## Slide 30: SpectreRSB Attack Steps
Force
mis-speculation
Read unauthorized data
Leak it (side channel)
Validation and permission checks are performed deep in the pipeline
Speculative instructions leave side-effects in micro-architectural structures such as caches

## Slide 31: SpectreRSB Example
Software Stack
RSB
main(){
call speculative;
check_array();
return;
}
Speculative(){
call pollute;
secret = kernel_mem;
array[secret];
}
pollute(){
pop_software_stack;
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000055
0X00000056
speculative
0X00000080
0X00000012
0X00000080
0X00000012
arguments
arguments
0X00000042
0X00000042
arguments
pollute
0X00000057
Memory request
popRSB
Cache
array[1]
assuming
secret = 1

## Slide 32: SpectreRSB Example
Software Stack
RSB
main(){
call speculative;
check_array();
return;
}
Speculative(){
call pollute;
secret = kernel_mem;
array[secret];
}
pollute(){
pop_software_stack;
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000055
0X00000056
speculative
0X00000080
0X00000012
0X00000080
0X00000012
arguments
arguments
0X00000057
Cache
array[1]
assuming
secret = 1
0X00000042
Memory response
?=
Mis-speculation

## Slide 33: SpectreRSB Example
Software Stack
RSB
main(){
call speculative;
check_array();
return;
}
Speculative(){
call pollute;
secret = kernel_mem;
array[secret];
}
pollute(){
pop_software_stack;
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000055
0X00000056
0X00000080
0X00000012
0X00000080
arguments
0X00000057
Cache
array[1]
assuming
secret = 1
Memory response
0X00000012
check_array(){
Time(array[0]);
Time(array[1]);
}
Time
secret value = 1

## Slide 34: SafeSpec [DAC’19]
Fetch
Decode
...
Commit
Processor pipeline
Shadow
state
Committed
state
speculative
update
update
update
Mis-speculation
Notes: Use SpectreRSB examples as demonstration for shadow structures
Use temporary structures (Shadow) to hold any state that is produced speculatively

## Slide 35
Fetch
Decode
...
Commit
Processor pipeline
Shadow
state
Committed
state
Squash
annul
annul
annul
move
SafeSpec [DAC’19]
Notes: Use SpectreRSB examples as demonstration for shadow structures
Use temporary structures (Shadow) to hold any state that is produced speculatively

## Slide 36: SafeSpec Example
Software Stack
RSB
main(){
call speculative;
check_array();
return;
}
Speculative(){
call pollute;
secret = kernel_mem;
array[secret];
}
pollute(){
pop_software_stack;
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000055
0X00000056
speculative
0X00000080
0X00000012
0X00000080
0X00000012
arguments
arguments
0X00000042
0X00000042
arguments
pollute
0X00000057
Memory request
popRSB
Shadow cache
array[1]
assuming
secret = 1
Cache

## Slide 37: SafeSpec Example
Software Stack
RSB
main(){
call speculative;
check_array();
return;
}
Speculative(){
call pollute;
secret = kernel_mem;
array[secret];
}
pollute(){
pop_software_stack;
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000055
0X00000056
speculative
0X00000080
0X00000012
0X00000080
0X00000012
arguments
arguments
0X00000057
0X00000042
Memory response
?=
Mis-speculation
Shadow cache
array[1]
assuming
secret = 1
Cache
if predicted (RSB value) == actual (software stack value)
Continue execution  Move shadow cache state to cache state (on commit stage)
else
Squash speculative instructions  Annul shadow cache state

## Slide 38: SafeSpec Example
Software Stack
RSB
main(){
call speculative;
check_array();
return;
}
Speculative(){
call pollute;
secret = kernel_mem;
array[secret];
}
pollute(){
pop_software_stack;
return;
}
main
0X00000010
0X00000011
0X00000012
0X00000013
0X00000040
0X00000041
0X00000042
0X00000055
0X00000056
0X00000080
0X00000012
0X00000080
arguments
0X00000057
Memory response
0X00000012
check_array(){
Time(array[0]);
Time(array[1]);
}
Time
assuming
secret = 1
Shadow cache
Cache
Attack failed

## Slide 39: Implementation and Results
Integrated SafeSpec to MARSSx86
Evaluated the performance using SPEC2017
Baseline

## Slide 40: Force mis-speculation: Spectre V2
Attacker
Victim
jmp
Address tag | Target
A:
B:
A
C
jmp
A:
B:
C:
Branch Target Buffer
Result: when victim executes, CPU uses injected target to start speculative execution at an address of attacker’s choice!
C:
Spectre
gadget

## Slide 41: Intuition
Attacker
Victim
Branch
Target
0x10
PC
jmp
rax
…
BHSR
0x10
A
0x10
A
Branch Predictor (BPU)
Victim’s Control Flow Graph
0x20
B
0x20
0x20

## Slide 42: Control Flow Integrity (CFI)
State of the art solution to mitigate Control-Flow Hijacking attacks
    Software: LLVM, GCC, Android, Microsoft, etc..
    Hardware: Intel Control-flow Enforcement Technology (CET) and ARM Branch target Indicators (BTI)
Idea: software execution must follow only legal paths within a control-flow graph (CFG) determined ahead of time
Implementation requires:
  1- Compute CFG of the program
  2- Regulate the control-flow transfers while program is executing
Can’t prevent spectre attacks since the regulation happen after instructions commits
Notes: Because of its effectiveness against control-flow
hijacking attacks, CFI has been adopted by both commodity
software and hardware.

## Slide 43
CFG
construction
Speculative
regulation
at run-time
Compiler
Valid Target Set
t1
t4
t2
t3
t5
Mov rbx,23
Add rax,1
Jmp rbx
...
...
Jmp rbx
CFI_check
...
SpecCFI
Forward-edge
Backward-edge
CFI_check
CFI_check
RSB
Shadow RSB
Similar to CFI
In contrast to CFI
Notes: Any CFI mechanism consists of two abstract components: the (often static) analysis component that recovers the Control-Flow Graph (CFG) of the application (at different levels of precision) and the dynamic enforcement mechanism that restricts control flows according to the generated CFG.
For normal programs, this
results in negligible performance degradation since it only
prevents speculation with mismatching CFI labels, which will
most likely result in misspeculation. By stopping misspeculation,
we benefit from avoiding cache pollution and other
resource waste during misspeculation.

## Slide 44: Performance Impact
Notes: Because of its effectiveness against control-flow
hijacking attacks, CFI has been adopted by both commodity
software and hardware.

## Slide 45: Number of Inserted Fences
Notes: Because of its effectiveness against control-flow
hijacking attacks, CFI has been adopted by both commodity
software and hardware.

## Slide 46: Concluding Remarks
SpecCFI is a complete defense against mis-speculation targeting BTB and RSB
SpecCFI interduce the idea of using CFI as a defense against speculation attacks
  Verifying forward-edge
  Verifying backward-edge
SpecCFI has little impact on performance, and with minimal hardware complexity
Combined with recent proposals to mitigate Spectre-PHT, we believe SpecCFI mitigates the threat from known speculation attacks
Notes: Because of its effectiveness against control-flow
hijacking attacks, CFI has been adopted by both commodity
software and hardware.
of CFI on the instructions in the speculative path labels match protecting against Spectre-BTB attacks
backward-edge using a unified shadow call stack, protecting against Spectre-RSB attacks

## Slide 47: Relaxed Fences Performance
Notes: Because of its effectiveness against control-flow
hijacking attacks, CFI has been adopted by both commodity
software and hardware.

## Slide 48: Overhead Breakdown
Notes: Because of its effectiveness against control-flow
hijacking attacks, CFI has been adopted by both commodity
software and hardware.

## Slide 49: Implementation Overhead
Notes: Because of its effectiveness against control-flow
hijacking attacks, CFI has been adopted by both commodity
software and hardware.

## Slide 50: Architecture support for defenses

## Slide 52: Traditional Software Malware Detection
Static malware detection
  Search for signatures in the executable
  Can detect all known malware with no false alarms
  Can be evaded by new malware and obfuscated malware
Dynamic malware detection
  Monitors the behavior of the program
  Can detect unknown malware
  High performance overhead (not practical)

## Slide 53: Hardware Malware Detectors (HMDs)
Use Machine Learning: detect malware as computational anomaly
Use low-level features collected from the hardware
Can be always-on without adding performance overhead
Notes: Qualcomm Snap the dragon

## Slide 54: Results
HPCA 2015 - San Francisco, CA

## Slide 55: Malware Aware Processors
Instruction Fetch
Instruction Cache
Rename/Decode
Branch Prediction
Physical Register File
Issue
Functional Units
ROB & Architectural Register File
MMU
Data Cache
Exception Unit
MAP
Notes: Collect sub-semantic features
Have a simple machine learning engine
Check executing program in real-time

## Slide 56: MAP FPGA Implementation

## Slide 57
Future of secure processors

## Slide 58: Some Trends (Arch2030)
Acceptance of Moore’s law ending
Specialization happening at scale
Cloud is ubiquitous
Machine learning important workload
3D devices, quantum, and DNA computing
Notes: inflection point of changes in terms of computer architecture
Earlier I have showed you the trends in computer architecture in 2010 .. as a results of those trends we are now at different place in computer terms of architecture .. Recently there was this computer architecture 2030 vision workshop were leaders in computer architecture got together and predicted what is going to happen .. And we are at an inflection point of changes in terms of computer architecture because of the end of moores law.. Computing models are changing we are investing in specialization at scale,.. the cloud is becoming ubiquitous.. We see that machine learning is becoming an important workload specialty in smart systems.

## Slide 59: Not just the CPU

## Slide 60: Side and covert channels are everywhere!
“Rendered Insecure: GPU side channel attacks are practical!”, to appear
in CCS 2018 – vulnerability reported to Nvidia, AMD and Intel

## Slide 61: Conclusions/Summary
Security traditionally considered a software problem to be solved in software
…but we see that architectures can be a source of vulnerability
  Architectures must be designed with security in mind
  …but they can also offer security mechanisms for software
Meltdown/Spectre will force a seismic rethinking of how to design speculative CPUs
  Will be played out over the next few years…