## Slide 1: RIC: Relaxed Inclusion Caches for Mitigating LLC Side-Channel Attacks
Nael Abu-Ghazaleh, University of California, Riverside
Mehmet Kayaalp, IBM Research
Khaled N. Khasawneh, University of California, Riverside
Hodjat Asghari Esfeden, University of California, Riverside
Jesse Elwell, Vencore Labs
Dmitry Ponomarev, Binghamton University
Aamer Jaleel, NVIDIA

## Slide 2: Cache Side Channel
f2 85 5c 06
6a 91 4e 0c
c4 fc da a8
d5 37 e9 9c
28 1e 4c 24
09 bf 15 82
30 6f 53 d9
a4 49 2d 0e
S-Box
SubBytes
Set-associative cache
ways
sets

## Slide 3: Flush+Reload Attack
Cache
L2
L1-I
Victim
1- Flush each line in the critical data
2- Victim accesses critical data
3- Reload critical data (measure time)
Evicted
Time
Core 1
ways
sets
L1-D
L2
L1-I
Attacker
L1-D
Shared L3
Core 2

## Slide 4: Prime+Probe: L1 Attack
L1 Cache
ways
sets
L2
L1-I
L1-D
Attacker
Victim
2-way SMT core
1- Prime each cache set
2- Victim accesses critical data
3- Probe each cache set (measure time)
Evicted
Time

## Slide 5: Prime+Probe: LLC Attack
Next access of the victim brings in critical data from memory
  To L1-D, L2, and L3; evicting attacker’s data from L3
Attacker detects accesses by looking at L3 state
Back-invalidation from inclusiveness makes critical accesses visible to attacker
L2
L1-I
Victim
2- Victim accesses critical data
CPU1
L1-D
L2
L1-I
Attacker
L1-D
Shared L3
CPU2
1- Prime each cache set
3- Probe each cache set (measure time)
Inclusive
Evict critical data
Back-invalidations

## Slide 6: Operation of Inclusive Caches
Victim
Attacker
L1
L1
LLC
Invalidated in L1
L1 miss!
Visible access to LLC
Back-Invalidation

## Slide 7: Relaxed Inclusion Caches
Victim
Attacker
L1
L1
LLC
Read only
Stays in L1
L1 hit!
No visible access to LLC

## Slide 8: Cache Inclusiveness
Inclusive: Each cache line in local cache exists also in shared cache
  If not in shared cache, it cannot be in ANY local caches
  Provides snoop filtering: no unnecessary cache traffic
Non-inclusive: Save cache space by not duplicating data
  For a cache miss, need to snoop all other local
  Extra snoop filtering hardware is required to eliminate unnecessary cache traffic
 | Inclusive | Non-inclusive
Shared cache hit | Copy | Copy
Shared cache evict | Evict from all local caches | Do nothing
Shared cache miss | Go to memory | Snoop local caches
Data duplication | All local data | Some local data

## Slide 9: Relaxed Inclusion Caches
Snoop filtering benefit is not relevant in some cases
  If the data cannot be in any other local cache (private)
  If the data cannot be in a modified state in any other local cache (read-only)
If the data is read-only, there is no problem
  Even if another cache has a copy, we can still ignore it
If the data is thread-private, and the thread is pinned to a core
  If we schedule the thread somewhere else, we need to write back the modified data from the local cache
 | Inclusive | Non-inclusive | Relaxed Inclusion Caches
Shared cache hit | Copy | Copy | Copy
Shared cache evict | Evict from all local caches | Do nothing | Do nothing if read-only or thread-private
Shared cache miss | Go to memory | Snoop local caches | Go to memory
Data duplication | All local data | Some local data | Only shared writable local data

## Slide 10: RIC Implementation
System software can manage relaxed-inclusion bit on a page basis
  Existing page table entry permissions extended to mark RIC data
    Read-only or thread private
A single bit added per cache line
  The relaxed-inclusion bit is copied from TLB on a cache fill
  Minimal hardware overhead

## Slide 11: Security Analysis
In RIC, the attacker cannot evict victim’s data
But the victim can still evict its own data
If the critical data fits in the local cache, side channel is eliminated
Critical accesses for AES with different local cache sizes

## Slide 12: Performance Analysis
RIC eliminates data duplication for all read-only and thread-private data, increasing effective cache size
  e.g. all instructions can be evicted from LLC
Parameters
4 cores
32KB 4-way L1D, L1I
256KB 8-way L2
4 MB 16-way shared L3

## Slide 13: Reduction in Back-invalidates
Notes: This figure shows that the percentage of back invalidates eliminated by RIC is fairly constant across the benchmarks (more elimination in 2MB LLC > we have more replacement in 2MB LLC, so we have more elimination by RIC in this case).

## Slide 14: RIC Results Summary

## Slide 15: Conclusion
Inclusive LLCs allow attackers to monitor victim’s critical accesses
  But efficient because they enable snoop filtering
RIC relaxes this property to eliminate the side channel
  While retaining snoop filtering
RIC is a simple mechanism that improves performance compared to inclusive caches